## Slide 1: CS252 Graduate Computer Architecture Spring 2014 Lecture 3: CISC versus RISC
Krste Asanovic
krste@eecs.berkeley.edu
http://inst.eecs.berkeley.edu/~cs252/sp14

## Slide 2: Last Time in Lecture 2
First 130 years of CompArch, from Babbage to IBM 360
  Move from calculators (no conditionals) to fully programmable machines
  Rapid change started in WWII (mid-1940s), move from electro-mechanical to pure electronic processors
Cost of software development becomes a large constraint on architecture (need compatibility)
IBM 360 introduces notion of “family of machines” running same ISA but very different implementations
  Six different machines released on same day (April 7, 1964)
  “Future-proofing” for subsequent generations of machine

## Slide 3: Instruction Set Architecture (ISA)
The contract between software and hardware
Typically described by giving all the programmer-visible state (registers + memory) plus the semantics of the instructions that operate on that state
IBM 360 was first line of machines to separate ISA from implementation (aka. microarchitecture)
Many implementations possible for a given ISA
  E.g., the Soviets build code-compatible clones of the IBM360, as did Amdahl after he left IBM.
  E.g.2., today you can buy AMD or Intel processors that run the x86-64 ISA.
  E.g.3: many cellphones use the ARM ISA with implementations from many different companies including TI, Qualcomm, Samsung, Marvell, etc.
We use Berkeley RISC-V 2.0 as standard ISA in class
  www.riscv.org

## Slide 4: Control versus Datapath
Processor designs can be split between datapath, where numbers are stored and arithmetic operations computed, and control, which sequences operations on datapath
Biggest challenge for early computer designers was getting control circuitry correct
Maurice Wilkes invented the idea of microprogramming to design the control unit of a processor for EDSAC-II, 1958
  Foreshadowed by Babbage’s “Barrel” and mechanisms in earlier programmable calculators
Condition?
Control
Main Memory
Address
Data
Control Lines
Datapath
PC
Inst. Reg.
Registers
ALU
Instruction
Busy?

## Slide 5: Technology Influence
When microcode appeared in 50s, different technologies for:
  Logic: Vacuum Tubes
  Main Memory: Magnetic cores
  Read-Only Memory: Diode matrix, punched metal cards,…
Logic very expensive compared to ROM or RAM
ROM cheaper than RAM
ROM much faster than RAM

## Slide 6: Microcoded CPU
Datapath
Main Memory
(holds user program written in macroinstructions, e.g., x86, RISC-V)
Address
Data
Decoder
µPC
Microcode ROM
(holds fixed µcode instructions)
Next State
Control Lines
Opcode
Condition
Busy?

## Slide 7: Single Bus Datapath for Microcoded RISC-V
Microinstructions written as register transfers:
MA:=PC means RegSel=PC; RegW=0; RegEn=1; MALd=1
B:=Reg[rs2] means RegSel=rs2; RegW=0; RegEn=1; BLd=1
Reg[rd]:=A+B means ALUop=Add; ALUEn=1; RegSel=rd; RegW=1
Condition?
Main Memory
PC
Registers
ALU
32 (PC)
rd
rs1
rs2
Register RAM
Address
In
Data Out
Instruction Reg.
Mem. Address
B
A
Immediate
ImmEn
RegEn
ALUEn
MemEn
ALUOp
MemW
ImmSel
RegW
BLd
InstLd
MALd
ALd
RegSel
Busy?
Opcode

## Slide 8: RISC-V Instruction Execution Phases
Instruction Fetch
Instruction Decode
Register Fetch
ALU Operations
Optional Memory Operations
Optional Register Writeback
Calculate Next Instruction Address

## Slide 9: Microcode Sketches (1)
Instruction Fetch: MA,A:=PC
PC:=A+4
wait for memory
IR:=Mem
dispatch on opcode
ALU: A:=Reg[rs1]
B:=Reg[rs2]
Reg[rd]:=ALUOp(A,B)
goto instruction fetch
ALUI: A:=Reg[rs1]
B:=ImmI //Sign-extend 12b immediate
Reg[rd]:=ALUOp(A,B)
goto instruction fetch

## Slide 10: Microcode Sketches (2)
LW: A:=Reg[rs1]
B:=ImmI //Sign-extend 12b immediate
MA:=A+B
wait for memory
Reg[rd]:=Mem
goto instruction fetch
JAL: Reg[rd]:=A // Store return address
A:=A-4 // Recover original PC
B:=ImmJ // Jump-style immediate
PC:=A+B
goto instruction fetch
Branch: A:=Reg[rs1]
B:=Reg[rs2]
if (!ALUOp(A,B)) goto instruction fetch //Not taken
A:=PC //Microcode fall through if branch taken
A:=A-4
B:=ImmB
PC:=A+B
goto instruction fetch

## Slide 11: Pure ROM Implementation
How many address bits?
  |µaddress| = |µPC|+|opcode|+ 1 + 1
How many data bits?
  |data| = |µPC|+|control signals| = |µPC| + 18
Total ROM size = 2|µaddress|x|data|
µPC
ROM
Address
Data
Opcode
Cond?
Busy?
Next µPC
Control Signals

## Slide 12: Pure ROM Contents
Address | Data
µPC Opcode Cond? Busy? | Control Lines Next µPC
fetch0 X X X | MA,A:=PC fetch1
fetch1 X X 1 | fetch1
fetch1 X X 0 | IR:=Mem fetch2
fetch2 ALU X X | PC:=A+4 ALU0
fetch2 ALUI X X | PC:=A+4 ALUI0
fetch2 LW X X | PC:=A+4 LW0
….
ALU0 X X X | A:=Reg[rs1] ALU1
ALU1 X X X | B:=Reg[rs2] ALU2
ALU2 X X X | Reg[rd]:=ALUOp(A,B) fetch0

## Slide 13: Single-Bus Microcode RISC-V ROM Size
Instruction fetch sequence 3 common steps
~12 instruction groups
Each group takes ~5 steps (1 for dispatch)
Total steps 3+12*5 = 63, needs 6 bits for µPC
Opcode is 5 bits, ~18 control signals
Total size = 2(6+5+2)x(6+18)=213x24 = ~25KB!

## Slide 14: Reducing Control Store Size
Reduce ROM height (#address bits)
  Use external logic to combine input signals
  Reduce #states by grouping opcodes
Reduce ROM width (#data bits)
  Restrict µPC encoding (next,dispatch,wait on memory,…)
  Encode control signals (vertical µcoding, nanocoding)

## Slide 15: Single-Bus RISC-V Microcode Engine
µPC
Decode
ROM
Address
Data
Opcode
Cond?
Busy?
Control Signals
+1
fetch0
µPC Jump Logic
µPC jump
µPC jump = next | spin | fetch | dispatch | ftrue | ffalse

## Slide 16: µPC Jump Types
next increments µPC
spin waits for memory
fetch jumps to start of instruction fetch
dispatch jumps to start of decoded opcode group
fture/ffalse jumps to fetch if Cond? true/false

## Slide 17: Encoded ROM Contents
Address | Data
µPC | Control Lines Next µPC
fetch0 | MA,A:=PC next
fetch1 | IR:=Mem spin
fetch2 | PC:=A+4 dispatch
ALU0 | A:=Reg[rs1] next
ALU1 | B:=Reg[rs2] next
ALU2 | Reg[rd]:=ALUOp(A,B) fetch
Branch0 | A:=Reg[rs1] next
Branch1 | B:=Reg[rs2] next
Branch2 | A:=PC ffalse
Branch3 | A:=A-4 next
Branch4 | B:=ImmB next
Branch5 | PC:=A+B fetch

## Slide 18: Implementing Complex Instructions
Memory-memory add: M[rd] = M[rs1] + M[rs2]
Address | Data
µPC | Control Lines Next µPC
MMA0 | MA:=Reg[rs1] next
MMA1 | A:=Mem spin
MMA2 | MA:=Reg[rs2] next
MMA3 | B:=Mem spin
MMA4 | MA:=Reg[rd] next
MMA5 | Mem:=ALUOp(A,B) spin
MMA6 | fetch
Complex instructions usually do not require datapath modifications, only extra space for control program
Very difficult to implement these instructions using a hardwired controller without substantial datapath modifications

## Slide 19: Horizontal vs Vertical µCode
Horizontal µcode has wider µinstructions
  Multiple parallel operations per µinstruction
  Fewer microcode steps per macroinstruction
  Sparser encoding  more bits
Vertical µcode has narrower µinstructions
  Typically a single datapath operation per µinstruction
      separate µinstruction for branches
  More microcode steps per macroinstruction
  More compact  less bits
Nanocoding
  Tries to combine best of horizontal and vertical µcode
# µInstructions
Bits per µInstruction

## Slide 20: Nanocoding
MC68000 had 17-bit µcode containing either 10-bit µjump or 9-bit nanoinstruction pointer
  Nanoinstructions were 68 bits wide, decoded to give 196 control signals
µcode ROM
nanoaddress
µcode
next-state
µaddress
PC (state)
nanoinstruction ROM
data
Exploits recurring control signal patterns in µcode, e.g.,
ALU0 A  Reg[rs1]
...
ALUi0 A  Reg[rs1]
...

## Slide 21: IBM 360: Initial Implementations
        Model 30 . . . Model 70
Storage 8K - 64 KB 256K - 512 KB
Datapath 8-bit 64-bit
Circuit Delay 30 nsec/level 5 nsec/level
Local Store Main Store Transistor Registers
Control Store Read only 1sec Conventional circuits
IBM 360 instruction set architecture (ISA) completely hid the underlying technological differences between various models.
Milestone: The first true ISA designed as portable hardware-software interface!
With minor modifications it still survives today!

## Slide 22: Microprogramming in IBM 360
Only the fastest models (75 and 95) were hardwired
 | M30 | M40 | M50 | M65
Datapath width (bits) | 8 | 16 | 32 | 64
µinst width (bits) | 50 | 52 | 85 | 87
µcode size (K µinsts) | 4 | 4 | 2.75 | 2.75
µstore technology | CCROS | TCROS | BCROS | BCROS
µstore cycle (ns) | 750 | 625 | 500 | 200
memory cycle (ns) | 1500 | 2500 | 2000 | 750
Rental fee ($K/month) | 4 | 7 | 15 | 35

## Slide 23: Microcode Emulation
IBM initially miscalculated the importance of software compatibility with earlier models when introducing the 360 series
Honeywell stole some IBM 1401 customers by offering translation software (“Liberator”) for Honeywell H200 series machine
IBM retaliated with optional additional microcode for 360 series that could emulate IBM 1401 ISA, later extended for IBM 7000 series
  one popular program on 1401 was a 650 simulator, so some customers ran many 650 programs on emulated 1401s
  (650 simulated on 1401 emulated on 360)

## Slide 24: Microprogramming thrived in Seventies
Significantly faster ROMs than DRAMs were available
For complex instruction sets, datapath and controller were cheaper and simpler
New instructions , e.g., floating point, could be supported without datapath modifications
Fixing bugs in the controller was easier
ISA compatibility across various models could be achieved easily and cheaply
Except for the cheapest and fastest machines, all computers were microprogrammed

## Slide 25: “Iron Law” of Processor Performance
Instructions per program depends on source code, compiler technology, and ISA
Cycles per instructions (CPI) depends on ISA and µarchitecture
Time per cycle depends upon the µarchitecture and base technology
Time = Instructions Cycles Time
Program Program * Instruction * Cycle

## Slide 26: CPI for Microcoded Machine
Inst 3
7 cycles
Inst 1
Inst 2
5 cycles
10 cycles
Total clock cycles = 7+5+10 = 22
Total instructions = 3
CPI = 22/3 = 7.33
CPI is always an average over a large number of instructions.
Time

## Slide 27: First Microprocessor Intel 4004, 1971
4-bit accumulator architecture
8µm pMOS
2,300 transistors
3 x 4 mm2
750kHz clock
8-16 cycles/inst.
Made possible by new integrated circuit technology
[© Intel]

## Slide 28: Microprocessors in the Seventies
Initial target was embedded control
  First micro, 4-bit 4004 from Intel, designed for a desktop printing calculator
  Constrained by what could fit on single chip
  Accumulator architectures, similar to earliest computers
  Hardwired state machine control
8-bit micros (8085, 6800, 6502) used in hobbyist personal computers
  Micral, Altair, TRS-80, Apple-II
  Usually had 16-bit address space (up to 64KB directly addressable)
  Often came with simple BASIC language interpreter built into ROM or loaded from cassette tape.
28

## Slide 29: VisiCalc – the first “killer” app for micros
Microprocessors had little impact on conventional computer market until VisiCalc spreadsheet for Apple-II
Apple-II used Mostek 6502 microprocessor running at 1MHz
[ Personal Computing Ad, 1979 ]
Floppy disks were originally invented by IBM as a way of shipping IBM 360 microcode patches to customers!

## Slide 30: DRAM in the Seventies
Dramatic progress in semiconductor memory technology
1970, Intel introduces first DRAM, 1Kbit 1103
1979, Fujitsu introduces 64Kbit DRAM
=> By mid-Seventies, obvious that PCs would soon have >64KBytes physical memory
30

## Slide 31: Microprocessor Evolution
Rapid progress in 70s, fueled by advances in MOSFET technology and expanding markets
Intel i432
  Most ambitious seventies’ micro; started in 1975 - released 1981
  32-bit capability-based object-oriented architecture
  Instructions variable number of bits long
  Severe performance, complexity, and usability problems
Motorola 68000 (1979, 8MHz, 68,000 transistors)
  Heavily microcoded (and nanocoded)
  32-bit general-purpose register architecture (24 address pins)
  8 address registers, 8 data registers
Intel 8086 (1978, 8MHz, 29,000 transistors)
  “Stopgap” 16-bit processor, architected in 10 weeks
  Extended accumulator architecture, assembly-compatible with 8080
  20-bit addressing through segmented addressing scheme
31

## Slide 32: IBM PC, 1981
Hardware
  Team from IBM building PC prototypes in 1979
  Motorola 68000 chosen initially, but 68000 was late
  IBM builds “stopgap” prototypes using 8088 boards from Display Writer word processor
  8088 is 8-bit bus version of 8086 => allows cheaper system
  Estimated sales of 250,000
  100,000,000s sold
Software
  Microsoft negotiates to provide OS for IBM. Later buys and modifies QDOS from Seattle Computer Products.
Open System
  Standard processor, Intel 8088
  Standard interfaces
  Standard OS, MS-DOS
  IBM permits cloning and third-party software

## Slide 33
[ Personal Computing Ad, 11/81]

## Slide 34: Microprogramming: early Eighties
Evolution bred more complex micro-machines
  Complex instruction sets led to need for subroutine and call stacks in µcode
  Need for fixing bugs in control programs was in conflict with read-only nature of µROM
  Writable Control Store (WCS) (B1700, QMachine, Intel i432, …)
With the advent of VLSI technology assumptions about ROM & RAM speed became invalid more complexity
Better compilers made complex instructions less important.
Use of numerous micro-architectural innovations, e.g., pipelining, caches and buffers, made multiple-cycle execution of reg-reg instructions unattractive

## Slide 35: Writable Control Store (WCS)
Implement control store in RAM not ROM
  MOS SRAM memories now almost as fast as control store (core memories/DRAMs were 2-10x slower)
  Bug-free microprograms difficult to write
User-WCS provided as option on several minicomputers
  Allowed users to change microcode for each processor
User-WCS failed
  Little or no programming tools support
  Difficult to fit software into small space
  Microcode control tailored to original ISA, less useful for others
  Large WCS part of processor state - expensive context switches
  Protection difficult if user can change microcode
  Virtual memory required restartable microcode

## Slide 36: Analyzing Microcoded Machines
John Cocke and group at IBM
  Working on a simple pipelined processor, 801, and advanced compilers inside IBM
  Ported experimental PL.8 compiler to IBM 370, and only used simple register-register and load/store instructions similar to 801
  Code ran faster than other existing compilers that used all 370 instructions! (up to 6MIPS whereas 2MIPS considered good before)
Emer, Clark, at DEC
  Measured VAX-11/780 using external hardware
  Found it was actually a 0.5MIPS machine, although usually assumed to be a 1MIPS machine
  Found 20% of VAX instructions responsible for 60% of microcode, but only account for 0.2% of execution time!
VAX8800
  Control Store: 16K*147b RAM, Unified Cache: 64K*8b RAM
  4.5x more microstore RAM than cache RAM!

## Slide 37: IC Technology Changes Tradeoffs
Logic, RAM, ROM all implemented using MOS transistors
Semiconductor RAM ~ same speed as ROM

## Slide 38: Nanocoding
MC68000 had 17-bit µcode containing either 10-bit µjump or 9-bit nanoinstruction pointer
  Nanoinstructions were 68 bits wide, decoded to give 196 control signals
µcode ROM
nanoaddress
µcode
next-state
µaddress
PC (state)
nanoinstruction ROM
data
Exploits recurring control signal patterns in µcode, e.g.,
ALU0 A  Reg[rs1]
...
ALUi0 A  Reg[rs1]
...
User PC
Inst. Cache
Hardwired Decode
RISC

## Slide 39: From CISC to RISC
Use fast RAM to build fast instruction cache of user-visible instructions, not fixed hardware microroutines
  Contents of fast instruction memory change to fit what application needs right now
Use simple ISA to enable hardwired pipelined implementation
  Most compiled code only used a few of the available CISC instructions
  Simpler encoding allowed pipelined implementations
Further benefit with integration
  In early ‘80s, could finally fit 32-bit datapath + small caches on a single chip
  No chip crossings in common case allows faster operation

## Slide 40: Berkeley RISC Chips
RISC-I (1982) Contains 44,420 transistors, fabbed in 5 µm NMOS, with a die area of 77 mm2, ran at 1 MHz. This chip is probably the first VLSI RISC.
RISC-II (1983) contains 40,760 transistors, was fabbed in 3 µm NMOS, ran at 3 MHz, and the size is 60 mm2.
Stanford built some too…

## Slide 41: Microprogramming is far from extinct
Played a crucial role in micros of the Eighties
    DEC uVAX, Motorola 68K series, Intel 286/386
Plays an assisting role in most modern micros
  e.g., AMD Bulldozer, Intel Ivy Bridge, Intel Atom, IBM PowerPC, …
  Most instructions executed directly, i.e., with hard-wired control
  Infrequently-used and/or complicated instructions invoke microcode
Patchable microcode common for post-fabrication bug fixes, e.g. Intel processors load µcode patches at bootup

## Slide 42: Acknowledgements
This course is partly inspired by previous MIT 6.823 and Berkeley CS252 computer architecture courses created by my collaborators and colleagues:
  Arvind (MIT)
  Joel Emer (Intel/MIT)
  James Hoe (CMU)
  John Kubiatowicz (UCB)
  David Patterson (UCB)