## Slide 1: CS252 Graduate Computer Architecture Spring 2014 Lecture 17: I/O
Krste Asanovic
krste@eecs.berkeley.edu
http://inst.eecs.berkeley.edu/~cs252/sp14

## Slide 2: Last Time in Lecture 16
Virtual Machines
User-Level
  ABI = ISA + I/O
  Emulating ISAs in software
System-Level (Virtual Machine Monitors)
  Requirements for virtualizable ISA
  Impact on virtual memory (page tables) and I/O

## Slide 3: (I/O) Input/Output
Computers useless without I/O
  Over time, literally thousands of forms of computer I/O: punch cards to brain interfaces
Broad categories:
Secondary/Tertiary storage (flash/disk/tape)
Network (Ethernet, WiFi, Bluetooth, LTE)
Human-machine interfaces (keyboard, mouse, touchscreen, graphics, audio, video, neural,…)
Printers (line, laser, inkjet, photo, 3D, …)
Sensors (process control, GPS, heartrate, …)
Actuators (valves, robots, car brakes, …)
Mix of I/O devices is highly application-dependent

## Slide 4: Interfacing to I/O Devices
Two general strategies
Memory-mapped
  I/O devices appear as memory locations to processor
  Reads and writes to I/O device locations configure I/O and transfer data (using either programmed I/O or DMA)
I/O channels
  Architecture specifies commands to execute I/O commands over defined channels
  I/O channel structure can be layered over memory-mapped device structure
In addition to data transfer, have to define synchronization method
  Polling: CPU checks status bits
  Interrupts: Device interrupts CPU on event

## Slide 5: Memory-Mapped I/O
Programmed I/O uses CPU to control I/O device using load and store instructions, with address specifying device register to access
  Load and store can have side effect on device
Usually, only privileged code can access I/O devices directly, to provide secure multiprogramming
  System calls sometimes provided for application to open and reserve a device for exclusive access
Processors provide “uncached” loads and stores to prevent caching of device registers
  Usually indicated by bits in page table entries or by reserving portions of physical address space

## Slide 6: Simple I/O Bus Structure
Some range of physical memory addresses map to I/O bus devices
I/O bus bridge reduces loading on critical CPU-DRAM bus
Devices can be “slaves”, only responding to I/O bus requests
Devices can be “masters”, initiating I/O bus transfers
CPU
Caches
DRAM
I/O Bus Bridge
Memory Bus
I/O Bus
I/O Device #1
I/O Device #2
I/O Device #3

## Slide 7: DMA (Direct Memory Access)
DMA engines offload CPU by autonomously transferring data between I/O device and main memory. Interrupt/poll for done
  DMA programmed through memory-mapped registers
  Some systems use dedicated processors inside DMA engines
Often, many separate DMA engines in modern systems
  Centralized in I/O bridge (usually supporting multiple concurrent channels to different devices), works on slave-only I/O busses
  Directly attached to each peripheral (if I/O bus supports mastering)
CPU
Caches
DRAM
I/O Bus Bridge
Memory Bus
I/O Bus
I/O Device #1
I/O Device #2
I/O Device #3
DMA
DMA

## Slide 8: More Complex Bus Structures
CPU
Caches
DRAM
I/O Bus Bridge
Memory Bus
Fast I/O Bus
I/O Device #1
I/O Device #3
Slow I/O Bus Bridge
DMA
I/O Device #2
Match speed of I/O connection to device demands
  Special direct connection for graphics
  Fast I/O bus for disk drives, ethernet
  Slow I/O bus for keyboard, mouse, touchscreen
    Reduces load on fast I/O bus + less bus logic needed on device
Slow I/O Bus
DMA
DMA
I/O Device #4
Graphics
DMA

## Slide 9: Move from Parallel to Serial I/O Off-chip
CPU I/O IF
I/O 1
I/O 2
Central Bus Arbiter
Shared Parallel Bus Wires
CPU I/O IF
I/O 1
I/O 2
Dedicated Point-to-point Serial Links
Parallel bus clock rate limited by clock skew across long bus (~100MHz)
High power to drive large number of loaded bus lines
Central bus arbiter adds latency to each transaction, sharing limits throughput
Expensive parallel connectors and backplanes/cables (all devices pay costs)
Examples: VMEbus, Sbus, ISA bus, PCI, SCSI, IDE
Point-to-point links run at multi-gigabit speed using advanced clock/signal encoding (requires lots of circuitry at each end)
Lower power since only one well-behaved load
Multiple simultaneous transfers
Cheap cables and connectors (trade greater endpoint transistor cost for lower physical wiring cost), customize bandwidth per device using multiple links in parallel
Examples: Ethernet, Infiniband, PCI Express, SATA, USB, Firewire, etc.

## Slide 10: Move from Bus to Crossbar On-Chip
Busses evolved in era where wires were expensive and had to be shared
Bus tristate drivers problematic in standard cell flows, so replace with combinational muxes
Crossbar exploits density of on-chip wiring, allows multiple simultaneous transactions
A
B
C
Tristated Bus
A
A
B
B
C
C
Crossbar

## Slide 11: I/O and Memory Mapping
I/O busses can be coherent or not
  Non-coherent simpler, but might require flushing caches or only non-cacheable accesses (much slower on modern processors)
  Some I/O systems can cache coherently also (SGI Origin)
I/O can use virtual addresses
  Simplifies DMA into user address space, otherwise contiguous user segment needs scatter/gather by DMA engine
  Provides protection from bad device drivers
  Adds complexity to I/O device

## Slide 12: Interrupts versus Polling
Two ways to detect I/O device status:
Interrupts
  No CPU overhead until event
  Large context-switch overhead on each event (trap flushes pipeline, disturbs current working set in cache/TLB)
  Can happen at awkward time
Polling
  CPU overhead on every poll
  Difficult to insert in all code
  Can control when handler occurs, reduce working set hit
Hybrid approach:
  Interrupt on first event, keep polling in kernel until sure no more events, then back to interrupts

## Slide 13: Example ARM SoC Structure
[©ARM]

## Slide 14: ARM Sample Smartphone Diagram
[©ARM]

## Slide 15: Intel Ivy Bridge Server Chip I/O
[©Intel]

## Slide 16: Intel Romley Server Platform
[©Intel]

## Slide 17: Acknowledgements
This course is partly inspired by previous MIT 6.823 and Berkeley CS252 computer architecture courses created by my collaborators and colleagues:
  Arvind (MIT)
  Joel Emer (Intel/MIT)
  James Hoe (CMU)
  John Kubiatowicz (UCB)
  David Patterson (UCB)