## Slide 1: CS 61C: Great Ideas in Computer Architecture Lecture 13 –Cache Basics (Cache II)
Instructors:
Mike Franklin
Dan Garcia
http://inst.eecs.berkeley.edu/~cs61c/fa11

## Slide 2: In the News… The importance of using the right performance metrics
The film is based on the best-selling 2003 book in Michael Lewis chronicled the data-driven resurgence of the Oakland A’s engineered by A’s general manager Billy Beane and DePodesta, who used computer analysis to identify undervalued players.
“We had a completely new set of metrics that bore no resemblance to anything you’d seen. We didn’t solve baseball. But we reduced the inefficiency of our decision making.”
www.datacenterknowledge.com/archives/2011/09/23/the-lessons-of-moneyball-for-big-data-analysis/

## Slide 3: Agenda
Review – Direct Mapped Caches
Handling Writes (updates)
Handling Hits and Misses
Performance Considerations

## Slide 4: TIO: Mapping the Memory Address
Lowest bits of address (Offset) determine which byte within a block it refers to.
Full address format (m-bit address):
n-bit Offset: a cache block is how many bytes?
n-bit Index: cache has how many blocks?
Tag
Memory Address
Index
Offset
0
m-1

## Slide 5: Direct Mapped Cache Example
One word (4 Byte) blocks, cache size = 1K words (or 4KB)
20
Tag
10
Index
Data
Index
Tag
Valid
0
1
2
.
.
.
1021
1022
1023
31 30 . . . 13 12 11 . . . 2 1 0
Byte offset
What kind of locality are we taking advantage of?
20
Data
32
Hit
Notes: Let’s use a specific example with realistic numbers: assume we have a 1 K word (4Kbyte) direct mapped cache with block size equals to 4 bytes (1 word).
In other words, each block associated with the cache tag will have 4 bytes in it (Row 1).
With Block Size equals to 4 bytes, the 2 least significant bits of the address will be used as byte select within the cache block.
Since the cache size is 1K word, the upper 32 minus 10+2 bits, or 20 bits of the address will be stored as cache tag.
The rest of the (10) address bits in the middle, that is bit 2 through 11, will be used as Cache Index to select the proper cache entry
Temporal!

## Slide 6: Direct Mapped Cache (1Byte words)
0
1
2
3
4
3
4
15
Consider the sequence of memory address accesses
  0 1 2 3 4 3 4 15
00 Mem(0)
00 Mem(0)
00 Mem(1)
00 Mem(0)
00 Mem(0)
00 Mem(1)
00 Mem(2)
miss
miss
miss
miss
miss
miss
hit!!!
hit!!!
00 Mem(0)
00 Mem(1)
00 Mem(2)
00 Mem(3)
01 Mem(4)
00 Mem(1)
00 Mem(2)
00 Mem(3)
01 Mem(4)
00 Mem(1)
00 Mem(2)
00 Mem(3)
01 Mem(4)
00 Mem(1)
00 Mem(2)
00 Mem(3)
01
4
11
15
00 Mem(1)
00 Mem(2)
00 Mem(3)
Start with an empty cache - all blocks initially marked as not valid
  8 requests, 2 hits, 6 misses = 25% hit rate
0000 0001 0010 0011 0100 0011 0100 1111
Time
Time
Notes: For lecture
Reference string is word addresses (or block number since we are using one word blocks) – i.e., the low order two bits used to selected the byte in the 32-bit word are ignored

## Slide 7: Taking Advantage of Spatial Locality
0
Let cache block hold more than one byte (say, two)
  0 1 2 3 4 3 4 15
1
2
3
4
3
4
15
00 Mem(1) Mem(0)
miss
00 Mem(1) Mem(0)
hit
00 Mem(3) Mem(2)
00 Mem(1) Mem(0)
miss
hit
00 Mem(3) Mem(2)
00 Mem(1) Mem(0)
miss
00 Mem(3) Mem(2)
00 Mem(1) Mem(0)
01
5
4
hit
00 Mem(3) Mem(2)
01 Mem(5) Mem(4)
hit
00 Mem(3) Mem(2)
01 Mem(5) Mem(4)
00 Mem(3) Mem(2)
01 Mem(5) Mem(4)
miss
11
15
14
Start with an empty cache - all blocks initially marked as not valid
  8 requests, 4 hites, 4 misses = 50% hit rate!
0000 0001 0010 0011 0100 0011 0100 1111
Notes: For lecture
Show the 4-bit address mapping – 2-bits of tag, 1-bit of set address (index), 1-bit of word-in-block select

## Slide 8: Multiword Block Direct Mapped Cache
Four words/block, cache size = 1K words (256 blocks) (4KB Total data)
8
Index
Data
Index
Tag
Valid
0
1
2
.
.
.
253
254
255
31 30 . . . 13 12 11 . . . 4 3 2 1 0
Byte offset
20
20
Tag
Hit
Data
32
Block offset
What kind of locality are we taking advantage of?
Notes: to take advantage for spatial locality want a cache block that is larger than word word in size.

## Slide 9: Miss Rate vs Block Size vs Cache Size
Chart: Block size (bytes)
| 16.0 | 32.0 | 64.0 | 128.0 | 256.0
8 KB | 8.5 | 7.5 | 7.25 | 7.75 | 9.5
16 KB | 4 | 2.75 | 2.75 | 3 | 3.5
64 KB | 2 | 1.7 | 1.55 | 1.4 | 1.4
256 KB | 1 | 0.7 | 0.5 | 0.5 | 0.6
Miss rate goes up if the block size becomes a significant fraction of the cache size because the number of blocks that can be held in the same size cache is smaller (increasing capacity misses)
Notes: Increasing the block size usually decreases the miss rate.
A more serious problem is that the miss penalty goes up since it is primarily determined by the time to fetch the block from the next lower level of the hierarchy and load it into the cache.

## Slide 10: Cache-Memory Consistency? (1/2)
Need to make sure cache and memory are consistent (i.e., know about all updates)
1) Write-Through Policy: write cache and write through the cache to memory
  Every write eventually gets to memory
  Too slow, so include Write Buffer to allow processor to continue once data in Buffer, Buffer updates memory in parallel to processor

## Slide 11: Cache-Memory Consistency? (2/2)
2) Write-Back Policy: write only to cache and then write cache block back to memory when evict block from cache
  Writes collected in cache, only single write to memory per block
  Include bit to see if wrote to block or not, and then only write back if bit is set
    Called “Dirty” bit (writing makes it “dirty”)

## Slide 12: Handling Cache Hits
Read hits (I$ and D$)
  Hits are good in helping us go fast
  Misses are bad/slow us down
Write hits (D$ only)
  Require cache and memory to be consistent
    Write-through: Always write the data into the cache block and the next level in the memory hierarchy
    Writes run at the speed of next level in memory hierarchy – so slow! – or can use a write buffer and stall only if the write buffer is full
  Allow cache and memory to be inconsistent
    Write-back: Write the data only into the cache block (cache block written back to next level in memory hierarchy when it is “evicted”)
    Need a dirty bit for each data cache block to tell if it needs to be written back to memory when evicted – can use a write buffer to help “buffer” write-backs of dirty blocks
Notes: In a write-back cache, because we cannot overwrite the block (since we may not have a backup copy anywhere), stores either require two cycles (one to check for a hit, followed by one to actually do the write) or require a write buffer to hold that data (essentially pipelining the write).
By comparison, a write-through cache can always be done in one cycle assuming there is room in the write buffer. Read the tag and write the data in parallel. If the tag doesn’t match, the generate a write miss to fetch the rest of that block from the next level in the hierarchy (and update the tag field).

## Slide 13: Handling Cache Misses (Single Word Blocks)
Read misses (I$ and D$)
  Stall execution, fetch the block from the next level in the memory hierarchy, install it in the cache and send requested word to processor, then resume execution
Write misses (D$ only)
  Stall execution, fetch the block from next level in the memory hierarchy, install it in cache (may involve evicting a dirty block if using write-back), write the word from processor to cache, resume
  or
  Write allocate: just write word into the cache updating both tag and data; no need to check for cache hit, no need to stall
  or
  No-write allocate: skip the cache write (but must invalidate cache block since it will now hold stale data) and just write the word to write buffer (and eventually to the next memory level); no need to stall if write buffer isn’t full (write through only)
Notes: Let’s look at our 1KB direct mapped cache again.
Assume we do a 16-bit write to memory location 0x000000 and causes a cache miss in our 1KB direct mapped cache that has 32-byte block select.
After we write the cache tag into the cache and write the 16-bit data into Byte 0 and Byte 1, do we have to read the rest of the block (Byte 2, 3, ... Byte 31) from memory?
If we do read the rest of the block in, it is called write allocate. But stop and think for a second. Is it really necessary to bring in the rest of the block on a write miss?
True, the principle of spatial locality implies that we are likely to access them soon.
But the type of access we are going to do is likely to be another write.
So if even if we do read in the data, we may end up overwriting them anyway so it is a common practice to NOT read in the rest of the block on a write miss.
If you don’t bring in the rest of the block, or use the more technical term, Write Not Allocate, you better have some way to tell the processor the rest of the block is no longer valid.
This bring us to the topic of sub-blocking.

## Slide 14: Handling Cache Misses (Multiword Block Considerations)
Read misses (I$ and D$)
  Processed the same as for single word blocks – a miss returns the entire block from memory
  Miss penalty grows as block size grows
    Early restart: processor resumes execution as soon as the requested word of the block is returned
    Requested word first: requested word is transferred from the memory to the cache (and processor) first
  Nonblocking cache – allows the processor to continue to access cache while cache is handling an earlier miss
Write misses (D$)
  If using write allocate must first fetch block from memory and then write word to block (or could end up with a “garbled” block in the cache.
  E.g., for 4 word blocks, a new tag, one word of data from the new block, and three words of data from the old block)
Notes: Early restart works best for instruction caches (since it works best for sequential accesses) – if the memory system can deliver a word every clock cycle, it can return words just in time. But if the processor needs another word from a different block before the previous transfer is complete, then the processor will have to stall until the memory is no longer busy.
Unless you have a nonblocking cache that come in two flavors
Hit under miss – allow additional cache hits during a miss with the goal of hiding some of the miss latency
Miss under miss – allow multiple outstanding cache misses (need a high bandwidth memory system to support it)

## Slide 15: “And In Conclusion..”
Direct Mapped Cache – Each block in memory maps to one block in the cache.
  Index to determine which block.
  Offset to determine which byte within block
  Tag to determine if it’s the right block.
AMAT to measure cache performance
Cache can have major impact on CPI
Multi-level cache can help

## Slide 16: Peer Instruction
  For a given cache size: a larger block size can cause a lower hit rate than a smaller one.
  If you know your computer’s cache size, you can often make your code run faster.
  Memory hierarchies take advantage of spatial locality by keeping the most recent data items closer to the processor.
ABC
1: FFF
1: FFT
2: FTF
2: FTT
3: TFF
3: TFT
4: TTF
5: TTT

## Slide 17: Peer Instruction Answer
  Yes – if the block size gets too big, fetches become more expensive and the big blocks force out more useful data.
  Certainly! That’s call “tuning”
  “Most Recent” items  Temporal locality
  For a given cache size: a larger block size can cause a lower hit rate than a smaller one.
  If you know your computer’s cache size, you can often make your code run faster.
  Memory hierarchies take advantage of spatial locality by keeping the most recent data items closer to the processor.
ABC
1: FFF
1: FFT
2: FTF
2: FTT
3: TFF
3: TFT
4: TTF
5: TTT