## Slide 1
Lecturer SOE Dan Garcia
www.cs.berkeley.edu/~ddgarcia
inst.eecs.berkeley.edu/~cs61c CS61C : Machine Structures Lecture 23
Introduction to Synchronous Digital Systems (SDS) Switches, Transistors, Gates 2011-10-19
Living in a Digital World  “We are using technology to dial down human contact.” “Heavy technology use can result in higher levels of loneliness and depression.” Suggestions? Try going offline once a week.
cacm.acm.org/magazines/2011/10/131393-living-in-a-digital-world/fulltext
Hello to Daniel Beck listening from Washington DC!
Notes: Greet class

## Slide 2: New-School Machine Structures (It’s a bit more complicated!)
Parallel Requests
  Assigned to computer
  e.g., Search “Garcia”
Parallel Threads
  Assigned to core
  e.g., Lookup, Ads
Parallel Instructions
  >1 instruction @ one time
  e.g., 5 pipelined instructions
Parallel Data
  >1 data item @ one time
  e.g., Add of 4 pairs of words
Hardware descriptions
  All gates @ one time
Smart Phone
Warehouse Scale Computer
Software Hardware
Harness Parallelism &
Achieve High Performance
Logic Gates
Core
Core
…
Memory (Cache)
Input/Output
Computer
Main Memory
Core
Instruction Unit(s)
Functional
Unit(s)
A3+B3
A2+B2
A1+B1
A0+B0
Today’s Lecture

## Slide 3: What is Machine Structures?
61C
Coordination of many levels of abstraction
I/O system
Processor
Compiler
Operating
System
(MacOS X)
Application (Chrome)
Digital Design
Circuit Design
Instruction Set
Architecture
Datapath & Control
transistors
Memory
Hardware
Software
Assembler
ISA is an important abstraction level: contract between HW & SW

## Slide 4: Levels of Representation/Interpretation
lw $t0, 0($2)
lw $t1, 4($2)
sw $t1, 0($2)
sw $t0, 4($2)
High Level Language Program (e.g., C)
Assembly Language Program (e.g., MIPS)
Machine Language Program (MIPS)
Hardware Architecture Description (e.g., block diagrams)
Compiler
Assembler
Machine Interpretation
temp = v[k];
v[k] = v[k+1];
v[k+1] = temp;
0000 1001 1100 0110 1010 1111 0101 1000
1010 1111 0101 1000 0000 1001 1100 0110
1100 0110 1010 1111 0101 1000 0000 1001
0101 1000 0000 1001 1100 0110 1010 1111
Logic Circuit Description (Circuit Schematic Diagrams)
Architecture Implementation
Anything can be represented as a number, i.e., data or instructions

## Slide 5: Synchronous Digital Systems
Hardware of a processor, such as the MIPS, is an example of a Synchronous Digital System
Synchronous:
  All operations coordinated by a central clock
    “Heartbeat” of the system!
Digital:
  All values represented by discrete values
  Electrical signals are treated as 1s and 0s; grouped together to form words

## Slide 6: Logic Design
Next several weeks: we’ll study how a modern processor is built; starting with basic elements as building blocks
Why study hardware design?
  Understand capabilities and limitations of hw in general and processors in particular
  What processors can do fast and what they can’t do fast (avoid slow things if you want your code to run fast!)
  Background for more in depth hw courses (CS 150, CS 152)
  There is just so much you can do with standard processors: you may need to design own custom hw for extra performance

## Slide 7: Switches: Basic Element of Physical Implementations
Close switch (if A is “1” or asserted) and turn on light bulb (Z)
A
Z
Open switch (if A is “0” or unasserted) and turn off light bulb (Z)
Implementing a simple circuit (arrow shows action if wire changes to “1”):
Z  A
A
Z

## Slide 8: Switches (cont’d)
AND
OR
Z  A and B
Z  A or B
A
B
A
B
Compose switches into more complex ones (Boolean functions):

## Slide 9: Transistor Networks
Modern digital systems designed in CMOS
  MOS: Metal-Oxide on Semiconductor
  C for complementary: normally-open and normally-closed switches
MOS transistors act as voltage-controlled switches

## Slide 10: MOS Transistors
n-channel open when voltage at G is low closes when:
voltage(G) > voltage (S) + 
p-channel closed when voltage at G is low opens when:
voltage(G) < voltage (S) – 
Three terminals: drain, gate, and source
  Switch action: if voltage on gate terminal is (some amount) higher/lower than source terminal then conducting path established between drain and source terminals
G
S
D
G
S
D
http://youtu.be/ZaBLiciesOU

## Slide 11: MOS Networks
3v
X
Y
0 volts
x
y
3 volts
0v
what is the relationship between x and y?
“0” (ground)
“1” (voltage source)

## Slide 12: Transistor Circuit Rep. vs. Block diagram
Chips are composed of nothing but transistors and wires.
Small groups of transistors form useful building blocks.
Block are organized in a hierarchy to build higher-level blocks: ex: adders.
a
b
c
0
0
1
0
1
1
1
0
1
1
1
0
“1” (voltage source)
“0” (ground)
(You can build AND, OR, NOT out of NAND!)

## Slide 13: Signals and Waveforms: Clocks
Signals
  When digital is only treated as 1 or 0
  Is transmitted over wires continuously
  Transmission is effectively instant
    Implies that any wire only contains 1 value at a time

## Slide 14: Signals and Waveforms

## Slide 15: Signals and Waveforms: Grouping

## Slide 16: Signals and Waveforms: Circuit Delay
2
3
3
4
5
10
0
1
5
13
4
6

## Slide 17: Sample Debugging Waveform

## Slide 18: Type of Circuits
Synchronous Digital Systems are made up of two basic types of circuits:
Combinational Logic (CL) circuits
  Our previous adder circuit is an example.
  Output is a function of the inputs only.
  Similar to a pure function in mathematics, y = f(x). (No way to store information from one invocation to the next. No side effects)
State Elements: circuits that store information.

## Slide 19: Circuits with STATE (e.g., register)

## Slide 20: Peer Instruction
SW can peek at HW (past ISA abstraction boundary) for optimizations
SW can depend on particular HW implementation of ISA
12
a) FF
b) FT
c) TF
d) TT
Notes: Answer: [correct=5, TFF] Individual (6, 3, 6, 3, 34, 37, 7, 4)% & Team (9, 4, 4, 4, 39, 34, 0, 7)%
A: T [18/82 & 25/75] (The game breaks up very quickly into separate, independent games -- big win to solve separated & put together)
B: F [80/20 & 86/14] (The game tree grows exponentially! A better static evaluator can make all the difference!)
C: F [53/57 & 52/48] (If you're just looking for the best move, just keep theBestMove around [ala memoizing max])

## Slide 21: Design Hierarchy
system
datapath
control
state registers
combinational logic
multiplexer
comparator
code registers
register
logic
switching networks

## Slide 22: And in conclusion…
ISA is very important abstraction layer
  Contract between HW and SW
Clocks control pulse of our circuits
Voltages are analog, quantized to 0/1
Circuit delays are fact of life
Two types of circuits:
  Stateless Combinational Logic (&,|,~)
  State circuits (e.g., registers)