## Slide 1: 61C In the News
A Touchscreen Anywhere You Want It
Published October 28, 2011 | By Brian Albright
http://www.engineeringontheedge.com/2011/10/a-touchscreen-anywhere-you-want-it/
OmniTouch combines a laser-based pico projector and depth-sensing camera (a prototype from PrimeSense), similar to the Kinect camera used for the Xbox 360. The system detects the proximity of the user’s finger to the surface to determine when a “touch” is actually occurring.

## Slide 2: CS 61C: Great Ideas in Computer Architecture (Machine Structures) Lecture 36: IO Basics
Instructors: Mike Franklin
Dan Garcia
http://inst.eecs.Berkeley.edu/~cs61c/Fa11

## Slide 3: Review
Manage memory to disk? Treat as cache
  Included protection as bonus, now critical
  Use Page Table of mappings for each process vs. tag/data in cache
  TLB is cache of Virtual  Physical addr trans
Virtual Memory allows protected sharing of memory between processes
Temporal and Spatial Locality means Working Set of Pages is all that must be in memory for process to run fairly well

## Slide 4: Memory Management Today
Reality: Slowdown too great to run much bigger programs than memory
  Called Thrashing
  Buy more memory or run program on bigger computer or reduce size of problem
Paging system today still important for
  Translation (mapping of virtual address to physical address)
  Protection (permission to access word in memory)
  Sharing of memory between independent tasks

## Slide 5: Impact of Paging on AMAT
Memory Parameters:
  L1 cache hit = 1 clock cycles, hit 95% of accesses
  L2 cache hit = 10 clock cycles, hit 60% of L1 misses
  DRAM = 200 clock cycles (~100 nanoseconds)
  Disk = 20,000,000 clock cycles (~ 10 milliseconds)
Average Memory Access Time (with no paging):
  1 + 5%*10 + 5%*40%*200 = 5.5 clock cycles
Average Memory Access Time (with paging) =
  5.5 (AMAT with no paging) + ?
Notes: 99.9% =20.005.5
D) ~ 4000X slower (3637X)
100X slower is Hitmemory = 99.997%
Or 1 in ~30,000 memory accesses to disk => 100X slower

## Slide 6: Impact of Paging on AMAT
Memory Parameters:
  L1 cache hit = 1 clock cycles, hit 95% of accesses
  L2 cache hit = 10 clock cycles, hit 60% of L1 misses
  DRAM = 200 clock cycles (~100 nanoseconds)
  Disk = 20,000,000 clock cycles (~ 10 milliseconds)
Average Memory Access Time (with paging) =
  5.5 + 5%*40%*(1-HitMemory)*20,000,000
AMAT if HitMemory = 99%?
  5.5 + 0.02 * 0.01 * 20,000,000 = 4005.5 (~728x slower)
  1 in 20,000 memory accesses goes to disk: 10 sec program takes 2 hours
AMAT if HitMemory = 99.9%?
  5.5 + 0.02 * 0.001 * 20,000,000 = 405.5
AMAT if HitMemory = 99.9999%
  5.5 + 0.02 * .000001 * 20,000,000 = 5.9

## Slide 7: Impact of TLBs on Performance
Each TLB miss to Page Table ~ L1 Cache miss
Page sizes are 4 KB to 8 KB (4 KB on x86)
TLB has typically 128 entries
  Set associative or Fully associative
TLB Reach: Size of largest virtual address space that can be simultaneously mapped by TLB:
128 * 4 KB = 512 KB = 0.5 MB!
What can you do to have better performance?

## Slide 8: Improving TLB Performance
Have 2 Levels of TLB just like 2 levels of cache instead of going directly to Page Table on L1 TLB miss
Add larger page size that operating system can use in situations when OS knows that object is big and protection of whole object OK
  X86 has 4 KB pages + 2 MB and 4 MB “superpages”

## Slide 9: Using Large Pages from Application?
Difficulty is communicating from application to operating system that want to use large pages
Linux: “Huge pages” via a library file system and memory mapping; beyond 61C
  See http://lwn.net/Articles/375096/
  http://www.ibm.com/developerworks/wikis/display/LinuxP/libhuge+short+and+simple
Max OS X: no support for applications to do this (OS decides if should use or not)

## Slide 10: Address Translation & Protection
Every instruction and data access needs address
translation and protection checks
A good VM design needs to be fast (~ one cycle) and space efficient
Physical Address
Virtual Address
Address
Translation
Virtual Page No. (VPN)
offset
Physical Page No. (PPN)
offset
Protection
Check
Exception?
Kernel/User Mode
Read/Write

## Slide 11: Nehalem Virtual Memory Details
48-bit virtual address space, 40-bit physical address space
Two-level TLB
I-TLB (L1) has shared 128 entries 4-way associative for 4KB pages, plus 7 dedicated fully-associative entries per SMT thread for large page (2/4MB) entries
D-TLB (L1) has 64 entries for 4KB pages and 32 entries for 2/4MB pages, both 4-way associative, dynamically shared between SMT threads
Unified L2 TLB has 512 entries for 4KB pages only, also 4-way associative
Data TLB Reach (4 KB only) L1: 64*4 KB =0.25 MB, L2:512*4 KB= 2MB (superpages) L1: 32 *2-4 MB = 64-128 MB
11/21/11
Fall 2011 -- Lecture #36

## Slide 12: Peer Instruction: True or False
A program tries to load a word X that causes a TLB miss but not a page fault. Which are True or False:
1. A TLB miss means that the page table does not contain a valid mapping for virtual page corresponding to the address X
2. There is no need to look up in the page table because there is no page fault
3. The word that the program is trying to load is present in physical memory.
123
A: FFT
B: FTF
C: FTT
D: TFF
E: TFT
Notes: B) Statements 1 and 2 are false; 3 is true

## Slide 13: Peer Instruction: True or False
A program tries to load a word X that causes a TLB miss but not a page fault. Which are True or False:
1. A TLB miss means that the page table does not contain a valid mapping for virtual page corresponding to the address X
2. There is no need to look up in the page table because there is no page fault
3. The word that the program is trying to load is present in physical memory.
123
A: FFT
B: FTF
C: FTT
D: TFF
E: TFT
F A L S E
F A L S E
TRUE
Notes: B) Statements 1 and 2 are false; 3 is true

## Slide 14: Recall : 5 components of any Computer
Processor
(active)
Computer
Control
(“brain”)
Datapath
(“brawn”)
Memory
(passive)
(where
programs,
data live
when
running)
Devices
Input
Output
Keyboard, Mouse
Display, Printer
Disk,
Network
Earlier Lectures
Current Lectures
Notes: That is, any computer, no matter how primitive or advance, can be divided into five parts:
1. The input devices bring the data from the outside world into the computer.
2. These data are kept in the computer’s memory until ...
3. The datapath request and process them.
4. The operation of the datapath is controlled by the computer’s controller.
All the work done by the computer will NOT do us any good unless we can get the data back to the outside world.
5. Getting the data back to the outside world is the job of the output devices.
The most COMMON way to connect these 5 components together is to use a network of busses.

## Slide 15: Motivation for Input/Output
I/O is how humans interact with computers
I/O gives computers long-term memory.
I/O lets computers do amazing things:
Computer without I/O like a car w/no wheels; great technology, but gets you nowhere
MIT Media Lab
“Sixth Sense”

## Slide 16: I/O Device Examples and Speeds
I/O Speed: bytes transferred per second (from mouse to Gigabit LAN: 7 orders of magnitude!)
Device Behavior Partner Data Rate (KBytes/s)
Keyboard Input Human 0.01
Mouse Input Human 0.02
Voice output Output Human 5.00
Floppy disk Storage Machine 50.00
Laser Printer Output Human 100.00
Magnetic Disk Storage Machine 10,000.00
Wireless Network I or O Machine 10,000.00
Graphics Display Output Human 30,000.00
Wired LAN Network I or O Machine 125,000.00
When discussing transfer rates, use 10x
Notes: Here are some examples of the various I/O devices you are probably familiar with.
Notice that most I/O devices that has human as their partner usually has relatively low peak data rates because human in general are slow relatively to the computer system.
The exceptions are the laser printer and the graphic displays.
Laser printer requires a high data rate because it takes a lot of bits to describe high resolution image you like to print by the laser writer.
The graphic display requires a high data rate because as I will show you later in today’s lecture, all the color objects we see in the real world and taken for granted is very hard to replicate on a graphic display.
Let’s take a closer look at one of the most popular storage device, magnetic disks.
+2 = 28 min. (Y:08)

## Slide 17: What do we need to make I/O work?
A way to connect many types of devices
A way to control these devices, respond to them, and transfer data
A way to present them to user programs so they are useful
cmd reg.
data reg.
Operating System
APIs
Files
Proc
Mem
PCI Bus
SCSI Bus

## Slide 18: Instruction Set Architecture for I/O
What must the processor do for I/O?
  Input: reads a sequence of bytes
  Output: writes a sequence of bytes
Some processors have special input and output instructions
Alternative model (used by MIPS):
  Use loads for input, stores for output (in small pieces)
  Called Memory Mapped Input/Output
  A portion of the address space dedicated to communication paths to Input or Output devices (no memory there)

## Slide 19: Memory Mapped I/O
Certain addresses are not regular memory
Instead, they correspond to registers in I/O devices
cntrl reg.
data reg.
0
0xFFFFFFFF
0xFFFF0000
address

## Slide 20: Processor-I/O Speed Mismatch
1GHz microprocessor can execute 1 billion load or store instructions per second, or 4,000,000 KB/s data rate
  I/O devices data rates range from 0.01 KB/s to 125,000 KB/s
Input: device may not be ready to send data as fast as the processor loads it
  Also, might be waiting for human to act
Output: device not be ready to accept data as fast as processor stores it
What to do?

## Slide 21: Processor Checks Status before Acting
Path to a device generally has 2 registers:
  Control Register, says it’s OK to read/write (I/O ready) [think of a flagman on a road]
  Data Register, contains data
Processor reads from Control Register in loop, waiting for device to set Ready bit in Control reg (0  1) to say its OK
Processor then loads from (input) or writes to (output) data register
  Load from or Store into Data Register resets Ready bit (1  0) of Control Register
This is called “Polling”

## Slide 22: I/O Example (polling)
Input: Read from keyboard into $v0
lui $t0, 0xffff #ffff0000 Waitloop: lw $t1, 0($t0) #control andi $t1,$t1,0x1 beq $t1,$zero, Waitloop lw $v0, 4($t0) #data
Output: Write to display from $a0
lui $t0, 0xffff #ffff0000 Waitloop: lw $t1, 8($t0) #control andi $t1,$t1,0x1 beq $t1,$zero, Waitloop sw $a0, 12($t0) #data
“Ready” bit is from processor’s point of view!

## Slide 23: Cost of Polling?
Assume for a processor with a 1GHz clock it takes 400 clock cycles for a polling operation (call polling routine, accessing the device, and returning). Determine % of processor time for polling
  Mouse: polled 30 times/sec so as not to miss user movement
  Floppy disk (Remember those?): transferred data in 2-Byte units and had a data rate of 50 KB/second. No data transfer can be missed.
  Hard disk: transfers data in 16-Byte chunks and can transfer at 16 MB/second. Again, no transfer can be missed. (we’ll come up with a better way to do this)

## Slide 24: % Processor time to poll
Mouse Polling [clocks/sec]
  = 30 [polls/s] * 400 [clocks/poll] = 12K [clocks/s]
% Processor for polling:
  12*103 [clocks/s] / 1*109 [clocks/s] = 0.0012%
   Polling mouse little impact on processor
Notes: was p 677 in book (not current edition)

## Slide 25: % Processor time to poll hard disk
Frequency of Polling Disk
  = 16 [MB/s] / 16 [B/poll] = 1M [polls/s]
Disk Polling, Clocks/sec = 1M [polls/s] * 400 [clocks/poll] = 400M [clocks/s]
% Processor for polling:
  400*106 [clocks/s] / 1*109 [clocks/s] = 40%
   Unacceptable
  (Polling is only part of the problem – main problem is that accessing in small chunks is inefficient)

## Slide 26: What is the alternative to polling?
Wasteful to have processor spend most of its time “spin-waiting” for I/O to be ready
Would like an unplanned procedure call that would be invoked only when I/O device is ready
Solution: use exception mechanism to help I/O. Interrupt program when I/O ready, return when done with data transfer

## Slide 27: “And in conclusion…”
I/O gives computers their 5 senses + long term memory
I/O speed range is 7 Orders of Magnitude (or more!)
Processor speed means must synchronize with I/O devices before use
Polling works, but expensive
  processor repeatedly queries devices
Interrupts work, more complex
  we’ll talk about these next
I/O control leads to Operating Systems