## Slide 1: CS 61C: Great Ideas in Computer Architecture Exceptions/Traps/Interrupts
Instructors:
Krste Asanovic, Randy H. Katz
http://inst.eecs.Berkeley.edu/~cs61c/fa12

## Slide 2: Review
Great Idea: Redundancy to Get Dependability
  Spatial (extra hardware) and Temporal (retry if error)
Reliability: MTTF & Annualized Failure Rate (AFR)
Availability: % uptime (MTTF-MTTR/MTTF)
Memory
  Hamming distance 2: Parity for Single Error Detect
  Hamming distance 3: Single Error Correction Code + encode bit position of error
  Hamming distance 4: SEC/Double Error Detection
CRC for many bit detection, Reed Solomon per disk sector for many bit error detection/correction

## Slide 3: You Are Here!
Parallel Requests
  Assigned to computer
  e.g., Search “Katz”
Parallel Threads
  Assigned to core
  e.g., Lookup, Ads
Parallel Instructions
  >1 instruction @ one time
  e.g., 5 pipelined instructions
Parallel Data
  >1 data item @ one time
  e.g., Add of 4 pairs of words
Hardware descriptions
  All gates @ one time
Programming Languages
Smart Phone
Warehouse Scale Computer
Software Hardware
Harness Parallelism &
Achieve High Performance
Logic Gates
Core
Core
…
Memory (Cache)
Input/Output
Computer
Main Memory
Core
Instruction Unit(s)
Functional
Unit(s)
A3+B3
A2+B2
A1+B1
A0+B0
Today’s
Lecture

## Slide 4: I/O Hardware
Input/Output Interface
Processor
Control
Datapath
PC
Registers
Arithmetic & Logic Unit
(ALU)
Device
Registers
Memory
Bytes
Enable?
Read/Write
Address
Write Data
ReadData
Processor-Memory Interface
I/O-Memory Interfaces
External Devices

## Slide 5: Interfacing to I/O Devices
Programmed I/O
  Software on CPU reads and writes to I/O device registers to explicitly transfer I/O data
  Usually “memory-mapped” where device I/O registers are given memory addresses allowing regular load and store instructions to change register contents
    Also possible to have special I/O instructions (x86, IBM mainframes)
  Cheap but slow, burdens CPU
DMA (Direct Memory Access)
  Extra hardware on device to autonomously transfer blocks of data into and out of memory
  Expensive but fast, offloads CPU

## Slide 6: When to get I/O data?
Most I/O devices are much slower than CPU
Polling
  Software occasionally checks I/O devices to see if data ready
  How often to poll?
    Too often, waste CPU time
    Too little, slow I/O
  What if software forgets?
Interrupts
  I/O device requests attention when something to do!

## Slide 7: I/O Hardware
Input/Output Interface
Processor
Control
Datapath
PC
Registers
Arithmetic & Logic Unit
(ALU)
Device
Registers
Memory
Bytes
Enable?
Read/Write
Address
Write Data
ReadData
Processor-Memory Interface
I/O-Memory Interfaces
Interrupt Request Signal
External Devices

## Slide 8: Invoking the interrupt handler
An I/O device requests attention by asserting one of the prioritized interrupt request signals
  Signals driven from external hardware
When the processor decides to process the interrupt
  Stops the current program at instruction Ii, completing all the instructions up to Ii-1
  Saves the PC of instruction Ii in a special register
    In MIPS, called EPC (Exception Program Counter)
  Disables interrupts and transfers control to a designated interrupt handler, switching CPU to kernel mode
    Most CPUs have a privileged execution mode to support operating systems, allowing software to do more than in regular user mode
After handling interrupt
  Interrupt handler restores user program state and jumps back to current program in regular user mode using a special instruction
    In MIPS, instruction is called RFE (Return From Exception)

## Slide 9: Interrupts: altering the normal flow of control
Ii-1
HI1
HI2
HIn
Ii
Ii+1
program
interrupt
handler
An external or internal event that needs to be processed by another (system) program. The event is usually unexpected or rare from program’s point of view.

## Slide 10: Types of Interrupts
Asynchronous: an external event
  input/output device service-request
  timer expiration
  power disruptions, hardware failure
Synchronous: an internal event (a.k.a. traps or exceptions)
  undefined opcode, privileged instruction
  arithmetic overflow, FPU exception
  misaligned memory access
  virtual memory exceptions: page faults, TLB misses, protection violations
  system calls, e.g., calling functions in operating system kernel
Interrupt: an event that requests the attention of the processor

## Slide 11: History of Exception Handling
First system with exceptions was Univac-I, 1951
  Arithmetic overflow would either
    1. trigger the execution a two-instruction fix-up routine at address 0, or
    2. at the programmer's option, cause the computer to stop
  Later Univac 1103, 1955, modified to add external interrupts
    Used to gather real-time wind tunnel data
First system with I/O interrupts was DYSEAC, 1954
  Had two program counters, and I/O signal caused switch between two PCs
  Also, first system with DMA (direct memory access by I/O device)
[Courtesy Mark Smotherman]

## Slide 12: DYSEAC, first mobile computer!
Carried in two tractor trailers, 12 tons + 8 tons
Built for US Army Signal Corps
[Courtesy Mark Smotherman]

## Slide 13: Interrupt Handler (software inside operating system)
Saves EPC before enabling interrupts to allow nested interrupts
  need an instruction to move EPC into GPRs
  need a way to mask further interrupts at least until EPC can be saved
Needs to read a status register that indicates the cause of the interrupt
Uses a special indirect jump instruction RFE (return-from-exception) which
  enables interrupts
  restores the processor to the user mode
  restores hardware status and control state

## Slide 14: Administrivia
Project 3 regrade requests – DON’T EMAIL INSTRUCTORS
  Email proj3.1regrade@gmail.com or proj3.2regrade@gmail.com
  See Piazza posting for more details

## Slide 15: CS61C in the News: Intel 4004, 41 years old yesterday
First microprocessor
4-bit accumulator architecture
8mm pMOS
2,300 transistors
3 x 4 mm2
750kHz clock
8-16 cycles/inst.

## Slide 16: CS61C In the News: “Texas Instruments Cuts 1,700 Jobs and Winds Down Tablet Chips”, NY Times 11/14/2012
“Texas Instruments is eliminating 1,700 jobs, as it winds down its mobile processor business to focus on chips for more profitable markets like cars and home appliances. Texas Instruments said in September it would halt costly investments in the increasingly competitive smartphone and tablet chip business, leading Wall Street to speculate that part of the company's processor unit, called OMAP, could be sold. The layoffs are equivalent to nearly 5 percent of the Austin, Texas-based company's global workforce.
TI has been under pressure in mobile processors, where it has lost ground to rival Qualcomm Inc. Leading smartphone makers Apple Inc and Samsung Electronics Co Ltd have been developing their own chips instead of buying them from suppliers like TI. Instead of competing in phones and tablets, TI wants to sell its OMAP processors in markets that require less investment, like industrial clients like carmakers. TI is expected to continue selling existing tablet and phone processors for products like Amazon.Com Inc's Kindle tablets for as long as demand remains, but stop developing new chips.”
[Rumors of Amazon being interested in buying this OMAP unit from TI ]

## Slide 17: Precise Interrupts
Interrupt handler’s view of machine state is that every instruction prior to the interrupted one has completed, and no instruction after the interrupt has executed.
  Instruction taking interrupt might have written some special state but can be restarted.
Implies that handler can return from interrupt by restoring user registers and jumping to EPC
  Software doesn’t need to understand the pipeline of the machine!
Providing precise interrupts is tricky in a pipelined superscalar out-of-order processor!
  But handling imprecise interrupts in software is even worse.

## Slide 18: Synchronous Trap
A synchronous trap is caused by a particular instruction
  E.g., system call, virtual memory page fault, unimplemented instruction, misaligned memory address
In general, the instruction cannot be completed and needs to be restarted after the trap has been handled
  requires undoing the effect of one or more partially executed instructions
In the case of a system call trap, the instruction is considered to have been completed
  a special jump instruction involving a change to privileged kernel mode

## Slide 19: Exception Handling 5-Stage Pipeline
How to handle multiple simultaneous exceptions in different pipeline stages?
How and where to handle external asynchronous interrupts?
PC
Inst. Mem
D
Decode
E
M
Data Mem
W
+
Illegal Opcode
Overflow
Data address Exceptions
PC address Exception
Asynchronous Interrupts

## Slide 20: Exception Handling 5-Stage Pipeline
PC
Inst. Mem
D
Decode
E
M
Data Mem
W
+
Illegal Opcode
Overflow
Data address Exceptions
PC address Exception
Asynchronous
Interrupts
Exc
D
PC
D
Exc
E
PC
E
Exc
M
PC
M
Cause
EPC
Kill D Stage
Kill F Stage
Kill E Stage
Select Handler PC
Kill Writeback
Commit Point

## Slide 21: Exception Handling 5-Stage Pipeline
Hold exception flags in pipeline until commit point (M stage)
Exceptions in earlier pipe stages override later exceptions for a given instruction
Inject external interrupts at commit point (override others)
If exception at commit: update Cause and EPC registers, kill all stages, inject handler PC into fetch stage

## Slide 22: Speculating on Exceptions to avoid Control Hazard
Prediction mechanism
  Exceptions are rare, so simply predicting no exceptions is very accurate!
Check prediction mechanism
  Exceptions detected at end of instruction execution pipeline, special hardware for various exception types
Recovery mechanism
  Only write architectural state at commit point, so can throw away partially executed instructions after exception
  Launch exception handler after flushing pipeline
Bypassing allows use of uncommitted instruction results by following instructions

## Slide 23: Exception Pipeline Diagram
  time
  t0 t1 t2 t3 t4 t5 t6 t7 . . . .
IF I1 I2 I3 I4 I5
ID I1 I2 I3 - I5
EX I1 I2 - - I5
MA I1 - - - I5
WB - - - - I5
      time
      t0 t1 t2 t3 t4 t5 t6 t7 . . . .
(I1) 096: ADD IF1 ID1 EX1 MA1 - overflow!
(I2) 100: XOR IF2 ID2 EX2 - -
(I3) 104: SUB IF3 ID3 - - -
(I4) 108: ADD IF4 - - - -
(I5) Exc. Handler code IF5 ID5 EX5 MA5 WB5
Resource
Usage

## Slide 24: Summary
Asynchronous interrupts versus synchronous traps
Precise interrupts simplify software view of interrupted state
Handling exceptions is one of the most difficult parts of processor design, even though they occur infrequently
  Separate “commit” from execute in design

## Slide 25: Acknowledgements
These slides contain material developed and copyright by:
  Arvind (MIT)
  Krste Asanovic (MIT/UCB)
  James Hoe (CMU)
MIT material derived from course 6.823
UCB material derived from course CS252