## Slide 1: CS 61C: Great Ideas in Computer Architecture Course Summary and Wrap-up
Instructors:
Krste Asanovic, Randy H. Katz
http://inst.eecs.Berkeley.edu/~cs61c/fa12

## Slide 2: New-School Machine Structures (It’s a bit more complicated!)
Parallel Requests
  Assigned to computer
  e.g., Search “Katz”
Parallel Threads
  Assigned to core
  e.g., Lookup, Ads
Parallel Instructions
  >1 instruction @ one time
  e.g., 5 pipelined instructions
Parallel Data
  >1 data item @ one time
  e.g., Add of 4 pairs of words
Hardware descriptions
  All gates functioning in parallel at same time
Programming Languages
Smart Phone
Warehouse Scale Computer
Software Hardware
Leverage Parallelism &
Achieve High Performance
Logic Gates
Core
Core
…
Memory
Input/Output
Computer
Cache Memory
Core
Instruction Unit(s)
Functional
Unit(s)
A3+B3
A2+B2
A1+B1
A0+B0
Project 2
Project 1
Project 3
Project 4

## Slide 3: 6 Great Ideas in Computer Architecture
Layers of Representation/Interpretation
Moore’s Law
Principle of Locality/Memory Hierarchy
Parallelism
Performance Measurement & Improvement
Dependability via Redundancy

## Slide 4: Powers of Ten inspired 61C Overview
Going Top Down cover 3 Views
Architecture (when possible)
Physical Implementation of that architecture
Programming system for that architecture and implementation (when possible)
http://www.powersof10.com/film
Notes: Start film at 5:40, lasts for 5 minutes
Google earth at steelhead way, and dam

## Slide 5: The Dalles, Oregon
104 meters

## Slide 6: The Dalles, Oregon
104 meters

## Slide 7: Google’s Oregon WSC
103 meters

## Slide 8: Google’s Oregon WSC
104 meters
103 meters
102 meters
10 kilometers

## Slide 9: Google Warehouse
90 meters by 75 meters, 10 Megawatts
Contains 40,000 servers, 190,000 disks
Power Utilization Effectiveness: 1.23
  85% of 0.23 overhead goes to cooling losses
  15% of 0.23 overhead goes to power losses
Contains 45, 40-foot long containers
  8 feet x 9.5 feet x 40 feet
30 stacked as double layer, 15 as single layer

## Slide 10: Containers in WSCs
102 meters
100 meters

## Slide 11: Google Container
101 meters

## Slide 12: Google Container
2 long rows, each with 29 racks
Cooling below raised floor
Hot air returned behind racks
100 meters
10 meters

## Slide 13: Equipment Inside a Container
Server (in rack format):
7 foot Rack: servers + Ethernet local area network switch in middle (“rack switch”)
Array (aka cluster): server racks + larger local area network switch (“array switch”) 10X faster => cost 100X: cost f(N2)

## Slide 14: Google Rack
Google rack with 20 servers + Network Switch in the middle
48-port 1 Gigabit/sec Ethernet switch every other rack
Array switches connect to racks via multiple 1 Gbit/s links
2 datacenter routers connect to array switches over 10 Gbit/s links
100 meters
1 meter

## Slide 15: Programming WSC: MapReduce
public static class SumReduce extends Reducer<Text, LongWritable, Text, LongWritable> {
/** Actual reduce function.
* @param key Word.
* @param values Values for this word (partial counts).
* @param context ReducerContext object for accessing output,
* configuration information, etc.
*/
@Override
public void reduce(Text key, Iterable<LongWritable>values,
Context context) throws IOException, InterruptedException { long sum = 0L;
for (LongWritable value : values) {sum += value.get();} context.write(key, new LongWritable(sum));
}
}

## Slide 16: 6 Great Ideas in Computer Architecture inside the Warehouse Scale Computer
Layers of Representation/Interpretation
  WSC, Container, Rack
Moore’s Law
Principle of Locality/Memory Hierarchy
Parallelism
  Task Level Parallelism, Data Level Parallelism
Performance Measurement & Improvement
  Measure PUE to improve PUE
Dependability via Redundancy
  Multiple WSCs, Multiple Racks, Multiple Switches

## Slide 17: Google Server Internals
Google Server
10-1 meters
10 centimeters
Notes: Most companies buy servers from the likes of Dell, Hewlett-Packard, IBM, or Sun Microsystems. But Google, which has hundreds of thousands of servers and considers running them part of its core expertise, designs and builds its own. Ben Jai, who designed many of Google's servers, unveiled a modern Google server before the hungry eyes of a technically sophisticated audience.
Google's big surprise: each server has its own 12-volt battery to supply power if there's a problem with the main source of electricity. The company also revealed for the first time that since 2005, its data centers have been composed of standard shipping containers--each with 1,160 servers and a power consumption that can reach 250 kilowatts.
It may sound geeky, but a number of attendees--the kind of folks who run data centers packed with thousands of servers for a living--were surprised not only by Google's built-in battery approach, but by the fact that the company has kept it secret for years. Jai said in an interview that Google has been using the design since 2005 and now is in its sixth or seventh generation of design.
Read more: http://news.cnet.com/8301-1001_3-10209580-92.html#ixzz0yo8bhTOH

## Slide 18: Google Board Details
Supplies only 12 volts
Battery per board vs. large battery room
  Improves PUE: 99.99% efficient local battery vs 94% for battery room
2 SATA Disk Drives
  1 Terabyte capacity each
  3.5 inch disk drive
  7200 RPM
2 AMD Opteron Microprocessors
  Dual Core, 2.2 GHz
8 DIMMs
  8 GB DDR2 DRAM
1 Gbit/sec Ethernet Network Interface Card

## Slide 19: Programming Multicore Microprocessor: OpenMP
#include <omp.h>
#include <stdio.h>
static long num_steps = 100000;
int value[num_steps];
int reduce()
{ int i; int sum = 0;
#pragma omp parallel for private(x) reduction(+:sum)
for (i=1; i<= num_steps; i++){
sum = sum + value[i];
}
}

## Slide 20: 6 Great Ideas in Computer Architecture inside the Server
Layers of Representation/Interpretation
Moore’s Law
  More transistors => Multicore
Principle of Locality/Memory Hierarchy
Parallelism
  Thread Level Parallelism
Performance Measurement & Improvement
  Timers, counters
Dependability via Redundancy

## Slide 21: AMD Opteron Microprocessor
10-2 meters
centimeters

## Slide 22: AMD Opteron Microarchitecture
72 physical registers

## Slide 23: AMD Opteron Pipeline Flow
For integer operations
  12 stages (Floating Point is 17 stages)
  Up to 106 RISC-ops in progress

## Slide 24: AMD Opteron Block Diagram
AGU
AGU
Int Decode & Rename
FADD
FMISC
FMUL
44-entry
Load/Store
Queue
36-entry FP scheduler
FP Decode & Rename
ALU
AGU
ALU
MULT
ALU
Res
Res
Res
L1
Icache
64B
L1
Dcache
64KB
Fetch
Branch
Prediction
Instruction Control Unit (72 entries)
Fastpath
Microcode Engine
Scan/Align/Decode
µops

## Slide 25: AMD Opteron Microprocessor
10-2 meters
centimeters

## Slide 26: AMD Opteron Core
10-3 meters
millimeters

## Slide 27: Programming One Core: C with Intrinsics
void mmult(int n, float *A, float *B, float *C)
{
for ( int i = 0; i < n; i+=4 )
for ( int j = 0; j < n; j++ )
{
__m128 c0 = _mm_load_ps(C+i+j*n);
for( int k = 0; k < n; k++ )
c0 = _mm_add_ps(c0, _mm_mul_ps(_mm_load_ps(A+i+k*n), _mm_load1_ps(B+k+j*n)));
_mm_store_ps(C+i+j*n, c0);
}
}

## Slide 28: Inner loop from gcc –O -S
Assembly snippet from innermost loop:
          movaps (%rax), %xmm9
          mulps %xmm0, %xmm9
          addps %xmm9, %xmm8
          movaps 16(%rax), %xmm9
          mulps %xmm0, %xmm9
          addps %xmm9, %xmm7
          movaps 32(%rax), %xmm9
          mulps %xmm0, %xmm9
          addps %xmm9, %xmm6
          movaps 48(%rax), %xmm9
          mulps %xmm0, %xmm9
          addps %xmm9, %xmm5

## Slide 29: 6 Great Ideas in Computer Architecture inside the Microprocessor
Layers of Representation/Interpretation
  Instruction Set Architecture, micro operations
Moore’s Law
Principle of Locality/Memory Hierarchy
Parallelism
  Instruction Level Parallelism (superscalar, pipelining)
  Data Level Parallelism
Performance Measurement & Improvement
Dependability via Redundancy

## Slide 30: SIMD Adder
Four 32-bit adders that operate in parallel
  Data Level Parallelism

## Slide 31: One 32-bit Adder

## Slide 32: 1 bit of 32-bit Adder

## Slide 33: Complementary MOS Transistors (NMOS and PMOS) of NAND Gate
3v
X
Y
0v
Z
x
y
z
0 volts
3 volts
0 volts
3 volts
0 volts
0 volts
3 volts
3 volts
3 volts
3 volts
3 volts
0 volts
NAND gate
Notes: Bottom
X = 0v Y = 0V both closed on top in series, so Z = 3v
X = 0v Y = 0V both open bottom
X = 0v Y = 3V 1st open on top,
X = 0v Y = 3V 2nd in series closed, so Z = 0v
X = 3v Y = 0V 2nd open on top
X = 3v Y = 0V 2nd in series closed, so Z = 0v
X = 3v Y = 3V both open on top
X = 3v Y = 3V both closed, so Z = 0v

## Slide 34: Physical Layout of NAND Gate
10-7 meters
100 nanometers

## Slide 35: Scanning Electron Microscope
10-7 meters
Cross Section
Top View
100 nanometers

## Slide 36: Block Diagram of Static RAM
10-6 meters

## Slide 37: 1 Bit SRAM in 6 Transistors
Notes: The core of this cell is formed by the four transistors M1 to M4 which form two cross-coupled inverters. They have two stable states, representing 0 and 1 respectively. The state is stable as long as power on Vdd is available.
If access to the state of the cell is needed the word access line WL is raised. This makes the state of the cell immediately available for reading on BL and BL. If the cell state must be overwritten the BL and BL lines are first set to the desired values and then WL is raised. Since the outside drivers are stronger than the four transistors (M1 through M4) this allows the old state to be overwritten.

## Slide 38: Physical Layout of SRAM Bit
10-7 meters
100 nanometers

## Slide 39: SRAM Cross Section
10-7 meters
100 nanometers

## Slide 40: DIMM Module
DDR = Double Data Rate
  Transfers bits on Falling AND Rising Clock Edge
Has Single Error Correcting, Double Error Detecting Redundancy (SEC/DED)
  72 bits to store 64 bits of data
  Uses “Chip kill” organization so that if single DRAM chip fails can still detect failure
Average server has 22,000 correctable errors and 1 uncorrectable error per year

## Slide 41: DRAM Bits
10-6 meters
1 micron

## Slide 42: DRAM Cell in Transistors

## Slide 43: Physical Layout of DRAM Bit

## Slide 44: Cross Section of DRAM Bits
10-7 meters
100 nanometers

## Slide 45: AMD Dependability
• L1 cache data is SEC/DED protected
• L2 cache and tags are SEC/DED protected
• DRAM is SEC/DED protected with chipkill
• On-chip and off-chip ECC protected arrays include autonomous, background hardware scrubbers
• Remaining arrays are parity protected
– Instruction cache, tags and TLBs
– Data tags and TLBs
– Generally read only data that can be recovered from lower levels

## Slide 46: Programming Memory Hierarchy: Cache Blocked Algorithm
The blocked version of the i-j-k algorithm is written simply as (A,B,C are submatricies of a, b, c)
for (i=0;i<N/r;i++)
for (j=0;j<N/r;j++)
for (k=0;k<N/r;k++)
C[i][j] += A[i][k]*B[k][j]
  r = block (sub-matrix) size (Assume r divides N)
  X[i][j] = a sub-matrix of X, defined by block row i and block column j

## Slide 47: 6 Great Ideas in Computer Architecture inside the chips
Layers of Representation/Interpretation
Moore’s Law
  Higher capacity caches and DRAM
Principle of Locality/Memory Hierarchy
  Caches, TLBs
Parallelism
  Data Level Parallelism
Performance Measurement & Improvement
  Memory Traffic, Cache Misses
Dependability via Redundancy
  Parity, SEC/DED

## Slide 48: Course Summary
As the field changes, cs61c had to change too!
It is still about the software-hardware interface
  Programming for performance!
  Parallelism: Task-, Thread-, Instruction-, and Data- MapReduce, OpenMP, C, SSE instrinsics
  Understanding the memory hierarchy and its impact on application performance
Interviewers ask what you did this semester!

## Slide 49: The Future for Future Cal Alumni
What’s The Future?
New Century, Many New Opportunties: Parallelism, Cloud, Statistics + CS, Bio + CS, Society (Health Care, 3rd world) + CS
“The best way to predict the future is to invent it” – Alan Kay (inventor of personal computing vision)
Future is up to you!

## Slide 50: Special Thanks to the TAs: Alan Christopher, Loc Thi Bao Do, James Ferguson, Anirudh Garg, William Ku, Brandon Luong, Ravi Punj, Sung Roa Yoon

## Slide 51: Storage System
Really 2 models: 1 Disk or 12 Disk servers
2nd tray with 10 disks, add extra 1 Gbit/s NIC
Hitachi Deskstar
  1 Terabyte capacity, 7200 RPM
  SATA => Serial ATA link Disk Drives
  5% fail per year (AFR)
Google File System (GFS) has multiple replicas of data to protect from disk failures (like RAID 1 or mirroring)

## Slide 52: Disk Organization

## Slide 53: Disk
10-1 meters

## Slide 54: Disk Internals
10-1 meters

## Slide 55: Closeup of Disk Surface
Topography via Atomic Force Microscopy (AFM)
Bits visible via Magnetic Force Microscopy (MFM)
http://www.dataclinic.co.uk/data-recovery/hard-disk-microscopy-ii.htm
10-7 meters

## Slide 56: Programming Storage
Operating System calls

## Slide 57: 6 Great Ideas in Computer Architecture
Layers of Representation/Interpretation
Moore’s Law
Principle of Locality/Memory Hierarchy
  Paging Memory
Parallelism
  Task Level Parallelism (Asynchronous I/O)
Performance Measurement & Improvement
Dependability via Redundancy
  Reed-Solomon ECC per disk sector, replicated files