## Slide 1: CS 61C: Great Ideas in Computer Architecture Virtual Machines/Programming Contest
Instructor:
Randy H. Katz
http://inst.eecs.Berkeley.edu/~cs61c/fa13

## Slide 2: Part II: You Are Here!
Parallel Requests
  Assigned to computer
  e.g., Search “Katz”
Parallel Threads
  Assigned to core
  e.g., Lookup, Ads
Parallel Instructions
  >1 instruction @ one time
  e.g., 5 pipelined instructions
Parallel Data
  >1 data item @ one time
  e.g., Add of 4 pairs of words
Hardware descriptions
  All gates @ one time
Programming Languages
Smart Phone
Warehouse Scale Computer
Software Hardware
Harness Parallelism &
Achieve High Performance
Logic Gates
Core
Core
…
Memory (Cache)
Input/Output
Computer
Main Memory
Core
Instruction Unit(s)
Functional
Unit(s)
A3+B3
A2+B2
A1+B1
A0+B0
Today’s
Lecture

## Slide 3: Agenda
Virtual Memory Review
Virtual Machines
Administrivia
Programming Contest
And, in Conclusion …

## Slide 4: Agenda
Virtual Memory Review
Virtual Machines
Administrivia
Programming Contest
And, in Conclusion …

## Slide 5: Modern Virtual Memory Systems Illusion of a large, private, uniform store
Protection & Privacy
  several users, each with their private address space and one or more shared address spaces
page table  name space
Demand Paging
  Provides the ability to run programs larger than the primary memory
  Hides differences in machine configurations
The price is address translation on
each memory reference
OS
useri
Primary
Memory
Swapping
Store
VA
PA
mapping
TLB
Notes: Portability on machines with different memory configurations.

## Slide 6: Paged Memory Systems
Processor-generated address can be split into:
Page tables make it possible to store the pages of a program non-contiguously.
0
1
2
3
0
1
2
3
Address Space
of User-1
Page Table
of User-1
1
0
2
3
page number offset
Physical Memory
A page table contains the physical address of the base of each page
Notes: Relaxes the contiguous allocation requirement.

## Slide 7: Hierarchical Page Table
Level 1
Page Table
Level 2
Page Tables
Data Pages
page in primary memory
page in secondary memory
Root of the Current
Page Table
p1
offset
p2
Virtual Address
(Processor
Register)
PTE of a nonexistent page
p1 p2 offset
0
11
12
21
22
31
10-bit
L1 index
10-bit
L2 index
Physical Memory

## Slide 8: Address Translation & Protection
Every instruction and data access needs address
translation and protection checks
A good VM design needs to be fast (~ one cycle) and space efficient
Physical Address
Virtual Address
Address
Translation
Virtual Page No. (VPN)
offset
Physical Page No. (PPN)
offset
Protection
Check
Exception?
Kernel/User Mode
Read/Write

## Slide 9: Translation Lookaside Buffers (TLB)
Address translation is very expensive!
  In a two-level page table, each reference becomes several memory accesses
Solution: Cache translations in TLB
TLB hit  Single-Cycle Translation
TLB miss  Page-Table Walk to refill
VPN offset
V R W D tag PPN
physical address
PPN offset
virtual address
hit?
(VPN = virtual page number)
(PPN = physical page number)
Notes: 3 memory references
2 page faults (disk accesses) + ..
Actually used in IBM before paged memory.

## Slide 10: Page-Based Virtual-Memory Machine (Hardware Page-Table Walk)
PC
Inst. TLB
Inst. Cache
D
Decode
E
M
Data Cache
W
+
Page Fault?
Protection violation?
Page Fault?
Protection violation?
Assumes page tables held in untranslated physical memory
Data TLB
Main Memory (DRAM)
Memory Controller
Physical Address
Physical Address
Physical Address
Physical Address
Page-Table Base Register
Virtual Address
Physical Address
Virtual Address
Hardware Page Table Walker
Miss?
Miss?

## Slide 11: Address Translation: Putting it All Together
Virtual Address
TLB
Lookup
Page Table
Walk
Update TLB
Page Fault
(OS loads page)
Protection
Check
Physical
Address
(to cache)
miss
hit
the page is
Ï memory Î memory
denied
permitted
Protection
Fault
hardware
hardware or software
software
SEGFAULT
Where?
Notes: Need to restart instruction.
Soft and hard page faults.

## Slide 12: Agenda
Virtual Memory Review
Virtual Machines
Administrivia
Programming Contest
And, in Conclusion …

## Slide 13: Safely Sharing a Machine
Amazon Web Services allows independent tasks run on same computer
  Can sell each “instance”
Can a “small” operating system (~10,000 LOC) simulate the hardware of some machine, so that
  Another operating system can run in that simulated hardware?
  More than one instance of that operating system run on the same hardware at the same time?
  More than one different operating system can share the same hardware at the same time?
  And none can access each others’ data?
Answer: Yes

## Slide 14: Solution – Virtual Machine
A virtual machine provides interface identical to underlying bare hardware
  I.e., all devices, interrupts, memory, etc.
Examples
  IBM VM/370 (1970s technology!)
  VMWare (founded by Mendel & Diane Rosenblum)
  Xen (used by AWS)
  Microsoft Virtual PC
Called “System Virtual Machines” vs. language interpreters (e.g., Java Virtual Machine)
Virtualization has some performance impact
  Feasible with modern high-performance computers

## Slide 15: Virtual Machines
Host Operating System:
  OS actually running on the hardware
  Together with virtualization layer, it simulates environment for …
Guest Operating System:
  OS running in the simulated environment
  Runs identical as if on native hardware (except performance)
  Cannot change access of real system resources
  Guest OS code runs in native machine ISA
The resources of the physical computer are shared to create the virtual machines
Processor scheduling by OS can create the appearance that each user has own processor

## Slide 16: Virtual Machine Monitor (a.k.a. Hypervisor)
Maps virtual resources to physical resources
  Memory, I/O devices, processors
VMM handles real I/O devices
  Emulates generic virtual I/O devices for guest OS
Host OS must intercept attempts by Guest OS to access real I/O devices, allocate resources

## Slide 17: Why Virtual Machines Popular (Again)?
Increased importance of isolation and security
Failures in security and reliability of modern OS’s
Sharing of single computer between many unrelated users
  E.g., Cloud computing
Dramatic increase in performance of processors makes VM overhead acceptable

## Slide 18: 5 Reasons Amazon Web Services uses Virtual Machines
(Uses x86 ISA, Linux Host OS, and Xen VMM)
Allow AWS protect users from each other
Simplified SW distribution within WSC
  Customers install image, AWS distributes to all instances
Can reliably “kill” a VM => control resource usage
VMs hide identity of HW => can keep selling old HW AND can introduce new more efficient HW
  VM Performance not need be integer multiple of real HW
VM limiting rate of processing, network, and disk space => AWS offers many price points

## Slide 19: Peer Instruction: True or False
Which statements is True about Virtual Machines?
Multiple Virtual Machines can run on one computer
Multiple Virtual Machine Monitors can run on one computer
III. The Guest OS must be the same as the Host OS
A) I only
B) II only
C) III only
D) I and II
Notes: I is true

## Slide 20: Peer Instruction: True or False
Which statements is True about Virtual Machines?
Multiple Virtual Machines can run on one computer
Multiple Virtual Machine Monitors can run on one computer
III. The Guest OS must be the same as the Host OS
A) I only
B) II only
C) III only
D) I and II
Notes: D) 1c, 2a, 3b

## Slide 21: Virtual Machine/Memory Instruction Set Support
2 modes in hardware: User and System modes
  Some instruction only run in System mode
Page Table Base Register (PTBR): Page Table addr
Privileged instructions only available in system mode
  Trap to system (and VMM) if executed in user mode
All physical resources only accessible using privileged instructions
  Including interrupt controls, I/O registers
Renaissance of virtualization support in ISAs
  Current ISAs (e.g., x86) adapting, following IBM’s path

## Slide 22: Example: Timer Virtualization
In native machine (no VMM), on timer interrupt
  OS suspends current process, handles interrupt, selects and resumes next process
With Virtual Machine Monitor
  VMM suspends current VM, handles interrupt, selects and resumes next VM
If a VM requires timer interrupts
  VMM emulates a virtual timer
  Emulates interrupt for VM when physical timer interrupt occurs

## Slide 23: Virtual Machine Monitor (a.k.a. Hypervisor)
Maps virtual resources to physical resources
  Memory, I/O devices, processors
Guest OS code runs on native machine ISA in user mode
  Traps to VMM on privileged instructions and access to protected resources
Guest OS may be different from host OS
VMM handles real I/O devices
  Emulates generic virtual I/O devices for guest

## Slide 24: Performance Impact of Virtual Machines?
No impact on computation bound program, since they spend ≈0 time in OS
  E.g., matrix multiply
Big impact on I/O-intensive programs, since spend lots of time in OS and execute many systems calls and many privileged instructions
  Although if I/O-bound => spend most time waiting for I/O device, then can hide VM overhead

## Slide 25: Virtual Machines and Cores
Host OS can also limit amount of time a virtual machine uses a processor (core)
Hence, at cost of swapping registers, it can run multiple virtual machines on a single core
AWS cheapest VM was originally 2 VMs per core
Now, with faster processors, can install more VMs per core and deliver same performance or have multiple speeds of cores

## Slide 26: Agenda
Virtual Memory Review
Virtual Machines
Administrivia
Programming Contest
And, in Conclusion …

## Slide 27: Administrivia
Verify all HW, Lab, Midterm, and Project Grades by Friday, 12/6!
Final Exam
  Friday, December 20, 8:00-11:00 RSF Fieldhouse!
  Short answer, fill in the blank, multiple choice, mix and match: 100 points/minutes
  Comprehensive, but concentrated on material since midterm examination
  Closed book/note, open crib sheet as before, MIPS Green Card provided
  Review Session, Monday, 12/9, 1-4 PM, Room 155 Dwinelle
  Special consideration students, please contact

## Slide 28: Administrivia
Topics for Final Exam
  Cache Aware Programming/Cache Blocking
  Data Level Parallelism: Intel SIMD SSE instructions and programming
  Thread Parallelism: Cache Coherency + Synchronization concepts
  OpenMP Programming
  Hardware: Transistors to Gates
  Hardware: Truth Tables to Boolean Algebra
  Hardware: Synchronous System Timing and Timing Diagrams
  Finite State Machines: State Diagrams and Implementation
  CPU Design: Data Path Design (ALUs, Shifters, Register Files, Muxes)
  CPU Design: Controller Design (FSMs for processor implementation)
  Instruction Level Parallelism/Instruction Pipelining
  Set Associative Caches
  Dependability: ECC + RAID
  Virtual Memory
  X-semester issues: Great Ideas in Computer Architecture

## Slide 29: Agenda
Virtual Memory Review
Virtual Machines
Administrivia
Programming Contest
And, in Conclusion …

## Slide 30: Programming Contest

## Slide 31: Agenda
Virtual Memory
Virtual Machines
Administrivia
Programming Contest
And, in Conclusion …

## Slide 32: Agenda
Virtual Memory
Administrivia
Virtual Machines
And, in Conclusion …

## Slide 33: And in Conclusion, …
Virtual Memory, Paging for Isolation and Protection, help Virtual Machines share memory
  Can think of as another level of memory hierarchy, but not really used like caches are today
  Not really routinely paging to disk today
Virtual Machines as even greater level of protection to allow greater level of sharing
  Enables fine control, allocation, software distribution, multiple price points for Cloud Computing