## Slide 1: CS 61C: Great Ideas in Computer Architecture Running a Program - CALL (Compiling, Assembling, Linking, and Loading)
Instructors:
Krste Asanović & Randy H. Katz
http://inst.eecs.Berkeley.edu/~cs61c/fa17
9/19/17
Fall 2017 - Lecture #8

## Slide 2: Outline
Review Instruction Formats + J/JAL
Multiply and Divide
Interpretation vs. Translation
Assembler
Linker
Loader
And in Conclusion …
9/19/17
Fall 2017 - Lecture #8

## Slide 3: Outline
Review Instruction Formats + J/JAL
Multiply and Divide
Interpretation vs. Translation
Assembler
Linker
Loader
And in Conclusion …
9/19/17
Fall 2017 - Lecture #8

## Slide 4: Review: Components of a Computer
Fall 2017 - Lecture #8
9/19/17
Processor
Control
Datapath
PC
Registers
Arithmetic & Logic Unit
(ALU)
Memory
Input
Output
Bytes
Enable?
Read/Write
Address
Write Data
Read Data
Processor-Memory Interface
I/O-Memory Interfaces
Program
Data
Instructions

## Slide 5: Review: RISC-V Instruction Formats
Fall 2017 - Lecture #8
9/19/17
rd = rs1 OP rs2
rd = rs1 OP Immediate; Load rd from Memory(rs1 + Immediate); JALR (rd = PC + 4, PC = rs1 + Immediate)
Store rs2 to Memory(rs1 + Immediate)
Branch if (rs1 condition rs2) is true to Memory(PC + Immediate*2), i.e., PC = PC + Immediate*2
Upper “Long” Immediate (AUIPC, LUI): PC or rd = {imm, 12b’0}
JAL to Memory (PC + Immediate*2), i.e., rd = PC + 4; PC = PC + immediate*2

## Slide 6: J-Format for Jump Instructions (JAL)
JAL saves PC+4 in register rd (the return address)
  Assembler “j” jump is pseudo-instruction, uses JAL but sets rd=x0 to discard return address
Set PC = PC + offset (PC-relative jump: offset = signed immediate * 2)
Target somewhere within ±219 locations, 2 bytes apart
  ±218 32-bit instructions, ±220 bytes
Immediate encoded optimized similarly to branch instruction to reduce hardware cost
Fall 2017 - Lecture #8
9/19/17

## Slide 7: Uses of JAL
# j pseudo-instruction
j Label = jal x0, Label # Discard return address
# Call function within 218 instructions of PC
jal ra, FuncName
Fall 2017 - Lecture #8
9/19/17

## Slide 8: JALR Instruction (I-Format)
JALR rd, rs, immediate
  Writes PC+4 to rd (return address)
  Sets PC = rs + immediate (12 bit, sign extended)
  Uses same immediates as arithmetic and loads
    Unlike branches, no multiplication by two before adding to rs to form the new PC
    Byte offset NOT halfword offset as in branches and JAL
Fall 2017 - Lecture #8
9/19/17

## Slide 9: Uses of JALR
# ret and jr pseudo-instructions
ret = jr ra = jalr x0, ra, 0
# Call function at any 32-bit absolute address
lui x1, <hi20bits>
jalr ra, x1, <lo12bits>
# Jump PC-relative with 32-bit offset
auipc x1, <hi20bits>
jalr x0, x1, <lo12bits>
Fall 2017 - Lecture #8
9/19/17

## Slide 10: Pseudo Instructions
9/19/17
Fall 2017 - Lecture #8
Valid in assembly language but not in machine language
(i.e., maps to multiple machine language instructions)
Notes: auipc: add upper immediate to PC R[rd] = PC + {imm, 12’b0}
Lui: load upper immediate R[rd] = imm + 12’b0
Ori: inclusive OR immediate R[rd] = R[rs1] ^ imm

## Slide 11: Outline
Review Instruction Formats + J/JAL
Multiply and Divide
Interpretation vs. Translation
Assembler
Linker
Loader
And in Conclusion …
9/19/17
Fall 2017 - Lecture #8

## Slide 12: Integer Multiplication (1/3)
Paper and pencil example (unsigned):
  Multiplicand 1000 8
  Multiplier x 1001 9 72
m bits x n bits = m + n bit product
9/19/17
Fall 2017 - Lecture #8

## Slide 13: Integer Multiplication (1/3)
Paper and pencil example (unsigned):
  Multiplicand 1000 8
  Multiplier x 1001 9 1000 72
m bits x n bits = m + n bit product
9/19/17
Fall 2017 - Lecture #8

## Slide 14: Integer Multiplication (1/3)
Paper and pencil example (unsigned):
  Multiplicand 1000 8
  Multiplier x 1001 9 1000 0000 72
m bits x n bits = m + n bit product
9/19/17
Fall 2017 - Lecture #8

## Slide 15: Integer Multiplication (1/3)
Paper and pencil example (unsigned):
  Multiplicand 1000 8
  Multiplier x 1001 9 1000 0000 0000 72
m bits x n bits = m + n bit product
9/19/17
Fall 2017 - Lecture #8

## Slide 16: Integer Multiplication (1/3)
Paper and pencil example (unsigned):
  Multiplicand 1000 8
  Multiplier x 1001 9 1000 0000 0000 + 1000 72
m bits x n bits = m + n bit product
9/19/17
Fall 2017 - Lecture #8

## Slide 17: Integer Multiplication (1/3)
Paper and pencil example (unsigned):
  Multiplicand 1000 8
  Multiplier x 1001 9 1000 0000 0000 + 1000 01001000 72
m bits x n bits = m + n bit product
9/19/17
Fall 2017 - Lecture #8

## Slide 18: Integer Multiplication (2/3)
In RISC-V, we multiply registers, so:
  32-bit value x 32-bit value = 64-bit value
Syntax of Multiplication (signed):
  MUL performs an 32-bit×32-bit multiplication and places the lower 32 bits in the destination register
  MULH performs the same multiplication but returns the upper 32 bits of the full 2×32-bit product
  If 64-bit product is required, then the recommended code sequence is: MULH rdh, rs1, rs2 MUL rdl, rs1, rs2 (source register specifiers must be in same order and rdh cannot be the same as rs1 or rs2)
9/19/17
Fall 2017 - Lecture #8

## Slide 19: Integer Multiplication (3/3)
Example:
  in C: a = b * c; # a should be declared long long
  in RISC-V:
    Let b be t2; let c be t3; and let a be t0 and t1 (since it may be up to 64 bits)
  # upper half of # product into $s0 # lower half of # product into $s1
9/19/17
Fall 2017 - Lecture #8

## Slide 20: Integer Multiplication (3/3)
Example:
  in C: a = b * c; # a should be declared long long
  in RISC-V:
    Let b be t2; let c be t3; and let a be t0 and t1 (since it may be up to 64 bits)
  mulh t0,t2,t3 # upper half of # product into $s0 # lower half of # product into $s1
9/19/17
Fall 2017 - Lecture #8

## Slide 21: Integer Multiplication (3/3)
Example:
  in C: a = b * c; # a should be declared long long
  in RISC-V:
    Let b be t2; let c be t3; and let a be t0 and t1 (since it may be up to 64 bits)
  mulh t0,t2,t3 # upper half of # product into $s0 mul t1,t2,t3 # lower half of # product into $s1
9/19/17
Fall 2017 - Lecture #8

## Slide 22: Integer Division (1/2)
Paper and pencil example (unsigned):
  Quotient Divisor 1000|1001010 Dividend
Dividend = Quotient x Divisor + Remainder
9/19/17
Fall 2017 - Lecture #8

## Slide 23: Integer Division (1/2)
Paper and pencil example (unsigned):
  1 Quotient Divisor 1000|1001010 Dividend -1000 1
Dividend = Quotient x Divisor + Remainder
9/19/17
Fall 2017 - Lecture #8

## Slide 24: Integer Division (1/2)
Paper and pencil example (unsigned):
  10 Quotient Divisor 1000|1001010 Dividend -1000 10
Dividend = Quotient x Divisor + Remainder
9/19/17
Fall 2017 - Lecture #8

## Slide 25: Integer Division (1/2)
Paper and pencil example (unsigned):
  100 Quotient Divisor 1000|1001010 Dividend -1000 10 101
Dividend = Quotient x Divisor + Remainder
9/19/17
Fall 2017 - Lecture #8

## Slide 26: Integer Division (1/2)
Paper and pencil example (unsigned):
  1001 Quotient Divisor 1000|1001010 Dividend -1000 10 101 1010
Dividend = Quotient x Divisor + Remainder
9/19/17
Fall 2017 - Lecture #8

## Slide 27: Integer Division (1/2)
Paper and pencil example (unsigned):
  1001 Quotient Divisor 1000|1001010 Dividend -1000 10 101 1010 -1000
Dividend = Quotient x Divisor + Remainder
9/19/17
Fall 2017 - Lecture #8

## Slide 28: Integer Division (1/2)
Paper and pencil example (unsigned):
  1001 Quotient Divisor 1000|1001010 Dividend -1000 10 101 1010 -1000 10 Remainder (or Modulo result)
Dividend = Quotient x Divisor + Remainder
9/19/17
Fall 2017 - Lecture #8

## Slide 29: Integer Division (2/2)
Syntax of Division (signed):
  DIV performs signed integer division of 32 bits by 32 bits. REM provides the remainder of the corresponding division operation
  If the quotient and remainder are required from the same division, the recommended code sequence is: DIV rdq, rs1, rs2 REM rdr, rs1, rs2 (rdq cannot be the same as rs1 or rs2)
Implements C division (/) and modulo (%)
Example in C: a = c / d; b = c % d;
In RISC-V: a↔t0; b↔t1; c↔t2; d↔t3
  div t0,t2,t3 # a=c/d
  rem t1,t2,t3 # b=c%d
9/19/17
Fall 2017 - Lecture #8

## Slide 30: Peer Question
Which of the following places the address of LOOP in t1?
la t2, LOOP
lw t1, 0(t2)
2) jal LOOP
LOOP: add t1, ra, x0
3) la t1, LOOP
1 2 3
T, T, T
T, T, F
F, T, T
F, T, F
9/19/17
Fall 2017 - Lecture #8

## Slide 31: Peer Question
Which of the following places the address of LOOP in t1?
la t2, LOOP
lw t1, 0(t2)
2) jal LOOP
LOOP: add t1, ra, x0
3) la t1, LOOP
1 2 3
T, T, T
T, T, F
F, T, T
F, T, F
9/19/17
Fall 2017 - Lecture #8

## Slide 32: Break!
9/19/17
Fall 2017 - Lecture #8

## Slide 33: Outline
Review Instruction Formats + J/JAL
Multiply and Divide
Interpretation vs. Translation
Assembler
Linker
Loader
And in Conclusion …
9/19/17
Fall 2017 - Lecture #8

## Slide 34: Levels of Representation/Interpretation
lw $t0, 0($2)
lw $t1, 4($2)
sw $t1, 0($2)
sw $t0, 4($2)
High Level Language Program (e.g., C)
Assembly Language Program (e.g., RISC-V)
Machine Language Program (RISC-V)
Hardware Architecture Description (e.g., block diagrams)
Compiler
Assembler
Machine Interpretation
temp = v[k];
v[k] = v[k+1];
v[k+1] = temp;
0000 1001 1100 0110 1010 1111 0101 1000
1010 1111 0101 1000 0000 1001 1100 0110
1100 0110 1010 1111 0101 1000 0000 1001
0101 1000 0000 1001 1100 0110 1010 1111
Architecture Implementation
Anything can be represented as a number, i.e., data or instructions
Logic Circuit Description (Circuit Schematic Diagrams)
+ How to take a program and run it
9/19/17
Fall 2017 - Lecture #8

## Slide 35: Language Execution Continuum
Interpreter is a program that executes other programs
Language translation gives us another option
In general, we interpret a high-level language when efficiency is not critical and translate to a lower-level language to increase performance
Easy to program
Inefficient to interpret
Difficult to program
Efficient to interpret
Python Java C++
C
Assembly
Machine code
Java bytecode
9/19/17
Fall 2017 - Lecture #8

## Slide 36: Interpretation vs Translation
How do we run a program written in a source language?
  Interpreter: Directly executes a program in the source language
  Translator: Converts a program from the source language to an equivalent program in another language
9/19/17
Fall 2017 - Lecture #8

## Slide 37: Interpretation
For example, consider a Python program foo.py
Python interpreter is just a program that reads a python program and performs the functions of that python program
Python program: foo.py
Python interpreter
9/19/17
Fall 2017 - Lecture #8

## Slide 38: Interpretation
WHY interpret machine language in software?
VENUS (Lab #3), Project #1: RISC-V simulator useful for learning/debugging
E.g., Apple Macintosh conversion
  Switched from Motorola 680x0 instruction architecture to PowerPC (before x86)
  Could require all programs to be re-translated from high level language
  Instead, let executables contain old and/or new machine code, interpret old code in software if necessary (emulation)
9/19/17
Fall 2017 - Lecture #8

## Slide 39: Interpretation vs. Translation? (1/2)
Generally easier to write interpreter
Interpreter closer to high-level, so can give better error messages (e.g., VENUS, Project #1)
  Translator reaction: add extra information to help debugging (line numbers, names)
Interpreter slower (10x?), code smaller (2x?)
Interpreter provides instruction set independence: run on any machine
9/19/17
Fall 2017 - Lecture #8

## Slide 40: Interpretation vs. Translation? (2/2)
Translated/compiled code almost always more efficient and therefore higher performance:
  Important for many applications, particularly operating systems
Translation/compilation helps “hide” the program “source” from the users:
  One model for creating value in the marketplace (e.g., Microsoft keeps all their source code secret)
  Alternative model, “open source”, creates value by publishing the source code and fostering a community of developers.
9/19/17
Fall 2017 - Lecture #8

## Slide 41: Steps in Compiling a C Program
C program: foo.c
Compiler
Executable (mach lang pgm): a.out
Memory
Assembly program: foo.s
Assembler
Object (mach lang module): foo.o
Linker
Loader
lib.o
9/19/17
Fall 2017 - Lecture #8
gcc -O2 -S -c foo.c

## Slide 42: Compiler
Input: High-Level Language Code (e.g., foo.c)
Output: Assembly Language Code (e.g., foo.s for RISC-V)
Note: Output may contain pseudo-instructions
Pseudo-instructions: instructions that assembler understands but not in machine For example (move t2 to t1):
  mv t1,t2  addi t1,t2,0
9/19/17
Fall 2017 - Lecture #8

## Slide 43: Outline
Review Instruction Formats + J/JAL
Multiply and Divide
Interpretation vs. Translation
Assembler
Linker
Loader
And in Conclusion …
9/19/17
Fall 2017 - Lecture #8

## Slide 44: Where Are We Now?
C program: foo.c
Compiler
Executable (mach lang pgm): a.out
Memory
Assembly program: foo.s
Assembler
Object (mach lang module): foo.o
Linker
Loader
lib.o
CS164
9/19/17
Fall 2017 - Lecture #8

## Slide 45: Assembler
Input: Assembly Language Code (includes pseudo ops) (e.g., foo.s for RISC-V)
Output: Object Code, information tables (true assembly only) (e.g., foo.o for RISC-V)
Reads and Uses Directives
Replace Pseudo-instructions
Produce Machine Language
Creates Object File
9/19/17
Fall 2017 - Lecture #8

## Slide 46: Assembler Directives (See RISCV Reader, Chapter 3)
Give directions to assembler, but do not produce machine instructions
  .text: Subsequent items put in user text segment (machine code)
  .data: Subsequent items put in user data segment (binary rep of data in source file)
  .globl sym: declares sym global and can be referenced from other files
  .string str: Store the string str in memory and null-terminate it
  .word w1…wn: Store the n 32-bit quantities in successive memory words
9/19/17
Fall 2017 - Lecture #8

## Slide 47: Pseudo-instruction Replacement
Assembler treats convenient variations of machine language instructions as if real instructions Pseudo: Real:
mv t0, t1
9/19/17
Fall 2017 - Lecture #8

## Slide 48: Pseudo-instruction Replacement
Assembler treats convenient variations of machine language instructions as if real instructions Pseudo: Real:
mv t0, t1 addi t0,t1,0
neg t0, t1 sub t0, zero, t1
li t0, imm addi t0, zero, imm
not t0, t1 xori t0, t1, -1
beqz t0, loop beq t0, zero, loop
la t0, str lui t0, str[31:12] addi t0, t0, str[11:0] OR
auipc t0, str[31:12] addi t0, t0, str[11:0]
9/19/17
Fall 2017 - Lecture #8
DON’T FORGET:
sign extended immediates
+
Branch immediates count halfwords)
STATIC Addressing PC-Relative Addressing

## Slide 49: Peer Instruction
Which of the following is a correct assembly language sequence sequence for the pseudoinstruction: la t1, FOO?*
A: ori t1, 0xABCD0 addi t1, 0x124
B: ori t1, 0x124 lui t1, 0xABCD0
C: lui t1, 0xD0124 ori t1, 0xABC D: lui t1, 0xABCD0 addi t1, 0x124
*Assume the address of FOO is 0xABCD0124
9/19/17
Fall 2017 - Lecture #8

## Slide 50: Peer Instruction
Which of the following is a correct assembly language sequence sequence for the pseudoinstruction: la t1, FOO?*
A: ori t1, 0xABCD0 addi t1, 0x124
B: ori t1, 0x124 lui t1, 0xABCD0
C: lui t1, 0xD0124 ori t1, 0xABC D: lui t1, 0xABCD0 addi t1, 0x124
*Assume the address of FOO is 0xABCD0124
9/19/17
Fall 2017 - Lecture #8

## Slide 51: Producing Machine Language (1/3)
Simple Case
  Arithmetic, Logical, Shifts, and so on
  All necessary info is within the instruction already
What about Branches and Jumps?
  PC-Relative (e.g., beq/bne and jal)
  So once pseudo-instructions are replaced by real ones, we know by how many instructions to branch/jump over
So these can be handled
9/19/17
Fall 2017 - Lecture #8

## Slide 52: Producing Machine Language (2/3)
“Forward Reference” problem
  Branch instructions can refer to labels that are “forward” in the program:
  Solved by taking two passes over the program
    First pass remembers position of labels
    Second pass uses label positions to generate code
addi t2, zero, 9 # t2 = 9 L1: slt t1, zero, t2 # 0 < t2? Set t1 beq t1, zero, L2 # NO! t2 <= 0; Go to L2 addi t2, t2, -1 # YES! t2 > 0; t2-- j L1 # Go to L1 L2:
9/19/17
Fall 2017 - Lecture #8
3 words back (6 halfwords)
3 words forward (6 halfwords)
addi t2, zero, 9 # t2 = 9 L1: bge zero, t2, L2 # 0 >= t2? Exit! addi t2, t2, -1 # 0 < t2; t2-- j L1 # Go to L1 L2:
2 words back (4 halfwords)
2 words forward (4 halfwords)

## Slide 53: Producing Machine Language (3/3)
What about PC-relative jumps (jal) and branches (beq, bne)?
  j offset pseudo instruction expands to JAL zero, offset
  Just count the number of instruction halfwords between target and jump to determine the offset: position-independent code (PIC)
What about references to static data?
  la gets broken up into lui and addi (use auipc/addi for PIC)
  These require the full 32-bit address of the data
These can’t be determined yet, so we create two tables …
9/19/17
Fall 2017 - Lecture #8

## Slide 54: Symbol Table
List of “items” in this file that may be used by other files
What are they?
  Labels: function calling
  Data: anything in the .data section; variables which may be accessed across files
9/19/17
Fall 2017 - Lecture #8

## Slide 55: Relocation Table
List of “items” whose address this file needs What are they?
  Any absolute label jumped to: jal, jalr
    Internal
    External (including lib files)
    Such as the la instruction E.g., for jalr base register
  Any piece of data in static section
    Such as the la instruction E.g., for lw/sw base register
9/19/17
Fall 2017 - Lecture #8

## Slide 56: Object File Format
object file header: size and position of the other pieces of the object file
text segment: the machine code
data segment: binary representation of the static data in the source file
relocation information: identifies lines of code that need to be fixed up later
symbol table: list of this file’s labels and static data that can be referenced
debugging information
A standard format is ELF (except MS) http://www.skyfree.org/linux/references/ELF_Format.pdf
9/19/17
Fall 2017 - Lecture #8

## Slide 57: Outline
Review Instruction Formats + J/JAL
Multiply and Divide
Interpretation vs. Translation
Assembler
Linker
Loader
And in Conclusion …
9/19/17
Fall 2017 - Lecture #8

## Slide 58: Where Are We Now?
C program: foo.c
Compiler
Executable (mach lang pgm): a.out
Memory
Assembly program: foo.s
Assembler
Object (mach lang module): foo.o
Linker
Loader
lib.o
9/19/17
Fall 2017 - Lecture #8

## Slide 59: Linker (1/3)
Input: Object code files, information tables (e.g., foo.o,libc.o for RISC-V)
Output: Executable code (e.g., a.out for RISC-V)
Combines several object (.o) files into a single executable (“linking”)
Enable separate compilation of files
  Changes to one file do not require recompilation of the whole program
    Linux source > 20 M lines of code!
  Old name “Link Editor” from editing the “links” in jump and link instructions
9/19/17
Fall 2017 - Lecture #8

## Slide 60: Linker (2/3)
.o file 1
text 1
data 1
info 1
.o file 2
text 2
data 2
info 2
Linker
a.out
Relocated text 1
Relocated text 2
Relocated data 1
Relocated data 2
9/19/17
Fall 2017 - Lecture #8

## Slide 61: Linker (3/3)
Step 1: Take text segment from each .o file and put them together
Step 2: Take data segment from each .o file, put them together, and concatenate this onto end of text segments
Step 3: Resolve references
  Go through Relocation Table; handle each entry
  I.e., fill in all absolute addresses
9/19/17
Fall 2017 - Lecture #8

## Slide 62: Four Types of Addresses
PC-Relative Addressing (beq, bne, jal; auipc/addi)
  Never need to relocate (PIC: position independent code)
Absolute Function Address (auipc/jalr)
  Always relocate
External Function Reference (auipc/jalr)
  Always relocate
Static Data Reference (often lui/addi)
  Always relocate
9/19/17
Fall 2017 - Lecture #8

## Slide 63: Absolute Addresses in RISC-V
Which instructions need relocation editing?
  J-format: jump/jump and link
  I-,S- Format: Loads and stores to variables in static area, relative to global pointer
  What about conditional branches?
  PC-relative addressing preserved even if code moves
jal
xxxxx
lw
gp
rd
xxx
beq bne
rs1
rs2
x
9/19/17
Fall 2017 - Lecture #8
rd
sw
rs1
gp
xx
xx
x

## Slide 64: Resolving References (1/2)
Linker assumes first word of first text segment is at address 0x10000 for RV32.
  (More later when we study “virtual memory”)
Linker knows:
  Length of each text and data segment
  Ordering of text and data segments
Linker calculates:
  Absolute address of each label to be jumped to (internal or external) and each piece of data being referenced
9/19/17
Fall 2017 - Lecture #8

## Slide 65: Resolving References (2/2)
To resolve references:
  Search for reference (data or label) in all “user” symbol tables
  If not found, search library files (e.g., for printf)
  Once absolute address is determined, fill in the machine code appropriately
Output of linker: executable file containing text and data (plus header)
9/19/17
Fall 2017 - Lecture #8

## Slide 66: Administrivia
Midterm #1 in 1 week: September 26!
  IN CLASS! 8-9:30 AM Wheeler Auditorium + five Spill Rooms based on class login
  Number Representations, C (pointers, arrays, strings), mapping C to RISC-V Assembly (and vice versa), NO MACHINE LANGUAGE ON THIS EXAM
  Single double sided 8.5” x 11” cheat sheet + we give you the RISC-V Green Card
  Review session Saturday, September 23: Time and place TBD
  DSP students: please make sure we know about your special accommodations (contact TA Steven Ho)
9/19/17
Fall 2017 - Lecture #8

## Slide 67: Break!
9/19/17
Fall 2017 - Lecture #8

## Slide 68: Outline
Review Instruction Formats + J/JAL
Multiply and Divide
Interpretation vs. Translation
Assembler
Linker
Loader
And in Conclusion …
9/19/17
Fall 2017 - Lecture #8

## Slide 69: Where Are We Now?
C program: foo.c
Compiler
Executable (mach lang pgm): a.out
Memory
Assembly program: foo.s
Assembler
Object (mach lang module): foo.o
Linker
Loader
lib.o
9/19/17
Fall 2017 - Lecture #8

## Slide 70: Loader Basics
Input: Executable Code (e.g., a.out for RISC-V)
Output: (program is run)
Executable files are stored on disk
When one is run, loader’s job is to load it into memory and start it running
In reality, loader is the operating system (OS)
  Loading is one of the OS tasks
9/19/17
Fall 2017 - Lecture #8

## Slide 71: Loader … What Does It Do?
Reads executable file’s header to determine size of text and data segments
Creates new address space for program large enough to hold text and data segments, along with a stack segment
Copies instructions + data from executable file into the new address space
Copies arguments passed to the program onto the stack
Initializes machine registers
  Most registers cleared, but stack pointer assigned address of 1st free stack location
Jumps to start-up routine that copies program’s arguments from stack to registers & sets the PC
  If main routine returns, start-up routine terminates program with the exit system call
9/19/17
Fall 2017 - Lecture #8

## Slide 72: Peer Instruction
At what point in process are all the machine code bits determined for the following assembly instructions:
1) add x6, x7, x8
2) jal x1, fprintf
A: 1) & 2) After compilation
B: 1) After compilation, 2) After assembly
C: 1) After assembly, 2) After linking
D: 1) After assembly, 2) After loading
9/19/17
Fall 2017 - Lecture #8

## Slide 73: Peer Instruction
At what point in process are all the machine code bits determined for the following assembly instructions:
1) add x6, x7, x8
2) jal x1, fprintf
A: 1) & 2) After compilation
B: 1) After compilation, 2) After assembly
C: 1) After assembly, 2) After linking
D: 1) After assembly, 2) After loading
9/19/17
Fall 2017 - Lecture #8

## Slide 74: Example C Program: Hello.c
#include <stdio.h>
int main()
{
printf("Hello, %s\n", "world");
return 0;
}
9/19/17
Fall 2017 - Lecture #8
74

## Slide 75: Compiled Hello.c: Hello.s
.text
.align 2
.globl main
main:
addi sp,sp,-16
sw ra,12(sp)
lui a0,%hi(string1)
addi a0,a0,%lo(string1)
lui a1,%hi(string2)
addi a1,a1,%lo(string2)
call printf
lw ra,12(sp)
addi sp,sp,16
li a0,0
ret
.section .rodata
.balign 4
string1:
.string "Hello, %s!\n"
string2:
.string "world"
# Directive: enter text section
# Directive: align code to 2^2 bytes
# Directive: declare global symbol main
# label for start of main
# allocate stack frame
# save return address
# compute address of
# string1
# compute address of
# string2
# call function printf
# restore return address
# deallocate stack frame
# load return value 0
# return
# Directive: enter read-only data section
# Directive: align data section to 4 bytes
# label for first string
# Directive: null-terminated string
# label for second string
# Directive: null-terminated string
9/19/17
Fall 2017 - Lecture #8
75

## Slide 76: Assembled Hello.s: Linkable Hello.o
00000000 <main>:
0: ff010113 addi sp,sp,-16
4: 00112623 sw ra,12(sp)
8: 00000537 lui a0,0x0 # addr placeholder
c: 00050513 addi a0,a0,0 # addr placeholder
10: 000005b7 lui a1,0x0 # addr placeholder
14: 00058593 addi a1,a1,0 # addr placeholder
18: 00000097 auipc ra,0x0 # addr placeholder
1c: 000080e7 jalr ra # addr placeholder
20: 00c12083 lw ra,12(sp)
24: 01010113 addi sp,sp,16
28: 00000513 addi a0,a0,0
2c: 00008067 jalr ra
9/19/17
Fall 2017 - Lecture #8
76

## Slide 77: Linked Hello.o: a.out
000101b0 <main>:
101b0: ff010113 addi sp,sp,-16
101b4: 00112623 sw ra,12(sp)
101b8: 00021537 lui a0,0x21
101bc: a1050513 addi a0,a0,-1520 # 20a10 <string1>
101c0: 000215b7 lui a1,0x21
101c4: a1c58593 addi a1,a1,-1508 # 20a1c <string2>
101c8: 288000ef jal ra,10450 # <printf>
101cc: 00c12083 lw ra,12(sp)
101d0: 01010113 addi sp,sp,16
101d4: 00000513 addi a0,0,0
101d8: 00008067 jalr ra
9/19/17
Fall 2017 - Lecture #8
Notes: 1520= 0x5F0
-0x5F0 = 0xFFFFFA10
0x00020A10 – X + 0xFFFFFA10
X = 0x00020A10 – 0xFFFFFA10
X[32:12] = 0x00020 – 0xFFFFF = 0x00020 + 1 = 0x21
0x20a10 = 0x00020000 + 0x00000a10 = 0x00020000 + 0xfffffa10 – 0xfffff000 = 0x00020000 + 0xfffffa10 + 0x00001000 (twos complement of 0xfffff000)
Note: there is NO subi in RISC-V

## Slide 78: LUI/ADDI Address Calculation in RISC-V
Target address of <string1> is 0x00020 A10
Instruction sequence LUI 0x00020, ADDI 0xA10 does not quite work because immediates in RISC-V are sign extended (and 0xA10 has a 1 in the high order bit)!
0x00020 000 + 0xFFFFF A10 = 0x0001F A10 (Off by 0x00001 000)
So we get the right address if we calculate it as follows:
(0x00020 000 + 0x00001 000) + 0xFFFFF A10 = 0x00020 A10
What is 0xFFFFF A10?
Twos complement of 0xFFFFF A10 = 0x00000 5EF + 1 = 0x00000 5F0 = 1520ten
So 0xFFFFF A10 = -1520ten
Instruction sequence LUI 0x00021, ADDI -1520 calculates 0x00020 A10
9/19/17
Fall 2017 - Lecture #8

## Slide 79: Static vs. Dynamically Linked Libraries
What we’ve described is the traditional way: statically-linked approach
  Library is now part of the executable, so if the library updates, we don’t get the fix (have to recompile if we have source)
  Includes the entire library even if not all of it will be used
  Executable is self-contained
Alternative is dynamically linked libraries (DLL), common on Windows & UNIX platforms
9/19/17
Fall 2017 - Lecture #8

## Slide 80: Dynamically Linked Libraries
Space/time issues
  + Storing a program requires less disk space
  + Sending a program requires less time
  + Executing two programs requires less memory (if they share a library)
  – At runtime, there’s time overhead to do link
Upgrades
  + Replacing one file (libXYZ.so) upgrades every program that uses library “XYZ”
  – Having the executable isn’t enough anymore
Overall, dynamic linking adds quite a bit of complexity to the compiler, linker, and operating system. However, it provides many benefits that often outweigh these
en.wikipedia.org/wiki/Dynamic_linking
9/19/17
Fall 2017 - Lecture #8

## Slide 81: Dynamically Linked Libraries
Prevailing approach to dynamic linking uses machine code as the “lowest common denominator”
  Linker does not use information about how the program or library was compiled (i.e., what compiler or language)
  Can be described as “linking at the machine code level”
  This isn’t the only way to do it ...
9/19/17
Fall 2017 - Lecture #8

## Slide 82: Outline
Review Instruction Formats + J/JAL
Multiply and Divide
Interpretation vs. Translation
Assembler
Linker
Loader
And in Conclusion …
9/19/17
Fall 2017 - Lecture #8

## Slide 83: And In Conclusion, …
C program: foo.c
Compiler
Executable (mach lang pgm): a.out
Memory
Assembly program: foo.s
Assembler
Object (mach lang module): foo.o
Linker
Loader
lib.o
Compiler converts a single HLL file into a single assembly language file
Assembler removes pseudo-instructions, converts what it can to machine language, and creates a checklist for the linker (relocation table): A .s file becomes a .o file
  Does 2 passes to resolve addresses, handling internal forward references
Linker combines several .o files and resolves absolute addresses
  Enables separate compilation, libraries that need not be compiled, and resolves remaining addresses
Loader loads executable into memory and begins execution
9/19/17
Fall 2017 - Lecture #8