## Slide 1: CS 61C: Great Ideas in Computer Architecture Building Blocks for Datapath and Control
Instructors:
Krste Asanović and Randy H. Katz
http://inst.eecs.Berkeley.edu/~cs61c/fa17

## Slide 2: You are Here!
Parallel Requests
  Assigned to computer
  e.g., Search “Katz”
Parallel Threads
  Assigned to core
  e.g., Lookup, Ads
Parallel Instructions
  >1 instruction @ one time
  e.g., 5 pipelined instructions
Parallel Data
  >1 data item @ one time
  e.g., Add of 4 pairs of words
Hardware descriptions
  All gates @ one time
Programming Languages
Smart Phone
Warehouse Scale Computer
Software Hardware
Harness Parallelism &
Achieve High Performance
Logic Gates
Core
Core
…
Memory (Cache)
Input/Output
Computer
Cache Memory
Core
Instruction Unit(s)
Functional
Unit(s)
A3+B3
A2+B2
A1+B1
A0+B0
Today

## Slide 3: Levels of Representation/Interpretation
lw $t0, 0($2)
lw $t1, 4($2)
sw $t1, 0($2)
sw $t0, 4($2)
High Level Language Program (e.g., C)
Assembly Language Program (e.g., RISC-V)
Machine Language Program (RISC-V)
Hardware Architecture Description (e.g., block diagrams)
Compiler
Assembler
Machine Interpretation
temp = v[k];
v[k] = v[k+1];
v[k+1] = temp;
0000 1001 1100 0110 1010 1111 0101 1000
1010 1111 0101 1000 0000 1001 1100 0110
1100 0110 1010 1111 0101 1000 0000 1001
0101 1000 0000 1001 1100 0110 1010 1111
Logic Circuit Description (Circuit Schematic Diagrams)
Architecture Implementation
Anything can be represented as a number, i.e., data or instructions

## Slide 4: Design Hierarchy
system
datapath
control
state registers
combinational logic
multiplexer
comparator
code registers
register
logic
switching networks

## Slide 5: Agenda
Boolean Algebra
Timing and State Machines
Datapath Elements: Mux + ALU
RISC-V Lite Datapath
And, in Conclusion, …

## Slide 6: Agenda
Boolean Algebra
Timing and State Machines
Datapath Elements: Mux + ALU
RISC-V Lite Datapath
And, in Conclusion, …

## Slide 7: Boolean Algebra
Use plus for OR
  “logical sum”
Use product for AND (ab or implied via ab)
  “logical product”
“Hat” to mean complement (NOT)
Thus
ab + a + c
= ab + a + c
= (a AND b) OR a OR (NOT c )

## Slide 8: Boolean Algebra: Circuit & Algebraic Simplification

## Slide 9: Laws of Boolean Algebra
X X = 0
X 0 = 0
X 1 = X
X X = X
X Y = Y X
(X Y) Z = X (Y Z)
X (Y + Z) = X Y + X Z
X Y + X = X
X Y + X = X + Y
X Y = X + Y
X + X = 1
X + 1 = 1
X + 0 = X
X + X = X
X + Y = Y + X
(X + Y) + Z = X + (Y + Z)
X + Y Z = (X + Y) (X + Z)
(X + Y) X = X
(X + Y) X = X Y
X + Y = X Y
Complementarity
Laws of 0’s and 1’s
Identities
Idempotent Laws
Commutativity
Associativity
Distribution
Uniting Theorem
Uniting Theorem v. 2
DeMorgan’s Law

## Slide 10: Boolean Algebraic Simplification Example
Notes: Do on black board
First write truth table
Then minimize and check truth table
From distribution: a(b +1) + c
Froms laws of 0s and 1s: b+1 = 1
= a + c
Truth Table
a b c y
0 0 0 0
0 0 1 1
0 0 1 1

## Slide 11: Boolean Algebraic Simplification Example
a b c y
0 0 0 0
0 0 1 1
0 1 0 0
0 1 1 1
1 0 0 1
1 0 1 1
1 1 0 1
1 1 1 1
Notes: Do on black board
From distribution: a(b +1) + c
Froms laws of 0s and 1s: b+1 = 1
= a + c
Truth Table
a b c y
0 0 0 0
0 0 1 1
0 1 0 0
0 1 1 1
1 0 0 1
1 0 1 1
1 1 0 1
1 1 1 1

## Slide 12: Agenda
Boolean Algebra
Timing and State Machines
Datapath Elements: Mux + ALU
RISC-V Lite Datapath
And, in Conclusion, …

## Slide 13: Types of Circuits
Synchronous Digital Systems consist of two basic types of circuits:
  Combinational Logic (CL) circuits
    Output is a function of the inputs only, not the history of its execution
    E.g., circuits to add A, B (ALUs)
    Last lecture was comninational logic
  Sequential Logic (SL)
    Circuits that “remember” or store information
    aka “State Elements”
    E.g., memories and registers (Registers)
    Rest of today’s lecture is sequential logic

## Slide 14: Design Hierarchy
system
datapath
control
state registers
combinational logic
multiplexer
comparator
code registers
register
logic
switching networks

## Slide 15: Uses for State Elements
Place to store values for later re-use:
  Register files (like $1-$31 on the RISC-V)
  Memory (caches and main memory)
Help control flow of information between combinational logic blocks
  State elements hold up the movement of information at input to combinational logic blocks to allow for orderly passage

## Slide 16: Program Counter: First Design
Program Counter “PC”
  Instruction address
  Next PC: add 4 to current value
  Let’s try …
PC
PC + 4
Something is not quite right:
  PC and PC+4 simutaneously on same wire???

## Slide 17: Fix
Memory element breaks the feedback loop
How does it work?

## Slide 18: RS Latch
Time
0
0
1
0
1
1
0
Q and Qbar keep state,
despite S deasserted  memory

## Slide 19: (Positive) Edge Triggered Flip-Flop
D
Q
clk
Time
Clock “clk”
RS latch operates on input levels
D FF operates on (clock) edges
Notes: {signal: [ {name: 'clk', wave: '0H..l..H...', node: '.a.....b'}, {name: 'D', wave: '1....0.....'}, {name: 'Q', wave: '0..1.....0.', node: '...c.....d'},], edge: [ 'a~->c', 'b~->d',]}

## Slide 20: Program Counter: Improved Design
Next PC
Current PC
Notes: {signal: [ {name: 'clk', wave: '0H..l..H...', node: '.a.....b'}, {name: 'Current PC', wave: '2.3.....4..', node: '..c.....d', data: 'PC PC+4 PC+8'}, {name: 'Next PC', wave: '3..4.....5.', node: '...e.....f', data:'PC+4 PC+8 PC+12'},], edge: [ 'a~>c', 'b~>d', 'c~>e', 'd~>f']}

## Slide 21: Clock
Clock frequency fs | Period tcycle = 1/fs
CPU 2.5 GHz | 400 ps
Drum/heartbeat, 1Hz | 1 s
fs = 1/ tcycle
Notes: Faster processors enabled
digital audio ~ 1980
digital video 199x
… now enables entirely new functions (e.g. search engines) that did not even exist with analog processing.
But: many physical signals are inherently analog. E.g. my voice: I cannot speak ”digital”, and you could not understand me anyway.
{signal: [ {name: 'clk', wave: 'P....'}, {name: 'instr', wave: '34534', data: 'instr_1 instr_2 instr_3 instr_4 instr_5'}, {node: 'abcdef'}], edge: ['a<->b t<sub>cycle', 'c<->b t<sub>cycle', 'c<->d t<sub>cycle', 'd<->e t<sub>cycle', 'e<->f t<sub>cycle', ], config: { hscale: 3 }}

## Slide 22: Maximum Clock Speed
How fast can the PC circuit operate?
  I.e. what is the maximum clock frequency?
Let’s look at the timing requirements of each part
  Let’s start with the flip-flop

## Slide 23: Flip-Flop Timing
Notes: {signal: [ {name: 'clk', wave: '0.H..', node: '..a'}, { node: '.bc'}, { node: '..de'}, {name: 'D', wave: 'x4.x.', node: '.k.l', data: 'Data'}, { node: '..f.g'}, {name: 'Q', wave: 'x...4', node: '....h', data:'Data'},], edge: [ 'b<->c t<sub>setup', 'k-b', 'a-f', 'd<->e t<sub>hold', 'e-l', 'f<->g t<sub>clk-to-Q', 'g-h' ], config: { hscale: 1.5 }}

## Slide 24: Flip-Flop Timing
Time | Description
tsetup | time during which D must not change before positive clock edge
thold | time during which D must not change after positive clock edge
tclk-to-Q | delay after positive clock edge after which D appears at Q output

## Slide 25: Camera Analogy
Notes: {signal: [ {name: 'clk', wave: '0.H..', node: '..a'}, { node: '.bc'}, { node: '..de'}, {name: 'You', wave: 'z4.z.', node: '.k.l', data: "hold-still"}, {name: 'Shutter', wave: 'z.4z.', node: '...h', data:'open'}, { node: '..f.g'}, {name: 'Display', wave: 'z...4', node: '....h', data:'portrait'},], edge: [ 'b<->c t<sub>setup', 'k-b', 'a-f', 'd<->e t<sub>hold', 'e-l', 'f<->g t<sub>clk-to-Q', 'g-h' ], config: { hscale: 1.5 }}

## Slide 26: Maximum Clock Speed
Combinatorial
Logic
(CL)
Register
(flip-flops)
Optional Feedback
Output
Input
Clock
CL
tCL
Notes: {signal: [ {name: 'clk', wave: 'H.lH.lH.', node: '...a..b'}, {name: 'Input', wave: '23..4..5', node: '.c..d..e', data: 'Input[-1] Input Input[+1] Input[+2]' }, {name: 'CL', wave: '2.3..4..', node: '..f..g..', data: 'CL[-1] CL CL[+1]' }, {name: 'Output', wave: '22..3..4', node: '.h..i..j', data: 'Output[-1] Output Output[+1]' }, {node: '.klmnopq'}, {node: '...y..z'},], edge: [ 'k<->l t<sub>CL', 'c-k', 'l-f', 'l<->m t<sub>setup', 'm-a', 'm<->n t<sub>clk-2-q', 'i-n', 'c~->f', 'a~->i', 'i->d', 'n<->o t<sub>CL', 'o<->p t<sub>setup', 'p<->q t<sub>clk-2-q', 'd~->g', 'b~->j', 'j->e', 'y<->z t<sub>cycle</sub> >= t<sub>clk-to-q</sub>+t<sub>CL</sub>+t<sub>setup</sub>', 'a-y', 'b-z'], config: { hscale: 2 }}

## Slide 27: Maximum PC Clock Speed
Minimum cycle time:
Maximum clock rate:
Example: tsetup ≥ 15ps, tadd = 75ps, tclk-toQ ≥ 10ps
tmin ≥ 100ps
fclk-max ≤ 10GHz
Notes: {signal: [ {name: 'clk', wave: '0.H.l.H', node: '..a...b'}, { node: '.cd..hi'}, { node: '..ef'}, {name: 'Current PC', wave: '2..3...', node: '...g', data: 'PC PC+4 PC+8'}, { node: '...lm'}, {name: 'Next PC', wave: '3...4..', node: '.o..rs', data:'PC+4 PC+8 PC+12'},], edge: [ 'c<->d t<sub>setup', 'c-o', 'a-d', 'e<->f t<sub>clk-to-Q', 'd-e', 'f-g', 'l<->m t<sub>add', 'g-l', 'm-r', 'h<->i t<sub>setup', 'h-s', 'b-i' ], config: { hscale: 2 }}

## Slide 28: Design Hierarchy
system
datapath
control
state registers
combinational logic
multiplexer
comparator
code registers
register
logic
switching networks

## Slide 29: Example: Serial Communication
Wifi sends data “1 bit at a time”
How do we know where a byte “starts”?
Send “preamble …”
  E.g. 3 one’s in a row
Notes: {signal: [ {name: 'clk', wave: 'P.............'}, {name: 'data', wave: '101..010.101.0', node: '..a', data: '1 0 1 1'}, {node: '..b..c.......d'}], edge: [ 'b<->c preamble', 'c<->d 1st Byte (8 bits)', 'a-b'],foot: {tock:-5 }, config: { hscale: 1 }}

## Slide 30: FSM* to Detect 3 One’s
State transition diagram:
FSM to detect the occurrence of 3 consecutive 1’s in the input.
* FSM = Finite State Machine
Notes: {signal: [ {name: 'clk', wave: 'l.H.l.H.l.H.l.H.l.H.l.H.l'}, {name: 'in', wave: '1...0...1...........0....'}, {name: 'out', wave: '0..................1...0.'}, {name: 'state', wave: '3..4...3...4...5...3...3.', data:['S0', 'S0', 'S1', 'S0', 'S1', 'S2', 'S0']},]}

## Slide 31: FSM* to Detect 3 One’s
State transition diagram:
FSM to detect the occurrence of 3 consecutive 1’s in the input.
* FSM = Finite State Machine
State transitions are controlled by
the clock: on each clock cycle the FSM
checks the inputs,
transitions to a new state, and
produces a new output …
Input/output
S0: idle
S1: detected 1
S2: detected 11
Notes: {signal: [ {name: 'clk', wave: 'l.H.l.H.l.H.l.H.l.H.l.H.l'}, {name: 'in', wave: '1...0...1...........0....'}, {name: 'out', wave: '0..................1...0.'}, {name: 'state', wave: '3..4...3...4...5...3...3.', data:['S0', 'S0', 'S1', 'S0', 'S1', 'S2', 'S0']},]}

## Slide 32: FSM Combinatorial Logic
Truth Table
Current State | Input | Next State | Output
State | Code
State Encoding

## Slide 33: FSM Combinatorial Logic
Truth Table
State | Code
State Encoding
State | Code
S0 | 00
S1 | 01
S2 | 10
unused | 11
PS | Input | NS | Output
XX | 0 | 00 | 0
00 | 1 | 01 | 0
01 | 1 | 10 | 0
10 | 1 | 00 | 1
11 | X | 00 | 0

## Slide 34: Hardware Implementation of FSM
clock

## Slide 35: Finite State Machines (FSM) - Summary
Describe computation over time
Represent FSM with “state transition diagram”
Start at given state and input, follow some edge to next (or same) state
With combinational logic and registers, any FSM can be implemented in hardware
state transition diagram

## Slide 36: Administrivia
Homework 2 set to be released Friday
  It will be multiple-choice and free response style (similar to HW0)
  Due in next Friday (in 1 week)
Project 1 Part 1 will also be released Friday
  Due Monday, Oct 9
Homework 1 regrades:
  Google form will be released tonight
  Instructions and guidelines will be on the piazza post

## Slide 37: Break!
10/5/17
Fall 2017 - Lecture #10

## Slide 38: Agenda
Boolean Algebra
Timing and State Machines
Datapath Elements: Mux + ALU
RISC-V Lite Datapath
And, in Conclusion, …

## Slide 39: Design Hierarchy
system
datapath
control
state registers
combinational logic
multiplexer
comparator
code registers
register
logic
switching networks

## Slide 40: Conceptual RISC-V Datapath

## Slide 41: Data Multiplexer (e.g., 2-to-1 x n-bit-wide)
“mux”
Notes: Go to Logisim and do design from mux

## Slide 42: N Instances of 1-bit-Wide Mux

## Slide 43: How Do We Build a 1-bit-Wide Mux (in Logisim)?
s
Notes: Draw on Board, Build in Logisim, create as subcircuit my mux
Make s north facing

## Slide 44: 4-to-1 Multiplexer
How many rows in TT?

## Slide 45: Alternative Hierarchical Approach (in Logisim)

## Slide 46: Arithmetic and Logic Unit
Most processors contain a special logic block called “Arithmetic and Logic Unit” (ALU)
We’ll show you an easy one that does ADD, SUB, bitwise AND, bitwise OR

## Slide 47: Simple ALU

## Slide 48: Adder/Subtractor: One-bit adder Least Significant Bit

## Slide 49: Adder/Subtractor: One-bit adder (1/2) …

## Slide 50: Adder/Subtractor: One-bit Adder (2/2) …

## Slide 51: N x 1-bit Adders  1 N-bit Adder
+
+
+
b0
Connect Carry Out i-1 to Carry in i:

## Slide 52: Twos Complement Adder/Subtractor

## Slide 53: Critical Path
When setting clock period in synchronous systems, must allow for worst case
Path through combinational logic that is worst case called “critical path”
  Can be estimated by number of “gate delays”: Number of gates must go through in worst case
Idea: Doesn’t matter if speedup other paths if don’t improve the critical path
What might critical path of ALU?

## Slide 54: Break!
10/5/17
Fall 2017 - Lecture #10

## Slide 55: Agenda
Boolean Algebra
Timing and State Machines
Datapath Elements: Mux + ALU
RISC-V Lite Datapath
And, in Conclusion, …

## Slide 56: Processor Design Process
Five steps to design a processor:
  1. Analyze instruction set  datapath requirements
  2. Select set of datapath components & establish clock methodology
  3. Assemble datapath meeting the requirements
  4. Analyze implementation of each instruction to determine setting of control points that effects the register transfer.
  5. Assemble the control logic
    Formulate Logic Equations
    Design Circuits
Control
Datapath
Memory
Processor
Input
Output

## Slide 57: The RISC-V Lite Subset
ADD and SUB
  add rd,rs1,rs2
  sub rd,rs1,rs2
OR Immediate:
  ori rd,rs1,imm12
LOAD and STORE Word
  lw rd,rs1,imm12
  sw rs2,rs1,imm12
BRANCH:
  beq rs1,rs2,imm12
Notes: In today’s lecture, I will show you how to implement the following subset of RISC-V instructions: add, subtract, or immediate, load, store, branch, and the jump instruction.
The Add and Subtract instructions use the R format. The Op together with the Func fields together specified all the different kinds of add and subtract instructions.
Rs and Rt specifies the source registers. And the Rd field specifies the destination register.
The Or immediate instruction uses the I format. It only uses one source register, Rs. The other operand comes from the immediate field. The Rt field is used to specified the destination register. (Note that dest is the Rt field!)
Both the load and store instructions use the I format and both add the Rs and the immediate filed together to from the memory address.
The difference is that the load instruction will load the data from memory into Rt while the store instruction will store the data in Rt into the memory.
The branch on equal instruction also uses the I format. Here Rs and Rt are used to specified the registers we need to compare.
If these two registers are equal, we will branch to a location offset by the immediate field.
Finally, the jump instruction uses the J format and always causes the program to jump to a memory location specified in the address field.
I know I went over this rather quickly and you may have missed something. But don’t worry, this is just an overview. You will keep seeing these (point to the format) all day today.
+3 = 13 min. (X:53)

## Slide 58: Register Transfer Language (RTL)
RTL gives the meaning of the instructions
All start by fetching the instruction
{op , rs1 , rs2 , rd , funct3}  MEM[ PC ]
{op , rs1 , rs2 , Imm12}  MEM[ PC ]
Inst Register Transfers
ADD R[rd]  R[rs1] + R[rs2]; PC  PC + 4
SUB R[rd]  R[rs1] – R[rs2]; PC  PC + 4
ORI R[rd]  R[rs1] | sign_ext(Imm12); PC  PC + 4
LW R[rd]  MEM[ R[rs1] + sign_ext(Imm12)]; PC  PC + 4
SW MEM[ R[rs1] + sign_ext(Imm12) ]  R[rs2]; PC  PC + 4
BEQ if ( R[rs] == R[rt] ) then PC  PC + (sign_ext(Imm12) || 0) else PC  PC + 4

## Slide 59: Step 1: Requirements of the Instruction Set
Memory (MEM)
  Instructions & data (will use one for each: really caches)
Registers (R: 32 x 32)
  Read rs1
  Read rs2
  Write rd
PC
Sign Extender
Add/Sub/OR unit for operation on register(s) or sign extended immediate
Add 4 (or maybe sign extended immediate) to PC
Compare if registers equal?

## Slide 60: Generic Steps of Datapath
instruction
memory
+4
rs2
rs1
rd
registers
ALU
Data
memory
imm
1. Instruction
Fetch
2. Decode/
Register
Read
3. Execute
4. Memory
5. Register
Write
PC
mux

## Slide 61: Step 2: Components of the Datapath
Combinational Elements
State Elements + Clocking Methodology
Building Blocks
32
32
A
B
32
Sum
CarryOut
CarryIn
Adder
32
A
B
32
Y
32
Select
MUX
Multiplexer
32
32
A
B
32
Result
OP
ALU
ALU
Adder
Zero

## Slide 62: ALU Needs for RISC-V Lite + Rest of RISC-V
Addition, subtraction, logical OR, ==:
  ADD R[rd] = R[rs1] + R[rs2]; ...
  SUB R[rd] = R[rs1] – R[rs2]; ...
  ORI R[rt] = R[rs1] | sign_ext(Imm12)...
  BEQ if ( R[rs] == R[rt] )...
Test to see if output == 0 for any ALU operation gives == test. How?
P&H Ch. 4 also adds AND, 64 bit LD/SD instructions
ALU from Appendix A, Section A.5

## Slide 63: Storage Element: Idealized Memory
Memory (idealized)
  One input bus: Data In
  One output bus: Data Out
Memory word is found by:
  Address selects the word to put on Data Out
  Write Enable = 1: address selects the memory word to be written via the Data In bus
Clock input (CLK)
  CLK input is a factor ONLY during write operation
  During read operation, behaves as a combinational logic block: Address valid  Data Out valid after “access time”
Clk
Data In
Write Enable
32
32
DataOut
Address
Notes: The last storage element you will need for the datapath is the idealized memory to store your data and instructions.
This idealized memory block has just one input bus (DataIn) and one output bus (DataOut).
When Write Enable is 0, the address selects the memory word to put on the Data Out bus.
When Write Enable is 1, the address selects the memory word to be written via the DataIn bus at the next clock tick.
Once again, the clock input is a factor ONLY during the write operation.
During read operation, it behaves as a combinational logic block.
That is if you put a valid value on the address lines, the output bus DataOut will become valid after the access time of the memory.
+2 = 35 min. (Y:15)

## Slide 64: Storage Element: Register (Building Block)
Similar to D Flip Flop except
  N-bit input and output
  Write Enable input
Write Enable:
  Negated (or deasserted) (0): Data Out will not change
  Asserted (1): Data Out will become Data In on rising edge of clock
clk
Data In
Write Enable
N
N
Data Out
Notes: As far as storage elements are concerned, we will need a N-bit register that is similar to the D flip-flop I showed you in class.
The significant difference here is that the register will have a Write Enable input.
That is the content of the register will NOT be updated if Write Enable is not asserted (0).
The content is updated at the clock tick ONLY if the Write Enable signal is asserted (1).
+1 = 31 min. (Y:11)

## Slide 65: Storage Element: Register File
Register File consists of 32 registers:
  Two 32-bit output busses:
  busA and busB
  One 32-bit input bus: busW
Register is selected by:
  RA (number) selects the register to put on busA (data)
  RB (number) selects the register to put on busB (data)
  RW (number) selects the register to be written via busW (data) when Write Enable is 1
Clock input (clk)
  Clk input is a factor ONLY during write operation
  During read operation, behaves as a combinational logic block:
    RA or RB valid  busA or busB valid after “access time.”
Clk
busW
Write Enable
32
32
busA
32
busB
5
5
5
RW
RA
RB
32 x 32-bit
Registers
Notes: We will also need a register file that consists of 32 32-bit registers with two output busses (busA and busB) and one input bus.
The register specifiers Ra and Rb select the registers to put on busA and busB respectively.
When Write Enable is 1, the register specifier Rw selects the register to be written via busW.
In our simplified version of the register file, the write operation will occurs at the clock tick.
Keep in mind that the clock input is a factor ONLY during the write operation.
During read operation, the register file behaves as a combinational logic block.
That is if you put a valid value on Ra, then bus A will become valid after the register file’s access time.
Similarly if you put a valid value on Rb, bus B will become valid after the register file’s access time. In both cases (Ra and Rb), the clock input is not a factor.
+2 = 33 min. (Y:13)

## Slide 66: Step 3: Assemble DataPath Meeting Requirements
Register Transfer Requirements  Datapath Assembly
Instruction Fetch
Read Operands and Execute Operation
Common RTL operations
  Fetch the Instruction: mem[PC]
  Update the program counter:
    Sequential Code: PC  PC + 4
    Branch and Jump: PC  “something else”
32
Instruction Word
Address
Instruction
Memory
PC
clk
Next Address
Logic

## Slide 67: Step 3: Add & Subtract
R[rd] = R[rs] op R[rt] (addu rd,rs,rt)
  Ra, Rb, and Rw come from instruction’s Rs1, Rs2, and Rd fields
  ALUctr and RegWr: control logic after decoding the instruction
… Already defined the register file & ALU
32
Result
ALUctr
clk
busW
RegWr
32
32
busA
32
busB
5
5
5
Rw
Ra
Rb
32 x 32-bit
Registers
rs1
rs2
rd
ALU
Zero
Notes: And here is the datapath that can do the trick.
First of all, we connect the register file’s Rw, Ra, and Rb input to the Rd, Rs, and Rt fields of the instruction bus (points to the format diagram).
Then we need to connect busA and busB of the register file to the ALU.
Finally, we need to connect the output of the ALU to the input bus of the register file.
Conceptually, this is how it works.
The instruction bus coming out of the Instruction memory will set the Ra and Rb to the register specifiers Rs and Rt.
This causes the register file to put the value of register Rs onto busA and the value of register Rt onto busB, respectively.
By setting the ALUctr appropriately, the ALU will perform either the Add and Subtract for us.
The result is then fed back to the register file where the register specifier Rw should already be set to the instruction bus’s Rd field.
Since the control, which we will design in our next lecture, should have already set the RegWr signal to 1, the result will be written back to the register file at the next clock tick (points to the Clk input).
+3 = 42 min. (Y:22)

## Slide 68: Agenda
Boolean Algebra
Timing and State Machines
Datapath Elements: Mux + ALU
RISC-V Lite Datapath
And, in Conclusion, …

## Slide 69: And in Conclusion, …
Five steps to processor design:
  1. Analyze instruction set  datapath requirements
  2. Select set of datapath components & establish clock methodology
  3. Assemble datapath meeting the requirements
  4. Analyze implementation of each instruction to determine setting of control points that effects the register transfer.
  5. Assemble the control logic
    Formulate Logic Equations
    Design Circuits
Control
Datapath
Memory
Processor
Input
Output
State Machines
  Finite State Machines: made from Stateless combinational logic and Stateful “Memory” Logic (aka Registers)
  Clocks synchronize D-FF change (Setup and Hold times important!)
  Pipeline long-delay CL for faster clock cycle— Split the critical path
Use muxes to select among inputs
  S input bits selects 2S inputs
  Each input can be n-bits wide, independent of S
Can implement muxes hierarchically
Arithmetic circuits are a kind of combinational logic