## Slide 1: CS 61C: Great Ideas in Computer Architecture Lecture 13: Pipelining
Krste Asanović & Randy Katz
http://inst.eecs.berkeley.edu/~cs61c/fa17

## Slide 2: Agenda
RISC-V Pipeline
Pipeline Control
Hazards
  Structural
  Data
    R-type instructions
    Load
  Control
Superscalar processors

## Slide 3: Recap: Pipelining with RISC-V
add t0, t1, t2
or t3, t4, t5
sll t6, t0, t3
tcycle
instruction sequence
tinstruction
 | Single Cycle | Pipelining
Timing | tstep = 100 … 200 ps | tcycle = 200 ps
 | Register access only 100 ps | All cycles same length
Instruction time, tinstruction | = tcycle = 800 ps | 1000 ps
Clock rate, fs | 1/800 ps = 1.25 GHz | 1/200 ps = 5 GHz
Relative speed | 1 x | 4 x
Notes: Tc = “Time between completion of instructions”

## Slide 4: RISC-V Pipeline
add t0, t1, t2
or t3, t4, t5
slt t6, t0, t3
tcycle
= 200 ps
instruction sequence
tinstruction = 1000 ps
sw t0, 4(t3)
lw t0, 8(t3)
addi t2, t2, 1
Resource use of instruction over time
Resource use in a particular time slot

## Slide 5: Single-Cycle RISC-V RV32I Datapath
IMEM
ALU
Imm.
Gen
+4
DMEM
Branch Comp.
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataW
DataR
1
0
0
1
2
1
0
pc
0
1
inst[11:7]
inst[19:15]
inst[24:20]
inst[31:7]
pc+4
alu
mem
wb
alu
pc+4
Reg[rs1]
pc
imm[31:0]
Reg[rs2]
inst[31:0]
ImmSel
RegWEn
BrUn
BrEq
BrLT
ASel
BSel
ALUSel
MemRW
WBSel
PCSel
wb

## Slide 6: Pipelining RISC-V RV32I Datapath
IMEM
ALU
Imm.
Gen
+4
DMEM
Branch Comp.
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataW
DataR
1
0
0
1
2
1
0
pc
0
1
inst[11:7]
inst[19:15]
inst[24:20]
inst[31:7]
pc+4
alu
mem
wb
alu
pc+4
Reg[rs1]
pc
imm[31:0]
Reg[rs2]
wb
Instruction Fetch
(F)
Instruction Decode/Register Read
(D)
ALU Execute
(X)
Memory Access
(M)
Write Back
(W)

## Slide 7: Pipelined RISC-V RV32I Datapath
IMEM
ALU
+4
DMEM
Branch Comp.
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataW
DataR
1
0
aluX
pcF+4
+4
pcD
pcF
pcX
pcM
instD
instX
rs1X
rs2X
aluM
rs2M
immX
Imm.
Recalculate PC+4 in M stage to avoid sending both PC and PC+4 down pipeline
instM
instW
Must pipeline instruction along with data, so control operates correctly in each stage

## Slide 8: Each stage operates on different instruction
IMEM
ALU
+4
DMEM
Branch Comp.
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataW
DataR
1
0
aluX
pcF+4
+4
pcD
pcF
pcX
pcM
instD
instX
rs1X
rs2X
aluM
rs2M
immX
Imm.
instM
instW
add t0, t1, t2
or t3, t4, t5
slt t6, t0, t3
sw t0, 4(t3)
lw t0, 8(t3)
Pipeline registers separate stages, hold data for each instruction in flight

## Slide 9: Agenda
RISC-V Pipeline
Pipeline Control
Hazards
  Structural
  Data
    R-type instructions
    Load
  Control
Superscalar processors

## Slide 10: Pipelined Control
Control signals derived from instruction
  As in single-cycle implementation
  Information is stored in pipeline registers for use by later stages

## Slide 11: Hazards Ahead

## Slide 12: Agenda
RISC-V Pipeline
Pipeline Control
Hazards
  Structural
  Data
    R-type instructions
    Load
  Control
Superscalar processors

## Slide 13: Structural Hazard
Problem: Two or more instructions in the pipeline compete for access to a single physical resource
Solution 1: Instructions take it in turns to use resource, some instructions have to stall
Solution 2: Add more hardware to machine
Can always solve a structural hazard by adding more hardware

## Slide 14: Regfile Structural Hazards
Each instruction:
  can read up to two operands in decode stage
  can write one value in writeback stage
Avoid structural hazard by having separate “ports”
  two independent read ports and one independent write port
Three accesses per cycle can happen simultaneously

## Slide 15: Structural Hazard: Memory Access
add t0, t1, t2
or t3, t4, t5
slt t6, t0, t3
instruction sequence
sw t0, 4(t3)
lw t0, 8(t3)
Instruction and data memory used simultaneously
  Use two separate memories

## Slide 16: Instruction and Data Caches
Processor
Control
Datapath
PC
Registers
Arithmetic & Logic Unit
(ALU)
Memory (DRAM)
Bytes
Program
Data
Instruction Cache
Data
Cache
Caches: small and fast “buffer” memories

## Slide 17: Structural Hazards – Summary
Conflict for use of a resource
In RISC-V pipeline with a single memory
  Load/store requires data access
  Without separate memories, instruction fetch would have to stall for that cycle
    All other operations in pipeline would have to wait
Pipelined datapaths require separate instruction/data memories
  Or separate instruction/data caches
RISC ISAs (including RISC-V) designed to avoid structural hazards
  e.g. at most one memory access/instruction

## Slide 18: Agenda
RISC-V Pipeline
Pipeline Control
Hazards
  Structural
  Data
    R-type instructions
    Load
  Control
Superscalar processors

## Slide 19: Data Hazard: Register Access
add t0, t1, t2
or t3, t4, t5
slt t6, t0, t3
instruction sequence
sw t0, 4(t3)
lw t0, 8(t3)
Separate ports, but what if write to same value as read?
Does sw in the example fetch the old or new value?

## Slide 20: Register Access Policy
add t0, t1, t2
or t3, t4, t5
slt t6, t0, t3
instruction sequence
sw t0, 4(t3)
lw t0, 8(t3)
Exploit high speed of register file (100 ps)
  WB updates value
  ID reads new value
Indicated in diagram by shading
Might not always be possible to write then read in same cycle, especially in high-frequency designs. Check assumptions in any question.

## Slide 21: Data Hazard: ALU Result
add s0, t0, t1
sub t2, s0, t0
or t6, s0, t3
instruction sequence
xor t5, t1, s0
sw s0, 8(t3)
5 | 5 | 5 | 5 | 5/9 | 9 | 9 | 9 | 9
Value of s0
Without some fix, sub and or will calculate wrong result!

## Slide 22: Data Hazard: ALU Result
add s0, t1, t2
sub t2, s0, t5
or t6, s0, t3
instruction sequence
xor t5, t1, s0
sw s0, 8(t3)
5 |  |  |  |  |  |  |  | 
Value of s0
Without some fix, sub and or will calculate wrong result!

## Slide 23: Solution 1: Stalling
Problem: Instruction depends on result from previous instruction
  add s0, t0, t1 sub t2, s0, t3
Bubble:
  effectively NOP: affected pipeline stages do “nothing”

## Slide 24: Stalls and Performance
Stalls reduce performance
  But stalls are required to get correct results
Compiler can arrange code to avoid hazards and stalls
  Requires knowledge of the pipeline structure

## Slide 25: Solution 2: Forwarding
add t0, t1, t2
or t3, t0, t5
sub t6, t0, t3
instruction sequence
xor t5, t1, t0
sw t0, 8(t3)
5 | 5 | 5 | 5 | 5/9 | 9 | 9 | 9 | 9
Value of t0
Forwarding: grab operand from pipeline stage,
rather than register file

## Slide 26: Forwarding (aka Bypassing)
Use result when it is computed
  Don’t wait for it to be stored in a register
  Requires extra connections in the datapath

## Slide 27: 1) Detect Need for Forwarding (example)
add t0, t1, t2
or t3, t0, t5
sub t6, t0, t3
X
M
W
D
instX.rd
instD.rs1
Compare destination of older instructions in pipeline with sources of new instruction in decode stage.
Must ignore writes to x0!

## Slide 28: Forwarding Path
IMEM
ALU
+4
DMEM
Branch Comp.
Reg[]
AddrA
AddrB
DataA
AddrD
DataB
DataD
Addr
DataW
DataR
1
0
aluX
pcF+4
+4
pcD
pcF
pcX
pcM
instD
instX
rs1X
rs2X
aluM
rs2M
immX
Imm.
instM
instW
Forwarding Control Logic

## Slide 29: Administrivia
Project 1 Part 2 due next Monday
  Project Party this Wednesday 7-9pm in Cory 293
HW3 will be released by Friday
Midterm 1 regrades due tonight
Guerrilla Session tonight 7-9pm in Cory 293

## Slide 30: Agenda
RISC-V Pipeline
Pipeline Control
Hazards
  Structural
  Data
    R-type instructions
    Load
  Control
Superscalar processors

## Slide 31: Load Data Hazard
1 cycle stall unavoidable
forward
unaffected

## Slide 32: Stall Pipeline
Stall
repeat and instruction and forward

## Slide 33: lw Data Hazard
Slot after a load is called a load delay slot
  If that instruction uses the result of the load, then the hardware will stall for one cycle
  Equivalent to inserting an explicit nop in the slot
    except the latter uses more code space
  Performance loss
Idea:
  Put unrelated instruction into load delay slot
  No performance loss!

## Slide 34: Code Scheduling to Avoid Stalls
Reorder code to avoid use of load result in the next instruction!
RISC-V code for D=A+B; E=A+C;
Original Order:
lw t1, 0(t0)
lw t2, 4(t0)
add t3, t1, t2
sw t3, 12(t0)
lw t4, 8(t0)
add t5, t1, t4
sw t5, 16(t0)
Alternative:
lw t1, 0(t0)
lw t2, 4(t0)
lw t4, 8(t0)
add t3, t1, t2
sw t3, 12(t0)
add t5, t1, t4
sw t5, 16(t0)
Stall!
Stall!
13 cycles
11 cycles

## Slide 35: Agenda
RISC-V Pipeline
Pipeline Control
Hazards
  Structural
  Data
    R-type instructions
    Load
  Control
Superscalar processors

## Slide 36: Control Hazards
beq t0, t1, label
sub t2, s0, t5
or t6, s0, t3
xor t5, t1, s0
sw s0, 8(t3)
executed regardless of branch outcome!
executed regardless of branch outcome!!!
PC updated reflecting branch outcome

## Slide 37: Observation
If branch not taken, then instructions fetched sequentially after branch are correct
If branch or jump taken, then need to flush incorrect instructions from pipeline by converting to NOPs

## Slide 38: Kill Instructions after Branch if Taken
beq t0, t1, label
sub t2, s0, t5
or t6, s0, t3
label: xxxxxx
PC updated reflecting branch outcome
Taken branch
Convert to NOP
Convert to NOP

## Slide 39: Reducing Branch Penalties
Every taken branch in simple pipeline costs 2 dead cycles
To improve performance, use “branch prediction” to guess which way branch will go earlier in pipeline
Only flush pipeline if branch prediction was incorrect

## Slide 40: Branch Prediction
beq t0, t1, label
label: …..
…..
Taken branch
Guess next PC!
Check guess correct

## Slide 41: Agenda
RISC-V Pipeline
Pipeline Control
Hazards
  Structural
  Data
    R-type instructions
    Load
  Control
Superscalar processors

## Slide 42: Increasing Processor Performance
Clock rate
  Limited by technology and power dissipation
Pipelining
  “Overlap” instruction execution
  Deeper pipeline: 5 => 10 => 15 stages
    Less work per stage  shorter clock cycle
    But more potential for hazards (CPI > 1)
Multi-issue ”super-scalar” processor
  Multiple execution units (ALUs)
    Several instructions executed simultaneously
    CPI < 1 (ideally)

## Slide 43: Superscalar Processor
P&H p. 340

## Slide 44: Benchmark: CPI of Intel Core i7
CPI = 1
P&H p. 350

## Slide 45: In Conclusion
Pipelining increases throughput by overlapping execution of multiple instructions
All pipeline stages have same duration
  Choose partition that accommodates this constraint
Hazards potentially limit performance
  Maximizing performance requires programmer/compiler assistance
  E.g. Load and Branch delay slots
Superscalar processors use multiple execution units for additional instruction level parallelism
  Performance benefit highly code dependent

## Slide 46: Extra Slides

## Slide 47: Pipelining and ISA Design
RISC-V ISA designed for pipelining
  All instructions are 32-bits
    Easy to fetch and decode in one cycle
    Versus x86: 1- to 15-byte instructions
  Few and regular instruction formats
    Decode and read registers in one step
  Load/store addressing
    Calculate address in 3rd stage, access memory in 4th stage
  Alignment of memory operands
    Memory access takes only one cycle

## Slide 48: Superscalar Processor
Multiple issue “superscalar”
  Replicate pipeline stages  multiple pipelines
  Start multiple instructions per clock cycle
  CPI < 1, so use Instructions Per Cycle (IPC)
  E.g., 4GHz 4-way multiple-issue
    16 BIPS, peak CPI = 0.25, peak IPC = 4
  Dependencies reduce this in practice
“Out-of-Order” execution
  Reorder instructions dynamically in hardware to reduce impact of hazards
CS152 discusses these techniques!