## Slide 1: Cray xt5-he is fastest supercomputer!
inst.eecs.berkeley.edu/~cs61c UCB CS61C : Machine Structures Lecture 36 – Performance 2010-04-23
Every 6 months (Nov/June), the fastest supercomputers in the world face off. The fastest computer is now the Jaguar, a Linux Cray XT5-HE Opteron Six Core 2.6 GHz, with 224,256 cores, achieves 2.3 PFlops. They use LINPACK floating point benchmark (A x = B).
Lecturer SOE Dan Garcia
www.top500.org/lists/2009/11
www.nccs.gov/computing-resources/jaguar/
How fast is your computer?

## Slide 2: Why Performance? Faster is better!
Purchasing Perspective: given a collection of machines (or upgrade options), which has the
    best performance ?
    least cost ?
    best performance / cost ?
Computer Designer Perspective: faced with design options, which has the
    best performance improvement ?
    least cost ?
    best performance / cost ?
All require basis for comparison and metric for evaluation!
  Solid metrics lead to solid progress!

## Slide 3: Two Notions of “Performance”
Which has higher performance?
  Interested in time to deliver 100 passengers?
  Interested in delivering as many passengers per day as possible?
In a computer, time for one task called Response Time or Execution Time
In a computer, tasks per unit time called Throughput or Bandwidth
Plane
Boeing 747
BAD/Sud Concorde
Top Speed
DC to Paris
Passen-gers
Throughput (pmph)
610 mph
6.5 hours
470
286,700
1350 mph
3 hours
132
178,200

## Slide 4: Definitions
Performance is in units of things per sec
  bigger is better
If mostly concerned with response time
  performance(x) = 1 execution_time(x)
“ F(ast) is n times faster than S(low) ” means:
performance(F) execution_time(S)
n = =
performance(S) execution_time(F)

## Slide 5: Example of Response Time v. Throughput
Time of Concorde vs. Boeing 747?
  Concord is 6.5 hours / 3 hours = 2.2 times faster
  Concord is 2.2 times (“120%”) faster in terms of flying time (response time)
Throughput of Boeing vs. Concorde?
  Boeing 747: 286,700 pmph / 178,200 pmph = 1.6 times faster
  Boeing is 1.6 times (“60%”) faster in terms of throughput
We will focus primarily on response time.

## Slide 6: Words, Words, Words…
Will (try to) stick to “n times faster”; its less confusing than “m % faster”
As faster means both decreased execution time and increased performance, to reduce confusion we will (and you should) use “improve execution time” or
“improve performance”

## Slide 7: What is Time?
Straightforward definition of time:
  Total time to complete a task, including disk accesses, memory accesses, I/O activities, operating system overhead, ...
  “real time”, “response time” or “elapsed time”
Alternative: just time processor (CPU) is working only on your program (since multiple processes running at same time)
  “CPU execution time” or “CPU time”
  Often divided into system CPU time (in OS) and user CPU time (in user program)

## Slide 8: How to Measure Time?
Real Time  Actual time elapsed
CPU Time: Computers constructed using a clock that runs at a constant rate and determines when events take place in the hardware
  These discrete time intervals called clock cycles (or informally clocks or cycles)
  Length of clock period: clock cycle time (e.g., ½ nanoseconds or ½ ns) and clock rate (e.g., 2 gigahertz, or 2 GHz), which is the inverse of the clock period; use these!

## Slide 9: Measuring Time using Clock Cycles (1/2)
CPU execution time for a program
  Units of [seconds / program] or [s/p]
= Clock Cycles for a program x Clock Period
  Units of [s/p] = [cycles / p] x [s / cycle] = [c/p] x [s/c]
Or
= Clock Cycles for a program [c / p] Clock Rate [c / s]

## Slide 10: Measuring Time using Clock Cycles (2/2)
One way to define clock cycles:
Clock Cycles for program [c/p]
= Instructions for a program [i/p] (called “Instruction Count”)
x Average Clock cycles Per Instruction [c/i] (abbreviated “CPI”)
CPI one way to compare two machines with same instruction set, since Instruction Count would be the same

## Slide 11: Performance Calculation (1/2)
CPU execution time for program [s/p] = Clock Cycles for program [c/p] x Clock Cycle Time [s/c]
Substituting for clock cycles:
CPU execution time for program [s/p] = ( Instruction Count [i/p] x CPI [c/i] ) x Clock Cycle Time [s/c]
= Instruction Count x CPI x Clock Cycle Time

## Slide 12: Performance Calculation (2/2)
CPU time = Instructions x Cycles x Seconds
Program Instruction Cycle
CPU time = Instructions x Cycles x Seconds
Program Instruction Cycle
CPU time = Instructions x Cycles x Seconds
Program Instruction Cycle
CPU time = Seconds
Program
Product of all 3 terms: if missing a term, can’t predict time, the real measure of performance

## Slide 13: How Calculate the 3 Components?
Clock Cycle Time: in specification of computer (Clock Rate in advertisements)
Instruction Count:
  Count instructions in loop of small program
  Use simulator to count instructions
  Hardware counter in spec. register
    (Pentium II,III,4)
CPI:
  Calculate: Execution Time / Clock cycle time Instruction Count
  Hardware counter in special register (PII,III,4)

## Slide 14: Calculating CPI Another Way
First calculate CPI for each individual instruction (add, sub, and, etc.)
Next calculate frequency of each individual instruction
Finally multiply these two for each instruction and add them up to get final CPI (the weighted sum)

## Slide 15: Example (RISC processor)
Op Freqi CPIi Prod (% Time)
ALU 50% 1 .5 (23%)
Load 20% 5 1.0 (45%)
Store 10% 3 .3 (14%)
Branch 20% 2 .4 (18%)
2.2
What if Branch instructions twice as fast?
Instruction Mix
(Where time spent)

## Slide 16: What Programs Measure for Comparison?
Ideally run typical programs with typical input before purchase, or before even build machine
  Called a “workload”; For example:
  Engineer uses compiler, spreadsheet
  Author uses word processor, drawing program, compression software
In some situations its hard to do
  Don’t have access to machine to “benchmark” before purchase
  Don’t know workload in future

## Slide 17: Benchmarks
Obviously, apparent speed of processor depends on code used to test it
Need industry standards so that different processors can be fairly compared
Companies exist that create these benchmarks: “typical” code used to evaluate systems
Need to be changed every ~5 years since designers could (and do!) target for these standard benchmarks

## Slide 18: Example Standardized Benchmarks (1/2)
Standard Performance Evaluation Corporation (SPEC) SPEC CPU2006
  CINT2006 12 integer (perl, bzip, gcc, go, ...)
  CFP2006 17 floating-point (povray, bwaves, ...)
  All relative to base machine (which gets 100) Sun Ultra Enterprise 2 w/296 MHz UltraSPARC II
  They measure
    System speed (SPECint2006)
    System throughput (SPECint_rate2006)
  www.spec.org/osg/cpu2006/

## Slide 19: Example Standardized Benchmarks (2/2)
SPEC
  Benchmarks distributed in source code
  Members of consortium select workload
    30+ companies, 40+ universities, research labs
  Compiler, machine designers target benchmarks, so try to change every 5 years
  SPEC CPU2006:
CFP2006 bwaves Fortran Fluid Dynamics
gamess Fortran Quantum Chemistry
milc C Physics / Quantum Chromodynamics
zeusmp Fortran Physics / CFD
gromacs C,Fortran Biochemistry / Molecular Dynamics
cactusADM C,Fortran Physics / General Relativity
leslie3d Fortran Fluid Dynamics
namd C++ Biology / Molecular Dynamics
dealll C++ Finite Element Analysis
soplex C++ Linear Programming, Optimization
povray C++ Image Ray-tracing
calculix C,Fortran Structural Mechanics
GemsFDTD Fortran Computational Electromegnetics
tonto Fortran Quantum Chemistry
lbm C Fluid Dynamics
wrf C,Fortran Weather
sphinx3 C Speech recognition
CINT2006 perlbench C Perl Programming language
bzip2 C Compression
gcc C C Programming Language Compiler
mcf C Combinatorial Optimization
gobmk C Artificial Intelligence : Go
hmmer C Search Gene Sequence
sjeng C Artificial Intelligence : Chess
libquantum C Simulates quantum computer
h264ref C H.264 Video compression
omnetpp C++ Discrete Event Simulation
astar C++ Path-finding Algorithms
xalancbmk C++ XML Processing

## Slide 20: Performance Evaluation: The Demo
If we’re talking about performance, let’s discuss the ways shady salespeople have fooled consumers (so you don’t get taken!)
5. Never let the user touch it
4. Only run the demo through a script
3. Run it on a stock machine in which “no expense was spared”
2. Preprocess all available data
1. Play a movie

## Slide 21: Megahertz Myth Marketing Movie

## Slide 22: Peer Instruction
The Sieve of Eratosthenes and Quicksort were early effective benchmarks.
A program runs in 100 sec. on a machine, mult accounts for 80 sec. of that. If we want to make the program run 6 times faster, we need to up the speed of mults by AT LEAST 6.
12
a) FF
b) FT
c) TF
d) TT
Notes: Answer: [correct=5, TFF] Individual (6, 3, 6, 3, 34, 37, 7, 4)% & Team (9, 4, 4, 4, 39, 34, 0, 7)%
A: T [18/82 & 25/75] (The game breaks up very quickly into separate, independent games -- big win to solve separated & put together)
B: F [80/20 & 86/14] (The game tree grows exponentially! A better static evaluator can make all the difference!)
C: F [53/57 & 52/48] (If you're just looking for the best move, just keep theBestMove around [ala memoizing max])

## Slide 23: Peer Instruction Answers
The Sieve of Eratosthenes and Quicksort were early effective benchmarks.
A program runs in 100 sec. on a machine, mult accounts for 80 sec. of that. If we want to make the program run 6 times faster, we need to up the speed of mults by AT LEAST 6.
F A L S E
1. Early benchmarks? Yes. Effective? No. Too simple!
2. 6 times faster = 16 sec. mults must take -4 sec! I.e., impossible!
F A L S E
12
a) FF
b) FT
c) TF
d) TT

## Slide 24: “And in conclusion…”
Latency v. Throughput
Performance doesn’t depend on any single factor: need Instruction Count, Clocks Per Instruction (CPI) and Clock Rate to get valid estimations
User Time: time user waits for program to execute: depends heavily on how OS switches between tasks
CPU Time: time spent executing a single program: depends solely on design of processor (datapath, pipelining effectiveness, caches, etc.)
Benchmarks
  Attempt to predict perf, Updated every few years
  Measure everything from simulation of desktop graphics programs to battery life
Megahertz Myth
  MHz ≠ performance, it’s just one factor
CPU time = Instructions x Cycles x Seconds
Program Instruction Cycle