MIPS instructions

| Instruction | Syntax | Example |
| --- | --- | --- |
| add/addu | add dest, src0, src1 | add $s0, $s1, $s2 |
| sub/subu | sub dest, src0, src1 | sub $s0, $s1, $s2 |
| addi/addiu | addi dest, src0, immediate | addi $s0, $s1, 12 |
| sll/srl | sll dest, src0, immediate | sll $s0, $s1, 5 |
| slt/sltu | slt dest, src0, src1 | slt $s0, $s1, $s2 |
| slti/sltiu | slti dest, src0, immediate | slti $s0, $s1, 10 |
| lw/lb/lbu | lw dest, offset(base addr) | lw $t0, 4($s0) |
| sw/sb | sw src, offset(base addr) | sw $t0, 4($s0) |
| bne | bne src0, src1, branchAddr | bne $t0, $t1, notEq |
| Beq | beq src0, src1, branchAddr | beq $t0, $t1, Eq |
| j/jal | j jumpAddr | j jumpWhenDone |
| jr | Jr dest | jr $ra |

MIPS registers

| Register Number | Register Name | Register Use |
| --- | --- | --- |
| $0 | $zero | The “zero-constant” |
| $1 | $at | Used by the assembler |
| $2-$3 | $v0-$v1 | Return values |
| $4-$7 | $a0-$a3 | Function arguments |
| $8-$15 | $t0-$t7 | Temporary registers |
| $16-$23 | $s0-$s7 | Saved registers |
| $24-$25 | $t8-$t9 | Temporary registers |
| $26-$27 | $k0-$k1 | Used by the kernel |
| $28 | $gp | Global pointer |
| $29 | $sp | Stack pointer |
| $30 | $fp | Frame pointer |
| $31 | $ra | Return address |

MIPS functions

If you plan on calling other functions or using saved registers, you’ll need to use the

following function template:

| Prologue: | FunctionFoo: addiu $sp, $sp, -FrameSize #reserve space on the stack sw $ra, 0($sp) #store needed registers sw $s0, 4($sp) … save the rest of the registers … sw $sx, FrameSize – 4($sp) |
| --- | --- |
| Body: | … Do some stuff … |
| Epilogue: | lw $sx, FrameSize -4($sp) #restore registers … load the rest of the registers… lw $s0, 4($sp) lw $ra, 0($sp) addiu $sp, $sp, FrameSize #release stack spaces jr $ra #return to normal execution |

Exercises:

What are the 3 meanings unsigned can have in MIPS?

Translate the following MIPS function into C or vice versa:

| C | MIPS |
| --- | --- |
| int foo (int *a0, int a1) { int v0 = 0; while (a1 >= 0) { v0 = v0 + *(a0 + a1); a1 = a1 – 1 } return v0; } | Foo: add $v0, $zero, $zero Loop: slti $t0, $a1, 0 bne $t0, $zero, End sll $t1, $a1, 2 add $t2, $a0, $t1 lw $t3, 0($t2) add $v0, $v0, $t3 addi $a1, $a1, -1 j Loop End: jr $ra |
| /* What does Mystery do? */ Mystery counts the number of bits in a when it is not 0-padded (note that the second argument of Recur effectively does nothing). int Mystery(int a){ // fill in rest Return Recur(a, 0); } int Recur(int a, int b){ // fill in rest if (a == 0) { return 0; } Return Recur(a>>1, b+1) + 1; } | Mystery: addi $a1, $0, $0 addiu $sp, $sp, -4 sw $ra, 0($sp) jal Recur lw $ra, 0($sp) addiu $sp, $sp 4 jr $ra Recur: bne $a0, $0, Body add $v0, $0, $0 jr $ra Body: addi $a1, $a1, 1 srl $a0, $a0, 1 addiu $sp, $sp, -4 sw $ra, 0($sp) jal Recur addi $v0, $v0, 1 lw $ra, 0($sp) addiu $sp, $sp 4 jr $ra |
| void swap(int * a, in * b){ int temp= *a; *a = *b; *b = temp; } | Swap: lw $t0, 0($a0) lw $t1, 0($a1) sw $t1, 0($a0) sw $t0, 0($a1) jr $ra |

| void insertionSort(int *arr, int size){ int i, j; for(i=1; i<size; i++){ j=i; while(j>0 && arr[j]<arr[j-1]){ swap(arr + j, arr + (j-1)); j--; } } } | # s0 -> i, s1 -> j, s2 -> arr, # s3 -> size # we save the inputs too # because we have to call # another function # prologue Sort: addiu $sp, $sp, -20 sw $ra, 0($sp) sw $s0, 4($sp) sw $s1, 8($sp) sw $s2, 12($sp) sw $s3, 16($sp) add $s0, $0, 1 add $s2, $a0, $0 add $s3, $a1, $0 # check if (i < size) Loop1: slt $t0, $s0, $s3 beq $t0, $0, End # for loop body add $s1, $s0, $0 # check the while # loop condition Loop2: sll $t0, $s1, 4 add $t1, $s2, $t0 #arr+j->t1 lw $t2, 0($t1) #arr[j]->t2 lw $t3, -4($t1) #arr[j-1]->t3 slt $t4, $t2, $t3 slt $t5, $0, $s1 #(j>0)->t5 and $t4, $t4, $t5 beq $t4, $0, L1End #while loop body add $a0, $0, $t1 addi $a1, $a0, -4 jal Swap addi $s1, $s1, -1 jump Loop2 L1End: addi $s0, $s0, 1 jump Loop1 #epilogue End: lw $ra, 0($sp) lw $s0, 4($sp) lw $s1, 8($sp) lw $s2, 12($sp) lw $s3, 16($sp) addiu $sp, $sp, 20 jr $ra |
| --- | --- |