## Slide 1: “so many gadgets, so many aches” ­ NYT
inst.eecs.berkeley.edu/~cs61c UCB CS61C : Machine Structures Lecture 07 Introduction to MIPS : Decisions II 2014-02-05
Guest Lecturer Alan Christopher
www.nytimes.com/2010/02/19/technology/19china.html
Laptops “do not meet any of the ergonomic requirements for a computer system”. Touch screens “should not be used heavily for typing” Texting is a problem because thumb bones have two bones instead of three … “if you want to get injured, do a lot of texting”. Advice? Take a break

## Slide 2: Review
Memory is byte-addressable, but lw and sw access one word at a time.
A pointer (used by lw and sw) is just a memory address, so we can add to it or subtract from it (using offset).
A Decision allows us to decide what to execute at run-time rather than compile-time.
C Decisions are made using conditional statements within if, while, do while, for.
MIPS Decision making instructions are the conditional branches: beq and bne.
New Instructions:
  lw, sw, beq, bne, j

## Slide 3: Last time: Loading, Storing bytes 1/2
In addition to word data transfers (lw, sw), MIPS has byte data transfers:
  load byte: lb
  store byte: sb
same format as lw, sw
E.g., lb $s0, 3($s1)
  contents of memory location with address = sum of “3” + contents of register s1 is copied to the low byte position of register s0.

## Slide 4: Loading, Storing bytes 2/2
x
What do with other 24 bits in the 32 bit register?
  lb: sign extends to fill upper 24 bits
Normally don’t want to sign extend chars
MIPS instruction that doesn’t sign extend when loading bytes:
  load byte unsigned: lbu
byte loaded
…is copied to “sign-extend”
This bit
xxxx xxxx xxxx xxxx xxxx xxxx
zzz zzzz

## Slide 5: Overflow in Arithmetic (1/2)
Reminder: Overflow occurs when there is a “mistake” in arithmetic due to the limited precision in computers.
Example (4-bit unsigned numbers):
  15 1111
  + 3 + 0011
  18 10010
  But we don’t have room for 5-bit solution, so the solution would be 0010, which is +2, and “wrong”.

## Slide 6: Overflow in Arithmetic (2/2)
Some languages detect overflow (Ada), some don’t (most C implementations)
MIPS solution is 2 kinds of arithmetic instructs:
  These cause overflow to be detected
    add (add)
    add immediate (addi)
    subtract (sub)
  These do not cause overflow detection
    add unsigned (addu)
    add immediate unsigned (addiu)
    subtract unsigned (subu)
Compiler selects appropriate arithmetic
  MIPS C compilers produce addu, addiu, subu

## Slide 7: Two “Logic” Instructions
Here are 2 more new instructions
Shift Left: sll $s1,$s2,2 #s1=s2<<2
  Store in $s1 the value from $s2 shifted 2 bits to the left (they fall off end), inserting 0’s on right; << in C.
  Before: 0000 0002hex 0000 0000 0000 0000 0000 0000 0000 0010two
  After: 0000 0008hex 0000 0000 0000 0000 0000 0000 0000 1000two
  What arithmetic effect does shift left have?
Shift Right: srl is opposite shift; >>

## Slide 8: Loops in C/Assembly (1/3)
Simple loop in C; A[] is an array of ints
  do { g = g + A[i]; i = i + j; } while (i != h);
Rewrite this as:
  Loop: g = g + A[i]; i = i + j; if (i != h) goto Loop;
Use this mapping: g, h, i, j, &A[0] $s1, $s2, $s3, $s4, $s5

## Slide 9: Loops in C/Assembly (2/3)
Final compiled MIPS code:
Loop: sll $t1,$s3,2 # $t1= 4*I addu $t1,$t1,$s5 # $t1=addr A+4i lw $t1,0($t1) # $t1=A[i] addu $s1,$s1,$t1 # g=g+A[i] addu $s3,$s3,$s4 # i=i+j bne $s3,$s2,Loop # goto Loop # if i!=h
Original code:
  Loop: g = g + A[i]; i = i + j; if (i != h) goto Loop;
Notes: Do goto first
Then I = I + J
Then 1st 4

## Slide 10: Loops in C/Assembly (3/3)
There are three types of loops in C:
  while
  do … while
  for
Each can be rewritten as either of the other two, so the method used in the previous example can be applied to these loops as well.
Key Concept: Though there are multiple ways of writing a loop in MIPS, the key to decision-making is conditional branch

## Slide 11: Administrivia
HW2 is due Sunday at 23:59:59

## Slide 12: Inequalities in MIPS (1/4)
Until now, we’ve only tested equalities (== and != in C). General programs need to test < and > as well.
Introduce MIPS Inequality Instruction:
  “Set on Less Than”
  Syntax: slt reg1,reg2,reg3
  Meaning:
  if (reg2 < reg3) reg1 = 1; else reg1 = 0;
  “set” means “change to 1”, “reset” means “change to 0”.
reg1 = (reg2 < reg3);
Same thing…

## Slide 13: Inequalities in MIPS (2/4)
How do we use this? Compile by hand: if (g < h) goto Less; #g:$s0, h:$s1
Answer: compiled MIPS code…
slt $t0,$s0,$s1 # $t0 = 1 if g<h bne $t0,$0,Less # goto Less # if $t0!=0 # (if (g<h)) Less:
Register $0 always contains the value 0, so bne and beq often use it for comparison after an slt instruction.
A slt  bne pair means if(… < …)goto…

## Slide 14: Inequalities in MIPS (3/4)
Now we can implement <, but how do we implement >, ≤ and ≥ ?
We could add 3 more instructions, but:
  MIPS goal: Simpler is Better
Can we implement ≤ in one or more instructions using just slt and branches?
  What about >?
  What about ≥?

## Slide 15: Inequalities in MIPS (4/4)
# a:$s0, b:$s1 slt $t0,$s0,$s1 # $t0 = 1 if a<b beq $t0,$0,skip # skip if a >= b <stuff> # do if a<b skip:
Two independent variations possible:
  Use slt $t0,$s1,$s0 instead of
  slt $t0,$s0,$s1
  Use bne instead of beq

## Slide 16: Immediates in Inequalities
There is also an immediate version of slt to test against constants: slti
  Helpful in for loops
if (g >= 1) goto Loop
Loop: . . . slti $t0,$s0,1 # $t0 = 1 if # $s0<1 (g<1) beq $t0,$0,Loop # goto Loop # if $t0==0 # (if (g>=1))
C
M I P S
An slt  beq pair means if(… ≥ …)goto…

## Slide 17: What about unsigned numbers?
Also unsigned inequality instructions:
sltu, sltiu
…which sets result to 1 or 0 depending on unsigned comparisons
What is value of $t0, $t1?
($s0 = FFFF FFFAhex, $s1 = 0000 FFFAhex)
slt $t0, $s0, $s1
sltu $t1, $s0, $s1

## Slide 18: MIPS Signed vs. Unsigned – diff meanings!
MIPS terms Signed/Unsigned “overloaded”:
  Do/Don't sign extend
    (lb, lbu)
  Do/Don't overflow
    (add, addi, sub, mult, div)
    (addu, addiu, subu, multu, divu)
  Do signed/unsigned compare
    (slt, slti/sltu, sltiu)

## Slide 19: Peer Instruction
What C code properly fills in the blank in loop below?
do {i--;} while(__);
Loop:addi $s0,$s0,-1 # i = i - 1 slti $t0,$s1,2 # $t0 = (j < 2) beq $t0,$0 ,Loop # goto Loop if $t0 == 0
slt $t0,$s1,$s0 # $t0 = (j < i) bne $t0,$0 ,Loop # goto Loop if $t0 != 0
a) j < 2 && j < i a) j ≥ 2 && j < i b) j < 2 && j ≥ i b) j ≥ 2 && j ≥ i c) j > 2 && j < i c) j < 2 || j < i d) j ≥ 2 || j < i d) j < 2 || j ≥ i e) j ≥ 2 || j ≥ i e) j > 2 || j < i
($s0=i, $s1=j)
Notes: Ans: 7
Beq is the opposite (opposite of j<2 is j≥2), bne is just the test (j<i), and you restart the loop if either is true, so it’s an or (||)

## Slide 20: “And in conclusion…”
To help the conditional branches make decisions concerning inequalities, we introduce: “Set on Less Than” called slt, slti, sltu, sltiu
One can store and load (signed and unsigned) bytes as well as words with lb, lbu
Unsigned add/sub don’t cause overflow
New MIPS Instructions: sll, srl, lb, lbu slt, slti, sltu, sltiu addu, addiu, subu

## Slide 21: Bonus Slides

## Slide 22: Example: The C Switch Statement (1/3)
Choose among four alternatives depending on whether k has the value 0, 1, 2 or 3. Compile this C code: switch (k) { case 0: f=i+j; break; /* k=0 */ case 1: f=g+h; break; /* k=1 */ case 2: f=g–h; break; /* k=2 */ case 3: f=i–j; break; /* k=3 */ }

## Slide 23: Example: The C Switch Statement (2/3)
This is complicated, so simplify.
Rewrite it as a chain of if-else statements, which we already know how to compile:
  if(k==0) f=i+j; else if(k==1) f=g+h; else if(k==2) f=g–h; else if(k==3) f=i–j;
Use this mapping:
  f:$s0, g:$s1, h:$s2, i:$s3, j:$s4, k:$s5

## Slide 24: Example: The C Switch Statement (3/3)
Final compiled MIPS code: bne $s5,$0,L1 # branch k!=0 add $s0,$s3,$s4 #k==0 so f=i+j j Exit # end of case so Exit L1: addi $t0,$s5,-1 # $t0=k-1 bne $t0,$0,L2 # branch k!=1 add $s0,$s1,$s2 #k==1 so f=g+h j Exit # end of case so Exit L2: addi $t0,$s5,-2 # $t0=k-2 bne $t0,$0,L3 # branch k!=2 sub $s0,$s1,$s2 #k==2 so f=g-h j Exit # end of case so Exit L3: addi $t0,$s5,-3 # $t0=k-3 bne $t0,$0,Exit # branch k!=3 sub $s0,$s3,$s4 # k==3 so f=i-j Exit: