## Slide 1: Memristor memory on its way (hopefully)
inst.eecs.berkeley.edu/~cs61c UCB CS61C : Machine Structures Lecture 13 – Caches II 2014-02-21
HP has begun testing research prototypes of a novel non-volatile memory element, the memristor. They have double the storage density of flash, and has 10x more read-write cycles than flash (106 vs 105). Memristors are (in principle) also capable of being memory and logic, how cool is that? Originally slated to be ready by 2013, HP later pushed that date to some time 2014.
Guest Lecturer Alan Christopher
www.technologyreview.com/computing/25018
http://www.technologyreview.com/view/512361/can-hp-save-itself/

## Slide 2: Review: New-School Machine Structures
Parallel Requests
  Assigned to computer
  e.g., Search “Katz”
Parallel Threads
  Assigned to core
  e.g., Lookup, Ads
Parallel Instructions
  >1 instruction @ one time
  e.g., 5 pipelined instructions
Parallel Data
  >1 data item @ one time
  e.g., Add of 4 pairs of words
Hardware descriptions
  All gates @ one time
Programming Languages
Smart Phone
Warehouse Scale Computer
Software Hardware
Harness Parallelism &
Achieve High Performance
Logic Gates
Core
Core
…
Memory (Cache)
Input/Output
Computer
Cache Memory
Core
Instruction Unit(s)
Functional
Unit(s)
A3+B3
A2+B2
A1+B1
A0+B0
Today’s
Lecture

## Slide 3: Review: Direct-Mapped Cache
All fields are read as unsigned integers.
Index
  specifies the cache index (or “row”/block)
Tag
  distinguishes betw the addresses that map to the same location
Offset
  specifies which byte within the block we want
tttttttttttttttttt iiiiiiiiii oooo
tag index byte to check to offset if have select within correct block block block

## Slide 4: TIO Dan’s great cache mnemonic
AREA (cache size, B) = HEIGHT (# of blocks) * WIDTH (size of one block, B/block)
WIDTH (size of one block, B/block)
HEIGHT (# of blocks)
AREA (cache size, B)
2(H+W) = 2H * 2W
Tag Index Offset
Addr size (often 32 bits)

## Slide 5: Memory Access without Cache
Load word instruction: lw $t0, 0($t1)
$t1 contains 1022ten, Memory[1022] = 99
  Processor issues address 1022ten to Memory
  Memory reads word at address 1022ten (99)
  Memory sends 99 to Processor
  Processor loads 99 into register $t1

## Slide 6: Memory Access with Cache
Load word instruction: lw $t0, 0($t1)
$t1 contains 1022ten, Memory[1022] = 99
With cache (similar to a hash)
  Processor issues address 1022ten to Cache
  Cache checks to see if has copy of data at address 1022ten
    2a. If finds a match (Hit): cache reads 99, sends to processor
    2b. No match (Miss): cache sends address 1022 to Memory
      Memory reads 99 at address 1022ten
      Memory sends 99 to Cache
      Cache replaces word with new 99
      Cache sends 99 to processor
  Processor loads 99 into register $t1

## Slide 7: Caching Terminology
When reading memory, 3 things can happen:
  cache hit: cache block is valid and contains proper address, so read desired word
  cache miss: nothing in cache in appropriate block, so fetch from memory
  cache miss, block replacement: wrong data is in cache at appropriate block, so discard it and fetch desired data from memory (cache always copy)

## Slide 8: Cache Terms
Hit rate: fraction of access that hit in the cache
Miss rate: 1 – Hit rate
Miss penalty: time to replace a block from lower level in memory hierarchy to cache
Hit time: time to access cache memory (including tag comparison)
Abbreviation: “$” = cache (A Berkeley innovation!)

## Slide 9: Accessing data in a direct mapped cache
Ex.: 16KB of data, direct-mapped, 4 word blocks
  Can you work out height, width, area?
Read 4 addresses
  0x00000014
  0x0000001C
  0x00000034
  0x00008014
Memory vals here:
Address (hex)
Value of Word
Memory
00000010
00000014
00000018
0000001C
a
b
c
d
...
...
00000030
00000034
00000038
0000003C
e
f
g
h
00008010
00008014
00008018
0000801C
i
j
k
l
...
...
...
...
...
...

## Slide 10: Accessing data in a direct mapped cache
4 Addresses:
  0x00000014, 0x0000001C, 0x00000034, 0x00008014
4 Addresses divided (for convenience) into Tag, Index, Byte Offset fields
000000000000000000 0000000001 0100
000000000000000000 0000000001 1100
000000000000000000 0000000011 0100
000000000000000010 0000000001 0100 Tag Index Offset

## Slide 11: 16 KB Direct Mapped Cache, 16B blocks
Valid bit: determines whether anything is stored in that row (when computer initially turned on, all entries invalid)
...
Valid
Tag
0xc-f
0x8-b
0x4-7
0x0-3
0
1
2
3
4
5
6
7
1022
1023
...
Index
0
0
0
0
0
0
0
0
0
0

## Slide 12: 1. Read 0x00000014
...
Valid
Tag
0
1
2
3
4
5
6
7
1022
1023
...
000000000000000000 0000000001 0100
Index
Tag field
Index field
Offset
0
0
0
0
0
0
0
0
0
0
0xc-f
0x8-b
0x4-7
0x0-3

## Slide 13: So we read block 1 (0000000001)
...
Valid
Tag
0
1
2
3
4
5
6
7
1022
1023
...
000000000000000000 0000000001 0100
Index
Tag field
Index field
Offset
0
0
0
0
0
0
0
0
0
0
0xc-f
0x8-b
0x4-7
0x0-3

## Slide 14: No valid data
...
Valid
Tag
0
1
2
3
4
5
6
7
1022
1023
...
000000000000000000 0000000001 0100
Index
Tag field
Index field
Offset
0
0
0
0
0
0
0
0
0
0
0xc-f
0x8-b
0x4-7
0x0-3

## Slide 15: So load that data into cache, setting tag, valid
...
Valid
Tag
0
1
2
3
4
5
6
7
1022
1023
...
1
0
d
c
b
a
000000000000000000 0000000001 0100
Index
Tag field
Index field
Offset
0
0
0
0
0
0
0
0
0
0xc-f
0x8-b
0x4-7
0x0-3

## Slide 16: Read from cache at offset, return word b
000000000000000000 0000000001 0100
...
Valid
Tag
0
1
2
3
4
5
6
7
1022
1023
...
1
0
Index
Tag field
Index field
Offset
0
0
0
0
0
0
0
0
0
0xc-f
0x8-b
0x4-7
0x0-3
d
c
b
a

## Slide 17: 2. Read 0x0000001C = 0…00 0..001 1100
...
Valid
Tag
0
1
2
3
4
5
6
7
1022
1023
...
1
0
000000000000000000 0000000001 1100
Index
Tag field
Index field
Offset
0
0
0
0
0
0
0
0
0
0xc-f
0x8-b
0x4-7
0x0-3
d
c
b
a

## Slide 18: Index is Valid
...
Valid
Tag
0
1
2
3
4
5
6
7
1022
1023
...
1
0
000000000000000000 0000000001 1100
Index
Tag field
Index field
Offset
0
0
0
0
0
0
0
0
0
0xc-f
0x8-b
0x4-7
0x0-3
d
c
b
a

## Slide 19: Index valid, Tag Matches
...
Valid
Tag
0
1
2
3
4
5
6
7
1022
1023
...
1
0
000000000000000000 0000000001 1100
Index
Tag field
Index field
Offset
0
0
0
0
0
0
0
0
0
0xc-f
0x8-b
0x4-7
0x0-3
d
c
b
a

## Slide 20: Index Valid, Tag Matches, return d
...
Valid
Tag
0
1
2
3
4
5
6
7
1022
1023
...
1
0
000000000000000000 0000000001 1100
Index
Tag field
Index field
Offset
0
0
0
0
0
0
0
0
0
0xc-f
0x8-b
0x4-7
0x0-3
d
c
b
a

## Slide 21: 3. Read 0x00000034 = 0…00 0..011 0100
...
Valid
Tag
0
1
2
3
4
5
6
7
1022
1023
...
1
0
000000000000000000 0000000011 0100
Index
Tag field
Index field
Offset
0
0
0
0
0
0
0
0
0
0xc-f
0x8-b
0x4-7
0x0-3
d
c
b
a

## Slide 22: So read block 3
...
Valid
Tag
0
1
2
3
4
5
6
7
1022
1023
...
1
0
000000000000000000 0000000011 0100
Index
Tag field
Index field
Offset
0
0
0
0
0
0
0
0
0
0xc-f
0x8-b
0x4-7
0x0-3
d
c
b
a

## Slide 23: No valid data
...
Valid
Tag
0
1
2
3
4
5
6
7
1022
1023
...
1
0
000000000000000000 0000000011 0100
Index
Tag field
Index field
Offset
0
0
0
0
0
0
0
0
0
0xc-f
0x8-b
0x4-7
0x0-3
d
c
b
a

## Slide 24: Load that cache block, return word f
...
Valid
Tag
0
1
2
3
4
5
6
7
1022
1023
...
1
0
000000000000000000 0000000011 0100
1
0
h
g
f
e
Index
Tag field
Index field
Offset
0
0
0
0
0
0
0
0
d
c
b
a
0xc-f
0x8-b
0x4-7
0x0-3

## Slide 25: 4. Read 0x00008014 = 0…10 0..001 0100
...
Valid
Tag
0
1
2
3
4
5
6
7
1022
1023
...
1
0
000000000000000010 0000000001 0100
1
0
Index
Tag field
Index field
Offset
0
0
0
0
0
0
0
0
0xc-f
0x8-b
0x4-7
0x0-3
d
c
b
a
h
g
f
e

## Slide 26: So read Cache Block 1, Data is Valid
...
Valid
Tag
0
1
2
3
4
5
6
7
1022
1023
...
1
0
000000000000000010 0000000001 0100
1
0
Index
Tag field
Index field
Offset
0
0
0
0
0
0
0
0
0xc-f
0x8-b
0x4-7
0x0-3
d
c
b
a
h
g
f
e

## Slide 27: Cache Block 1 Tag does not match (0 != 2)
...
Valid
Tag
0
1
2
3
4
5
6
7
1022
1023
...
1
0
000000000000000010 0000000001 0100
1
0
Index
Tag field
Index field
Offset
0
0
0
0
0
0
0
0
0xc-f
0x8-b
0x4-7
0x0-3
d
c
b
a
h
g
f
e

## Slide 28: Miss, so replace block 1 with new data & tag
...
Valid
Tag
0
1
2
3
4
5
6
7
1022
1023
...
1
2
l
k
j
i
000000000000000010 0000000001 0100
1
0
Index
Tag field
Index field
Offset
0
0
0
0
0
0
0
0
0xc-f
0x8-b
0x4-7
0x0-3
h
g
f
e

## Slide 29: And return word J
...
Valid
Tag
0
1
2
3
4
5
6
7
1022
1023
...
1
2
000000000000000010 0000000001 0100
1
0
Index
Tag field
Index field
Offset
0
0
0
0
0
0
0
0
l
k
j
i
0xc-f
0x8-b
0x4-7
0x0-3
h
g
f
e

## Slide 30: Do an example yourself. What happens?
Chose from: Cache: Hit, Miss, Miss w. replace Values returned: a ,b, c, d, e, ..., k, l
Read address 0x00000030 ? 000000000000000000 0000000011 0000
Read address 0x0000001c ? 000000000000000000 0000000001 1100
...
Valid
Tag
0xc-f
0x8-b
0x4-7
0x0-3
0
1
2
3
4
5
6
7
...
1
2
l
k
j
i
1
0
h
g
f
e
Index
0
0
0
0
0
0
Cache

## Slide 31: Answers
0x00000030 a hit
  Index = 3, Tag matches, Offset = 0, value = e
0x0000001c a miss
  Index = 1, Tag mismatch, so replace from memory, Offset = 0xc, value = d
Since reads, values must = memory values whether or not cached:
  0x00000030 = e
  0x0000001c = d
Address (hex)
Value of Word
Memory
00000010
00000014
00000018
0000001C
a
b
c
d
...
...
00000030
00000034
00000038
0000003C
e
f
g
h
00008010
00008014
00008018
0000801C
i
j
k
l
...
...
...
...
...
...

## Slide 32: Administrivia
Proj 1-2 due Sunday

## Slide 33: Multiword-Block Direct-Mapped Cache
Four words/block, cache size = 4K words
10
Index
Data
Index
Tag
Valid
0
1
2
.
.
.
1021
1022
1023
31 30 . . . 15 14 13 . . . 4 3 2 1 0
Byte offset
18
18
Tag
Hit
AND
“MUX” 41 Multiplexor
Data
32
Block offset
2
What kind of locality are we taking advantage of?
Notes: to take advantage for spatial locality want a cache block that is larger than word word in size.

## Slide 34: Peer Instruction
  1) Mem hierarchies were invented before 1950. (UNIVAC I wasn’t delivered ‘til 1951)
  2) All caches take advantage of spatial locality.
3) All caches take advantage of temporal locality.
123
a) FFF
a) FFT
b) FTF
b) FTT
c) TFF
d) TFT
e) TTF
e) TTT
Notes: Answer: [correct=5, TFF] Individual (6, 3, 6, 3, 34, 37, 7, 4)% & Team (9, 4, 4, 4, 39, 34, 0, 7)%
A: T [18/82 & 25/75] (The game breaks up very quickly into separate, independent games -- big win to solve separated & put together)
B: F [80/20 & 86/14] (The game tree grows exponentially! A better static evaluator can make all the difference!)
C: F [53/57 & 52/48] (If you're just looking for the best move, just keep theBestMove around [ala memoizing max])

## Slide 35: Peer Instruction Answer
  1) Mem hierarchies were invented before 1950. (UNIVAC I wasn’t delivered ‘til 1951)
  2) All caches take advantage of spatial locality.
3) All caches take advantage of temporal locality.
123
a) FFF
a) FFT
b) FTF
b) FTT
c) TFF
d) TFT
e) TTF
e) TTT
T R U E
F A L S E
2) Block size = 1, no spatial!
3) That’s the idea of caches; We’ll need it again soon.
  “We are…forced to recognize the possibility of constructing a hierarchy of memories, each of which has greater capacity than the preceding but which is less accessible.” – von Neumann, 1946
T R U E
Notes: Answer: [correct=5, TFF] Individual (6, 3, 6, 3, 34, 37, 7, 4)% & Team (9, 4, 4, 4, 39, 34, 0, 7)%
A: T [18/82 & 25/75] (The game breaks up very quickly into separate, independent games -- big win to solve separated & put together)
B: F [80/20 & 86/14] (The game tree grows exponentially! A better static evaluator can make all the difference!)
C: F [53/57 & 52/48] (If you're just looking for the best move, just keep theBestMove around [ala memoizing max])

## Slide 36: And in Conclusion…
Mechanism for transparent movement of data among levels of a storage hierarchy
  set of address/value bindings
  address  index to set of candidates
  compare desired address with tag
  service hit or miss
    load new block and binding on miss
Valid
Tag
0xc-f
0x8-b
0x4-7
0x0-3
0
1
2
3
...
1
0
d
c
b
a
000000000000000000 0000000001 1100
address: tag index offset