## Slide 1: CS 61C: Great Ideas in Computer Architecture Intro to Assembly Language, MIPS Intro
Instructors:
Vladimir Stojanovic & Nicholas Weaver
http://inst.eecs.Berkeley.edu/~cs61c/sp16

## Slide 2: Levels of Representation/Interpretation
lw $t0, 0($2)
lw $t1, 4($2)
sw $t1, 0($2)
sw $t0, 4($2)
High Level Language Program (e.g., C)
Assembly Language Program (e.g., MIPS)
Machine Language Program (MIPS)
Hardware Architecture Description (e.g., block diagrams)
Compiler
Assembler
Machine Interpretation
temp = v[k];
v[k] = v[k+1];
v[k+1] = temp;
0000 1001 1100 0110 1010 1111 0101 1000
1010 1111 0101 1000 0000 1001 1100 0110
1100 0110 1010 1111 0101 1000 0000 1001
0101 1000 0000 1001 1100 0110 1010 1111
Architecture Implementation
Anything can be represented as a number, i.e., data or instructions
Logic Circuit Description (Circuit Schematic Diagrams)

## Slide 3: Assembly Language
Basic job of a CPU: execute lots of instructions.
Instructions are the primitive operations that the CPU may execute.
Different CPUs implement different sets of instructions. The set of instructions a particular CPU implements is an Instruction Set Architecture (ISA).
  Examples: ARM, Intel x86, MIPS, RISC-V, IBM/Motorola PowerPC (old Mac), Intel IA64 (aka Itanic), ...

## Slide 4: Instruction Set Architectures
Early trend was to add more and more instructions to new CPUs to do elaborate operations
  VAX architecture had an instruction to multiply polynomials!
RISC philosophy (Cocke IBM, Patterson, Hennessy, 1980s) – Reduced Instruction Set Computing
  Keep the instruction set small and simple, makes it easier to build fast hardware.
  Let software do complicated operations by composing simpler ones.

## Slide 5: Berkeley Acknowledge for the first RISC computer

## Slide 6: From RISC-I to RISC-V
EECS151/251A, CS152, CS250, CS252 use RISC-V
Notes: ARM license fees

## Slide 7: MIPS Architecture
MIPS – semiconductor company that built one of the first commercial RISC architectures
We will study the MIPS architecture in some detail in this class (also used in upper division courses. When an upper division course uses RISC-V instead, the ISA is very similar)
Why MIPS instead of Intel x86?
  MIPS is simple, elegant. Don’t want to get bogged down in gritty details.
  MIPS widely used in embedded apps, x86 little used in embedded, and more embeded computers than PCs
Why MIPS instead of ARM?
  Accident of history: Patterson & Hennesey is in MIPS
  MIPS also designed more for performance than ARM, ARM is instead designed for small code size

## Slide 8: Assembly Variables: Registers
Unlike HLL like C or Java, assembly cannot use variables
  Why not? Keep Hardware Simple
Assembly Operands are registers
  Limited number of special locations built directly into the hardware
  Operations can only be performed on these!
Benefit: Since registers are directly in hardware, they are very fast (faster than 1 ns - light travels 30cm in 1 ns!!! )

## Slide 9: Number of MIPS Registers
Drawback: Since registers are in hardware, there are a predetermined number of them
  Solution: MIPS code must be very carefully put together to efficiently use registers
32 registers in MIPS
  Why 32? Smaller is faster, but too small is bad. Goldilocks problem.
  X86 has many fewer registers
Each MIPS register is 32 bits wide
  Groups of 32 bits called a word in MIPS

## Slide 10: Names of MIPS Registers
Registers are numbered from 0 to 31
Each register can be referred to by number or name
Number references:
  $0, $1, $2, … $30, $31
For now:
  $16 - $23 $s0 - $s7 (correspond to C variables)
  $8 - $15  $t0 - $t7 (correspond to temporary variables)
  Later will explain other 16 register names
In general, use names to make your code more readable

## Slide 11: C, Java variables vs. registers
In C (and most High Level Languages) variables declared first and given a type
  Example: int fahr, celsius; char a, b, c, d, e;
Each variable can ONLY represent a value of the type it was declared as (cannot mix and match int and char variables).
In Assembly Language, registers have no type; operation determines how register contents are treated

## Slide 12: Addition and Subtraction of Integers
Addition in Assembly
  Example: add $s0,$s1,$s2 (in MIPS)
  Equivalent to: a = b + c (in C)
  where C variables ⇔ MIPS registers are:
  a ⇔ $s0, b ⇔ $s1, c ⇔ $s2
Subtraction in Assembly
  Example: sub $s3,$s4,$s5 (in MIPS)
  Equivalent to: d = e - f (in C)
  where C variables ⇔ MIPS registers are: d ⇔ $s3, e ⇔ $s4, f ⇔ $s5

## Slide 13: Addition and Subtraction of Integers Example 1
How to do the following C statement?
a = b + c + d - e;
Break into multiple instructions
  add $t0, $s1, $s2 # temp = b + c
  add $t0, $t0, $s3 # temp = temp + d
  sub $s0, $t0, $s4 # a = temp - e
A single line of C may break up into several lines of MIPS.
Notice the use of temporary registers – don’t want to modify the variable registers $s
Everything after the hash mark on each line is ignored (comments)

## Slide 14: Immediates
Immediates are numerical constants
They appear often in code, so there are special instructions for them
Add Immediate:
  addi $s0,$s1,-10 (in MIPS)
  f = g - 10 (in C)
  where MIPS registers $s0,$s1 are associated with C variables f, g
Syntax similar to add instruction, except that last argument is a number instead of a register
  add $s0,$s1,$zero (in MIPS)
  f = g (in C)

## Slide 15: Overflow in Arithmetic
Reminder: Overflow occurs when there is a “mistake” in arithmetic due to the limited precision in computers.
Example (4-bit unsigned numbers):
  15 1111
  + 3 + 0011
  18 10010
But we don’t have room for 5-bit solution, so the solution would be 0010, which is +2, and “wrong”.

## Slide 16: Overflow handling in MIPS
Some languages detect overflow (Ada), some don’t (most C implementations)
MIPS solution is 2 kinds of arithmetic instructions:
  These cause overflow to be detected
    add (add)
    add immediate (addi)
    subtract (sub)
  These do not cause overflow detection
    add unsigned (addu)
    add immediate unsigned (addiu)
    subtract unsigned (subu)
Compiler selects appropriate arithmetic
  MIPS C compilers produce addu, addiu, subu

## Slide 17: Data Transfer: Load from and Store to memory
Processor
Control
Datapath
PC
Registers
Arithmetic & Logic Unit
(ALU)
Memory
Input
Output
Bytes
Enable?
Read/Write
Address
Write Data = Store to memory
Read Data = Load from
memory
Processor-Memory Interface
I/O-Memory Interfaces
Program
Data

## Slide 18: Memory Addresses are in Bytes
0
1
2
3
…
Lots of data is smaller than 32 bits, but rarely smaller than 8 bits – works fine if everything is a multiple of 8 bits
8 bit chunk is called a byte
(1 word = 4 bytes)
Memory addresses are really in bytes, not words
Word addresses are 4 bytes apart
  Word address is same as address of
  leftmost byte – most significant byte (i.e. Big-endian convention)
0
4
8
12
…
1
5
9
13
…
2
6
10
14
…
3
7
11
15
…
Most significant byte in a word

## Slide 19: Transfer from Memory to Register
C code
int A[100];
g = h + A[3];
Using Load Word (lw) in MIPS:
lw $t0,12($s3) # Temp reg $t0 gets A[3]
add $s1,$s2,$t0 # g = h + A[3]
Note: $s3 – base register (pointer)
12 – offset in bytes
Offset must be a constant known at assembly time
Notes: 80 – 5 (Clicker) – 3 (News/Administrativia) = 72 (36 slides max)
Clicker at 20 (half+)

## Slide 20: Transfer from Register to Memory
C code
int A[100];
A[10] = h + A[3];
Using Store Word (sw) in MIPS:
lw $t0,12($s3) # Temp reg $t0 gets A[3]
add $t0,$s2,$t0 # Temp reg $t0 gets h + A[3]
sw $t0, 40($s3) # A[10] = h + A[3]
Note: $s3 – base register (pointer)
12,40 – offsets in bytes
$s3+12 and $s3+40 must be multiples of 4: Word alignment!
Notes: 80 – 5 (Clicker) – 3 (News/Administrativia) = 72 (36 slides max)
Clicker at 20 (half+)

## Slide 21: Loading and Storing bytes
In addition to word data transfers (lw, sw), MIPS has byte data transfers:
  load byte: lb
  store byte: sb
Same format as lw, sw
E.g., lb $s0, 3($s1)
  contents of memory location with address = sum of “3” + contents of register $s1 is copied to the low byte position of register $s0.
byte loaded
zzz zzzz
x
…is copied to “sign-extend”
This bit
xxxx xxxx xxxx xxxx xxxx xxxx
$s0:

## Slide 22: Speed of Registers vs. Memory
Given that
  Registers: 32 words (128 Bytes)
  Memory: Billions of bytes (2 GB to 8 GB on laptop)
and the RISC principle is…
  Smaller is faster
How much faster are registers than memory??
About 100-500 times faster!
  in terms of latency of one access

## Slide 23: Administrivia
Hopefully everyone turned-in HW0
Project 1 out – due 02/07 @ 23:59:59
  Make sure you test your code on hive machines, that’s where we’ll grade them! This is critical: Your “lucky” not-crash due to a memory error on your machine may not be “lucky not crash” on our grading
Bitbucket/edX forms
  Fill out @ http://goo.gl/forms/AiKsGIieIP
  Due 2/12/16
Guerrilla sections starting soon
  Look for Piazza post and webpage schedule update

## Slide 24: How many hours h on Homework 0?
A: 0 ≤ h < 5
B: 5 ≤ h < 10
C: 10 ≤ h < 15
D: 15 ≤ h < 20
E: 20 ≤ h

## Slide 25: Clickers/Peer Instruction
  We want to translate *x = *y +1 into MIPS
  (x, y pointers stored in: $s0 $s1)
  A: addi $s0,$s1,1
  B: lw $s0,1($s1)
  sw $s1,0($s0)
  C: lw $t0,0($s1)
  addi $t0,$t0,1
  sw $t0,0($s0)
  D: sw $t0,0($s1)
  addi $t0,$t0,1
  lw $t0,0($s0)
  E: lw $s0,1($t0)
  sw $s1,0($t0)
Notes: Answer: [correct=c]
We must first load the contents of y’s pointee into a temp variable [$t0], then add 1, and then we have to store $t0 back into x’s pointee

## Slide 26: MIPS Logical Instructions
Logical operations | C operators | Java operators | MIPS instructions
Bit-by-bit AND | & | & | and
Bit-by-bit OR | ¦ | ¦ | or
Bit-by-bit NOT | ~ | ~ | not
Shift left | << | << | sll
Shift right | >> | >>> | srl
Useful to operate on fields of bits within a word
  e.g., characters within a word (8 bits)
Operations to pack /unpack bits into words
Called logical operations

## Slide 27: Logic Shifting
Shift Left: sll $s1,$s2,2 #s1=s2<<2
  Store in $s1 the value from $s2 shifted 2 bits to the left (they fall off end), inserting 0’s on right; << in C.
    Before: 0000 0002hex 0000 0000 0000 0000 0000 0000 0000 0010two
  After: 0000 0008hex 0000 0000 0000 0000 0000 0000 0000 1000two
  What arithmetic effect does shift left have?
Shift Right: srl is opposite shift; >>

## Slide 28: Arithmetic Shifting
Shift right arithmetic moves n bits to the right (insert high order sign bit into empty bits)
For example, if register $s0 contained
  1111 1111 1111 1111 1111 1111 1110 0111two= -25ten
If executed sra $s0, $s0, 4, result is:
1111 1111 1111 1111 1111 1111 1111 1110two= -2ten
  Unfortunately, this is NOT same as dividing by 2n
    Fails for odd negative numbers
    C arithmetic semantics is that division should round towards 0
Notes: \

## Slide 29: And In Conclusion …
Computer words and vocabulary are called instructions and instruction set respectively
MIPS is example RISC instruction set in this class
Rigid format: 1 operation, 2 source operands, 1 destination
  add,sub,mul,div,and,or,sll,srl,sra
  lw,sw,lb,sb to move data to/from registers from/to memory
  beq, bne, j, slt, slti for decision/flow control
Simple mappings from arithmetic expressions, array access, if-then-else in C to MIPS instructions