## Slide 1: CS 61C: Great Ideas in Computer Architecture MIPS Instruction Formats
Instructors:
Vladimir Stojanovic and Nicholas Weaver
http://inst.eecs.Berkeley.edu/~cs61c/sp16

## Slide 2: Levels of Representation/Interpretation
lw $t0, 0($2)
lw $t1, 4($2)
sw $t1, 0($2)
sw $t0, 4($2)
High Level Language Program (e.g., C)
Assembly Language Program (e.g., MIPS)
Machine Language Program (MIPS)
Hardware Architecture Description (e.g., block diagrams)
Compiler
Assembler
Machine Interpretation
temp = v[k];
v[k] = v[k+1];
v[k+1] = temp;
0000 1001 1100 0110 1010 1111 0101 1000
1010 1111 0101 1000 0000 1001 1100 0110
1100 0110 1010 1111 0101 1000 0000 1001
0101 1000 0000 1001 1100 0110 1010 1111
Architecture Implementation
Anything can be represented as a number, i.e., data or instructions
Logic Circuit Description (Circuit Schematic Diagrams)

## Slide 3: Instruction Formats
I-format: used for instructions with immediates, lw and sw (since offset counts as an immediate), and branches (beq and bne)
  (but not the shift instructions; later)
J-format: used for j and jal
R-format: used for all other instructions
It will soon become clear why the instructions have been partitioned in this way

## Slide 4: R-Format Instructions (1/5)
Define “fields” of the following number of bits each: 6 + 5 + 5 + 5 + 5 + 6 = 32
For simplicity, each field has a name:
Important: On these slides and in book, each field is viewed as a 5- or 6-bit unsigned integer, not as part of a 32-bit integer
  Consequence: 5-bit fields can represent any number 0-31, while 6-bit fields can represent any number 0-63
6
5
5
5
6
5
opcode
rs
rt
rd
funct
shamt

## Slide 5: R-Format Example (1/2)
MIPS Instruction:
  add $8,$9,$10
  opcode = 0 (look up in table in book)
  funct = 32 (look up in table in book)
  rd = 8 (destination)
  rs = 9 (first operand)
  rt = 10 (second operand)
  shamt = 0 (not a shift)

## Slide 6: R-Format Example (2/2)
MIPS Instruction:
  add $8,$9,$10
  Decimal number per field representation:
  Binary number per field representation:
  hex representation: 012A 4020hex
  Called a Machine Language Instruction
0
9
10
8
32
0
000000
01001
01010
01000
100000
00000
hex
opcode
rs
rt
rd
funct
shamt

## Slide 7: I-Format Instructions (1/2)
Define “fields” of the following number of bits each: 6 + 5 + 5 + 16 = 32 bits
  Again, each field has a name:
  Key Concept: Only one field is inconsistent with R-format. Most importantly, opcode is still in same location.
6
5
5
16
opcode
rs
rt
immediate

## Slide 8: I-Format Instructions (2/2)
The Immediate Field:
  addi, slti, sltiu, the immediate is sign-extended to 32 bits. Thus, it’s treated as a signed integer.
  16 bits  can be used to represent immediate up to 216 different values
  This is large enough to handle the offset in a typical lw or sw, plus a vast majority of values that will be used in the slti instruction.
  Later, we’ll see what to do when a value is too big for 16 bits

## Slide 9: I-Format Example (1/2)
MIPS Instruction:
  addi $21,$22,-50
  opcode = 8 (look up in table in book)
  rs = 22 (register containing operand)
  rt = 21 (target register)
  immediate = -50 (by default, this is decimal in assembly code)

## Slide 10: I-Format Example (2/2)
MIPS Instruction:
  addi $21,$22,-50
8
22
21
-50
001000
10110
10101
1111111111001110
  Decimal/field representation:
  Binary/field representation:
  hexadecimal representation: 22D5 FFCEhex

## Slide 11: Clicker/Peer Instruction
Which instruction has same representation as integer 35ten?
  a) add $0, $0, $0
  b) subu $s0,$s0,$s0
  c) lw $0, 0($0)
  d) addi $0, $0, 35
  e) subu $0, $0, $0
  Registers numbers and names: 0: $0, .. 8: $t0, 9:$t1, ..15: $t7, 16: $s0, 17: $s1, .. 23: $s7
  Opcodes and function fields:
  add: opcode = 0, funct = 32
  subu: opcode = 0, funct = 35
  addi: opcode = 8
  lw: opcode = 35
opcode
rs
rt
offset
rd
funct
shamt
opcode
rs
rt
opcode
rs
rt
immediate
rd
funct
shamt
opcode
rs
rt
rd
funct
shamt
opcode
rs
rt

## Slide 12: Branching Instructions
beq and bne
  Need to specify a target address if branch taken
  Also specify two registers to compare
Use I-Format:
  opcode specifies beq (4) vs. bne (5)
  rs and rt specify registers
  How to best use immediate to specify addresses?
opcode
rs
rt
immediate
31
0

## Slide 13: Branching Instruction Usage
Branches typically used for loops (if-else, while, for)
  Loops are generally small (< 50 instructions)
  Function calls and unconditional jumps handled with jump instructions (J-Format)
Recall: Instructions stored in a localized area of memory (Code/Text)
  Largest branch distance limited by size of code
  Address of current instruction stored in the program counter (PC)

## Slide 14: PC-Relative Addressing
PC-Relative Addressing: Use the immediate field as a two’s complement offset to PC
  Branches generally change the PC by a small amount
  Can specify ± 215 addresses from the PC

## Slide 15: Branch Calculation
If we don’t take the branch:
  PC = PC + 4 = next instruction
If we do take the branch:
  PC = (PC+4) + (immediate*4)
Observations:
  immediate is number of instructions to jump (remember, specifies words) either forward (+) or backwards (–)
  Branch from PC+4 for hardware reasons; will be clear why later in the course

## Slide 16: Branch Example (1/2)
MIPS Code:
  Loop: beq $9,$0,End addu $8,$8,$10 addiu $9,$9,-1 j Loop End:
I-Format fields:
  opcode = 4 (look up on Green Sheet)
  rs = 9 (first operand)
  rt = 0 (second operand)
  immediate = ???
Start counting from instruction AFTER the branch
1
2
3
3

## Slide 17: Branch Example (2/2)
MIPS Code:
  Loop: beq $9,$0,End addu $8,$8,$10 addiu $9,$9,-1 j Loop End:
  Field representation (decimal):
  Field representation (binary):
4
9
0
3
31
0
000100
01001
00000
0000000000000011
31
0

## Slide 18: Questions on PC-addressing
Does the value in branch immediate field change if we move the code?
  If moving individual lines of code, then yes
  If moving all of code, then no
What do we do if destination is > 215 instructions away from branch?
  Other instructions save us
  beq $s0,$0,far bne $s0,$0,next # next instr  j far next: # next instr
Notes: As we will see, jumping instructions can reach farther than branching

## Slide 19: J-Format Instructions (1/4)
For branches, we assumed that we won’t want to branch too far, so we can specify a change in the PC
For general jumps (j and jal), we may jump to anywhere in memory
  Ideally, we would specify a 32-bit memory address to jump to
  Unfortunately, we can’t fit both a 6-bit opcode and a 32-bit address into a single 32-bit word

## Slide 20: J-Format Instructions (2/4)
Define two “fields” of these bit widths:
As usual, each field has a name:
Key Concepts:
  Keep opcode field identical to R-Format and I-Format for consistency
  Collapse all other fields to make room for large target address
6
26
31
0
opcode
target address
31
0

## Slide 21: J-Format Instructions (3/4)
We can specify 226 addresses
  Still going to word-aligned instructions, so add 0b00 as last two bits (multiply by 4)
  This brings us to 28 bits of a 32-bit address
Take the 4 highest order bits from the PC
  Cannot reach everywhere, but adequate almost all of the time, since programs aren’t that long
  Only problematic if code straddles a 256MB boundary
If necessary, use 2 jumps or jr (R-Format) instead

## Slide 22: J-Format Instructions (4/4)
Jump instruction:
  New PC = { (PC+4)[31..28], target address, 00 }
Notes:
  { , , } means concatenation { 4 bits , 26 bits , 2 bits } = 32 bit address
    Book uses || instead
  Array indexing: [31..28] means highest 4 bits
  For hardware reasons, use PC+4 instead of PC

## Slide 23: MAL vs. TAL
True Assembly Language (TAL)
  The instructions a computer understands and executes
MIPS Assembly Language (MAL)
  Instructions the assembly programmer can use (includes pseudo-instructions)
  Each MAL instruction becomes 1 or more TAL instruction

## Slide 24: Assembler Pseudo-Instructions
Certain C statements are implemented unintuitively in MIPS
  e.g. assignment (a=b) via add $zero
MIPS has a set of “pseudo-instructions” to make programming easier
  More intuitive to read, but get translated into actual instructions later
Example:
move dst,src
translated into add dst,src,$zero

## Slide 25: Assembler Pseudo-Instructions
List of pseudo-instructions: http://en.wikipedia.org/wiki/MIPS_architecture#Pseudo_instructions
  List also includes instruction translation
Load Address (la)
  la dst,label
  Loads address of specified label into dst
Load Immediate (li)
  li dst,imm
  Loads 32-bit immediate into dst
MARS has additional pseudo-instructions
  See Help (F1) for full list

## Slide 26: Assembler Register
Problem:
  When breaking up a pseudo-instruction, the assembler may need to use an extra register
  If it uses a regular register, it’ll overwrite whatever the program has put into it
Solution:
  Reserve a register ($1 or $at for “assembler temporary”) that assembler will use to break up pseudo-instructions
  Since the assembler may use this at any time, it’s not safe to code with it

## Slide 27: Dealing With Large Immediates
How do we deal with 32-bit immediates?
  Sometimes want to use immediates > ± 215 with addi, lw, sw and slti
  Bitwise logic operations with 32-bit immediates
Solution: Don’t mess with instruction formats, just add a new instruction
Load Upper Immediate (lui)
  lui reg,imm
  Moves 16-bit imm into upper half (bits 16-31) of reg and zeros the lower half (bits 0-15)

## Slide 28: lui Example
Want: addiu $t0,$t0,0xABABCDCD
  This is a pseudo-instruction!
Translates into:
lui $at,0xABAB # upper 16 ori $at,$at,0xCDCD # lower 16 addu $t0,$t0,$at # move
Now we can handle everything with a 16-bit immediate!
Only the assembler gets to use $at ($1)

## Slide 29: Clicker Question
Which of the following place the address of LOOP in $v0?
la $t1, LOOP
lw $v0, 0($t1)
2) jal LOOP
LOOP: addu $v0, $ra, $zero
3) la $v0, LOOP
1 2 3
T, T, T
T, T, F
F, T, T
F, T, F
F, F, T
Notes: B

## Slide 30: Administrivia
Project 2-1 is out – start early
HW1 (ungraded) C-to-MIPS practice problems (due 02/14 @ 23:59:59)
  Will help you a lot with the midterm so don’t skip
Piazza Etiquette
  Please don’t post code. We do not debug over piazza. Come to OH instead!
  Search through other posts, FAQs before posting a question

## Slide 31: Integer Multiplication (1/3)
Paper and pencil example (unsigned):
  Multiplicand 1000 8
  Multiplier x1001 9 1000 0000 0000 +1000 01001000 72
m bits x n bits = m + n bit product

## Slide 32: Integer Multiplication (2/3)
In MIPS, we multiply registers, so:
  32-bit value x 32-bit value = 64-bit value
Syntax of Multiplication (signed):
  mult register1, register2
  Multiplies 32-bit values in those registers & puts 64-bit product in special result registers:
    puts product upper half in hi, lower half in lo
  hi and lo are 2 registers separate from the 32 general purpose registers
  Use mfhi register & mflo register to move from hi, lo to another register

## Slide 33: Integer Multiplication (3/3)
Example:
  in C: a = b * c;
  in MIPS:
    let b be $s2; let c be $s3; and let a be $s0 and $s1 (since it may be up to 64 bits)
  mult $s2,$s3 # b*c
  mfhi $s0 # upper half of # product into $s0 mflo $s1 # lower half of # product into $s1
Note: Often, we only care about the lower half of the product
  Pseudo-inst. mul expands to mult/mflo

## Slide 34: Integer Division (1/2)
Paper and pencil example (unsigned):
  1001 Quotient Divisor 1000|1001010 Dividend -1000 10 101 1010 -1000 10 Remainder (or Modulo result)
Dividend = Quotient x Divisor + Remainder

## Slide 35: Integer Division (2/2)
Syntax of Division (signed):
  div register1, register2
  Divides 32-bit register 1 by 32-bit register 2:
  puts remainder of division in hi, quotient in lo
Implements C division (/) and modulo (%)
Example in C: a = c / d; b = c % d;
in MIPS: a↔$s0; b↔$s1; c↔$s2; d↔$s3
  div $s2,$s3 # lo=c/d, hi=c%d
  mflo $s0 # get quotient mfhi $s1 # get remainder

## Slide 36: Summary
I-Format: instructions with immediates, lw/sw (offset is immediate), and beq/bne
  But not the shift instructions
  Branches use PC-relative addressing
J-Format: j and jal (but not jr)
  Jumps use absolute addressing
R-Format: all other instructions
opcode
rs
rt
immediate
I:
opcode
target address
J:
opcode
funct
rs
rt
rd
shamt
R: