## Slide 1: CS 61C: Great Ideas in Computer Architecture Sequential Elements, Synchronous Digital Systems
Instructors:
Vladimir Stojanovic & Nicholas Weaver
http://inst.eecs.Berkeley.edu/~cs61c/sp16

## Slide 2: Levels of Representation/Interpretation
lw $t0, 0($2)
lw $t1, 4($2)
sw $t1, 0($2)
sw $t0, 4($2)
High Level Language Program (e.g., C)
Assembly Language Program (e.g., MIPS)
Machine Language Program (MIPS)
Hardware Architecture Description (e.g., block diagrams)
Compiler
Assembler
Machine Interpretation
temp = v[k];
v[k] = v[k+1];
v[k+1] = temp;
0000 1001 1100 0110 1010 1111 0101 1000
1010 1111 0101 1000 0000 1001 1100 0110
1100 0110 1010 1111 0101 1000 0000 1001
0101 1000 0000 1001 1100 0110 1010 1111
Logic Circuit Description (Circuit Schematic Diagrams)
Architecture Implementation
Anything can be represented as a number, i.e., data or instructions

## Slide 3: Boolean Algebra: Circuit & Algebraic Simplification

## Slide 4: Laws of Boolean Algebra
X X = 0
X 0 = 0
X 1 = X
X X = X
X Y = Y X
(X Y) Z = Z (Y Z)
X (Y + Z) = X Y + X Z
X Y + X = X
X Y + X = X + Y
X Y = X + Y
X + X = 1
X + 1 = 1
X + 0 = X
X + X = X
X + Y = Y + X
(X + Y) + Z = Z + (Y + Z)
X + Y Z = (X + Y) (X + Z)
(X + Y) X = X
(X + Y) X = X Y
X + Y = X Y
Complementarity
Laws of 0’s and 1’s
Identities
Idempotent Laws
Commutativity
Associativity
Distribution
Uniting Theorem
Uniting Theorem v. 2
DeMorgan’s Law

## Slide 5: Boolean Algebraic Simplification Example
Notes: Do on black board
First write truth table
Then minimize and check truth table
From distribution: a(b +1) + c
Froms laws of 0s and 1s: b+1 = 1
= a + c
Truth Table
a b c y
0 0 0 0
0 0 1 1
0 0 1 1

## Slide 6: Boolean Algebraic Simplification Example
a b c y
0 0 0 0
0 0 1 1
0 1 0 0
0 1 1 1
1 0 0 1
1 0 1 1
1 1 0 1
1 1 1 1
Notes: Do on black board
From distribution: a(b +1) + c
Froms laws of 0s and 1s: b+1 = 1
= a + c
Truth Table
a b c y
0 0 0 0
0 0 1 1
0 1 0 0
0 1 1 1
1 0 0 1
1 0 1 1
1 1 0 1
1 1 1 1

## Slide 7: Signals and Waveforms: Grouping

## Slide 8: Signals and Waveforms: Circuit Delay
2
3
3
4
5
10
0
1
5
13
4
6

## Slide 9: Sample Debugging Waveform

## Slide 10: Clickers/Peer Instruction
Simplify Z = A+BC + A(BC)
A: Z = 0
B: Z = A(1+ BC)
C: Z = (A + BC)
D: Z = BC
E: Z = 1

## Slide 11: Type of Circuits
Synchronous Digital Systems consist of two basic types of circuits:
  Combinational Logic (CL) circuits
    Output is a function of the inputs only, not the history of its execution
    E.g., circuits to add A, B (ALUs)
  Sequential Logic (SL)
    Circuits that “remember” or store information
    aka “State Elements”
    E.g., memories and registers (Registers)

## Slide 12: Uses for State Elements
Place to store values for later re-use:
  Register files (like $1-$31 in MIPS)
  Memory (caches and main memory)
Help control flow of information between combinational logic blocks
  State elements hold up the movement of information at input to combinational logic blocks to allow for orderly passage

## Slide 13: Accumulator Example
Want: S=0;
for (i=0;i<n;i++)
S = S + Xi
Why do we need to control the flow of information?
Assume:
  Each X value is applied in succession, one per cycle
  After n cycles the sum is present on S
SUM
Xi
S

## Slide 14: First Try: Does this work?
No!
Reason #1: How to control the next iteration of the ‘for’ loop?
Reason #2: How do we say: ‘S=0’?
Feedback

## Slide 15: Register Internals
n instances of a “Flip-Flop”
Flip-flop name because the output flips and flops between 0 and 1
D is “data input”, Q is “data output”
Also called “D-type Flip-Flop”

## Slide 16: Flip-Flop Operation
Edge-triggered d-type flip-flop
  This one is “positive edge-triggered”
“On the rising edge of the clock, the input d is sampled and transferred to the output. At all other times, the input d is ignored.”
Example waveforms:

## Slide 17: Flip-Flop Timing
Edge-triggered d-type flip-flop
  This one is “positive edge-triggered”
“On the rising edge of the clock, the input d is sampled and transferred to the output. At all other times, the input d is ignored.”
Example waveforms (more detail):

## Slide 18: Camera Analogy Timing Terms
Want to take a portrait – timing right before and after taking picture
Set up time – don’t move since about to take picture (open camera shutter)
Hold time – need to hold still after shutter opens until camera shutter closes
Time click to data – time from open shutter until can see image on output (viewscreen)

## Slide 19: Hardware Timing Terms
Setup Time: when the input must be stable before the edge of the CLK
Hold Time: when the input must be stable after the edge of the CLK
“CLK-to-Q” Delay: how long it takes the output to change, measured from the edge of the CLK

## Slide 20: Accumulator Timing 1/2
Reset input to register is used to force it to all zeros (takes priority over D input).
Si-1 holds the result of the ith-1 iteration.
Analyze circuit timing starting at the output of the register.

## Slide 21: Accumulator Timing 2/2
reset signal shown.
Also, in practice X might not arrive to the adder at the same time as Si-1
Si temporarily is wrong, but register always captures correct value.
In good circuits, instability never happens around rising edge of clk.

## Slide 22: Model for Synchronous Systems
Collection of Combinational Logic blocks separated by registers
Feedback is optional
Clock signal(s) connects only to clock input of registers
Clock (CLK): steady square wave that synchronizes the system
Register: several bits of state that samples on rising edge of CLK (positive edge-triggered) or falling edge (negative edge-triggered)

## Slide 23: Maximum Clock Frequency
What is the maximum frequency of this circuit?
Period = Max Delay = CLK-to-Q Delay + CL Delay + Setup Time
Hint:
Frequency = 1/Period

## Slide 24: Critical Paths
Timing…
Note: delay of 1 clock cycle from input to output.
Clock period limited by propagation delay of adder/shifter.

## Slide 25: Pipelining to improve performance
Timing…
Insertion of register allows higher clock frequency
More outputs per second (higher bandwidth)
But each individual result takes longer (greater latency)

## Slide 26: Recap of Timing Terms
Clock (CLK) - steady square wave that synchronizes system
Setup Time - when the input must be stable before the rising edge of the CLK
Hold Time - when the input must be stable after the rising edge of the CLK
“CLK-to-Q” Delay - how long it takes the output to change, measured from the rising edge of the CLK
Flip-flop - one bit of state that samples every rising edge of the CLK (positive edge-triggered)
Register - several bits of state that samples on rising edge of CLK or on LOAD (positive edge-triggered)

## Slide 27: Clickers/Peer Instruction
What is maximum clock frequency? (assume all unconnected inputs come from some register)
A: 5 GHz
B: 200 MHz
C: 500 MHz
D: 1/7 GHz
E: 1/6 GHz
Clock->Q 1ns
Setup 1ns
Hold 1ns
AND delay 1ns

## Slide 28: Administrivia
No lecture on Wed – study for midterm
Midterm 1 is on Thu 2/25
  Time 6-8pm
  Location
    2050 VLSB(aa-lz)
    1 Pimentel(ma-zz)
  Covers up to and including 02/17 lecture (CALL 2)
  1 handwritten, double sided, 8.5”x11” cheat sheet
  We’ll give you MIPS green sheet
Emails sent-out to students requiring special accommodation for the exam – please respond

## Slide 29: Study Advice
Review slides, book, worksheets, etc. and add to your cheatsheet as you do so
  This step is not the end
Take a mock exam in the allotted time, using only your cheatsheet
Go over solutions, look at why the answers are what they are (especially for questions you answered incorrectly)
Update cheatsheet as necessary
if (!perfect) goto 2;
Notes: see hkn for old exams