## Slide 1: CS 61C: Great Ideas in Computer Architecture Single-Cycle CPU Datapath and Control II
Instructors:
Nicholas Weaver & Vladimir Stojanovic
http://inst.eecs.Berkeley.edu/~cs61c/sp16

## Slide 2: Clocking Methodology
Storage elements clocked by same edge
Flip-flops (FFs) and combinational logic have some delays
  Gates: delay from input change to output change
  Signals at FF D input must be stable before active clock edge to allow signal to travel within the FF (set-up time), and we have the usual clock-to-Q delay
“Critical path” (longest path through logic) determines length of clock period
Clk
.
.
.
.
.
.
.
.
.
.
.
.
Notes: Remember, we will be using a clocking methodology where all storage elements are clocked by the same clock edge.
Consequently, our cycle time will be the sum of:
(a) The Clock-to-Q time of the input registers.
(b) The longest delay path through the combinational logic block.
(c) The set up time of the output register.
(d) And finally the clock skew.
In order to avoid hold time violation, you have to make sure this inequality is fulfilled.
+2 = 18 min. (X:58)

## Slide 3: Register-Register Timing: One Complete Cycle (Add/Sub)
Clk
PC
Rs, Rt, Rd,
Op, Func
ALUctr
Instruction Memory Access Time
Old Value
New Value
RegWr
Old Value
New Value
Delay through Control Logic
busA, B
Register File Access Time
Old Value
New Value
busW
ALU Delay
Old Value
New Value
Old Value
New Value
New Value
Old Value
Register Write
Occurs Here
32
clk
busW
32
busA
32
busB
5
5
Rw
Ra
Rb
RegFile
Rs
Rt
ALU
5
Rd
ALUctr
RegWr
Notes: Let’s take a more quantitative picture of what is happening.
At each clock tick, the Program Counter will present its latest value to the Instruction memory after Clk-to-Q time.
After a delay of the Instruction Memory Access time, the Opcode, Rd, Rs, Rt, and Function fields will become valid on the instruction bus.
Once we have the new instruction, that is the Add or Subtract instruction, on the instruction bus, two things happen in parallel.
First of all, the control unit will decode the Opcode and Func field and set the control signals ALUctr and RegWr accordingly. We will cover this in the next lecture.
While this is happening (points to Control Delay), we will also be reading the register file (Register File Access Time).
Once the data is valid on busA and busB, the ALU will perform the Add or Subtract operation based on the ALUctr signal.
Hopefully, the ALU is fast enough that it will finish the operation (ALU Delay) before the next clock tick.
At the next clock tick, the output of the ALU will be written into the register file because the RegWr signal will be equal to 1.
+3 = 45 min. (Y:25)

## Slide 4: Register-Register Timing: One Complete Cycle (Add/Sub)
Clk
PC
Rs, Rt, Rd,
Op, Func
ALUctr
Instruction Memory Access Time
Old Value
New Value
RegWr
Old Value
New Value
Delay through Control Logic
busA, B
Register File Access Time
Old Value
New Value
busW
ALU Delay
Old Value
New Value
Old Value
New Value
New Value
Old Value
Register Write
Occurs Here
32
clk
busW
32
busA
32
busB
5
5
Rw
Ra
Rb
RegFile
Rs
Rt
ALU
5
Rd
ALUctr
RegWr
Notes: Let’s take a more quantitative picture of what is happening.
At each clock tick, the Program Counter will present its latest value to the Instruction memory after Clk-to-Q time.
After a delay of the Instruction Memory Access time, the Opcode, Rd, Rs, Rt, and Function fields will become valid on the instruction bus.
Once we have the new instruction, that is the Add or Subtract instruction, on the instruction bus, two things happen in parallel.
First of all, the control unit will decode the Opcode and Func field and set the control signals ALUctr and RegWr accordingly. We will cover this in the next lecture.
While this is happening (points to Control Delay), we will also be reading the register file (Register File Access Time).
Once the data is valid on busA and busB, the ALU will perform the Add or Subtract operation based on the ALUctr signal.
Hopefully, the ALU is fast enough that it will finish the operation (ALU Delay) before the next clock tick.
At the next clock tick, the output of the ALU will be written into the register file because the RegWr signal will be equal to 1.
+3 = 45 min. (Y:25)

## Slide 5: 3c: Logical Op (or) with Immediate
R[rt] = R[rs] op ZeroExt[imm16]
op
rs
rt
immediate
0
16
21
26
31
6 bits
16 bits
5 bits
5 bits
immediate
0
16
15
31
16 bits
16 bits
0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0
What about Rt Read?
32
ALUctr
clk
RegWr
32
32
busA
32
busB
5
5
Rw
Ra
Rb
RegFile
Rs
Rt
Rt
Rd
ZeroExt
32
16
imm16
ALUSrc
0
1
0
1
ALU
5
RegDst
Writing to Rt register (not Rd)!!
Notes: Here is the datapath for the Or immediate instructions.
We cannot use the Rd field here (Rw) because in this instruction format, we don’t have a Rd field. The Rd field in the R-type is used here as part of the immediate field.
For this instruction type, Rw input of the register file, that is the address of the register to be written, comes from the Rt field of the instruction.
Recalled from earlier slide that for R-type instruction, the Rw comes from the Rd field.
That’s why we need a MUX here to put Rd onto Rw for R-type instructions and to put Rt onto Rw for the I-type instruction.
Since the second operation of this instruction will be the immediate field zero extended to 32 bits, we also need a MUX here to block off bus B from the register file.
Since bus B is blocked off by the MUX, the value on bus B is don’t care. Therefore we do not have to worry about what ends up on the register file’s Rb register specifier.
To keep things simple, we may just as well keep it the same as the R-type instruction and put the Rt field here.
So to summarize, this is how this datapath works. With Rs on Register File’s Ra input, bus A will get the value of Rs as the first ALU operand.
The second operand will come from the immediate field of the instruction.
Once the ALU complete the OR operation, the result will be written into the register specified by the instruction’s Rt field.
+3 = 50 min. (Y:30)

## Slide 6: 3d: Load Operations
R[rt] = Mem[R[rs] + SignExt[imm16]] Example: lw rt,rs,imm16
op
rs
rt
immediate
0
16
21
26
31
6 bits
16 bits
5 bits
5 bits
32
ALUctr
clk
busW
RegWr
32
32
busA
32
busB
5
5
Rw
Ra
Rb
RegFile
Rs
Rt
Rt
Rd
RegDst
Extender
32
16
Imm16
ALUSrc
ExtOp
MemtoReg
clk
0
1
0
1
ALU
0
1
Adr
Data
Memory
5
Notes: Once again we cannot use the instruction’s Rd field for the Register File’s Rw input because load is a I-type instruction and there is no such thing as the Rd field in the I format.
So instead of Rd, the Rt field is used to specify the destination register through this two to one multiplexor.
The first operand of the ALU comes from busA of the register file which contains the value of Register Rs (points to the Ra input of the register file).
The second operand, on the other hand, comes from the immediate field of the instruction.
Instead of using the Zero Extender I used in datapath for the or immediate datapath, I have to use a more general purpose Extender that can do both Sign Extend and Zero Extend.
The ALU then adds these two operands together to form the memory address.
Consequently, the output of the ALU has to go to two places:
(a) First the address input of the data memory.
(b) And secondly, also to the input of this two-to-one multiplexer.
The other input of this multiplexer comes from the output of the data memory so we can place the output of the data memory onto the register file’s input bus for the load instruction.
For Add, Subtract, and the Or immediate instructions, the output of the ALU will be selected to be placed on the input bus of the register file.
In either case, the control signal RegWr should be asserted so the register file will be written at the end of the cycle.
+3 = 60 min. (Y:40)

## Slide 7: 3e: Store Operations
Mem[ R[rs] + SignExt[imm16] ] = R[rt] Ex.: sw rt, rs, imm16
op
rs
rt
immediate
0
16
21
26
31
6 bits
16 bits
5 bits
5 bits
32
ALUctr
clk
busW
RegWr
32
32
busA
32
busB
5
5
Rw
Ra
Rb
RegFile
Rs
Rt
Rt
Rd
RegDst
Extender
32
16
Imm16
ALUSrc
ExtOp
MemtoReg
clk
Data_In
32
MemWr
0
1
0
1
ALU
0
1
WrEn
Adr
Data
Memory
5
Notes: And here is the datapath for the store instruction.
The Register File, the ALU, and the Extender are the same as the datapath for the load instruction because the memory address has to be calculated the same exact way:
(a) Put the register selected by Rs onto bus A and sign extend the 16 bit immediate field.
(b) Then make the ALU (ALUctr) adds these two (busA and output of Extender) together.
The new thing we added here is busB extension (DataIn).
More specifically, in order to send the register selected by the Rt field (Rb of the register file) to data memory, we need to connect bus B to the data memory’s Data In bus.
Finally, the store instruction is the first instruction we encountered that does not do any register write at the end.
Therefore the control unit must make sure RegWr is zero for this instruction.
+2 = 64 min. (Y:44)

## Slide 8: 3e: Store Operations
Mem[ R[rs] + SignExt[imm16] ] = R[rt] Ex.: sw rt, rs, imm16
op
rs
rt
immediate
0
16
21
26
31
6 bits
16 bits
5 bits
5 bits
32
ALUctr
clk
busW
RegWr
32
32
busA
32
busB
5
5
Rw
Ra
Rb
RegFile
Rs
Rt
Rt
Rd
RegDst
Extender
32
16
imm16
ALUSrc
ExtOp
MemtoReg
clk
Data In
32
MemWr
0
1
0
1
ALU
0
1
WrEn
Adr
Data
Memory
5
Notes: And here is the datapath for the store instruction.
The Register File, the ALU, and the Extender are the same as the datapath for the load instruction because the memory address has to be calculated the same exact way:
(a) Put the register selected by Rs onto bus A and sign extend the 16 bit immediate field.
(b) Then make the ALU (ALUctr) adds these two (busA and output of Extender) together.
The new thing we added here is busB extension (DataIn).
More specifically, in order to send the register selected by the Rt field (Rb of the register file) to data memory, we need to connect bus B to the data memory’s Data In bus.
Finally, the store instruction is the first instruction we encountered that does not do any register write at the end.
Therefore the control unit must make sure RegWr is zero for this instruction.
+2 = 64 min. (Y:44)

## Slide 9: 3f: The Branch Instruction
beq rs, rt, imm16
  mem[PC] Fetch the instruction from memory
  Equal = (R[rs] == R[rt]) Calculate branch condition
  if (Equal) Calculate the next instruction’s address
    PC = PC + 4 + ( SignExt(imm16) x 4 )
  else
    PC = PC + 4
op
rs
rt
immediate
0
16
21
26
31
6 bits
16 bits
5 bits
5 bits
Notes: How does the branch on equal instruction work?
Well it calculates the branch condition by subtracting the register selected by the Rt field from the register selected by the Rs field.
If the result of the subtraction is zero, then these two registers are equal and we take a branch. Otherwise, we keep going down the sequential path (PC = PC +4).
+1 = 65 min. (Y:45)

## Slide 10: Datapath for Branch Operations
beq rs, rt, imm16
Datapath generates condition (Equal)
op
rs
rt
immediate
0
16
21
26
31
6 bits
16 bits
5 bits
5 bits
Already have mux, adder, need special sign extender for PC, need equal compare (sub?)
Imm16
clk
PC
00
4
nPC_sel
PC Ext
Adder
Adder
Mux
Inst Address
32
ALUctr
clk
busW
RegWr
32
busA
32
busB
5
5
Rw
Ra
Rb
RegFile
Rs
Rt
ALU
5
=
Equal
Notes: The datapath for calculating the branch condition is rather simple.
All we have to do is feed the Rs and Rt fields of the instruction into the Ra and Rb inputs of the register file.
Bus A will then contain the value from the register selected by Rs.
And bus B will contain the value from the register selected by Rt.
The next thing to do is to ask the ALU to perform a subtract operation and feed the output Zero to the next address logic.
How does the next address logic block look like?
Well, before I show you that, let’s take a look at the binary arithmetics behind the program counter (PC).
+2 = 67 min. (Y:47)

## Slide 11: Instruction Fetch Unit including Branch
if (Equal == 1) then PC = PC + 4 + SignExt[imm16]*4 ; else PC = PC + 4
op
rs
rt
immediate
0
16
21
26
31
How to encode nPC_sel?
  Direct MUX select?
  Branch inst. / not branch inst.
Let’s pick 2nd option
Adr
Inst
Memory
nPC_sel
Instruction<31:0>
Equal
nPC_sel
Q: What logic gate?
imm16
clk
PC
00
4
PC Ext
Adder
Adder
Mux
0
1
MUX_ctrl
Equal
MUX_ctrl
Notes: Let’s look at the interesting case where the branch condition Zero is true (Zero = 1).
Well, if Zero is not asserted, we will have our boring case where PC + 1 is selected.
Anyway, with Branch = 1 and Zero = 1, the output of the second adder will be selected.
That is, we will add the seqential address, that is output of the first adder, to the sign extended version of the immediate field, to form the branch target address (output of 2nd adder).
With the control signal Jump set to zero, this branch target address will be written into the Program Counter register (PC) at the end of the clock cycle.
+2 = 35 min. (Y:15)

## Slide 12: Putting it All Together:A Single Cycle Datapath
Imm16
32
ALUctr
clk
busW
RegWr
32
32
busA
32
busB
5
5
Rw
Ra
Rb
RegFile
Rs
Rt
Rt
Rd
RegDst
Extender
32
16
Imm16
ALUSrc
ExtOp
MemtoReg
clk
Data_In
32
MemWr
Equal
Instruction<31:0>
<21:25>
<16:20>
<11:15>
<0:15>
Imm16
Rd
Rt
Rs
clk
PC
00
4
nPC_sel & Equal
PC Ext
Adr
Inst
Memory
Adder
Adder
Mux
0
1
0
1
=
ALU
0
1
WrEn
Adr
Data
Memory
5
Notes: So here is the single cycle datapath we just built.
If you push into the Instruction Fetch Unit, you will see the last slide showing the PC, the next address logic, and the Instruction Memory.
Here I have shown how we can get the Rt, Rs, Rd, and Imm16 fields out of the 32-bit instruction word.
The Rt, Rs, and Rd fields will go to the register file as register specifiers while the Imm16 field will go to the Extender where it is either Zero and Sign extended to 32 bits.
The signals ExtOp, ALUSrc, ALUctr, MemWr, MemtoReg, RegDst, RegWr, Branch, and Jump are control signals.
And I will show you how to generate them on Friday.
+2 = 80 min. (Z:00)

## Slide 13: Clickers/Peer Instruction
imm16
32
ALUctr
clk
busW
RegWr
32
32
busA
32
busB
5
5
Rw
Ra
Rb
RegFile
Rs
Rt
Rt
Rd
RegDst
Extender
32
16
imm16
ALUSrc
ExtOp
MemtoReg
clk
Data In
32
MemWr
Equal
Instruction<31:0>
<21:25>
<16:20>
<11:15>
<0:15>
Imm16
Rd
Rt
Rs
clk
PC
00
4
nPC_sel & Equal
PC Ext
Adr
Inst
Memory
Adder
Adder
Mux
0
1
0
1
=
ALU
0
1
WrEn
Adr
Data
Memory
5
What new instruction would need no new datapath hardware?
A: branch if reg==immediate
B: add two registers and branch if result zero
C: store with auto-increment of base address:
  sw rt, rs, offset // rs incremented by offset after store
D: shift left logical by two bits
Notes: B

## Slide 14: Administrivia
Project 2-2 released, due 3/08 (a Tuesday!)
Guerrilla Session:
  Synchronous Digital Systems
  Sat 3/05 1 - 3 PM @ 521 Cory

## Slide 15: Processor Design: 5 steps
  Step 1: Analyze instruction set to determine datapath requirements
  Meaning of each instruction is given by register transfers
  Datapath must include storage element for ISA registers
  Datapath must support each register transfer
  Step 2: Select set of datapath components & establish clock methodology
  Step 3: Assemble datapath components that meet the requirements
  Step 4: Analyze implementation of each instruction to determine setting of control points that realizes the register transfer
  Step 5: Assemble the control logic

## Slide 16: Datapath Control Signals
ExtOp: “zero”, “sign”
ALUsrc: 0  regB; 1  immed
ALUctr: “ADD”, “SUB”, “OR”
MemWr: 1  write memory
MemtoReg: 0  ALU; 1  Mem
RegDst: 0  “rt”; 1  “rd”
RegWr: 1  write register
32
ALUctr
clk
busW
RegWr
32
32
busA
32
busB
5
5
Rw
Ra
Rb
RegFile
Rs
Rt
Rt
Rd
RegDst
Extender
32
16
Imm16
ALUSrc
ExtOp
MemtoReg
clk
Data In
32
MemWr
0
1
0
1
ALU
0
1
WrEn
Adr
Data
Memory
5
Imm16
clk
PC
00
4
nPC_sel & Equal
PC Ext
Adder
Adder
Mux
Inst Address
0
1

## Slide 17: Given Datapath: RTL  Control
ALUctr
RegDst
ALUSrc
ExtOp
MemtoReg
MemWr
Instruction<31:0>
<21:25>
<16:20>
<11:15>
<0:15>
Imm16
Rd
Rs
Rt
nPC_sel
Adr
Inst
Memory
DATA PATH
Control
Op
<0:5>
Fun
RegWr
<26:31>

## Slide 18: RTL: The Add Instruction
add rd, rs, rt
  MEM[PC] Fetch the instruction from memory
  R[rd] = R[rs] + R[rt] The actual operation
  PC = PC + 4 Calculate the next instruction’s address
op
rs
rt
rd
shamt
funct
0
6
11
16
21
26
31
6 bits
6 bits
5 bits
5 bits
5 bits
5 bits
Notes: OK, let’s get on with today’s lecture by looking at the simple add instruction.
In terms of Register Transfer Language, this is what the Add instruction need to do.
First, you need to fetch the instruction from Memory.
Then you perform the actual add operation. More specifically:
(a) You add the contents of the register specified by the Rs and Rt fields of the instruction.
(b) Then you write the results to the register specified by the Rd field.
And finally, you need to update the program counter to point to the next instruction.
Now, let’s take a detail look at the datapath during various phase of this instruction.
+2 = 10 min. (X:50)

## Slide 19: Instruction Fetch Unit at the Beginning of Add
Fetch the instruction from Instruction memory: Instruction = MEM[PC]
  same for all instructions
imm16
clk
PC
00
4
nPC_sel
PC Ext
Adder
Adder
Mux
Inst Address
Inst
Memory
Instruction<31:0>

## Slide 20: Single Cycle Datapath during Add
R[rd] = R[rs] + R[rt]
op
rs
rt
rd
shamt
funct
0
6
11
16
21
26
31
32
ALUctr=ADD
clk
busW
RegWr=1
32
32
busA
32
busB
5
5
Rw
Ra
Rb
RegFile
Rs
Rt
Rt
Rd
RegDst=1
Extender
32
16
imm16
ALUSrc=0
ExtOp=x
MemtoReg=0
clk
Data In
32
MemWr=0
zero
0
1
0
1
=
ALU
0
1
WrEn
Adr
Data
Memory
5
Instruction<31:0>
<21:25>
<16:20>
<11:15>
<0:15>
Imm16
Rd
Rt
Rs
nPC_sel=+4
instr
fetch
unit
clk
Notes: This picture shows the activities at the main datapath during the execution of the Add or Subtract instructions.
The active parts of the datapath are shown in different color as well as thicker lines.
First of all, the Rs and Rt of the instructions are fed to the Ra and Rb address ports of the register file and cause the contents of registers specified by the Rs and Rt fields to be placed on busA and busB, respectively.
With the ALUctr signals set to either Add or Subtract, the ALU will perform the proper operation and with MemtoReg set to 0, the ALU output will be placed onto busW.
The control we are going to design will also set RegWr to 1 so that the result will be written to the register file at the end of the cycle.
Notice that ExtOp is don’t care because the Extender in this case can either do a SignExt or ZeroExt. We DON’T care because ALUSrc will be equal to 0--we are using busB.
The other control signals we need to worry about are:
(a) MemWr has to be set to zero because we do not want to write the memory.
(b) And Branch and Jump, we have to set to zero. Let me show you why.
+3 = 15 min. (X:55)

## Slide 21: Instruction Fetch Unit at End of Add
PC = PC + 4
  Same for all instructions except: Branch and Jump
imm16
clk
PC
00
4
nPC_sel=+4
PC Ext
Adder
Adder
Mux
Inst Address
Inst
Memory
Notes: This picture shows the control signals setting for the Instruction Fetch Unit at the end of the Add or Subtract instruction.
Both the Branch and Jump signals are set to 0.
Consequently, the output of the first adder, which implements PC plus 1, is selected through the two 2-to-1 mux and got placed into the input of the Program Counter register.
The Program Counter is updated to this new value at the next clock tick.
Notice that the Program Counter is updated at every cycle. Therefore it does not have a Write Enable signal to control the write.
Also, this picture is the same for or all instructions other than Branch andJjump.
Therefore I will only show this picture again for the Branch and Jump instructions and will not repeat this for all other instructions.
+2 = 17 min. (X:57)

## Slide 22: Single Cycle Datapath during Jump
32
ALUctr =
Clk
busW
RegWr =
32
32
busA
32
busB
5
5
5
Rw
Ra
Rb
32 x 32-bit
Registers
Rs
Rt
Rt
Rd
RegDst =
Extender
Mux
Mux
32
16
imm16
ALUSrc =
ExtOp =
Mux
MemtoReg =
Clk
Data In
WrEn
32
Adr
Data
Memory
32
MemWr =
ALU
Instruction
Fetch Unit
Clk
Zero
Instruction<31:0>
0
1
0
1
0
1
<21:25>
<16:20>
<11:15>
<0:15>
Imm16
Rd
Rt
Rs
New PC = { PC[31..28], target address, 00 }
nPC_sel=
op
target address
0
26
31
J-type
jump
25
Jump=
<0:25>
TA26
Notes: So how does the branch instruction work?
As far as the main datapath is concerned, it needs to calculate the branch condition. That is, it subtracts the register specified in the Rt field from the register specified in the Rs field and set the condition Zero accordingly.
In order to place the register values on busA and busB, we need to feed the Rs and Rt fields of the instruction to the Ra and Rb ports of the register file and set ALUSrc to 0.
Then we have to instruction the ALU to perform the subtract (ALUctr = sub) operation and set the Zero bit accordingly.
The Zero bit is sent to the Instruction Fetch Unit. I will show you the internal of the Instruction Fetch Unit in a second.
But before we leave this slide, I want you to notice that ExtOp, MemtoReg, and RegDst are don’t cares but RegWr and MemWr have to be ZERO to prevent any write to occur.
And finally, the controller needs to set the Branch signal to 1 so the Instruction Fetch Unit knows what to do. So now let’s take a look at the Instruction Fetch Unit.
+2 = 33 min. (Y:13)

## Slide 23: Single Cycle Datapath during Jump
32
ALUctr =x
Clk
busW
RegWr = 0
32
32
busA
32
busB
5
5
5
Rw
Ra
Rb
32 x 32-bit
Registers
Rs
Rt
Rt
Rd
RegDst = x
Extender
Mux
Mux
32
16
imm16
ALUSrc = x
ExtOp = x
Mux
MemtoReg = x
Clk
Data In
WrEn
32
Adr
Data
Memory
32
MemWr = 0
ALU
Instruction
Fetch Unit
Clk
Zero
Instruction<31:0>
0
1
0
1
0
1
<21:25>
<16:20>
<11:15>
<0:15>
Rd
Rt
Rs
New PC = { PC[31..28], target address, 00 }
nPC_sel=?
Jump=1
Imm16
<0:25>
TA26
op
target address
0
26
31
J-type
jump
25
Notes: So how does the branch instruction work?
As far as the main datapath is concerned, it needs to calculate the branch condition. That is, it subtracts the register specified in the Rt field from the register specified in the Rs field and set the condition Zero accordingly.
In order to place the register values on busA and busB, we need to feed the Rs and Rt fields of the instruction to the Ra and Rb ports of the register file and set ALUSrc to 0.
Then we have to instruction the ALU to perform the subtract (ALUctr = sub) operation and set the Zero bit accordingly.
The Zero bit is sent to the Instruction Fetch Unit. I will show you the internal of the Instruction Fetch Unit in a second.
But before we leave this slide, I want you to notice that ExtOp, MemtoReg, and RegDst are don’t cares but RegWr and MemWr have to be ZERO to prevent any write to occur.
And finally, the controller needs to set the Branch signal to 1 so the Instruction Fetch Unit knows what to do. So now let’s take a look at the Instruction Fetch Unit.
+2 = 33 min. (Y:13)

## Slide 24: Instruction Fetch Unit at the End of Jump
Adr
Inst
Memory
Adder
Adder
PC
Clk
00
Mux
4
nPC_sel
imm16
Instruction<31:0>
0
1
Zero
nPC_MUX_sel
New PC = { PC[31..28], target address, 00 }
op
target address
0
26
31
J-type
jump
25
How do we modify this to account for jumps?
Jump
Notes: Let’s look at the interesting case where the branch condition Zero is true (Zero = 1).
Well, if Zero is not asserted, we will have our boring case where PC + 1 is selected.
Anyway, with Branch = 1 and Zero = 1, the output of the second adder will be selected.
That is, we will add the seqential address, that is output of the first adder, to the sign extended version of the immediate field, to form the branch target address (output of 2nd adder).
With the control signal Jump set to zero, this branch target address will be written into the Program Counter register (PC) at the end of the clock cycle.
+2 = 35 min. (Y:15)

## Slide 25: Instruction Fetch Unit at the End of Jump
Adr
Inst
Memory
Adder
Adder
PC
Clk
00
Mux
4
nPC_sel
imm16
Instruction<31:0>
0
1
Zero
nPC_MUX_sel
New PC = { PC[31..28], target address, 00 }
op
target address
0
26
31
J-type
jump
25
Mux
1
0
Jump
TA
4 (MSBs)
00
Query
Can Zero still get asserted?
Does nPC_sel need to be 0?
  If not, what?
26
Notes: Let’s look at the interesting case where the branch condition Zero is true (Zero = 1).
Well, if Zero is not asserted, we will have our boring case where PC + 1 is selected.
Anyway, with Branch = 1 and Zero = 1, the output of the second adder will be selected.
That is, we will add the seqential address, that is output of the first adder, to the sign extended version of the immediate field, to form the branch target address (output of 2nd adder).
With the control signal Jump set to zero, this branch target address will be written into the Program Counter register (PC) at the end of the clock cycle.
+2 = 35 min. (Y:15)

## Slide 26: Clicker Question
Which of the following is TRUE?
The clock can have a shorter period for instructions that don’t use memory
The ALU is used to set PC to PC+4 when necessary
Worst-delay path in Instruction Fetch unit is Add+mux delay
The CPU’s control needs only opcode to determine the next PC value to select
npc_sel affects the next PC address on a jump
Notes: D

## Slide 27: Summary of the Control Signals (1/2)
inst Register Transfer
add R[rd]  R[rs] + R[rt]; PC  PC + 4
ALUsrc=RegB, ALUctr=“ADD”, RegDst=rd, RegWr, nPC_sel=“+4”
sub R[rd]  R[rs] – R[rt]; PC  PC + 4
ALUsrc=RegB, ALUctr=“SUB”, RegDst=rd, RegWr, nPC_sel=“+4”
ori R[rt]  R[rs] + zero_ext(Imm16); PC  PC + 4
ALUsrc=Im, Extop=“Z”, ALUctr=“OR”, RegDst=rt,RegWr, nPC_sel=“+4”
lw R[rt]  MEM[ R[rs] + sign_ext(Imm16)]; PC  PC + 4
ALUsrc=Im, Extop=“sn”, ALUctr=“ADD”, MemtoReg, RegDst=rt, RegWr, nPC_sel = “+4”
sw MEM[ R[rs] + sign_ext(Imm16)]  R[rs]; PC  PC + 4
ALUsrc=Im, Extop=“sn”, ALUctr = “ADD”, MemWr, nPC_sel = “+4”
beq if (R[rs] == R[rt]) then PC  PC + sign_ext(Imm16)] || 00 else PC  PC + 4
nPC_sel = “br”, ALUctr = “SUB”

## Slide 28: Summary of the Control Signals (2/2)
add
sub
ori
lw
sw
beq
jump
RegDst
ALUSrc
MemtoReg
RegWrite
MemWrite
nPCsel
Jump
ExtOp
ALUctr<2:0>
1
0
0
1
0
0
0
x
Add
1
0
0
1
0
0
0
x
Subtract
0
1
0
1
0
0
0
0
Or
0
1
1
1
0
0
0
1
Add
x
1
x
0
1
0
0
1
Add
x
0
x
0
0
1
0
x
Subtract
x
x
x
0
0
?
1
x
x
op
target address
op
rs
rt
rd
shamt
funct
0
6
11
16
21
26
31
op
rs
rt
immediate
R-type
I-type
J-type
add, sub
ori, lw, sw, beq
jump
func
op
00 0000
00 0000
00 1101
10 0011
10 1011
00 0100
00 0010
Appendix A
10 0000
See
10 0010
We Don’t Care :-)
Notes: Here is a table summarizing the control signals setting for the seven (add, sub, ...) instructions we have looked at.
Instead of showing you the exact bit values for the ALU control (ALUctr), I have used the symbolic values here.
The first two columns are unique in the sense that they are R-type instrucions and in order to uniquely identify them, we need to look at BOTH the op field as well as the func fiels.
Ori, lw, sw, and branch on equal are I-type instructions and Jump is J-type. They all can be uniquely idetified by looking at the opcode field alone.
Now let’s take a more careful look at the first two columns. Notice that they are identical except the last row.
So we can combine these two rows here if we can “delay” the generation of ALUctr signals.
This lead us to something call “local decoding.”
+3 = 42 min. (Y:22)

## Slide 29: Boolean Expressions for Controller
RegDst = add + sub ALUSrc = ori + lw + sw MemtoReg = lw RegWrite = add + sub + ori + lw MemWrite = sw nPCsel = beq Jump = jump ExtOp = lw + sw ALUctr[0] = sub + beq (assume ALUctr is 00 ADD, 01 SUB, 10 OR) ALUctr[1] = or
Where:
rtype = ~op5  ~op4  ~op3  ~op2  ~op1  ~op0, ori = ~op5  ~op4  op3  op2  ~op1  op0 lw = op5  ~op4  ~op3  ~op2  op1  op0 sw = op5  ~op4  op3  ~op2  op1  op0 beq = ~op5  ~op4  ~op3  op2  ~op1  ~op0 jump = ~op5  ~op4  ~op3  ~op2  op1  ~op0
add = rtype  func5  ~func4  ~func3  ~func2  ~func1  ~func0 sub = rtype  func5  ~func4  ~func3  ~func2  func1  ~func0
How do we implement this in gates?
Notes: ADD 0000 00ss ssst tttt dddd d000 0010 0000
SUB 0000 00ss ssst tttt dddd d000 0010 0010
ORI 0011 01ss ssst tttt iiii iiii iiii iiii
LW 1000 11ss ssst tttt iiii iiii iiii iiii
SW 1010 11ss ssst tttt iiii iiii iiii iiii
BEQ 0001 00ss ssst tttt iiii iiii iiii iiii
JUMP 0000 10ii iiii iiii iiii iiii iiii iiii

## Slide 30: Controller Implementation
add
sub
ori
lw
sw
beq
jump
RegDst
ALUSrc
MemtoReg
RegWrite
MemWrite
nPCsel
Jump
ExtOp
ALUctr[0]
ALUctr[1]
“AND” logic
“OR” logic
opcode
func

## Slide 31: P&H Figure 4.17

## Slide 32: Summary: Single-cycle Processor
Five steps to design a processor:
  1. Analyze instruction set  datapath requirements
  2. Select set of datapath components & establish clock methodology
  3. Assemble datapath meeting the requirements
  4. Analyze implementation of each instruction to determine setting of control points that effects the register transfer.
  5. Assemble the control logic
    Formulate Logic Equations
    Design Circuits
Control
Datapath
Memory
Processor
Input
Output

## Slide 33: Single Cycle Performance
Assume time for actions are
  100ps for register read or write; 200ps for other events
Clock period is?
Instr | Instr fetch | Register read | ALU op | Memory access | Register write | Total time
lw | 200ps | 100 ps | 200ps | 200ps | 100 ps | 800ps
sw | 200ps | 100 ps | 200ps | 200ps |  | 700ps
R-format | 200ps | 100 ps | 200ps |  | 100 ps | 600ps
beq | 200ps | 100 ps | 200ps |  |  | 500ps
Clock rate (cycles/second = Hz) = 1/Period (seconds/cycle)
Notes: 1.25 GHz

## Slide 34: Single Cycle Performance
Assume time for actions are
  100ps for register read or write; 200ps for other events
Clock period is?
Instr | Instr fetch | Register read | ALU op | Memory access | Register write | Total time
lw | 200ps | 100 ps | 200ps | 200ps | 100 ps | 800ps
sw | 200ps | 100 ps | 200ps | 200ps |  | 700ps
R-format | 200ps | 100 ps | 200ps |  | 100 ps | 600ps
beq | 200ps | 100 ps | 200ps |  |  | 500ps
What can we do to improve clock rate?
Will this improve performance as well?
  Want increased clock rate to mean faster programs
Notes: 1.25 GHz

## Slide 35: Levels of Representation/Interpretation
lw $t0, 0($2)
lw $t1, 4($2)
sw $t1, 0($2)
sw $t0, 4($2)
High Level Language Program (e.g., C)
Assembly Language Program (e.g., MIPS)
Machine Language Program (MIPS)
Hardware Architecture Description (e.g., block diagrams)
Compiler
Assembler
Machine Interpretation
temp = v[k];
v[k] = v[k+1];
v[k+1] = temp;
0000 1001 1100 0110 1010 1111 0101 1000
1010 1111 0101 1000 0000 1001 1100 0110
1100 0110 1010 1111 0101 1000 0000 1001
0101 1000 0000 1001 1100 0110 1010 1111
Logic Circuit Description (Circuit Schematic Diagrams)
Architecture Implementation
Anything can be represented as a number, i.e., data or instructions

## Slide 36: No More Magic!
CS61A
CS61B
CS61C ✔
CS61C ✔
CS61C ✔
CS61C 
CS61C ✔
EE40
Phys 7B
I/O system
Processor
Compiler
Operating
System
(Mac OSX)
Application (ex: browser)
Digital Design
Circuit Design
Instruction Set Architecture
Datapath & Control
transistors
Memory
Hardware
Software
Assembler