## Slide 1: CS 61C: Great Ideas in Computer Architecture Control and Pipelining
Instructors:
Vladimir Stojanovic and Nicholas Weaver
http://inst.eecs.Berkeley.edu/~cs61c/sp16

## Slide 2: Datapath Control Signals
ExtOp: “zero”, “sign”
ALUsrc: 0  regB; 1  immed
ALUctr: “ADD”, “SUB”, “OR”
MemWr: 1  write memory
MemtoReg: 0  ALU; 1  Mem
RegDst: 0  “rt”; 1  “rd”
RegWr: 1  write register
32
ALUctr
clk
busW
RegWr
32
32
busA
32
busB
5
5
Rw
Ra
Rb
RegFile
Rs
Rt
Rt
Rd
RegDst
Extender
32
16
Imm16
ALUSrc
ExtOp
MemtoReg
clk
Data In
32
MemWr
0
1
0
1
ALU
0
1
WrEn
Adr
Data
Memory
5
Imm16
clk
PC
00
4
nPC_sel & Equal
PC Ext
Adder
Adder
Mux
Inst Address
0
1

## Slide 3: Summary of the Control Signals (1/2)
inst Register Transfer
add R[rd]  R[rs] + R[rt]; PC  PC + 4
ALUsrc=RegB, ALUctr=“ADD”, RegDst=rd, RegWr, nPC_sel=“+4”
sub R[rd]  R[rs] – R[rt]; PC  PC + 4
ALUsrc=RegB, ALUctr=“SUB”, RegDst=rd, RegWr, nPC_sel=“+4”
ori R[rt]  R[rs] + zero_ext(Imm16); PC  PC + 4
ALUsrc=Im, Extop=“Z”, ALUctr=“OR”, RegDst=rt,RegWr, nPC_sel=“+4”
lw R[rt]  MEM[ R[rs] + sign_ext(Imm16)]; PC  PC + 4
ALUsrc=Im, Extop=“sn”, ALUctr=“ADD”, MemtoReg, RegDst=rt, RegWr, nPC_sel = “+4”
sw MEM[ R[rs] + sign_ext(Imm16)]  R[rs]; PC  PC + 4
ALUsrc=Im, Extop=“sn”, ALUctr = “ADD”, MemWr, nPC_sel = “+4”
beq if (R[rs] == R[rt]) then PC  PC + sign_ext(Imm16)] || 00 else PC  PC + 4
nPC_sel = “br”, ALUctr = “SUB”

## Slide 4: Summary of the Control Signals (2/2)
add
sub
ori
lw
sw
beq
jump
RegDst
ALUSrc
MemtoReg
RegWrite
MemWrite
nPCsel
Jump
ExtOp
ALUctr<2:0>
1
0
0
1
0
0
0
x
Add
1
0
0
1
0
0
0
x
Subtract
0
1
0
1
0
0
0
0
Or
0
1
1
1
0
0
0
1
Add
x
1
x
0
1
0
0
1
Add
x
0
x
0
0
1
0
x
Subtract
x
x
x
0
0
?
1
x
x
op
target address
op
rs
rt
rd
shamt
funct
0
6
11
16
21
26
31
op
rs
rt
immediate
R-type
I-type
J-type
add, sub
ori, lw, sw, beq
jump
func
op
00 0000
00 0000
00 1101
10 0011
10 1011
00 0100
00 0010
Appendix A
10 0000
See
10 0010
We Don’t Care :-)
Notes: Here is a table summarizing the control signals setting for the seven (add, sub, ...) instructions we have looked at.
Instead of showing you the exact bit values for the ALU control (ALUctr), I have used the symbolic values here.
The first two columns are unique in the sense that they are R-type instrucions and in order to uniquely identify them, we need to look at BOTH the op field as well as the func fiels.
Ori, lw, sw, and branch on equal are I-type instructions and Jump is J-type. They all can be uniquely idetified by looking at the opcode field alone.
Now let’s take a more careful look at the first two columns. Notice that they are identical except the last row.
So we can combine these two rows here if we can “delay” the generation of ALUctr signals.
This lead us to something call “local decoding.”
+3 = 42 min. (Y:22)

## Slide 5: Boolean Expressions for Controller
RegDst = add + sub ALUSrc = ori + lw + sw MemtoReg = lw RegWrite = add + sub + ori + lw MemWrite = sw nPCsel = beq Jump = jump ExtOp = lw + sw ALUctr[0] = sub + beq (assume ALUctr is 00 ADD, 01 SUB, 10 OR) ALUctr[1] = or
Where:
rtype = ~op5  ~op4  ~op3  ~op2  ~op1  ~op0, ori = ~op5  ~op4  op3  op2  ~op1  op0 lw = op5  ~op4  ~op3  ~op2  op1  op0 sw = op5  ~op4  op3  ~op2  op1  op0 beq = ~op5  ~op4  ~op3  op2  ~op1  ~op0 jump = ~op5  ~op4  ~op3  ~op2  op1  ~op0
add = rtype  func5  ~func4  ~func3  ~func2  ~func1  ~func0 sub = rtype  func5  ~func4  ~func3  ~func2  func1  ~func0
How do we implement this in gates?
Notes: ADD 0000 00ss ssst tttt dddd d000 0010 0000
SUB 0000 00ss ssst tttt dddd d000 0010 0010
ORI 0011 01ss ssst tttt iiii iiii iiii iiii
LW 1000 11ss ssst tttt iiii iiii iiii iiii
SW 1010 11ss ssst tttt iiii iiii iiii iiii
BEQ 0001 00ss ssst tttt iiii iiii iiii iiii
JUMP 0000 10ii iiii iiii iiii iiii iiii iiii

## Slide 6: Controller Implementation
add
sub
ori
lw
sw
beq
jump
RegDst
ALUSrc
MemtoReg
RegWrite
MemWrite
nPCsel
Jump
ExtOp
ALUctr[0]
ALUctr[1]
“AND” logic
“OR” logic
opcode
func

## Slide 7: P&H Figure 4.17

## Slide 8: Summary: Single-cycle Processor
Five steps to design a processor:
  1. Analyze instruction set  datapath requirements
  2. Select set of datapath components & establish clock methodology
  3. Assemble datapath meeting the requirements
  4. Analyze implementation of each instruction to determine setting of control points that effects the register transfer.
  5. Assemble the control logic
    Formulate Logic Equations
    Design Circuits
Control
Datapath
Memory
Processor
Input
Output

## Slide 9: Single Cycle Performance
Assume time for actions are
  100ps for register read or write; 200ps for other events
Clock period is?
Instr | Instr fetch | Register read | ALU op | Memory access | Register write | Total time
lw | 200ps | 100 ps | 200ps | 200ps | 100 ps | 800ps
sw | 200ps | 100 ps | 200ps | 200ps |  | 700ps
R-format | 200ps | 100 ps | 200ps |  | 100 ps | 600ps
beq | 200ps | 100 ps | 200ps |  |  | 500ps
Clock rate (cycles/second = Hz) = 1/Period (seconds/cycle)
Notes: 1.25 GHz

## Slide 10: Single Cycle Performance
Assume time for actions are
  100ps for register read or write; 200ps for other events
Clock period is?
Instr | Instr fetch | Register read | ALU op | Memory access | Register write | Total time
lw | 200ps | 100 ps | 200ps | 200ps | 100 ps | 800ps
sw | 200ps | 100 ps | 200ps | 200ps |  | 700ps
R-format | 200ps | 100 ps | 200ps |  | 100 ps | 600ps
beq | 200ps | 100 ps | 200ps |  |  | 500ps
What can we do to improve clock rate?
Will this improve performance as well?
  Want increased clock rate to mean faster programs
Notes: 1.25 GHz

## Slide 11: Levels of Representation/Interpretation
lw $t0, 0($2)
lw $t1, 4($2)
sw $t1, 0($2)
sw $t0, 4($2)
High Level Language Program (e.g., C)
Assembly Language Program (e.g., MIPS)
Machine Language Program (MIPS)
Hardware Architecture Description (e.g., block diagrams)
Compiler
Assembler
Machine Interpretation
temp = v[k];
v[k] = v[k+1];
v[k+1] = temp;
0000 1001 1100 0110 1010 1111 0101 1000
1010 1111 0101 1000 0000 1001 1100 0110
1100 0110 1010 1111 0101 1000 0000 1001
0101 1000 0000 1001 1100 0110 1010 1111
Logic Circuit Description (Circuit Schematic Diagrams)
Architecture Implementation
Anything can be represented as a number, i.e., data or instructions

## Slide 12: No More Magic!
CS61A
CS61B
CS61C ✔
CS61C ✔
CS61C ✔
CS61C 
CS61C ✔
EE40
Phys 7B
I/O system
Processor
Compiler
Operating
System
(Mac OSX)
Application (ex: browser)
Digital Design
Circuit Design
Instruction Set Architecture
Datapath & Control
transistors
Memory
Hardware
Software
Assembler

## Slide 13: Administrivia
Project 2-2 due 3/8 @ 23:59:59 (Tue)
Guerrilla Sessions: MIPS CPU
  Wed 3/09 3 - 5 PM @ 241 Cory
  Sat 3/12 1 - 3 PM @ 651 @ 611 Soda

## Slide 14: Gotta Do Laundry
Ann, Brian, Cathy, Dave each have one load of clothes to wash, dry, fold, and put away
  Washer takes 30 minutes
  Dryer takes 30 minutes
  “Folder” takes 30 minutes
  “Stasher” takes 30 minutes to put clothes into drawers
A
B
C
D

## Slide 15: Sequential Laundry
Sequential laundry takes 8 hours for 4 loads
T
a
s
k
O
r
d
e
r
B
C
D
A
30
Time
30
30
30
30
30
30
30
30
30
30
30
30
30
30
30
6 PM
7
8
9
10
11
12
1
2 AM

## Slide 16: Pipelined Laundry
Pipelined laundry takes 3.5 hours for 4 loads!
T
a
s
k
O
r
d
e
r
B
C
D
A
12
2 AM
6 PM
7
8
9
10
11
1
Time
30
30
30
30
30
30
30

## Slide 17: Pipelining Lessons (1/2)
Pipelining doesn’t help latency of single task, it helps throughput of entire workload
Multiple tasks operating simultaneously using different resources
Potential speedup = Number pipe stages
Time to “fill” pipeline and time to “drain” it reduces speedup: 2.3x (8/3.5) v. 4x (8/2) in this example
6 PM
7
8
9
Time
B
C
D
A
30
30
30
30
30
30
30
T
a
s
k
O
r
d
e
r

## Slide 18: Pipelining Lessons (2/2)
Suppose new Washer takes 20 minutes, new Stasher takes 20 minutes. How much faster is pipeline?
Pipeline rate limited by slowest pipeline stage
Unbalanced lengths of pipe stages reduces speedup
6 PM
7
8
9
Time
B
C
D
A
30
30
30
30
30
30
30
T
a
s
k
O
r
d
e
r

## Slide 19: Execution Steps in MIPS Datapath
1) IFtch: Instruction Fetch, Increment PC
2) Dcd: Instruction Decode, Read Registers
3) Exec: Mem-ref: Calculate Address Arith-log: Perform Operation
4) Mem: Load: Read Data from Memory Store: Write Data to Memory
5) WB: Write Data Back to Register

## Slide 20: Single Cycle Datapath
PC
instruction
memory
+4
rt
rs
rd
registers
ALU
Data
memory
imm
1. Instruction
Fetch
2. Decode/
Register Read
3. Execute
4. Memory
5. Write Back

## Slide 21: Pipeline registers
PC
instruction
memory
+4
rt
rs
rd
registers
ALU
Data
memory
imm
1. Instruction
Fetch
2. Decode/
Register Read
3. Execute
4. Memory
5. Write Back
Need registers between stages
  To hold information produced in previous cycle

## Slide 22: More Detailed Pipeline

## Slide 23: IF for Load, Store, …

## Slide 24: ID for Load, Store, …

## Slide 25: EX for Load

## Slide 26: MEM for Load

## Slide 27: WB for Load – Oops!
Wrong register number!

## Slide 28: Corrected Datapath for Load

## Slide 29: Pipelined Execution Representation
Every instruction must take same number of steps, so some stages will idle
  e.g. MEM stage for any arithmetic instruction
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
Time
Notes: Each instruction has identical latency!

## Slide 30: Graphical Pipeline Diagrams
Use datapath figure below to represent pipeline:
IF
ID
EX
Mem
WB
ALU
I$
Reg
D$
Reg
1. Instruction
Fetch
2. Decode/
Register Read
3. Execute
4. Memory
5. Write
Back
PC
instruction
memory
+4
Register
File
rt
rs
rd
ALU
Data
memory
imm
MUX

## Slide 31: Graphical Pipeline Representation
I
n
s
t
r
O
r
d
e
r
Load
Add
Store
Sub
Or
I$
Time (clock cycles)
I$
ALU
Reg
Reg
I$
D$
ALU
ALU
Reg
D$
Reg
I$
D$
Reg
ALU
Reg
Reg
Reg
D$
Reg
D$
ALU
RegFile: left half is write, right half is read
Reg
I$

## Slide 32: Pipelining Performance (1/3)
Use Tc (“time between completion of instructions”) to measure speedup
  Equality only achieved if stages are balanced (i.e. take the same amount of time)
If not balanced, speedup is reduced
Speedup due to increased throughput
  Latency for each instruction does not decrease

## Slide 33: Pipelining Performance (2/3)
Assume time for stages is
  100ps for register read or write
  200ps for other stages
What is pipelined clock rate?
  Compare pipelined datapath with single-cycle datapath
Instr | Instr fetch | Register read | ALU op | Memory access | Register write | Total time
lw | 200ps | 100 ps | 200ps | 200ps | 100 ps | 800ps
sw | 200ps | 100 ps | 200ps | 200ps |  | 700ps
R-format | 200ps | 100 ps | 200ps |  | 100 ps | 600ps
beq | 200ps | 100 ps | 200ps |  |  | 500ps

## Slide 34: Pipelining Performance (3/3)
Single-cycle
Tc = 800 ps
f = 1.25GHz
Pipelined
Tc = 200 ps
f = 5GHz
Notes: Here using Tc as “time between completion of instructions.”

## Slide 35: Clicker/Peer Instruction
Logic in some stages takes 200ps and in some 100ps. Clk-Q delay is 30ps and setup-time is 20ps. What is the maximum clock frequency at which a pipelined design can operate?
A: 10GHz
B: 5GHz
C: 6.7GHz
D: 4.35GHz
E: 4GHz