## Slide 1: CS 61C: Great Ideas in Computer Architecture Pipelining and Hazards
Instructors:
Vladimir Stojanovic and Nicholas Weaver
http://inst.eecs.Berkeley.edu/~cs61c/sp16

## Slide 2: Pipelined Execution Representation
Every instruction must take same number of steps, so some stages will idle
  e.g. MEM stage for any arithmetic instruction
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
Time
Notes: Each instruction has identical latency!

## Slide 3: Graphical Pipeline Diagrams
Use datapath figure below to represent pipeline:
IF
ID
EX
Mem
WB
ALU
I$
Reg
D$
Reg
1. Instruction
Fetch
2. Decode/
Register Read
3. Execute
4. Memory
5. Write
Back
PC
instruction
memory
+4
Register
File
rt
rs
rd
ALU
Data
memory
imm
MUX

## Slide 4: Graphical Pipeline Representation
I
n
s
t
r
O
r
d
e
r
Load
Add
Store
Sub
Or
I$
Time (clock cycles)
I$
ALU
Reg
Reg
I$
D$
ALU
ALU
Reg
D$
Reg
I$
D$
Reg
ALU
Reg
Reg
Reg
D$
Reg
D$
ALU
RegFile: left half is write, right half is read
Reg
I$

## Slide 5: Pipelining Performance (1/3)
Use Tc (“time between completion of instructions”) to measure speedup
  Equality only achieved if stages are balanced (i.e. take the same amount of time)
If not balanced, speedup is reduced
Speedup due to increased throughput
  Latency for each instruction does not decrease
  In fact, latency must increase as the pipeline registers themselves add delay (why Nick's Ph.D. thesis has a "this was a stupid idea" chapter)

## Slide 6: Pipelining Performance (2/3)
Assume time for stages is
  100ps for register read or write
  200ps for other stages
What is pipelined clock rate?
  Compare pipelined datapath with single-cycle datapath
Instr | Instr fetch | Register read | ALU op | Memory access | Register write | Total time
lw | 200ps | 100 ps | 200ps | 200ps | 100 ps | 800ps
sw | 200ps | 100 ps | 200ps | 200ps |  | 700ps
R-format | 200ps | 100 ps | 200ps |  | 100 ps | 600ps
beq | 200ps | 100 ps | 200ps |  |  | 500ps

## Slide 7: Pipelining Performance (3/3)
Single-cycle
Tc = 800 ps
f = 1.25GHz
Pipelined
Tc = 200 ps
f = 5GHz
Notes: Here using Tc as “time between completion of instructions.”

## Slide 8: Clicker/Peer Instruction
Logic in some stages takes 200ps and in some 100ps. Clk-Q delay is 30ps and setup-time is 20ps. What is the maximum clock frequency at which a pipelined design can operate?
A: 10GHz
B: 5GHz
C: 6.7GHz
D: 4.35GHz
E: 4GHz

## Slide 9: Administrivia…
Start on Project 3-1 now
  Logisim can be a bit, well, tedious: The project isn't necessarily hard but it will take a fair amount of time
    Alternative would be to have you learn yet another programming language in this class!
  For reference, it took Nick about an hour of tediously drawing lines for his solution to part 1
    5 minutes to know what he wanted to do…
    And 55 minutes to actually do it. 

## Slide 10: Pipelining Hazards
A hazard is a situation that prevents starting the next instruction in the next clock cycle
Structural hazard
  A required resource is busy (e.g. needed in multiple stages)
Data hazard
  Data dependency between instructions
  Need to wait for previous instruction to complete its data read/write
Control hazard
  Flow of execution depends on previous instruction

## Slide 11: Structural Hazard #1: Single Memory
I$
Load
Instr 1
Instr 2
Instr 3
Instr 4
ALU
I$
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
ALU
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
I
n
s
t
r
O
r
d
e
r
Time (clock cycles)
Trying to read same memory twice in same clock cycle

## Slide 12: Solving Structural Hazard #1 with Caches

## Slide 13: Structural Hazard #2: Registers (1/2)
I$
Load
Instr 1
Instr 2
Instr 3
Instr 4
ALU
I$
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
ALU
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
I
n
s
t
r
O
r
d
e
r
Time (clock cycles)
Can we read and write to registers simultaneously?

## Slide 14: Structural Hazard #2: Registers (2/2)
Two different solutions have been used:
  Split RegFile access in two: Write during 1st half and Read during 2nd half of each clock cycle
    Possible because RegFile access is VERY fast (takes less than half the time of ALU stage)
  Build RegFile with independent read and write ports (E.g. for your project)
Conclusion: Read and Write to registers during same clock cycle is okay
Structural hazards can (almost) always be removed by adding hardware resources

## Slide 15: Data Hazards (1/2)
Consider the following sequence of instructions:
add $t0, $t1, $t2
sub $t4, $t0, $t3
and $t5, $t0, $t6
or $t7, $t0, $t8
xor $t9, $t0, $t10

## Slide 16: 2. Data Hazards (2/2)
Data-flow backwards in time are hazards
sub $t4,$t0,$t3
ALU
I$
Reg
D$
Reg
and $t5,$t0,$t6
ALU
I$
Reg
D$
Reg
or $t7,$t0,$t8
I$
ALU
Reg
D$
Reg
xor $t9,$t0,$t10
ALU
I$
Reg
D$
Reg
add $t0,$t1,$t2
IF
ID/RF
EX
MEM
WB
ALU
I$
Reg
D$
Reg
I
n
s
t
r
O
r
d
e
r
Time (clock cycles)

## Slide 17: Data Hazard Solution: Forwarding
Forward result as soon as it is available
  OK that it’s not stored in RegFile yet
sub $t4,$t0,$t3
ALU
I$
Reg
D$
Reg
and $t5,$t0,$t6
ALU
I$
Reg
D$
Reg
or $t7,$t0,$t8
I$
ALU
Reg
D$
Reg
xor $t9,$t0,$t10
ALU
I$
Reg
D$
Reg
add $t0,$t1,$t2
IF
ID/RF
EX
MEM
WB
ALU
I$
Reg
D$
Reg

## Slide 18: Datapath for Forwarding (1/2)
What changes need to be made here?

## Slide 19: Datapath for Forwarding (2/2)
Handled by forwarding unit
Notes: Scan figure 4.54 on p. 368.

## Slide 20: Datapath and Control
The control signals are pipelined, too

## Slide 21: Data Hazard: Loads (1/3)
Recall: Dataflow backwards in time are hazards
Can’t solve all cases with forwarding
  Must stall instruction dependent on load, then forward (more hardware)
sub $t3,$t0,$t2
ALU
I$
Reg
D$
Reg
lw $t0,0($t1)
IF
ID/RF
EX
MEM
WB
ALU
I$
Reg
D$
Reg

## Slide 22: Data Hazard: Loads (2/3)
Stalled instruction converted to “bubble”, acts like nop
sub $t3,$t0,$t2
and $t5,$t0,$t4
or $t7,$t0,$t6
I$
ALU
Reg
D$
lw $t0, 0($t1)
ALU
I$
Reg
D$
Reg
bubble
bubble
bubble
ALU
I$
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
sub $t3,$t0,$t2
I$
Reg
First two pipe stages stall by repeating stage one cycle later

## Slide 23: Data Hazard: Loads (4/4)
Slot after a load is called a load delay slot
  If that instruction uses the result of the load, then the hardware interlock will stall it for one cycle
  Letting the hardware stall the instruction in the delay slot is equivalent to putting an explicit nop in the slot (except the latter uses more code space)
Idea: Let the compiler put an unrelated instruction in that slot  no stall!

## Slide 24: Clicker Question
How many cycles (pipeline fill+process+drain) does it take to execute the following code?
lw $t1, 0($t0)
lw $t2, 4($t0)
add $t3, $t1, $t2
sw $t3, 12($t0)
lw $t4, 8($t0)
add $t5, $t1, $t4
sw $t5, 16($t0)
7
9
11
13
14

## Slide 25: Code Scheduling to Avoid Stalls
Reorder code to avoid use of load result in the next instruction!
MIPS code for D=A+B; E=A+C;
# Method 1:
lw $t1, 0($t0)
lw $t2, 4($t0)
add $t3, $t1, $t2
sw $t3, 12($t0)
lw $t4, 8($t0)
add $t5, $t1, $t4
sw $t5, 16($t0)
# Method 2:
lw $t1, 0($t0)
lw $t2, 4($t0)
lw $t4, 8($t0)
add $t3, $t1, $t2
sw $t3, 12($t0)
add $t5, $t1, $t4
sw $t5, 16($t0)
Stall!
Stall!
13 cycles
11 cycles

## Slide 26: 3. Control Hazards
Branch determines flow of control
  Fetching next instruction depends on branch outcome
  Pipeline can’t always fetch correct instruction
    Still working on ID stage of branch
BEQ, BNE in MIPS pipeline
Simple solution Option 1: Stall on every branch until branch condition resolved
  Would add 2 bubbles/clock cycles for every Branch! (~ 20% of instructions executed)

## Slide 27: Stall => 2 Bubbles/Clocks
Where do we do the compare for the branch?
I$
beq
Instr 1
Instr 2
Instr 3
Instr 4
ALU
I$
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
ALU
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
I
n
s
t
r.
O
r
d
e
r
Time (clock cycles)

## Slide 28: Control Hazard: Branching
Optimization #1:
  Insert special branch comparator in Stage 2
  As soon as instruction is decoded (Opcode identifies it as a branch), immediately make a decision and set the new value of the PC
  Benefit: since branch is complete in Stage 2, only one unnecessary instruction is fetched, so only one no-op is needed
  Side Note: means that branches are idle in Stages 3, 4 and 5

## Slide 29: One Clock Cycle Stall
Branch comparator moved to Decode stage.
I$
beq
Instr 1
Instr 2
Instr 3
Instr 4
ALU
I$
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
ALU
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
I
n
s
t
r.
O
r
d
e
r
Time (clock cycles)

## Slide 30: Control Hazards: Branching
Option 2: Predict outcome of a branch, fix up if guess wrong
  Must cancel all instructions in pipeline that depended on guess that was wrong
  This is called “flushing” the pipeline
Simplest hardware if we predict that all branches are NOT taken
  Why?

## Slide 31: Control Hazards: Branching
Option #3: Redefine branches
  Old definition: if we take the branch, none of the instructions after the branch get executed by accident
  New definition: whether or not we take the branch, the single instruction immediately following the branch gets executed (the branch-delay slot)
Delayed Branch means we always execute inst after branch
This optimization is used with MIPS

## Slide 32: Example: Nondelayed vs. Delayed Branch
add $1, $2, $3
sub $4, $5, $6
beq $1, $4, Exit
or $8, $9, $10
xor $10, $1, $11
Nondelayed Branch
add $1, $2,$3
sub $4, $5, $6
beq $1, $4, Exit
or $8, $9, $10
xor $10, $1, $11
Delayed Branch
Exit:
Exit:

## Slide 33: Control Hazards: Branching
Notes on Branch-Delay Slot
  Worst-Case Scenario: put a nop in the branch-delay slot
  Better Case: place some instruction preceding the branch in the branch-delay slot—as long as the changed doesn’t affect the logic of program
    Re-ordering instructions is common way to speed up programs
    Compiler usually finds such an instruction 50% of time
    Jumps also have a delay slot …

## Slide 34: Greater Instruction-Level Parallelism (ILP)
Deeper pipeline (5 => 10 => 15 stages)
  Less work per stage  shorter clock cycle
Multiple issue “superscalar”
  Replicate pipeline stages  multiple pipelines
  Start multiple instructions per clock cycle
  CPI < 1, so use Instructions Per Cycle (IPC)
  E.g., 4GHz 4-way multiple-issue
    16 BIPS, peak CPI = 0.25, peak IPC = 4
  But dependencies reduce this in practice
“Out-of-Order” execution
  Reorder instructions dynamically in hardware to reduce impact of hazards
"Multithreading"
  Share functional units between independent threads of execution
Take CS152 next to learn about these techniques!

## Slide 35: In Conclusion
Pipelining increases throughput by overlapping execution of multiple instructions in different pipestages
Pipestages should be balanced for highest clock rate
Three types of pipeline hazard limit performance
  Structural (always fixable with more hardware)
  Data (use interlocks or bypassing to resolve)
  Control (reduce impact with branch prediction or branch delay slots)