## Slide 1: CS 61C: Great Ideas in Computer Architecture Floating Point Arithmetic
Instructors:
Vladimir Stojanovic & Nicholas Weaver
http://inst.eecs.berkeley.edu/~cs61c/

## Slide 2: New-School Machine Structures (It’s a bit more complicated!)
Parallel Requests
  Assigned to computer
  e.g., Search “Katz”
Parallel Threads
  Assigned to core
  e.g., Lookup, Ads
Parallel Instructions
  >1 instruction @ one time
  e.g., 5 pipelined instructions
Parallel Data
  >1 data item @ one time
  e.g., Add of 4 pairs of words
Hardware descriptions
  All gates @ one time
Programming Languages
Smart Phone
Warehouse Scale Computer
Software Hardware
Harness Parallelism &
Achieve High Performance
Logic Gates
Core
Core
…
Memory (Cache)
Input/Output
Computer
Cache Memory
Core
Instruction Unit(s)
Functional
Unit(s)
A3+B3
A2+B2
A1+B1
A0+B0
How do we know?

## Slide 3: Review of Numbers
Computers are made to deal with numbers
What can we represent in N bits?
  2N things, and no more! They could be…
  Unsigned integers:
  0 to 2N - 1
  (for N=32, 2N–1 = 4,294,967,295)
  Signed Integers (Two’s Complement)
  -2(N-1) to 2(N-1) - 1
  (for N=32, 2(N-1) = 2,147,483,648)

## Slide 4: What about other numbers?
Very large numbers? (seconds/millennium)  31,556,926,000ten (3.155692610 x 1010)
Very small numbers? (Bohr radius)  0.0000000000529177ten (5.2917710 x 10-11)
Numbers with both integer & fractional parts?  1.5
First consider #3.
…our solution will also help with #1 and #2.

## Slide 5: Representation of Fractions
“Binary Point” like decimal point signifies boundary between integer and fractional parts:
xx.yyyy
21
20
2-1
2-2
2-3
2-4
Example 6-bit representation:
10.1010two = 1x21 + 1x2-1 + 1x2-3 = 2.625ten
If we assume “fixed binary point”, range of 6-bit representations with this format:
0 to 3.9375 (almost 4)

## Slide 6: Fractional Powers of 2
0 1.0 1
0.5 1/2
0.25 1/4
0.125 1/8
0.0625 1/16
0.03125 1/32
0.015625
0.0078125
0.00390625
0.001953125
0.0009765625
0.00048828125
0.000244140625
0.0001220703125
0.00006103515625
0.000030517578125
i 2-i

## Slide 7: Representation of Fractions with Fixed Pt.
What about addition and multiplication?
Addition is straightforward:
01.100 1.5ten
+ 00.100 0.5ten
10.000 2.0ten
Multiplication a bit more complex:
01.100 1.5ten
00.100 0.5ten
00 000
000 00
0110 0
00000
00000
0000110000
Where’s the answer, 0.11? (need to remember where point is)

## Slide 8: Representation of Fractions
So far, in our examples we used a “fixed” binary point. What we really want is to “float” the binary point. Why?
Floating binary point most effective use of our limited bits (and thus more accuracy in our number representation):
… 000000.001010100000…
Any other solution would lose accuracy!
example: put 0.1640625ten into binary. Represent with 5-bits choosing where to put the binary point.
Store these bits and keep track of the binary point 2 places to the left of the MSB
With floating-point rep., each numeral carries an exponent field recording the whereabouts of its binary point.
The binary point can be outside the stored bits, so very large and small numbers can be represented.

## Slide 9: Scientific Notation (in Decimal)
6.02ten x 1023
radix (base)
decimal point
mantissa
exponent
Normalized form: no leading 0s (exactly one digit to left of decimal point)
Alternatives to representing 1/1,000,000,000
  Normalized: 1.0 x 10-9
  Not normalized: 0.1 x 10-8,10.0 x 10-10

## Slide 10: Scientific Notation (in Binary)
1.01two x 2-1
radix (base)
“binary point”
exponent
Computer arithmetic that supports it called floating point, because it represents numbers where the binary point is not fixed, as it is for integers
  Declare such variable in C as float
    double for double precision.
mantissa

## Slide 11: Floating-Point Representation (1/2)
Normal format: +1.xxx…xtwo*2yyy…ytwo
Multiple of Word Size (32 bits)
0
31
S
Exponent
30
23
22
Significand
1 bit
8 bits
23 bits
S represents Sign Exponent represents y’s Significand represents x’s
Represent numbers as small as 2.0ten x 10-38 to as large as 2.0ten x 1038

## Slide 12: Floating-Point Representation (2/2)
What if result too large?
  (> 2.0x1038 , < -2.0x1038 )
  Overflow!  Exponent larger than represented in 8-bit Exponent field
What if result too small?
  (>0 & < 2.0x10-38 , <0 & > -2.0x10-38 )
  Underflow!  Negative exponent larger than represented in 8-bit Exponent field
What would help reduce chances of overflow and/or underflow?
0
2x10-38
2x1038
1
-1
-2x10-38
-2x1038
underflow
overflow
overflow

## Slide 13: IEEE 754 Floating-Point Standard (1/3)
Single Precision (Double Precision similar):
Sign bit: 1 means negative 0 means positive
Significand in sign-magnitude format (not 2’s complement)
  To pack more bits, leading 1 implicit for normalized numbers
  1 + 23 bits single, 1 + 52 bits double
  always true: 0 < Significand < 1 (for normalized numbers)
Note: 0 has no leading 1, so reserve exponent value 0 just for number 0
0
31
S
Exponent
30
23
22
Significand
1 bit
8 bits
23 bits

## Slide 14: IEEE 754 Floating Point Standard (2/3)
IEEE 754 uses “biased exponent” representation
  Designers wanted FP numbers to be used even if no FP hardware; e.g., sort records with FP numbers using integer compares
  Wanted bigger (integer) exponent field to represent bigger numbers
  2’s complement poses a problem (because negative numbers look bigger)
    Use just magnitude and offset by half the range

## Slide 15: IEEE 754 Floating Point Standard (3/3)
Called Biased Notation, where bias is number subtracted to get final number
  IEEE 754 uses bias of 127 for single prec.
  Subtract 127 from Exponent field to get actual value for exponent
Summary (single precision):
0
31
S
Exponent
30
23
22
Significand
1 bit
8 bits
23 bits
(-1)S x (1 + Significand) x 2(Exponent-127)
  Double precision identical, except with exponent bias of 1023 (half, quad similar)

## Slide 16: “Father” of the Floating point standard
IEEE Standard 754 for Binary Floating-Point Arithmetic.
www.cs.berkeley.edu/~wkahan/ieee754status/754story.html
Prof. Kahan
1989 ACM Turing Award Winner!
Notes: 1:30 in

## Slide 17: Clickers
Guess this Floating Point number:
1 1000 0000 1000 0000 0000 0000 0000 000
A: -1x 2128
B: +1x 2-128
C: -1x 21
D: +1.5x 2-1
E: -1.5x 21
Notes: E

## Slide 18: Administrivia
Project 3-2 extended until 03/20 @ 23:59:59
Guerrilla Session: Caches/ Proj 3-2 OH
  Sat 3/19 1 - 3 PM @ 521 Cory
Notes: E

## Slide 19: Representation for ± ∞
In FP, divide by 0 should produce ± ∞, not overflow.
Why?
  OK to do further computations with ∞ E.g., X/0 > Y may be a valid comparison
IEEE 754 represents ± ∞
  Most positive exponent reserved for ∞
  Significands all zeroes

## Slide 20: Representation for 0
Represent 0?
  exponent all zeroes
  significand all zeroes
  What about sign? Both cases valid
  +0: 0 00000000 00000000000000000000000
  -0: 1 00000000 00000000000000000000000

## Slide 21: Special Numbers
What have we defined so far? (Single Precision)
  Exponent Significand Object
  0 0 0
  0 nonzero ???
  1-254 anything +/- fl. pt. #
  255 0 +/- ∞
  255 nonzero ???
Professor Kahan had clever ideas:
  Wanted to use Exp=0,255 & Sig!=0

## Slide 22: Representation for Not a Number
What do I get if I calculate sqrt(-4.0)or 0/0?
  If ∞ not an error, these shouldn’t be either
  Called Not a Number (NaN)
  Exponent = 255, Significand nonzero
Why is this useful?
  Hope NaNs help with debugging?
  They contaminate: op(NaN, X) = NaN
  Can use the significand to identify which!

## Slide 23: Representation for Denorms (1/2)
Problem: There’s a gap among representable FP numbers around 0
  Smallest representable pos num:
    a = 1.0… two * 2-126 = 2-126
  Second smallest representable pos num:
    b = 1.000……1 two * 2-126 = (1 + 0.00…1two) * 2-126 = (1 + 2-23) * 2-126 = 2-126 + 2-149
  a - 0 = 2-126
  b - a = 2-149
b
a
0
+
-
Gaps!
Normalization and implicit 1 is to blame!

## Slide 24: Representation for Denorms (2/2)
Solution:
  We still haven’t used Exponent = 0, Significand nonzero
  DEnormalized number: no (implied) leading 1, implicit exponent = -126.
  Smallest representable pos num:
    a = 2-149
  Second smallest representable pos num:
    b = 2-148
0
+
-

## Slide 25: Special Numbers Summary
Reserve exponents, significands:
  Exponent Significand Object
  0 0 0
  0 nonzero Denorm
  1-254 anything +/- fl. pt. #
  255 0 +/- ∞
  255 nonzero NaN

## Slide 26: Conclusion
Floating Point lets us:
  Represent numbers containing both integer and fractional parts; makes efficient use of available bits.
  Store approximate values for very large and very small #s.
IEEE 754 Floating-Point Standard is most widely accepted attempt to standardize interpretation of such numbers (Every desktop or server computer sold since ~1997 follows these conventions)
Summary (single precision):
0
31
S
Exponent
30
23
22
Significand
1 bit
8 bits
23 bits
(-1)S x (1 + Significand) x 2(Exponent-127)
  Double precision identical, except with exponent bias of 1023 (half, quad similar)
Exponent tells Significand how much (2i) to count by (…, 1/4, 1/2, 1, 2, …)
Can store NaN, ± ∞
www.h-schmidt.net/FloatApplet/IEEE754.html