## Slide 1: CS 61C: Great Ideas in Computer Architecture (Machine Structures) Intro to Virtual Memory
Instructors:
Vladimir Stojanovic and Nicholas Weaver
http://inst.eecs.berkeley.edu/~cs61c/

## Slide 2: Agenda
Multiprogramming/time-sharing
Introduction to Virtual Memory

## Slide 3: Multiprogramming
The OS runs multiple applications at the same time.
  But not really: have many more processes/threads than available cores
Switches between processes very quickly. This is called a “context switch”.
When jumping into process, set timer interrupt.
  When it expires, store PC, registers, etc. (process state).
  Pick a different process to run and load its state.
  Set timer, change to user mode, jump to the new PC.
Deciding what process to run is called scheduling.

## Slide 4: Protection, Translation, Paging
Supervisor mode does things that normal mode can't…
  But...
Supervisor mode is not enough to fully isolate applications from each other or from the OS.
  Application could overwrite another application’s memory.
  Also, may want to address more memory than we actually have (e.g., for sparse data structures).
Solution: Virtual Memory. Gives each process the illusion of a full memory address space that it has completely for itself.

## Slide 5: What do we need Virtual Memory for? Reason 1: Adding Disks to Hierarchy
Need to devise a mechanism to “connect” memory and disk in the memory hierarchy

## Slide 6: What do we need Virtual Memory for? Reason 2: Simplifying Memory for Apps
Applications should see the straightforward memory layout we saw earlier ->
User-space applications should think they own all of memory
So we give them a virtual view of memory
code
static data
heap
stack
~ 7FFF FFFFhex
~ 0000 0000hex
Notes: Location independent automatically

## Slide 7: What do we need Virtual Memory for? Reason 3: Protection Between Processes
With a bare system, addresses issued with loads/stores are real physical addresses
This means any program can issue any address, therefore can access any part of memory, even areas which it doesn’t own
  Ex: The OS data structures
We should send all addresses through a mechanism that the OS controls, before they make it out to DRAM - a translation mechanism

## Slide 8: VM + Supervisor Mode combine to Create Isolation
Supervisor mode is only entered into at the trap handler
  So its always known (and hopefully correct) code that is part of the core operating system
    This is why "syscall" generates an exception
Only Supervisor mode can change Virtual Memory mappings
  So only the core of the operating system can bypass the protections imposed on memory
These are the invariants necessary for isolation
  Anything that can affect these invariants completely compromises the security of the system

## Slide 9: Address Spaces
The set of addresses labeling all of memory that we can access
Now, 2 kinds:
  Virtual Address Space - the set of addresses that the user program knows about
  Physical Address Space - the set of addresses that map to actual physical cells in memory
    Hidden from user applications
So, we need a way to map between these two address spaces
Notes: because the programs will issue virtual addresses, but we need physical addresses to access data in DRAM

## Slide 10: Blocks vs. Pages
In caches, we dealt with individual blocks
  Usually ~64B on modern systems
  We could “divide” memory into a set of blocks
In VM, we deal with individual pages
  Usually ~4 KB on modern systems
  Now, we’ll “divide” memory into a set of pages
Common point of confusion: Bytes, Words, Blocks, Pages are all just different ways of looking at memory!

## Slide 11: Bytes, Words, Blocks, Pages
Ex: 16 KiB DRAM, 4 KiB Pages (for VM), 128 B blocks (for caches), 4 B words (for lw/sw)
Page 3
Page 2
Page 1
Page 0
16 KiB
Block 0
Block 31
Word 0
Word 31
1 Memory
1 Page
1 Block
Can think of memory as:
- 4 Pages
OR
- 128 Blocks
OR
- 4096 Words
Can think of a page as:
- 32 Blocks
OR
- 1024 Words

## Slide 12: Address Translation
So, what do we want to achieve at the hardware level?
  Take a Virtual Address, that points to a spot in the Virtual Address Space of a particular program, and map it to a Physical Address, which points to a physical spot in DRAM of the whole machine
Virtual Page Number | Offset
Virtual Address
Physical Address
Physical Page Number | Offset

## Slide 13: Address Translation
Virtual Page Number | Offset
Physical Page Number | Offset
Virtual Address
Physical Address
Address Translation
Copy Bits
The rest of the lecture is all about implementing
Notes: Phys addr will then go to the cache just like before, cache will split that same addr into TIO. you can think of them completely separately for now. caches work just like before

## Slide 14: “Bare” 5-Stage Pipeline
In a bare machine, the only kind of address is a physical address
PC
Inst. Cache
D
Decode
E
M
Data Cache
W
+
Main Memory (DRAM)
Memory Controller
Physical Address
Physical Address
Physical Address
Physical Address
Physical Address

## Slide 15: Modern Virtual Memory Systems Illusion of a large, private, uniform store
Protection
several users, each with their private address space and one or more shared address spaces
Demand Paging
Provides the ability to run programs larger than the primary memory
Hides differences in machine configurations
The price is address translation on
each memory reference
OS
useri
Primary
Memory
Swapping
Store
VA
PA
mapping
TLB
Notes: Portability on machines with different memory configurations.

## Slide 16: Dynamic Address Translation
Motivation
  Multiprogramming, multitasking: Desire to execute more than one process at a time (more than one process can reside in main memory at the same time).
Location-independent programs
  Programming and storage management ease
 base register – add offset to each address
Protection
  Independent programs should not affect
  each other inadvertently
 bound register – check range of access
(Note: Multiprogramming drives requirement for resident supervisor (OS) software to manage context switches between multiple programs)
prog1
prog2
Physical Memory
OS

## Slide 17: Simple Base and Bound Translation
Load X
Program
Address Space
Bound
Register
Bounds
Violation?
Physical Memory
current
segment
Base
Register
+
Physical
Address
Logical
Address
Base and bounds registers are visible/accessible only when processor is running in supervisor mode
Base Physical Address
Segment Length
≤

## Slide 18: Separate Areas for Program and Data
Physical Address
Physical Address
Load X
Program
Address
Space
Main Memory
data
segment
Data Bound Register
Mem. Address Register
Data Base Register
≤
+
Bounds
Violation?
Program Bound Register
Program Counter
Program Base Register
≤
+
Bounds
Violation?
program
segment
Logical Address
Logical Address
What is an advantage of this separation?
(Scheme used on all Cray vector supercomputers prior to X1, 2002)
Notes: Permits sharing of program segments.

## Slide 19: Base and Bound Machine
[ Can fold addition of base register into (register+immediate) address calculation using a carry-save adder (sums three numbers with only a few gate delays more than adding two numbers) ]
PC
Inst. Cache
D
Decode
E
M
Data Cache
W
+
Main Memory (DRAM)
Memory Controller
Physical Address
Physical Address
Physical Address
Physical Address
Data Bound Register
Data Base Register
≤
+
Logical Address
Bounds Violation?
Physical Address
Prog. Bound Register
Program Base Register
≤
+
Logical Address
Bounds Violation?

## Slide 20: Memory Fragmentation
As users come and go, the storage is “fragmented”.
Therefore, at some stage programs have to be moved
around to compact the storage.
OS
Space
16K
24K
24K
32K
24K
user 1
user 2
user 3
OS
Space
16K
24K
16K
32K
24K
user 1
user 2
user 3
user 5
user 4
8K
Users 4 & 5
arrive
Users 2 & 5
leave
OS
Space
16K
24K
16K
32K
24K
user 1
user 4
8K
user 3
free
Notes: Called Burping the memory.

## Slide 21: Paged Memory Systems
Processor-generated address can be split into:
Page tables make it possible to store the pages of a program non-contiguously.
0
1
2
3
0
1
2
3
Address Space
of User-1
Page Table
of User-1
1
0
2
3
page number offset
Physical Memory
A page table contains the physical address of the base of each page
Notes: Relaxes the contiguous allocation requirement.

## Slide 22: Private Address Space per User
Each user has a page table
Page table contains an entry for each user page
VA1
User 1
Page Table
VA1
User 2
Page Table
VA1
User 3
Page Table
Physical Memory
free
OS
pages
Notes: OS ensures that the page tables are disjoint.

## Slide 23: Where Should Page Tables Reside?
Space required by the page tables (PT) is proportional to the address space, number of users, ...
    Too large to keep in cpu registers
Idea: Keep PTs in the main memory
  Needs one reference to retrieve the page base address and another to access the data word
   doubles the number of memory references!
  Caching helps
  Automatic caching if the processor uses full page tables
  Manual caching controlled by the OS with the Translation Lookaside Buffer (TLB)

## Slide 24: Page Tables in Physical Memory
VA1
User 1 Virtual Address Space
User 2 Virtual Address Space
PT User 1
PT User 2
VA1
Physical Memory

## Slide 25: Page Table Tricks…
Can actually have multiple processes referring to the same physical memory
  Enables "shared memory" between processes
Page table entry can say "this exists on disk"
  When such memory is accessed it triggers an exception instead
  The operating system can copy the data into memory ("swap it in") and then resume the trapped instruction
    How it gives the illusion of infinite memory
Can use that same method to efficiently read files
  File is "memory mapped", when read it is simply paged in like other
  Allows an efficient method to handle large files conveniently
  When data is changed can use the same method used to "swap out" unused memory

## Slide 26: The Ultimate Page-Table Trick: Rowhammer
An unspeakably cool security vulnerability…
DRAM (unless you pay for error correcting (ECC) memory) is actually unreliable
  Can repeatedly read/write the same location ("hammer the row" and eventually cause an error in some physically distinct memory location
Can tell the OS "I want to map this same block of memory at multiple addresses in my process…"
  Which creates additional page table entries
Enter Rowhammer
  It seems all vunerabilities get named now, but this one is cool enough to deserve a name!

## Slide 27: How RowHammer Works
Step 1: Allocate a single page of memory
Step 2: Make the OS make a gazillion page-table entries pointing to the same page
Step 3: Hammer the DRAM until one of those entries gets corrupted
  Now causes that memory page to point to a set of page table entries instead
Step 4: Profit
  Well, the ability to read and write to any physical address in the system, same difference
Physical Memory
Process's
Virtual Memory
…

## Slide 28: Clicker Question…
So how cool is this?
  A -> Supercool
  E -> Eh, whatever

## Slide 29: In Conclusion
Once we have a basic machine, it’s mostly up to the OS to use it and define application interfaces.
Hardware helps by providing the right abstractions and features (e.g., Virtual Memory, I/O).
If you want to learn more about operating systems, you should take CS162!
What’s next in CS61C?
  More details on I/O
  More about Virtual Memory