## Slide 1: CS 61C: Great Ideas in Computer Architecture Virtual Memory Cont.
Instructors:
Vladimir Stojanovic & Nicholas Weaver
http://inst.eecs.berkeley.edu/~cs61c/

## Slide 2: “Bare” 5-Stage Pipeline
In a bare machine, the only kind of address is a physical address
PC
Inst. Cache
D
Decode
E
M
Data Cache
W
+
Main Memory (DRAM)
Memory Controller
Physical Address
Physical Address
Physical Address
Physical Address
Physical Address

## Slide 3: Address Translation
So, what do we want to achieve at the hardware level?
  Take a Virtual Address, that points to a spot in the Virtual Address Space of a particular program, and map it to a Physical Address, which points to a physical spot in DRAM of the whole machine
Virtual Page Number | Offset
Virtual Address
Physical Address
Physical Page Number | Offset

## Slide 4: Address Translation
Virtual Page Number | Offset
Physical Page Number | Offset
Virtual Address
Physical Address
Address Translation
Copy Bits
The rest of the lecture is all about implementing
Notes: Phys addr will then go to the cache just like before, cache will split that same addr into TIO. you can think of them completely separately for now. caches work just like before

## Slide 5: Paged Memory Systems
Processor-generated address can be split into:
Page tables make it possible to store the pages of a program non-contiguously.
0
1
2
3
0
1
2
3
Address Space
of Program #1
Page Table
of Program #1
1
0
2
3
Physical Memory
A page table contains the physical address of the base of each page
Virtual Page Number | Offset
Notes: Relaxes the contiguous allocation requirement.

## Slide 6: Private (Virtual) Address Space per Program
VA1
Prog 1
Page Table
VA1
Prog 2
Page Table
VA1
Prog 3
Page Table
Physical Memory
free
OS
pages
Each prog has a page table
Page table contains an entry for each prog page
Physical Memory acts like a “cache” of pages for currently running programs. Not recently used pages are stored in secondary memory, e.g. disk (in “swap partition”)
Notes: Pages are fixed sized chunks. So no fragmentation in terms of pages

## Slide 7: Where Should Page Tables Reside?
Space required by the page tables (PT) is proportional to the address space, number of users, ...
    Too large to keep in registers inside CPU
Idea: Keep page tables in the main memory
  Needs one reference to retrieve the page base address and another to access the data word
   doubles the number of memory references! (but we can fix this using something we already know about…)
Notes: for each program, keep track of the PHYSICAL ADDRESS of the start of the page table inside the CPU

## Slide 8: Page Tables in Physical Memory
VA1
Prog 1 Virtual Address Space
Prog 2 Virtual Address Space
PT Prog1
PT Prog2
VA1
Physical Memory

## Slide 9: Linear (simple) Page Table
VPN
Offset
Virtual address
PT Base Register
VPN
Data word
Data Pages
Offset
PPN
PPN
DPN
PPN
PPN
PPN
Page Table
DPN
PPN
DPN
DPN
DPN
PPN
Page Table Entry (PTE) contains:
  1 bit to indicate if page exists
  And either PPN or DPN:
  PPN (physical page number) for a memory-resident page
  DPN (disk page number) for a page on the disk
  Status bits for protection and usage (read, write, exec)
OS sets the Page Table Base Register whenever active user process changes

## Slide 10: Suppose an instruction references a memory page that isn’t in DRAM?
We get an exception of type “page fault”
Page fault handler does the following:
  If virtual page doesn’t yet exist, assign an unused page in DRAM, or if page exists …
  Initiate transfer of the page we’re requesting from disk to DRAM, assigning to an unused page
  If no unused page is left, a page currently in DRAM is selected to be replaced (based on usage)
  The replaced page is written (back) to disk, page table entry that maps that VPN->PPN is marked as invalid/DPN
  Page table entry of the page we’re requesting is updated with a (now) valid PPN

## Slide 11: Size of Linear Page Table
With 32-bit memory addresses, 4-KiB pages:
  232 / 212 = 220 virtual pages per user, assuming 4-Byte PTEs,
  220 PTEs, i.e, 4 MiB page table per user!
Larger pages?
  Internal fragmentation (Not all memory in page gets used)
  Larger page fault penalty (more time to read from disk)
What about 64-bit virtual address space???
  Even 1MiB pages would require 244 8-Byte PTEs (128 TiB!)
What is the “saving grace” ?
Most processes only use a set of high address (stack), and a set of low address (instructions, heap)
Notes: Virtual address space is large but only a small fraction of the
pages are populated. So we can use a sparse representation
of the table.

## Slide 12: Hierarchical Page Table – exploits sparsity of virtual address space use
Level 1
Page Table
Level 2
Page Tables
Data Pages
page in primary memory
page in secondary memory
Root of the Current
Page Table
p1
p2
Virtual Address
(Processor
Register)
PTE of a nonexistent page
p1 p2 offset
0
11
12
21
22
31
10-bit
L1 index
10-bit
L2 index
Physical Memory

## Slide 13: MT2 Grades
59%

## Slide 14: Administrivia
Upcoming Lecture Schedule
  04/18: VM (today)
  04/20: I/O: DMA, Disks
  04/22: Networking
  04/25: Dependability: Parity, ECC (+ HKN reviews)
  04/27: RAID
    Last day of new material
  04/29: Summary, What’s Next?

## Slide 15: Administrivia
Project 4 programming competition rules posted
Project 5 released – due on 4/26
Guerrilla Session: Virtual Memory
  Wed 4/20 3 - 5 PM @ 241 Cory
  Sat 4/22 1 - 3 PM @ 521 Cory
Last HW (3) Virtual Memory
  Due 05/01

## Slide 16: Address Translation & Protection
Every instruction and data access needs address
translation and protection checks
A good VM design needs to be fast (~ one cycle) and space efficient
Physical Address
Virtual Address
Address
Translation
Virtual Page No. (VPN)
offset
Physical Page No. (PPN)
offset
Protection
Check
Exception?
Kernel/User Mode
Read/Write

## Slide 17: Translation Lookaside Buffers (TLB)
Address translation is very expensive!
  In a two-level page table, each reference becomes several memory accesses
Solution: Cache some translations in TLB
TLB hit  Single-Cycle Translation
TLB miss  Page-Table Walk to refill
VPN offset
V R W D tag PPN
physical address
PPN offset
virtual address
hit?
(VPN = virtual page number)
(PPN = physical page number)
Notes: 3 memory references
2 page faults (disk accesses) + ..
Actually used in IBM before paged memory.

## Slide 18: TLB Designs
Typically 32-128 entries, usually fully associative
  Each entry maps a large page, hence less spatial locality across pages => more likely that two entries conflict
  Sometimes larger TLBs (256-512 entries) are 4-8 way set-associative
  Larger systems sometimes have multi-level (L1 and L2) TLBs
Random or FIFO replacement policy
“TLB Reach”: Size of largest virtual address space that can be simultaneously mapped by TLB
  Example: 64 TLB entries, 4KiB pages, one page per entry
  TLB Reach = _____________________________________________?
Notes: 256 KiB mapped at once in the TLB

## Slide 19: VM-related events in pipeline
Handling a TLB miss needs a hardware or software mechanism to refill TLB
  usually done in hardware now
Handling a page fault (e.g., page is on disk) needs a precise trap so software handler can easily resume after retrieving page
Handling protection violation may abort process
PC
Inst TLB
Inst. Cache
D
Decode
E
M
Data TLB
Data Cache
W
+
TLB miss? Page Fault?
Protection violation?
TLB miss? Page Fault?
Protection violation?

## Slide 20: Hierarchical Page Table Walk: SPARC v8
31 11 0
Virtual Address
Index 1 Index 2 Index 3 Offset
31 23 17 11 0
Context
Table
Register
Context
Register
root ptr
PTP
PTP
PTE
Context Table
L1 Table
L2 Table
L3 Table
Physical Address
PPN Offset
MMU does this table walk in hardware on a TLB miss
Notes: 4 memory references

## Slide 21: Page-Based Virtual-Memory Machine (Hardware Page-Table Walk)
PC
Inst. TLB
Inst. Cache
D
Decode
E
M
Data Cache
W
+
Page Fault?
Protection violation?
Page Fault?
Protection violation?
Assumes page tables held in untranslated physical memory
Data TLB
Main Memory (DRAM)
Memory Controller
Physical Address
Physical Address
Physical Address
Physical Address
Page-Table Base Register
Virtual Address
Physical Address
Virtual Address
Hardware Page Table Walker
Miss?
Miss?

## Slide 22: Address Translation: putting it all together
Virtual Address
TLB
Lookup
Page Table
Walk
Update TLB
Page Fault
(OS loads page)
Protection
Check
Physical
Address
(to cache)
miss
hit
the page is
Ï memory Î memory
denied
permitted
Protection
Fault
hardware
hardware or software
software
SEGFAULT
Where?
Notes: Need to restart instruction.
Soft and hard page faults.

## Slide 23: Modern Virtual Memory Systems Illusion of a large, private, uniform store
Protection & Privacy
  several users, each with their private address space and one or more shared address spaces
page table  name space
Demand Paging
  Provides the ability to run programs larger than the primary memory
  Hides differences in machine configurations
The price is address translation on
each memory reference
OS
useri
Primary
Memory
Swapping Store
(Disk)
VA
PA
mapping
TLB
Notes: Portability on machines with different memory configurations.

## Slide 24: Clicker Question
Let’s try to extrapolate from caches… Which one is false?
A. # offset bits in V.A. = log2(page size)
B. # offset bits in P.A. = log2(page size)
C. # VPN bits in V.A. = log2(# of physical pages)
D. # PPN bits in P.A. = log2(# of physical pages)
E. A single-level page table contains a PTE for every possible VPN in the system
Notes: C. it’s the # of virtual pages, which is != to # of physical pages

## Slide 25: Conclusion: VM features track historical uses
Bare machine, only physical addresses
  One program owned entire machine
Batch-style multiprogramming
  Several programs sharing CPU while waiting for I/O
  Base & bound: translation and protection between programs (not virtual memory)
  Problem with external fragmentation (holes in memory), needed occasional memory defragmentation as new jobs arrived

## Slide 26: Conclusion: VM features track historical uses
Time sharing
  More interactive programs, waiting for user. Also, more jobs/second.
  Motivated move to fixed-size page translation and protection, no external fragmentation (but now internal fragmentation, wasted bytes in page)
  Motivated adoption of virtual memory to allow more jobs to share limited physical memory resources while holding working set in memory
Virtual Machine Monitors
  Run multiple operating systems on one machine
  Idea from 1970s IBM mainframes, now common on laptops
    e.g., run Windows on top of Mac OS X
  Hardware support for two levels of translation/protection
    Guest OS virtual -> Guest OS physical -> Host machine physical
  Also basis of Cloud Computing
    Virtual machine instances on EC2