## Slide 1
Instructor: Justin Hsia
CS 61C: Great Ideas in Computer Architecture
Cache Performance,
Set Associative Caches

## Slide 2: Great Idea #3: Principle of Locality/ Memory Hierarchy

## Slide 3: Extended Review of Last Lecture
Why have caches?
  Intermediate level between CPU and memory
  In-between in size, cost, and speed
Memory (hierarchy, organization, structures) set up to exploit temporal and spatial locality
  Temporal: If accessed, will access again soon
  Spatial: If accessed, will access others around it
Caches hold a subset of memory (in blocks)
  We are studying how they are designed for fast and efficient operation (lookup, access, storage)

## Slide 4: Extended Review of Last Lecture
Direct-Mapped Caches:
  Use hash function to determine location for block
    Each block maps into a single row
    (block address) modulo (# of blocks in the cache)
  TIO breakdown of memory address
    Index field is result of hash function (which row)
    Tag field is identifier (which block is currently in row)
    Offset field indexes into block
  Each cache row holds block data, tag, valid bit, and dirty bit (dirty bit is only for write-back)

## Slide 5: Extended Review of Last Lecture
Cache design considerations
  Affect hit rate/miss rate (HR/MR), hit time (HT), and miss penalty (MP)
  So far introduced cache size and block size
Cache read and write policies:
  Affect consistency of data between cache and memory
  Write-back vs. write-through
  Write allocate vs. no-write allocate

## Slide 6: Direct-Mapped Cache Layout
8-bit address space, 32-byte cache with 8-byte (2 word) blocks, write-back and write allocate
Offset – 3 bits, Index – 2 bits, Tag – 3 bits
Each row has 69 bits; cache has 4*69 = 276 bits
V | D | Tag | 000 | 001 | 010 | 011 | 100 | 101 | 110 | 111
X | X | XXX | 0x?? | 0x?? | 0x?? | 0x?? | 0x?? | 0x?? | 0x?? | 0x??
X | X | XXX | 0x?? | 0x?? | 0x?? | 0x?? | 0x?? | 0x?? | 0x?? | 0x??
X | X | XXX | 0x?? | 0x?? | 0x?? | 0x?? | 0x?? | 0x?? | 0x?? | 0x??
X | X | XXX | 0x?? | 0x?? | 0x?? | 0x?? | 0x?? | 0x?? | 0x?? | 0x??
Offset
Index
00
01
10
11
cache size
block size
256 B address space
Need dirty bit

## Slide 7: Direct-Mapped Cache Request
On memory request (read or write):
  Extract Index field and find corresponding row
  Check Valid bit (otherwise cache miss)
  Extract Tag field and compare to Tag in row (otherwise cache miss with replacement)
  Use Offset to select correct byte/word from block (cache hit)
On write, set Dirty bit if write-back

## Slide 8: Agenda
Cache Performance
Administrivia
Multilevel Caches
Set Associative Caches
Improving Cache Performance
Bonus: Multilevel Cache Performance Practice
Bonus: Contemporary Cache Specs

## Slide 9: Cache Performance
Two things hurt the performance of a cache:
  Miss rate and miss penalty
  Average Memory Access Time (AMAT): average time to access memory considering both hits and misses
  AMAT = Hit time + Miss rate × Miss penalty
  (abbreviated AMAT = HT + MR × MP)
Goal 1: Examine how changing the different cache parameters affects our AMAT (Lec 12)
Goal 2: Examine how to optimize your code for better cache performance (Lec 13, Proj 2)

## Slide 10: AMAT Example Usage
Processor specs: 200 ps clock, MP of 50 clock cycles, MR of 0.02 misses/instruction, and HT of 1 clock cycle
  AMAT = ???
Which improvement would be best?
  190 ps clock
  MP of 40 clock cycles
  MR of 0.015 misses/instruction
380 ps
360 ps
350 ps
1 + 0.02 × 50 = 2 clock cycles = 400 ps

## Slide 11: Cache Parameter Example
What is the potential impact of much larger cache on AMAT? (same block size)
  Increase HR
  Longer HT: smaller is faster
  At some point, increase in hit time for a larger cache may overcome the improvement in hit rate, yielding a decrease in performance
Effect on TIO? Bits in cache? Cost?

## Slide 12: Effect of Cache Performance on CPI
Recall: CPU Performance
CPU Time = Instructions × CPI × Clock Cycle Time
Include memory accesses in CPI:
  CPIstall = CPIbase + Average Memory-stall Cycles
  CPU Time = IC × CPIstall × CC
Simplified model for memory-stall cycles:
  Memory-stall cycles
  We will discuss more complicated models soon
(CC)
(IC)
Notes: Memory-stall clock cycles = Read-stall cycles + Write-stall cycles.
Reasonable write buffer depth (e.g., four or more words) and a memory capable of accepting writes at a rate that significantly exceeds the average write frequency means write buffer stalls are small.
Here we are assuming same MR and MP for reads and writes.

## Slide 13: CPI Example
Processor specs: CPIbase of 2, a 100 cycle MP, 36% load/store instructions, and 2% I$ and 4% D$ MRs
  How many times per instruction do we access the I$? The D$?
  MP is assumed the same for both I$ and D$
  Memory-stall cycles will be sum of stall cycles for both I$ and D$
Notes: I$ accessed at EVERY instruction (need to fetch from Code portion of memory!).
D$ is accessed only on loads and stores.
Naturally, you expect the I$ MR < D$ MR.

## Slide 14: CPI Example
Processor specs: CPIbase of 2, a 100 cycle MP, 36% load/store instructions, and 2% I$ and 4% D$ MRs
  Memory-stall cycles = (100% × 2% + 36% × 4%) × 100 = 3.44
  CPIstall = 2 + 3.44 = 5.44 (more than 2x CPIbase!)
What if the CPIbase is reduced to 1?
What if the D$ miss rate went up by 1%?
I$
D$
Notes: If CPIbase = 1, CPIstall = 4.44, with memory-stall cycles accounting for 77.5% as opposed to 63.2%.
If D$ MR = 0.05, then memory-stall cycles = 3.8 and CPIstall = 5.8. Memory-stall cycles now account for 65.5% of CPIstall.

## Slide 15: Impacts of Cache Performance
CPIstall = CPIbase + Memory-stall Cycles
Relative penalty of cache performance increases as processor performance improves (faster clock rate and/or lower CPIbase)
  Relative contribution of CPIbase and memory-stall cycles to CPIstall
  Memory speed unlikely to improve as fast as processor cycle time
What can we do to improve cache performance?
Notes: For CPIbase = 1, then CPIstall = 4.44 and the amount of execution time spent on memory stalls would have risen from 3.44/5.44 = 63% to 3.44/4.44 = 77%
For miss penalty of 200, memory stall cycles = 2% 200 + 36% x 4% x 200 = 6.88 so that CPIstall = 8.88
This assumes that hit time (so hit time is 1 cycle) is not a factor in determining cache performance. A larger cache would have a longer access time (if a lower miss rate), meaning either a slower clock cycle or more stages in the pipeline for memory access.

## Slide 16: The 3Cs Revisited: Design Solutions
Compulsory:
  Increase block size (increases MP; too large blocks could increase MR)
Capacity:
  Increase cache size (may increase HT)
Conflict:
  Increase cache size
  Increase associativity (may increase HT)
Notes: We will talk about associativity later in this lecture.

## Slide 17: Agenda
Cache Performance
Administrivia
Multilevel Caches
Set Associative Caches
Improving Cache Performance
Bonus: Multilevel Cache Performance Practice
Bonus: Contemporary Cache Specs

## Slide 18: Administrivia
HW3 due Wednesday
Midterm: Friday @ 9am in 245 Li Ka Shing
  Take old exams for practice (see Piazza post @209)
  One-sided sheet of handwritten notes
  MIPS Green Sheet provided; no calculators
  Will cover up through caches
Mid-Semester Survey
  Short survey to complete as part of Lab 7
Found some copied code already; don’t do it!

## Slide 19: Agenda
Cache Performance
Administrivia
Multilevel Caches
Set Associative Caches
Improving Cache Performance
Bonus: Multilevel Cache Performance Practice
Bonus: Contemporary Cache Specs

## Slide 20: Multiple Cache Levels
With advancing technology, have more room on die for bigger L1 caches and for L2 (and in some cases even L3) cache
  Normally lower-level caches are unified (i.e. holds both instructions and data)
Multilevel caching is a way to reduce miss penalty
So what does this look like?

## Slide 21: Multilevel Cache Diagram
Return
L1$
L2$
Main Memory
.
.
.
CPU
Memory
Access
Path of data back to CPU
Miss
Miss
Hit
Hit
Legend:
Request for data
Return of data
Store
Store
Notes: The stores back in higher-level caches depends on your write-miss policy (write allocate or no-write allocate).

## Slide 22: Multilevel Cache AMAT
AMAT = L1 HT + L1 MR × L1 MP
  Now L1 MP depends on other cache levels
L1 MP = L2 HT + L2 MR × L2 MP
  If more levels, then continue this chain (i.e. MPi = HTi+1 + MRi+1 × MPi+1)
  Final MP is main memory access time
For two levels:
  AMAT = L1 HT + L1 MR × (L2 HT + L2 MR × L2 MP)

## Slide 23: Multilevel Cache AMAT Example
Processor specs: 1 cycle L1 HT, 2% L1 MR, 5 cycle L2 HT, 5% L2 MR, 100 cycle main memory HT
  Here assuming unified L1$
Without L2$:
AMAT1 = 1 + 0.02 × 100 = 3
With L2$:
AMAT2 = 1 + 0.02 × (5 + 0.05 × 100) = 1.2

## Slide 24: Local vs. Global Miss Rates
Local miss rate: Fraction of references to one level of a cache that miss
  e.g. L2$ local MR = L2$ misses/L1$ misses
  Specific to level of caching (as used in AMAT)
Global miss rate: Fraction of all references that miss in all levels of a multilevel cache
  Property of the overall memory hierarchy
  Global MR is the product of all local MRs
    Start at Global MR = Ln misses/L1 accesses and expand
    So by definition, global MR ≤ any local MR
Notes: L1$ misses are the only requests that reach L2$

## Slide 25: Memory Hierarchy with Two Cache Levels
For every 1000 CPU to memory references
  40 will miss in L1$; what is the local MR?
  20 will miss in L2$; what is the local MR?
  Global miss rate?
CPU
L1$
L2$
MM
1000 mem refs
40 mem refs
20 mem refs
1 cycle
10 cycles
100 cycles
0.04
0.5
0.02

## Slide 26: Rewriting Performance
For a two level cache, we know: MRglobal = L1 MR × L2 MR
AMAT:
  AMAT = L1 HT + L1 MR × (L2 HT + L2 MR × L2 MP)
  AMAT = L1 HT + L1 MR × L2 HT + MRglobal × L2 MP
CPI:
  CPIstall = CPIbase + × L1 MR × (L1 MP + L2 MR × L2 MP)
  CPIstall = CPIbase + (L1 MR × L1 MP + MRglobal × L2 MP)
Accesses
Instr
Accesses
Instr

## Slide 27: Design Considerations
L1$ focuses on low hit time (fast access)
  minimize HT to achieve shorter clock cycle
  L1 MP significantly reduced by presence of L2$, so can be smaller/faster even with higher MR
  e.g. smaller $ (fewer rows)
L2$, L3$ focus on low miss rate
  As much as possible avoid reaching to main memory (heavy penalty)
  e.g. larger $ with larger block sizes (same # rows)

## Slide 28: Agenda
Cache Performance
Administrivia
Multilevel Caches
Set Associative Caches (Part 1)
Improving Cache Performance
Bonus: Multilevel Cache Performance Practice
Bonus: Contemporary Cache Specs

## Slide 29: Reducing Cache Misses
Allow more flexible block placement in cache:
Direct-mapped: Memory block maps to exactly one cache block
Fully associative: Memory block can go in any slot
N-way set-associative: Divide $ into sets, each of which consists of n slots to place memory block
  Memory block maps to a set determined by Index field and is placed in any of the n slots of that set
  Hash function: (block address) modulo (# sets in the cache)
Notes: All of the tags of all of the elements of the set must be searched for a match.

## Slide 30: Block Placement Schemes
Place memory block 12 in a cache that holds 8 blocks
Direct-mapped: Can only go in row (12 mod 8) = 4
Fully associative: Can go in any of the slots (1 set/row)
2-way set associative: Can go in either slot of set (12 mod 4) = 0

## Slide 31: Effect of Associativity on TIO (1/2)
Here we assume a cache of fixed size (C)
Offset: # of bytes in a block (same as before)
Index: Instead of pointing to a row, now points to a set, so I = C/B/associativity
  Fully associative (1 set): 0 Index bits!
  Direct-mapped (associativity of 1): max Index bits
  Set associative: somewhere in-between
Tag: Remaining identifier bits (T = A – I – O)
Notes: C = cache size, B = block size

## Slide 32: Effect of Associativity on TIO (2/2)
For a fixed-size cache, each increase by a factor of two in associativity doubles the number of blocks per set (i.e. the number of slots) and halves the number of sets – decreasing the size of the Index by 1 bit and increases the size of the Tag by 1 bit
Block offset
Byte offset
Index
Tag
Decreasing associativity
Fully associative
(only one set)
Direct mapped
(only one way)
Increasing associativity
Selects the set
Used for tag comparison
Selects the word in the block
Notes: For lecture
In 2008, the greater size and power consumption of CAMs generally leads to 2-way and 4-way set associativity being built from standard SRAMs with comparators with 8-way and above being built using CAMs

## Slide 33: Set Associative Example (1/2)
Cache parameters:
  6-bit addresses, block size of 1 word, cache size of 4 words, 2-way set associative
How many sets?
  C/B/associativity = 4/1/2 = 2 sets
TIO Breakdown:
  O = log2(4) = 2, I = log2(2) = 1, T = 6 – 1 – 2 = 3
XXX
X
XX
Memory Addresses:
Block address

## Slide 34: Set Associative Example (2/2)
0000xx
0001xx
0010xx
0011xx
0100xx
0101xx
0110xx
0111xx
1000xx
1001xx
1010xx
1011xx
1100xx
1101xx
1110xx
1111xx
0
Cache:
Tag
Data
V
Slot
1
0
1
Set
0
1
Main Memory:
Each block maps into one set (either slot)
(see colors)
On a memory request: (let’s say 001011two)
1) Take Index field (0)
2) For EACH slot in set,
check valid bit,
then compare Tag
Set numbers exactly match the Index field
Main Memory shown in blocks, so offset bits not shown (x’s)

## Slide 35
Question: What is the TIO breakdown for the following cache?
32-bit address space
32 KiB 4-way set associative cache
8 word blocks
21 8 3
☐
19 8 5
☐
19 10 3
☐
17 10 5
☐
T I O

## Slide 36: Get To Know Your Staff
Category: Food

## Slide 37: Agenda
Cache Performance
Administrivia
Multilevel Caches
Set Associative Caches (Part 2)
Improving Cache Performance
Bonus: Multilevel Cache Performance Practice
Bonus: Contemporary Cache Specs

## Slide 38: Worst-Case for Direct-Mapped
Example: direct-mapped $ that holds 4 blocks
  Starts empty (all initially not valid)
Consider the memory accesses: 0, 4, 0, 4, ...
HR of 0%
  Ping pong effect: alternating requests that map into the same cache row
0
4
0
Miss
Miss
Miss
00 Mem(0)
00 Mem(0)
01
4
01 Mem(4)
0
00
. . .

## Slide 39: Set Associative Benefits
Example: 2-way associative $ holds 4 blocks
  Starts empty (all initially not valid)
Consider the memory accesses: 0, 4, 0, 4, ...
HR of (n-2)/n – big improvement!
  Reduced conflict misses because memory locations that map into the same set can co-exist
Miss
Miss
Hit
Hit
000 Mem(0)
000 Mem(0)
0
4
0
4
010 Mem(4)
010 Mem(4)
000 Mem(0)
000 Mem(0)
010 Mem(4)
Notes: For lecture
Another sample string to try 0 1 2 3 0 8 11 0 3

## Slide 40: Example: Eight-Block Cache Configs
Total size of $ = # sets × associativity
For fixed $ size, associativity ↑ means # sets ↓ and slots per set ↑
With 8 blocks, an 8-way set associative $ is same as a fully associative $

## Slide 41: 4-Way Set Associative Cache
28 = 256 sets each with four slots for blocks
31 30 . . . 13 12 11 . . . 2 1 0
Byte offset
Data
Tag
V
0
1
2
.
.
.
253
254
255
Data
Tag
V
0
1
2
.
.
.
253
254
255
Data
Tag
V
0
1
2
.
.
.
253
254
255
Index
Data
Tag
V
0
1
2
.
.
.
253
254
255
8
Index
22
Tag
Hit
Data
32
4x1 select
Slot 0
Slot 1
Slot 2
Slot 3
Notes: This is called a 4-way set associative cache because there are four cache entries for each cache index. Essentially, you have four direct mapped cache working in parallel.
This is how it works: the cache index selects a set from the cache. The four tags in the set are compared in parallel with the upper bits of the memory address.
If no tags match the incoming address tag, we have a cache miss.
Otherwise, we have a cache hit and we will select the data from the slot where the tag match occurred.

## Slide 42: Costs of Set-Associative Caches
For n-way set associative cache:
  Need n comparators for Tag comparisons
  Must choose data from correct slot (multiplexer)
On cache miss, which block do you replace in the set?
  Use a cache block replacement policy
  There are many (most are intuitively named), but we will just cover a few in this class
  http://en.wikipedia.org/wiki/Cache_algorithms#Examples
Notes: First of all, a N-way set associative cache will need N comparators instead of just one comparator (use the right side of the diagram for direct mapped cache).
A N-way set associative cache will also be slower than a direct mapped cache because of this extra multiplexer delay.
Finally, for a N-way set associative cache, the data will be available AFTER the hit/miss signal becomes valid because the hit/mis is needed to control the data MUX.
For a direct mapped cache, that is everything before the MUX on the right or left side, the cache block will be available BEFORE the hit/miss signal (AND gate output) because the data does not have to go through the comparator.
This can be an important consideration because the processor can now go ahead and use the data without knowing if it is a Hit or Miss. Just assume it is a hit.
Since cache hit rate is in the upper 90% range, you will be ahead of the game 90% of the time and for those 10% of the time that you are wrong, just make sure you can recover.
You cannot play this speculation game with a N-way set-associative cache because as I said earlier, the data will not be available to you until the hit/miss signal is valid.
+2 = 38 min. (Y:18)

## Slide 43: Block Replacement Policies (1/2)
Random Replacement:
  Hardware randomly selects a cache block in set
Least Recently Used (LRU):
  Hardware keeps track of access history and replaces the entry that has not been used for the longest time
  For 2-way set associative cache, can get away with just one bit per set
Example of a Simple “Pseudo” LRU Implementation:
  For each set, store a hardware replacement pointer that points to one slot
    Takes just log2(associativity) bits
  Whenever that slot is accessed, move pointer to next slot
    That slot is the most recently used and cannot be the LRU

## Slide 44: Benefits of Set-Associative Caches
Consider cost of a miss vs. cost of implementation
Largest gains are in going from direct mapped to 2-way (20%+ reduction in miss rate)
Notes: As cache sizes grow, the relative improvement from associativity increases only slightly; since the overall miss rate of a larger cache is lower, the opportunity for improving the miss rate decreases and the absolute improvement in miss rate from associativity shrinks significantly.

## Slide 45: Agenda
Cache Performance
Administrivia
Multilevel Caches
Set Associative Caches
Improving Cache Performance
Bonus: Multilevel Cache Performance Practice
Bonus: Contemporary Cache Specs

## Slide 46: Improving Cache Performance (1/2)
Reduce the Hit Time of the cache
  Smaller cache (less to search/check)
  1 word blocks (no MUX/selector to pick word)
Reduce the Miss Rate
  Bigger cache (capacity)
  Larger blocks (compulsory & spatial locality)
  Increased associativity (conflict)

## Slide 47: Improving Cache Performance (2/2)
Reduce the Miss Penalty
  Smaller blocks (less to move)
  Use multiple cache levels
  Use a write buffer
    Can also check on read miss (may get lucky)

## Slide 48: The Cache Design Space
Several interacting dimensions
Cache parameters:
  Cache size, Block size, Associativity
Policy choices:
  Write-through vs. write-back
  Write allocation vs. no-write allocation
  Replacement policy
Optimal choice is a compromise
  Depends on access characteristics
    Workload and use (I$, D$)
  Depends on technology / cost
Simplicity often wins
(Associativity)
Cache Size
Block Size
Bad
Good
Less
More
Factor A
Factor B
Notes: No fancy replacement policy is needed for the direct mapped cache.
As a matter of fact, that is what cause direct mapped trouble to begin with: only one place to go in the cache--causes conflict misses.
No fancy replacement policy is needed for the direct mapped cache.
As a matter of fact, that is what cause direct mapped trouble to begin with: only one place to go in the cache--causes conflict misses.
Besides working at Sun, I also teach people how to fly whenever I have time.
Statistic have shown that if a pilot crashed after an engine failure, he or she is more likely to get killed in a multi-engine light airplane than a single engine airplane.
The joke among us flight instructors is that: sure, when the engine quit in a single engine stops, you have one option: sooner or later, you land. Probably sooner.
But in a multi-engine airplane with one engine stops, you have a lot of options. It is the need to make a decision that kills those people.

## Slide 49: Summary (1/2)
Cache Performance
  AMAT = HT + MR × MP
  CPU time = IC × CPIstall × CC = IC × (CPIbase + Memory-stall cycles) × CC
Multilevel caches reduce miss penalty
  Local vs. global miss rate
  Optimize first level to be fast (low HT)
  Optimize lower levels to not miss (minimize MP)

## Slide 50: Summary (2/2)
Set associativity reduces miss rate
  N-way: cache split into sets, each of which have n slots to place memory blocks
  Fully associative: blocks can go anywhere
  Memory block maps into more than one slot, reducing conflict misses
Cache performance depends heavily on cache design (there are many choices)
  Effects of parameters and policies
  Cost vs. effectiveness

## Slide 51
You are responsible for the material contained on the following slides, though we may not have enough time to get to them in lecture.
They have been prepared in a way that should be easily readable and the material will be touched upon in the following lecture.
BONUS SLIDES

## Slide 52: Agenda
Cache Performance
Administrivia
Multilevel Caches
Set-associative Caches
Improving Cache Performance
Bonus: Multilevel Cache Performance Practice
Bonus: Contemporary Cache Specs

## Slide 53: Multilevel Cache Practice (1/3)
Processor specs:
  CPIbase of 2
  100 cycle miss penalty to main memory
  25 cycle miss penalty to unified L2$
  36% of instructions are load/stores
  2% L1 I$ miss rate; 4% L1 D$ miss rate
  0.5% global U(nified)L2$ miss rate
What is CPIstall with and without the L2$?

## Slide 54: Multilevel Cache Practice (2/3)
Notes:
  Both L1 I$ and L1 D$ send misses to L2$
  What does the global L2$ MR mean?
    MR to main memory
    Since there are 2 L1$s, implies L2$ has 2 different local MRs depending on source of access
  Use formula shown at bottom of slide 26

## Slide 55: Multilevel Cache Practice (3/3)
Without L2$:
CPIstall = 2 + 1×0.02×100 + 0.36×0.04×100
CPIstall = 5.44
With L2$:
CPIstall = 2 + 1x.02×25 + .36×.04×25 + 1x.005×100 + .36×.005×100 CPIstall = 3.54
L1
L2
Instr Fetch
Load/Store

## Slide 56: Agenda
Cache Performance
Administrivia
Multilevel Caches
Set-associative Caches
Improving Cache Performance
Bonus: Multilevel Cache Performance Practice
Bonus: Contemporary Cache Specs

## Slide 58: Intel Nehalem Die Photo
Shared L3 Cache
Core
Core
Core
Core
Memory Controller
18.9 mm (0.75 inch)
13.6 mm (0.54 inch)
Memory
Queue
Misc
IO
Misc
IO
QPI
0
QPI
1
Notes: QPI – QuickPath Interconnect (for floating point)

## Slide 59: Core Area Breakdown
Execution Units
L2 Cache & Interrupt Servicing
L1 Inst cache & Inst Fetch
L1 Data cache
L3 Cache
Memory Controller
Load Store Queue
32KiB I$ per core
32KiB D$ per core
512KiB L2$ per core
Share one 8-MiB L3$