## Slide 1: CS 61C: Great Ideas in Computer Architecture Dependability
Guest Lecturer:
Paul Ruan

## Slide 2: Review
WSC
  Servers on a rack, rack part of cluster
  Issues to handle include load balancing, failures, power usage
  PUE = Total building power / IT equipment power
Request Level Parallelism
MapReduce Data Level Parallelism
  Framework to divide up data to be processed in parallel
  Mapper outputs intermediate kv-pairs
  Reducer “combines” intermediate values with same key

## Slide 3: Agenda
Dependability
Administrivia
RAID
Error Correcting Codes

## Slide 4: Review - 6 Great Ideas in Computer Architecture
Layers of Representation/Interpretation
Moore’s Law
Principle of Locality/Memory Hierarchy
Parallelism
Performance Measurement & Improvement
Dependability via Redundancy

## Slide 5: Great Idea #6: Dependability via Redundancy
Redundancy so that a failing piece doesn’t make the whole system fail
1+1=2
1+1=2
1+1=1
1+1=2
2 of 3 agree
FAIL!

## Slide 6: Great Idea #6: Dependability via Redundancy
Applies to everything from datacenters to memory
  Redundant datacenters so that can lose 1 datacenter but Internet service stays online
  Redundant routes so can lose nodes but Internet doesn’t fail
  Redundant disks so that can lose 1 disk but not lose data (Redundant Arrays of Independent Disks/RAID)
  Redundant memory bits of so that can lose 1 bit but no data (Error Correcting Code/ECC Memory)

## Slide 7: Dependability
Fault: failure of a component
  May or may not lead to system failure
Service accomplishment
Service delivered as specified
Service interruption
Deviation from specified service
Failure
Restoration

## Slide 8: Dependability Measures
Reliability: Mean Time To Failure (MTTF)
Service interruption: Mean Time To Repair (MTTR)
Mean time between failures (MTBF)
  MTBF = MTTF + MTTR
Availability = MTTF / (MTTF + MTTR) = MTTF / MTBF
Improving Availability
  Increase MTTF: More reliable hardware/software + Fault Tolerance
  Reduce MTTR: improved tools and processes for diagnosis and repair

## Slide 9: Reliability Measures
MTTF, MTBF usually measured in hours
  E.g., average MTTF is 100,000 hours
Another measure is average number of failures per year
  E.g., 1000 disks with 100,000 hour MTTF
  365 days * 24 hours = 8760 hours
  (1000 disks * 8760 hrs/year) / 100,000 hrs = 87.6 failed disks per year on average
  87.6/1000 = 8.76% annualized failure rate (AFR)

## Slide 10: Availability Measures
Availability = MTTF / (MTTF + MTTR) as %
Since hope rarely down, shorthand is “number of 9s of availability per year”
1 nine: 90% => 36 days of repair/year
2 nines: 99% => 3.6 days of repair/year
3 nines: 99.9% => 526 minutes of repair/year
4 nines: 99.99% => 53 minutes of repair/year
5 nines: 99.999% => 5 minutes of repair/year

## Slide 11: Dependability Design Principle
No single points of failure
“Chain is only as strong as its weakest link”
Dependability Corollary of Amdahl’s Law
  Doesn’t matter how dependable you make one portion of system
  Dependability limited by part you do not improve

## Slide 12: Agenda
Dependability
RAID
Administrivia
Error Correcting Codes

## Slide 13: Arrays of Small Disks
  Can smaller disks be used to close gap in performance between disks and CPUs?
14”
10”
5.25”
3.5”
3.5”
Disk Array: 1 disk type
Conventional: 4 disk types
Low End
High End

## Slide 14: Replace Small Number of Large Disks with Large Number of Small Disks! (1988 Disks)
Capacity
Volume
Power
Data Rate
I/O Rate
MTTF
Cost
IBM 3390K
20 GBytes
97 cu. ft.
3 KW
15 MB/s
600 I/Os/s
250 KHrs
$250K
IBM 3.5" 0061
320 MBytes
0.1 cu. ft.
11 W
1.5 MB/s
55 I/Os/s
50 KHrs
$2K
x70
23 GBytes
11 cu. ft.
1 KW
120 MB/s
3900 IOs/s
??? Hrs
$150K
Disk Arrays have potential for large data and I/O rates, high MB per cu. ft., high MB per KW, but what about reliability?
9X
3X
8X
6X

## Slide 15: Replace Small Number of Large Disks with Large Number of Small Disks! (1988 Disks)
Capacity
Volume
Power
Data Rate
I/O Rate
MTTF
Cost
IBM 3390K
20 GBytes
97 cu. ft.
3 KW
15 MB/s
600 I/Os/s
250 KHrs
$250K
IBM 3.5" 0061
320 MBytes
0.1 cu. ft.
11 W
1.5 MB/s
55 I/Os/s
50 KHrs
$2K
x70
23 GBytes
11 cu. ft.
1 KW
120 MB/s
3900 IOs/s
~700 Hrs
$150K
Disk Arrays have potential for large data and I/O rates, high MB per cu. ft., high MB per KW, but what about reliability?
9X
3X
8X
6X

## Slide 16: RAID: Redundant Arrays of Inexpensive Disks
Files are "striped" across multiple disks
Redundancy yields high data availability
  service still provided to user, even if some components failed
Disks will still fail
Contents reconstructed from data redundantly stored in the array
  Capacity penalty to store redundant info
  Bandwidth penalty to update redundant info

## Slide 17: Redundant Arrays of Inexpensive Disks RAID 1: Disk Mirroring/Shadowing
• Each disk is fully duplicated onto its “mirror”
  Very high availability can be achieved
• Bandwidth sacrifice on write:
  Logical write = two physical writes
  Reads may be optimized
• Most expensive solution: 100% capacity overhead
recovery
group

## Slide 18: Parity Bit
Describes whether group of bits contains an even or odd number of 1’s
Assume from now that 1 means odd and 0 means even
  Can use xor to compute parity bit
Adding the parity bit to group will always result in an even number of 1’s (“even parity”)
  100 Parity: 1
  101 Parity: 0
If we know number of 1’s must be even, can we figure out what a single missing bit should be?
  10?11

## Slide 19: Redundant Array of Inexpensive Disks RAID 3: Parity Disk
P
10010011
11001101
10010011
. . .
logical record
1
0
1
0
0
0
1
1
1
1
0
0
1
1
0
1
1
0
1
0
0
0
1
1
1
1
0
0
1
1
0
1
P contains parity bits of the other disks.
If any disk fails, can use other disks to recover data.
Striped physical
records
X
Y
Z

## Slide 20: Administrivia
Project 3 (individual) due Sunday 8/5
Final Review – Friday 8/3, 3‐6pm in 306 Soda
Final – Thurs 8/9, 9am‐12pm, 245 Li Ka Shing – Focus on 2nd half material, though midterm material still fair game
  MIPS Green Sheet provided again
  Two‐sided handwritten cheat sheet
    Can use the back side of your midterm cheat sheet!

## Slide 21: Redundant Arrays of Inexpensive Disks RAID 4: Higher I/O Rate
D0
D1
D2
D3
P
D4
D5
D6
P
D7
D8
D9
P
D10
D11
D12
P
D13
D14
D15
P
D16
D17
D18
D19
D20
D21
D22
D23
P
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
Disk Columns
Increasing
Logical
Disk
Address
Stripe
Insides of 5 disks
Example: small read D0 & D5, large write D12-D15

## Slide 22: Inspiration for RAID 5
When writing to a disk, need to update Parity
Small writes are bottlenecked by Parity Disk: Write to D0, D5 both also write to P disk
D0
D1
D2
D3
P
D4
D5
D6
P
D7

## Slide 23: RAID 5: High I/O Rate Interleaved Parity
Independent writes
possible because of
interleaved parity
D0
D1
D2
D3
P
D4
D5
D6
P
D7
D8
D9
P
D10
D11
D12
P
D13
D14
D15
P
D16
D17
D18
D19
D20
D21
D22
D23
P
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
Disk Columns
Increasing
Logical
Disk
Addresses
Example: write to D0, D5 uses disks 0, 1, 3, 4

## Slide 24: Updating the Parity Data
D0
D1
D2
D3
P
D0'
+
+
D0'
D1
D2
D3
P'
new
data
old
data
old
parity
XOR
XOR
(1. Read)
(2. Read)
(3. Write)
(4. Write)
RAID-5: Small Write Algorithm
1 Logical Write = 2 Physical Reads + 2 Physical Writes
1 only if bit changed
Flip corresponding bits

## Slide 25: RAID 6: Recovering from 2 failures
Why > 1 failure recovery?
  operator accidentally replaces wrong disk during a failure
  since disk bandwidth is growing more slowly than disk capacity, the MTT Repair a disk in a RAID system is increasing increases the chances of a 2nd failure during repair since takes longer
  reading much more data during reconstruction meant increasing the chance of an uncorrectable media failure during read, which would result in data loss

## Slide 26: Agenda
Dependability
Administrivia
RAID
Error Correcting Codes

## Slide 27: Error Detection/Correction Codes
Memory systems generate errors (accidentally flipped-bits)
  DRAMs store very little charge per bit
  “Soft” errors occur occasionally when cells are struck by alpha particles or other environmental upsets
  “Hard” errors occur when chips permanently fail.
  Problem gets worse as memories get denser and larger

## Slide 28: Error Detection/Correction Codes
Protect against errors with EDC/ECC
Extra bits are added to each M-bit data word to produce an N-bit code word.
  Extra bits are a function of the data
  Each data word value is mapped to a valid code word.
  Certain errors change valid code words to invalid ones.

## Slide 29: Detecting/Correcting Code Concept
Detection: fails code word validity check
Correction: map to nearest valid code word
Space of possible bit patterns
2N but only 2M are valid code words
Error changes bit pattern to
an invalid code word.

## Slide 30: Block Code Principles
Hamming distance = difference in # of bits
p = 011011, q = 001111, Ham. distance (p,q) = 2
p = 011011, q = 110001, distance (p,q) = ?
Consider if the minimum distance between valid code words is 2 and get a 1 bit error.
  Can we detect it?
  Can we correct it?
Richard Hamming, 1915-98
Turing Award Winner

## Slide 31: 3 Bit Example
Organized this way, each edge represents a Hamming distance of 1.

## Slide 32: Minimum Hamming Distance 2: Detection
No 1 bit error goes to another valid code word
½ of the code words are valid

## Slide 33: Minimum Hamming Distance 3: Correction
No 2 bit error goes to another valid code
1/4 of the code words are valid
Nearest 000
(one 1)
Nearest 111
(one 0)

## Slide 34: Parity: Simple Error Detection Coding
Add parity bit when writing block of data
When data is read, check parity:
  Ok if even number of 1s
  Error if otherwise
b7b6b5b4b3b2b1b0p
+
b7b6b5b4b3b2b1b0p
+
c
Minimum Hamming distance of parity code is 2
A non-zero parity indicates an error occurred:
  Two bit errors are not detected (nor any even number of errors)
  odd numbers of errors are detected.

## Slide 35: Parity Example
Data 0101 0101
4 ones, even parity now
Write to memory: 0101 0101 0 to keep parity even
Data 0101 0111
5 ones, odd parity now
Write to memory: 0101 0111 1 to make parity even
Read from memory 0101 0101 0
4 ones => even parity, so no error
Read from memory 1101 0101 0
5 ones => odd parity, so error
What if error in parity bit?

## Slide 36: Suppose want to Correct 1 Error?
Can we correct if minimum distance is 2?
What must minimum distance be?
Richard Hamming came up with simple to understand mapping to allow Error Correction at minimum distance of 3
Called Hamming ECC for Error Correction Code

## Slide 37: Get To Know Your Staff
Category: Wishlist
 | Paul | Sung Roa
Bucketlist Item | Build a giant sandcastle | Sky diving
Skill | Drawing | Singing
Language | French | Russian
Superpower | Time Travel | Teleportation

## Slide 38: Hamming Error Correction Code
Use of extra parity bits to allow the position identification of a single error
Mark all bit positions in the code word that are powers of 2 as parity bits. (positions 1, 2, 4, 8, 16, …)
  Start numbering bits at 1 at left, not at 0 on right
2. All other bit positions are for the data bits. (positions 3, 5, 6, 7, 9, 10, 11, 12, 13, 14, 15, …)

## Slide 39: Hamming ECC
3. Each parity bit calculates the parity for some of the bits in the code word
The position of parity bit determines group of bits that it checks
Bit 1 (00012): checks bits 1,3,5,7, … (XXX12)
Bit 2 (00102): checks bits 2,3,6,7, … (XX1X2)
Bit 4 (01002): checks bits 4-7, 12-15, … (X1XX2)
Bit 8 (10002): checks bits 8-15, 24-31, … (1XXX2)

## Slide 40: Hamming ECC
4. Set parity bits to create even parity for each group
A byte of data: 10011010
Create the code word, leaving spaces for the parity bits:
_1 _2 13 _4 05 06 17 _8 19 010 111 012
Calculate the parity bits

## Slide 41: Hamming ECC
Position 1 checks bits 1,3,5,7,9,11: ? _ 1 _ 0 0 1 _ 1 0 1 0
Position 2 checks bits 2,3,6,7,10,11: 0 ? 1 _ 0 0 1 _ 1 0 1 0
Position 4 checks bits 4,5,6,7,12: 0 1 1 ? 0 0 1 _ 1 0 1 0
Position 8 checks bits 8,9,10,11,12: 0 1 1 1 0 0 1 ? 1 0 1 0
Notes: Bit 1 is 0
Bit 2 is 1
Bit 4 is 1

## Slide 42: Hamming ECC
Final code word: 011100101010
Data word: 1 001 1010
Notes: Bit 8 set to 0

## Slide 43: Hamming ECC
Finding and fixing a corrupted bit:
Suppose receive 011213140506170819110111012
Parity bits 2 and 8 incorrect. As 2 + 8 = 10, bit position 10 is location of bad bit: flip value!
Corrected value: 011100101010
Why does Hamming ECC work?
Notes: Do on the blackboard
Bit 1: 1, 3, 5, 7, 9, 11
Bit 2: 2,3, 6,7, 10,11
Bit 4: 4, 5, 6, 7, 12
Bit 8: 8, 9, 10, 11, 12

## Slide 44: Hamming Error Correcting Code
Overhead involved in single error correction code
Let p be total number of parity bits and d number of data bits in p + d bit word
If p error correction bits are to point to error bit (p + d cases) + indicate that no error exists (1 case), we need:
  2p >= p + d + 1,
  thus p >= log(p + d + 1)
  for large d, p approaches log(d)
8 bits data => d = 8, 2p = p + 8 + 1 => p = 4
16 data => 5 parity, 32 data => 6 parity, 64 data => 7 parity

## Slide 45: Hamming Single Error Correction, Double Error Detection (SEC/DED)
Adding extra parity bit covering the entire SEC code word provides double error detection as well
1 2 3 4 5 6 7 8
p1 p2 d1 p3 d2 d3 d4 p4
Let H be the position of the incorrect bit we would find from checking p1,p2, and p3 (note that 0 means no error) and let P be parity of complete code word.
H=0 P=0, no error
H≠0 P=1, correctable single error (odd parity if 1 error => p4=1)
H≠0 P=0, double error occurred (even parity if 2 errors=> p4=0)
H=0 P=1, an error occurred in p4 bit, not in rest of word
Typical modern codes in DRAM memory systems:
64-bit data blocks (8 bytes) with 72-bit code words (9 bytes).

## Slide 46: Hamming Single Error Correction + Double Error Detection: Hamming Distance 4
1 bit error (one 1) Nearest 0000
1 bit error (one 0) Nearest 1111
2 bit error (two 0s, two 1s) Halfway Between Both
Notes: 1 bit error from 0000, all numbers with one 1
1 bit error from 1111, all numbers with one 0
2 bit error from 0000, all numbers with two 1s and two 0s
2 bit error from 1111, all numbers with two 1s and two 0s

## Slide 47: What if More Than 2 Bit Errors?
Network transmissions, disks, distributed storage common failure mode is bursts of bit errors, not just one or two bit errors
  contiguous sequence of B bits in which first, last and any number of intermediate bits are in error
  caused by impulse noise or by fading in wireless
  effect is greater at higher data rates
Other tools: cyclic redundancy check, Reed-Solomon, other linear codes

## Slide 48: Summary
Great Idea: Redundancy to Get Dependability
Reliability: MTTF & Annual failure rate
Availability: % uptime (MTTF-MTTR/MTTF)
RAID: Redundant Arrays of Inexpensive Disks
  Improve I/O rate while ensuring dependability
Memory Errors:
  Hamming distance 2: Parity for Single Error Detect
  Hamming distance 3: Single Error Correction Code + encode bit position of error
  Hamming distance 4: SEC/Double Error Detection