## Slide 1
Instructor: Justin Hsia
CS 61C: Great Ideas in Computer Architecture
Course Introduction,
Number Representation

## Slide 2: Introducing Your Instructor
I’m not a professor – call me Justin
Upbringing: Born and raised in the Bay
Education: I bleed Blue and Gold (Go Bears!)
  B.S. ME, B.S. EECS, M.S. EECS
  Ph.D. EECS (expected 2014)
Research: Synthetic Biology
Teaching: EE128, EE40, CS61C (Su11, Su12, Sp13)
Interests:

## Slide 3: Agenda
Course Overview
  Six Great Ideas in Computer Architecture
Administrivia
Number Representation
  Number Bases
  Signed Representations
  Overflow
  Sign Extension

## Slide 4: What is CS 61C about?
It is about the hardware-software interface
  What does the programmer need to know to achieve the highest possible performance?
Use low-level programming languages (closer to underlying hardware)
  Allows us to talk about key hardware features in higher-level terms
  Allows programmers to harness underlying hardware parallelism for high performance

## Slide 5: Machine Structures
CS 61C
I/O system
Processor
Compiler
Operating
System
(Mac OSX)
Application (ex: browser)
Digital Design
Circuit Design
Instruction Set
Architecture
Datapath & Control
Transistors
Memory
Hardware
Software
Assembler

## Slide 6: New-School: Parallelism
Smart Phone
Warehouse Scale Computer
Leverage Parallelism &
Achieve High Performance
Core
…
Memory
Input/Output
Computer
Core
Parallel Requests
  Assigned to computer
  e.g. search “Garcia”
Parallel Threads
  Assigned to core
  e.g. lookup, ads
Parallel Instructions
  > 1 instruction @ one time
  e.g. 5 pipelined instructions
Parallel Data
  > 1 data item @ one time
  e.g. add of 4 pairs of words
Hardware descriptions
  All gates functioning in parallel at same time
Software Hardware
Cache Memory
Core
Instruction Unit(s)
Functional
Unit(s)
A0+B0
A1+B1
A2+B2
A3+B3
Logic Gates

## Slide 7: Post-PC Era: Late 2000s - ???
  Enabling Tech: Wireless networking, smartphones
  Big Players: Apple, Nokia, …
  Cost: $500, Target: Consumers on the go
  Using: Objective C, Android OS
Personal Mobile
Devices (PMD):

## Slide 8: iPhone Innards
You will learn about multiple processors, the memory hierarchy, and I/O in 61C
I/O
I/O
I/O
Processor
Memory

## Slide 9: Post-PC Era: Late 2000s - ???
  Enabling Tech: Local Area Networks, broadband Internet
  Big Players: Amazon, Google, …
  Target: Transient users or users who cannot afford high-end equipment
Cloud
Computing:

## Slide 10: Post-PC Era: Late 2000s - ???
Datacenters and
Warehouse Scale
Computers (WSC):
  Enabling Tech: Local Area Networks, cheap servers
  Cost: $200M clusters + maintenance costs
  Target: Internet services and PMDs
  Usages: MapReduce, Ruby on Rails

## Slide 11: Six Great Ideas in Computer Architecture
Layers of Representation/Interpretation
Technology Trends
Principle of Locality/Memory Hierarchy
Parallelism
Performance Measurement & Improvement
Dependability via Redundancy

## Slide 12: Great Idea #1: Levels of Representation/Interpretation
Anything can be represented as a number!
e.g. words, colors, data, logic,
code, even other numbers
lw $t0, 0($2)
lw $t1, 4($2)
sw $t1, 0($2)
sw $t0, 4($2)
Higher-Level Language Program (e.g. C)
Assembly Language Program (e.g. MIPS)
Machine Language Program (MIPS)
Hardware Architecture Description (e.g. block diagrams)
Compiler
Assembler
Machine Interpretation
temp = v[k];
v[k] = v[k+1];
v[k+1] = temp;
0000 1001 1100 0110 1010 1111 0101 1000
1010 1111 0101 1000 0000 1001 1100 0110
1100 0110 1010 1111 0101 1000 0000 1001
0101 1000 0000 1001 1100 0110 1010 1111
Logic Circuit Description (Circuit Schematic Diagrams)
Architecture Implementation

## Slide 13: Great Idea #2: Technology Trends
Predicts: Transistor count
per chip doubles
every 2 years
Gordon Moore
Intel Cofounder B.S. Cal 1950
# of transistors on an integrated circuit (IC)
Year:

## Slide 14: Great Idea #3: Principle of Locality/ Memory Hierarchy
Trade-off in speed and cost vs. capacity!
Increasing distance from application/user

## Slide 15: Storage Latency Analogy: How Far Away is the Data?
Registers
On Chip Cache
On Board Cache
Memory
Disk
1
2
10
100
Tape /Optical
Robot
10
9
10
6
Sacramento
This Campus
This Room
My Head
10 min
1.5 hr
2 Years
1 min
Pluto
2,000 Years
Andromeda
(ns)
Jim Gray Turing Award
B.S. Cal 1966
Ph.D. Cal 1969!

## Slide 16: Great Idea #4: Parallelism

## Slide 17: Great Idea #5: Performance Measurement and Improvement
Allows direct comparisons of architectures and quantification of improvements
  Most common measures are time to finish (latency) and rate of execution (throughput)
  Latency includes both setup and execution time
Match application and hardware to exploit:
  Locality, parallelism, special hardware features
Notes: Special hardware features could be specialized instructions.

## Slide 18: Great Idea #6: Dependability via Redundancy
Redundancy so that a failing piece doesn’t make the whole system fail
1+1=2
1+1=2
1+1=1
1+1=2
2 of 3 agree
FAIL!

## Slide 19: Great Idea #6: Dependability via Redundancy
Applies to everything from datacenters to storage to memory
  Redundant datacenters so that can lose 1 datacenter but Internet service stays online
  Redundant disks so that can lose 1 disk but not lose data (Redundant Arrays of Independent Disks/RAID)
  Redundant memory bits of so that can lose 1 bit but no data (Error Correcting Code/ECC Memory)
Increasing transistor density reduces the cost of redundancy

## Slide 20: Agenda
Course Overview
  Six Great Ideas in Computer Architecture
Administrivia
Number Representation
  Number Bases
  Overflow
  Signed Representations
  Sign Extension

## Slide 21: Course Information
This information can also be found on the course syllabus
Website: http://inst.eecs.berkeley.edu/~cs61c/su13
Instructor: Justin Hsia
Teaching Assistants: Albert Magyar, Jeffrey Dong, Justin Fu, Kevin Yeun, Sagar Karandikar, Shaun Benjamin
Textbooks: average 15 pages of reading/week
  Patterson & Hennessey, Computer Organization and Design, Revised 4th Edition (not ≤ 3rd Edition, not Asian 4th Edition)
  Kernighan & Ritchie, The C Programming Language, 2nd Edition
  Barroso & Holzle, The Datacenter as a Computer, 1st Edition (free!)
Piazza (http://piazza.com/class#summer2013/cs61c) is the class forum
  Every announcement, discussion, clarification happens there

## Slide 22: Course Assignments and Grading
Homework (15%) – 5 total, weighted by difficulty
Labs (6%) – 12 total, weighted equally
  Done in partners, good learning environment
Projects (24%) – 3 total, weighted equally
  MIPS Instruction Set Simulator
  Performance Tuning of a Parallel Application
  Computer Processor Pipelined Design
Midterm (24%): Friday, July 19 @ 9am
Final (26%): Friday, August 16 @ 9am
Participation and Altruism (5%)

## Slide 23: Projects
Smart Phone
Warehouse Scale Computer
Leverage Parallelism &
Achieve High Performance
Core
…
Memory
Input/Output
Computer
Core
Parallel Requests
  Assigned to computer
  e.g. search “Garcia”
Parallel Threads
  Assigned to core
  e.g. lookup, ads
Parallel Instructions
  >1 instruction @ one time
  e.g. 5 pipelined instructions
Parallel Data
  > 1 data item @ one time
  e.g. add of 4 pairs of words
Hardware descriptions
  All gates functioning in parallel at same time
Software Hardware
Cache Memory
Core
Instruction Unit(s)
Functional
Unit(s)
A0+B0
A1+B1
A2+B2
A3+B3
Logic Gates
MapReduce
Project 1: MIPS Emulator
Project 3:
CPU Design
Project 2:
Matrix Multiply

## Slide 24: Participation and Altruism
Participation
  Asking great questions in discussion and lecture and making it more interactive
  Attending office hours, completing all assignments
  Peer instruction voting (more on this next)
Altruism
  Helping others in lab, discussion, and on Piazza
This is a subjective score (internal)
  Reward for helping, not a penalty for not helping
  The point is to encourage class-wide learning!

## Slide 25: Peer Instruction
Increase real-time learning in lecture, test understanding of concepts vs. details mazur-www.harvard.edu/education/pi.phtml
Multiple choice question at end of a “segment”
  1 minute to decide yourself
  2 minutes in pairs to reach consensus
  Learn by teaching!
Vote using i>clicker remote
  Can buy from bookstore or online
  Will start using tomorrow
  Counts towards P&A grade

## Slide 26
To offer a dependable system, you must use components that almost never fail
(A)
Memory hierarchy goal is to look as fast as most expensive memory, as big as cheapest
(B)
Moore’s Law means computers will continue to get put twice as many transistors/chip every ≈2 years without fail
(C)
The levels of interpretation/representation mean that we can represent anything as 0’s and 1’s
(D)
Question: Which statement is FALSE about Great Ideas in Computer Architecture?

## Slide 27: Late Policy – Slip Days
Assignments due at 11:59:59pm (time-stamped)
You have 3 slip day tokens
  Token used for every day your project or homework is late (even by a second)
  Keep in mind how much each assignment is worth
After tokens, it’s 33% deducted per day
  No credit if more than 2 days late
  Cannot retroactively “reassign” slip days

## Slide 28: Policy on Assignments and Independent Work
With the exception of Project 2, all homework and projects are to be YOUR work and your work ALONE.
You are encouraged to discuss your assignments with other students (ideas), but we expect that what you hand in is yours.
It is NOT acceptable to copy solutions from other students.
It is NOT acceptable to copy (or start your) solutions from the Web.

## Slide 29: Policy on Assignments and Independent Work
We have tools and methods, developed over many years, for detecting this. You WILL be caught, and the penalties WILL be severe.
Both the cheater and the enabler receive –100% for the assignment. Letter to your university record documenting the incidence of cheating.
  Possible automatic F in the course
People are caught every semester of 61C

## Slide 30: Comments on Summer Version
Summer is EXTREMELY hectic!
  Double the standard pace
  Less time to synthesize material
  Falling behind just a little can be fatal
No MapReduce project
Starts deceptively slowly (first two weeks)
  If the course begins to overwhelm you, don’t wait, contact me or your TA immediately!

## Slide 31: Pedagogic Comments
Deep learning does not happen in lecture
  Learn by doing: labs, discussions, and assignments
Engaging the material outside of class and lab is critical to your success
  Study groups, testing out your own questions
  Talking with others helps solidify your own understanding
You learn best from your mistakes
  Don’t be afraid to be wrong; only you lose if you remain silent

## Slide 32: Architecture of a Lecture
Attention
Time (minutes)
0
20
25
50
53
78
80
Administrivia
+ stretch break
Summary
+ Bonus
Tech break
+ GTKYS
Full

## Slide 33: Last Things…
Discussions, labs, and OHs start immediately
  Yes, that means today!
  Switching sections: if you find another 61C student willing to swap lab, talk to your TAs
  Attend whichever discussion you want, as long as there is enough physical room
HW0 due this Tuesday, June 25th
  Find a small digital image of yourself
HW1 due this Sunday, June 30th

## Slide 34: Get To Know Your Staff
Category: Cal

## Slide 35: Agenda
Course Overview
  Six Great Ideas in Computer Architecture
Administrivia
Number Representation
  Number Bases
  Signed Representations
  Overflow
  Sign Extension

## Slide 36: Number Representation
Numbers are an abstract concept!
  Recognize that these are arbitrary symbols
Inside a computer, everything stored as a sequence of 0’s and 1’s (bits)
  Even this is an abstraction!
How do we represent numbers in this format?
  Let’s start with integers

## Slide 37: Number Bases
Key terminology: digit (d) and base (B)
Value of i-th digit is d×Bi where i starts at 0 and increases from right to left
  n digit number dn-1dn-2 ... d1d0
  value = dn-1Bn-1 + dn-2Bn-2 + ... + d1B1 + d0B0
In base B, each digit is one of B possible symbols
Base is indicated using either a prefix or a subscript

## Slide 38: Commonly Used Number Bases
Decimal (base 10)
  Symbols: 0, 1, 2, 3, 4, 5, 6, 7, 8, 9
  Notation: 9472ten = 9472
Binary (base 2)
  Symbols: 0, 1
  Notation: 101011two = 0b101011
Hexadecimal (base 16)
  Symbols: 0, 1, 2, 3, 4, 5, 6, 7, 8, 9, A, B, C, D, E, F
  Notation: 2A5Dhex = 0x2A5D
Notes: You will want to memorize this table!

## Slide 39: Number Base Examples
Examples:
9472ten = 9000 + 400 + 70 + 2
9x1000 + 4x100 + 7x10 + 2x1
9x103 + 4x102 + 7x101 + 2x100
9472ten = 2x163 + 5x162 + 0x161 + 0x160
9472ten = 2500hex
0xA15 = 0b 1010 0001 0101
3 2 1 0
Notes: Decomposition of base
Converting between bases
Skipping base 10 intermediate step

## Slide 40: Bits Can Represent Anything
n digits in base B can represent at most Bn things!
  Each of the n digits is one of B possible symbols
  Have more things? Add more digits!
Example: Logical values (1 bit) – 0 is False, 1 is True
Example: Characters
  26 letters require 5 bits (25 = 32 > 26)
Example: Students in this class (8 bits)
For convenience, can group into nibbles (4 bits) and bytes (8 bits)

## Slide 41: So What Number Is It Anyway?
Here we are using binary bit patterns to represent numbers
  Strictly speaking they are called numerals and have no meaning until you interpret them
  Is CAB a word (taxi) or a number (3243ten)?
  Is 0x999999 a number or a color (RGB)?
Keep in mind that the same bit pattern will mean different things depending on how you choose to interpret it

## Slide 42: Numbers in a Computer (1/2)
The number line:
Alt text: The Wikipedia page "List of Numbers" opens with "This list is incomplete; you can help by expanding it.“
(Source: http://xkcd.com/899)
What do we choose to represent?
Notes: Alt text is now inaccurate: “This is an incomplete list, which may never be able to satisfy particular standards for completeness. You can help by expanding it with reliably sourced entries.”

## Slide 43: Numbers in a Computer (2/2)
Numbers really have  digits, but hardware can only store a finite number of them (fixed)
  Usually ignore leading zeros
  Leftmost is most significant bit (MSB)
  Rightmost is least significant bit (LSB)
“Circle” of binary numerals: (3-bit example)

## Slide 44: Unsigned Integers
  0000two = 0ten
  0001two = 1ten
  . . .
  0110two = 6ten
  0111two = 7ten
  1000two = 8ten
  1001two = 9ten
  . . .
  1110two = 14ten
  1111two = 15ten
Represent only non-negative (unsigned) integers:
Zero?
0…0two = 0ten
Most neg number?
0…0two = 0ten
Most pos number?
1…1two = (2n-1)ten
Increment?
Notes: Notice that adding one to an unsigned integer ALWAYS results in a larger (more positive) number, with the exception of overflow.

## Slide 45: Signed Integers
n bits can represent 2n different things
  Ideally, want the range evenly split between positive and negative
How do we want to encode zero?
Can we encode them in such a way that we can use the same hardware regardless of whether the numbers are signed or unsigned?
  e.g. incrementing pos/neg numbers

## Slide 46: Sign and Magnitude
  0000two = +0ten
  0001two = +1ten
  . . .
  0110two = +6ten
  0111two = +7ten
  1000two = -0ten
  1001two = -1ten
  . . .
  1110two = -6ten
  1111two = -7ten
MSB gives sign, rest treated as unsigned (magnitude):
Zero?
0…0two and 10…0two = ±0ten
Most neg number?
1…1two = -(2(n-1)-1)ten
Most pos number?
01…1two = (2(n-1)-1)ten
Increment?
Notes: Two zeros! Incrementing negative numerals results in decrementing numbers.

## Slide 47: Biased Notation
  0000two = -7ten
  0001two = -6ten
  . . .
  0110two = -1ten
  0111two = 0ten
  1000two = +1ten
  1001two = +2ten
  . . .
  1110two = +7ten
  1111two = +8ten
Like unsigned, but “shifted” so zero is in the middle:
Zero?
01…1two = 0ten
Most neg number?
0…0two = -(2(n-1)-1)ten
Most pos number?
1…1two = 2(n-1)ten
Increment?
Notes: How do you find the number zero? Choice of 1 extra pos or neg # is arbitrary. Same as reading as unsigned but subtracting a bias of 2^(n-1)-1.

## Slide 48: One’s Complement
  0000two = +0ten
  0001two = +1ten
  . . .
  0110two = +6ten
  0111two = +7ten
  1000two = -7ten
  1001two = -6ten
  . . .
  1110two = -1ten
  1111two = -0ten
New negation procedure – complement the bits:
Zero?
0…0two and 1…1two = ±0ten
Most neg number?
10…0two = -(2(n-1)-1)ten
Most pos number?
01…1two = (2(n-1)-1)ten
Increment?
Notes: One’s complement is NOT a verb. Can still use MSB as sign bit.

## Slide 49: Two’s Complement
  0000two = 0ten
  0001two = +1ten
  . . .
  0110two = +6ten
  0111two = +7ten
  1000two = -8ten
  1001two = -7ten
  . . .
  1110two = -2ten
  1111two = -1ten
Like One’s Complement, but “shift” negative #s by 1:
Zero?
0…0two = 0ten
Most neg number?
10…0two = -2(n-1)ten
Most pos number?
01…1two = (2(n-1)-1)ten
Increment?
Notes: One’s complement is NOT a verb. Can still use MSB as sign bit.

## Slide 50: Two’s Complement Summary
Used by all modern hardware
Roughly evenly split between positive and negative
  One more negative # because positive side has 0
Can still use MSB as sign bit
To negate: Flip the bits and add one
  Example: +7 = 0b 0000 0111, -7 = 0b 1111 1001

## Slide 51: Two’s Complement Review
Suppose we had 5 bits. What integers can be represented in two’s complement?
(A) -31 to +31
(B) -15_to +15
(C) -0_to +31
(D) -16_to +15
(E) -32 to +31
 need 6 bits
 one’s complement
 unsigned
 two’s complement
 need 6 bits

## Slide 52: Overflow
Overflow is when the result of an arithmetic operation can’t be represented by the hardware bits
  i.e. the result is mathematically incorrect
Examples:
  Unsigned: 0b1…1 + 110 = 0b0…0 = 0?
  Two’s: 0b01…1 + 110 = 0b10…0 = -2(n-1)ten?
0b 0000
0001
0010
1111
1110
unsigned
Notes: Notice that the examples for unsigned and 2’s DON’T work in the other representation!

## Slide 53: Sign Extension
Want to represent the same number using more bits than before
  Easy for positive #s (add leading 0’s), more complicated for negative #s
  Sign and magnitude: add 0’s after the sign bit
  One’s complement: copy MSB
  Two’s complement: copy MSB
Example:
  Sign and magnitude: 0b 11 = 0b 1001
  One’s/Two’s complement: 0b 11 = 0b 1111
Notes: Why this is useful will become apparent later in the course.

## Slide 54: Summary (1/2)
CS61C: Learn 6 Great Ideas in Computer Architecture to enable high performance programming via parallelism
  Layers of Representation/Interpretation
  Technology Trends
  Principle of Locality/Memory Hierarchy
  Parallelism
  Performance Measurement and Improvement
  Dependability via Redundancy

## Slide 55: Summary (2/2)
Number Representation: How to represent positive and negative integers using binary
  Unsigned: Interpret numeral in base 2
  Signed: Two’s Complement
  Biased: Subtract bias
  Sign extension must preserve signed number