## Slide 1
Instructor: Justin Hsia
CS 61C: Great Ideas in Computer Architecture
Direct-Mapped Caches,
Set Associative Caches,
Cache Performance

## Slide 2: Great Idea #3: Principle of Locality/ Memory Hierarchy

## Slide 3: Extended Review of Last Lecture
Why have caches?
  Intermediate level between CPU and memory
  In-between in size, cost, and speed
Memory (hierarchy, organization, structures) set up to exploit temporal and spatial locality
  Temporal: If accessed, will access again soon
  Spatial: If accessed, will access others around it
Caches hold a subset of memory (in blocks)
  We are studying how they are designed for fast and efficient operation (lookup, access, storage)

## Slide 4: Extended Review of Last Lecture
Fully Associative Caches:
  Every block can go in any slot
    Use random or LRU replacement policy when cache full
  Memory address breakdown (on request)
    Tag field is identifier (which block is currently in slot)
    Offset field indexes into block
  Each cache slot holds block data, tag, valid bit, and dirty bit (dirty bit is only for write-back)
    The whole cache maintains LRU bits

## Slide 5: Extended Review of Last Lecture
Cache read and write policies:
  Affect consistency of data between cache and memory
  Write-back vs. write-through
  Write allocate vs. no-write allocate
On memory access (read or write):
  Look at ALL cache slots in parallel
  If Valid bit is 0, then ignore
  If Valid bit is 1 and Tag matches, then use that data
On write, set Dirty bit if write-back

## Slide 6: Extended Review of Last Lecture
Fully associative cache layout
  8-bit address space, 32-byte cache with 8-byte blocks
  LRU replacement (2 bits), write-back and write allocate
  Offset – 3 bits, Tag – 5 bits
Each slot has 71 bits; cache has 4*71+2 = 286 bits
V | D | Tag | 000 | 001 | 010 | 011 | 100 | 101 | 110 | 111
X | X | XXXXX | 0x?? | 0x?? | 0x?? | 0x?? | 0x?? | 0x?? | 0x?? | 0x??
X | X | XXXXX | 0x?? | 0x?? | 0x?? | 0x?? | 0x?? | 0x?? | 0x?? | 0x??
X | X | XXXXX | 0x?? | 0x?? | 0x?? | 0x?? | 0x?? | 0x?? | 0x?? | 0x??
X | X | XXXXX | 0x?? | 0x?? | 0x?? | 0x?? | 0x?? | 0x?? | 0x?? | 0x??
Offset
Slot
0
1
2
3
cache size (C)
block size (K)
256 B address space
Need dirty bit
LRU
XX
LRU bits

## Slide 7: Agenda
Direct-Mapped Caches
Administrivia
Set Associative Caches
Cache Performance

## Slide 8: Direct-Mapped Caches (1/3)
Each memory block is mapped to exactly one slot in the cache (direct-mapped)
  Every block has only one “home”
  Use hash function to determine which slot
Comparison with fully associative
  Check just one slot for a block (faster!)
  No replacement policy necessary
  Access pattern may leave empty slots in cache
Notes:   Check just one location to see if block is in cache.

## Slide 9: Direct-Mapped Caches (2/3)
Offset field remains the same as before
Recall: blocks consist of adjacent bytes
  Do we want adjacent blocks to map to same slot?
  Index field: Apply hash function to block address to determine which slot the block goes in
    (block address) modulo (# of blocks in the cache)
Tag field maintains same function (identifier), but is now shorter

## Slide 10: TIO Address Breakdown
Memory address fields:
Meaning of the field sizes:
  O bits ↔ 2O bytes/block = 2O-2 words/block
  I bits ↔ 2I slots in cache = cache size / block size
  T bits = A – I – O, where A = # of address bits (A = 32 here)
Tag
Index
Offset
31
0
T bits
I bits
O bits

## Slide 11: Direct-Mapped Caches (3/3)
What’s actually in the cache?
  Block of data (8 × K = 8 × 2O bits)
  Tag field of address as identifier (T bits)
  Valid bit (1 bit)
  Dirty bit (1 bit if write-back)
  No replacement management bits!
Total bits in cache = # slots × (8×K + T + 1 + 1) = 2I × (8×2O + T + 1 + 1) bits

## Slide 12: DM Cache Example (1/5)
Cache parameters:
  Direct-mapped, address space of 64B, block size of 1 word, cache size of 4 words, write-through
TIO Breakdown:
  1 word = 4 bytes, so O = log2(4) = 2
  Cache size / block size = 4, so I = log2(4) = 2
  A = log2(64) = 6 bits, so T = 6 – 2 – 2 = 2
Bits in cache = 22 × (8×22 + 2 + 1) = 140 bits
XX
XX
XX
Memory Addresses:
Block address
Notes: Compare with fully associative example from last lecture. This takes 140 bits to implement instead of 150 bits because of shorter Tag and no LRU bits.

## Slide 13: DM Cache Example (2/5)
Cache parameters:
  Direct-mapped, address space of 64B, block size of 1 word, cache size of 4 words, write-through
  Offset – 2 bits, Index – 2 bits, Tag – 2 bits
35 bits per index/slot, 140 bits to implement
V | Tag | 00 | 01 | 10 | 11
X | XX | 0x?? | 0x?? | 0x?? | 0x??
X | XX | 0x?? | 0x?? | 0x?? | 0x??
X | XX | 0x?? | 0x?? | 0x?? | 0x??
X | XX | 0x?? | 0x?? | 0x?? | 0x??
Index
00
01
10
11
Offset

## Slide 14: DM Cache Example (3/5)
Main Memory:
Which blocks map to each row of the cache?
(see colors)
On a memory request: (let’s say 001011two)
1) Take Index field (10)
2) Check if Valid bit is true in that row of cache
3) If valid, then check if Tag matches
0000xx
0001xx
0010xx
0011xx
0100xx
0101xx
0110xx
0111xx
1000xx
1001xx
1010xx
1011xx
1100xx
1101xx
1110xx
1111xx
00
01
10
11
Cache:
Tag
Data
Valid
Index
Cache slots exactly match the Index field
Which blocks map to each row of the cache?
(see colors)
Main Memory shown in blocks, so offset bits not shown (x’s)

## Slide 15: DM Cache Example (4/5)
Consider the sequence of memory address accesses
  0 2 4 8 20 16 0 2
0
4
miss
miss
Starting with a cold cache:
0 | 00 | 0x?? | 0x?? | 0x?? | 0x??
0 | 00 | 0x?? | 0x?? | 0x?? | 0x??
0 | 00 | 0x?? | 0x?? | 0x?? | 0x??
0 | 00 | 0x?? | 0x?? | 0x?? | 0x??
1 | 00 | M[0] | M[1] | M[2] | M[3]
0 | 00 | 0x?? | 0x?? | 0x?? | 0x??
0 | 00 | 0x?? | 0x?? | 0x?? | 0x??
0 | 00 | 0x?? | 0x?? | 0x?? | 0x??
1 | 00 | M[0] | M[1] | M[2] | M[3]
0 | 00 | 0x?? | 0x?? | 0x?? | 0x??
0 | 00 | 0x?? | 0x?? | 0x?? | 0x??
0 | 00 | 0x?? | 0x?? | 0x?? | 0x??
1 | 00 | M[0] | M[1] | M[2] | M[3]
0 | 00 | 0x?? | 0x?? | 0x?? | 0x??
0 | 00 | 0x?? | 0x?? | 0x?? | 0x??
0 | 00 | 0x?? | 0x?? | 0x?? | 0x??
2
hit
1 | 00 | M[0] | M[1] | M[2] | M[3]
1 | 00 | M[4] | M[5] | M[6] | M[7]
0 | 00 | 0x?? | 0x?? | 0x?? | 0x??
0 | 00 | 0x?? | 0x?? | 0x?? | 0x??
1 | 00 | M[0] | M[1] | M[2] | M[3]
1 | 00 | M[4] | M[5] | M[6] | M[7]
0 | 00 | 0x?? | 0x?? | 0x?? | 0x??
0 | 00 | 0x?? | 0x?? | 0x?? | 0x??
8
miss
1 | 00 | M[0] | M[1] | M[2] | M[3]
1 | 00 | M[4] | M[5] | M[6] | M[7]
1 | 00 | M[8] | M[9] | M[10] | M[11]
0 | 00 | 0x?? | 0x?? | 0x?? | 0x??
00
01
10
11
00
01
10
11
00
01
10
11
00
01
10
11

## Slide 16: DM Cache Example (5/5)
Consider the sequence of memory address accesses
  0 2 4 8 20 16 0 2
20
0
miss
miss
Starting with a cold cache:
  8 requests, 6 misses – last slot was never used!
1 | 00 | M[0] | M[1] | M[2] | M[3]
1 | 00 | M[4] | M[5] | M[6] | M[7]
1 | 00 | M[8] | M[9] | M[10] | M[11]
0 | 00 | 0x?? | 0x?? | 0x?? | 0x??
1 | 00 | M[0] | M[1] | M[2] | M[3]
1 | 01 | M[20] | M[21] | M[22] | M[23]
1 | 00 | M[8] | M[9] | M[10] | M[11]
0 | 00 | 0x?? | 0x?? | 0x?? | 0x??
1 | 01 | M[16] | M[17] | M[18] | M[19]
1 | 01 | M[20] | M[21] | M[22] | M[23]
1 | 00 | M[8] | M[9] | M[10] | M[11]
0 | 00 | 0x?? | 0x?? | 0x?? | 0x??
16
miss
1 | 00 | M[0] | M[1] | M[2] | M[3]
1 | 01 | M[20] | M[21] | M[22] | M[23]
1 | 00 | M[8] | M[9] | M[10] | M[11]
0 | 00 | 0x?? | 0x?? | 0x?? | 0x??
2
hit
00
01
10
11
00
01
10
11
00
01
10
11
00
01
10
11

## Slide 17: Worst-Case for Direct-Mapped
Cold DM $ that holds 4 1-word blocks
Consider the memory accesses: 0, 16, 0, 16,...
HR of 0%
  Ping pong effect: alternating requests that map into the same cache slot
Does fully associative have this problem?
0
16
0
Miss
Miss
Miss
00 M[0-3]
00 M[0-3]
01 M[16-19]
. . .

## Slide 18: Comparison So Far
Fully associative
  Block can go into any slot
  Must check ALL cache slots on request (“slow”)
  TO breakdown (i.e. I = 0 bits)
  “Worst case” still fills cache (more efficient)
Direct-mapped
  Block goes into one specific slot (set by Index field)
  Only check ONE cache slot on request (“fast”)
  TIO breakdown
  “Worst case” may only use 1 slot (less efficient)

## Slide 19: Agenda
Direct-Mapped Caches
Administrivia
Set Associative Caches
Cache Performance

## Slide 20: Administrivia
Proj1 due Sunday
  Shaun extra OH Saturday 4-7pm
HW4 released Friday, due next Sunday
Midterm:
  Please keep Sat 7/20 open just in case
  Take old exams for practice
  Doubled-sided sheet of handwritten notes
  MIPS Green Sheet provided; no calculators
  Will cover up through caches

## Slide 21: Agenda
Direct-Mapped Caches
Administrivia
Set Associative Caches
Cache Performance

## Slide 22: Set Associative Caches
Compromise!
  More flexible than DM, more structured than FA
N-way set-associative: Divide $ into sets, each of which consists of N slots
  Memory block maps to a set determined by Index field and is placed in any of the N slots of that set
  Call N the associativity
  New hash function: (block address) modulo (# sets in the cache)
  Replacement policy applies to every set
Notes: All of the tags of all of the elements of the set must be searched for a match.

## Slide 23: Effect of Associativity on TIO (1/2)
Here we assume a cache of fixed size (C)
Offset: # of bytes in a block (same as before)
Index: Instead of pointing to a slot, now points to a set, so I = log2(C/K/N)
  Fully associative (1 set): 0 Index bits!
  Direct-mapped (N = 1): max Index bits
  Set associative: somewhere in-between
Tag: Remaining identifier bits (T = A – I – O)
Notes: C = cache size, B = block size

## Slide 24: Effect of Associativity on TIO (2/2)
For a fixed-size cache, each increase by a factor of two in associativity doubles the number of blocks per set (i.e. the number of slots) and halves the number of sets – decreasing the size of the Index by 1 bit and increasing the size of the Tag by 1 bit
Block offset
Byte offset
Index
Tag
Decreasing associativity
Fully associative
(only one set)
Direct mapped
(only one way)
Increasing associativity
Selects the set
Used for tag comparison
Selects the word in the block
Notes: For lecture
In 2008, the greater size and power consumption of CAMs generally leads to 2-way and 4-way set associativity being built from standard SRAMs with comparators with 8-way and above being built using CAMs

## Slide 25: Example: Eight-Block Cache Configs
Total size of $ = # sets × associativity
For fixed $ size, associativity ↑ means # sets ↓ and slots per set ↑
With 8 blocks, an 8-way set associative $ is same as a fully associative $

## Slide 26: Block Placement Schemes
Place memory block 12 in a cache that holds 8 blocks
Fully associative: Can go in any of the slots (all 1 set)
Direct-mapped: Can only go in slot (12 mod 8) = 4
2-way set associative: Can go in either slot of set (12 mod 4) = 0

## Slide 27: SA Cache Example (1/5)
Cache parameters:
  2-way set associative, 6-bit addresses, 1-word blocks, 4-word cache, write-through
How many sets?
  C/K/N = 4/1/2 = 2 sets
TIO Breakdown:
  O = log2(4) = 2, I = log2(2) = 1, T = 6 – 1 – 2 = 3
XXX
X
XX
Memory Addresses:
Block address

## Slide 28: SA Cache Example (2/5)
Cache parameters:
  2-way set associative, 6-bit addresses, 1-word blocks, 4-word cache, write-through
  Offset – 2 bits, Index – 1 bit, Tag – 3 bits
36 bits per slot, 36*2+1 = 73 bits per set, 2*73 = 146 bits to implement
V | Tag | 00 | 01 | 10 | 11
X | XXX | 0x?? | 0x?? | 0x?? | 0x??
X | XXX | 0x?? | 0x?? | 0x?? | 0x??
X | XXX | 0x?? | 0x?? | 0x?? | 0x??
X | XXX | 0x?? | 0x?? | 0x?? | 0x??
Index
 | 0
 | 1
 | 0
 | 1
Offset
0
1
LRU
X
LRU
X

## Slide 29: SA Cache Example (3/5)
0000xx
0001xx
0010xx
0011xx
0100xx
0101xx
0110xx
0111xx
1000xx
1001xx
1010xx
1011xx
1100xx
1101xx
1110xx
1111xx
0
Cache:
Tag
Data
V
Slot
1
0
1
Set
0
1
Main Memory:
Each block maps into one set (either slot)
(see colors)
On a memory request: (let’s say 001011two)
1) Take Index field (0)
2) For EACH slot in set,
check valid bit,
then compare Tag
Set numbers exactly match the Index field
Main Memory shown in blocks, so offset bits not shown (x’s)

## Slide 30: SA Cache Example (4/5)
Consider the sequence of memory address accesses
  0 2 4 8 20 16 0 2
0
4
miss
miss
Starting with a cold cache:
0 | 000 | 0x?? | 0x?? | 0x?? | 0x??
0 | 000 | 0x?? | 0x?? | 0x?? | 0x??
0 | 000 | 0x?? | 0x?? | 0x?? | 0x??
0 | 000 | 0x?? | 0x?? | 0x?? | 0x??
1 | 000 | M[0] | M[1] | M[2] | M[3]
0 | 000 | 0x?? | 0x?? | 0x?? | 0x??
0 | 000 | 0x?? | 0x?? | 0x?? | 0x??
0 | 000 | 0x?? | 0x?? | 0x?? | 0x??
1 | 000 | M[0] | M[1] | M[2] | M[3]
0 | 000 | 0x?? | 0x?? | 0x?? | 0x??
0 | 000 | 0x?? | 0x?? | 0x?? | 0x??
0 | 000 | 0x?? | 0x?? | 0x?? | 0x??
1 | 000 | M[0] | M[1] | M[2] | M[3]
0 | 000 | 0x?? | 0x?? | 0x?? | 0x??
0 | 000 | 0x?? | 0x?? | 0x?? | 0x??
0 | 000 | 0x?? | 0x?? | 0x?? | 0x??
2
hit
1 | 000 | M[0] | M[1] | M[2] | M[3]
0 | 000 | 0x?? | 0x?? | 0x?? | 0x??
1 | 000 | M[4] | M[5] | M[6] | M[7]
0 | 000 | 0x?? | 0x?? | 0x?? | 0x??
1 | 000 | M[0] | M[1] | M[2] | M[3]
0 | 000 | 0x?? | 0x?? | 0x?? | 0x??
1 | 000 | M[4] | M[5] | M[6] | M[7]
0 | 000 | 0x?? | 0x?? | 0x?? | 0x??
8
miss
1 | 000 | M[0] | M[1] | M[2] | M[3]
1 | 001 | M[8] | M[9] | M[10] | M[11]
1 | 000 | M[4] | M[5] | M[6] | M[7]
0 | 000 | 0x?? | 0x?? | 0x?? | 0x??
0
1
0
1
0
1
0
1
0
1
0
1
0
1
0
1
0
1
0
1
0
1
0
1

## Slide 31: SA Cache Example (5/5)
Consider the sequence of memory address accesses
  0 2 4 8 20 16 0 2
20
0
miss
miss
Starting with a cold cache:
  8 requests, 6 misses
1 | 000 | M[0] | M[1] | M[2] | M[3]
1 | 001 | M[8] | M[9] | M[10] | M[11]
1 | 000 | M[4] | M[5] | M[6] | M[7]
0 | 000 | 0x?? | 0x?? | 0x?? | 0x??
1 | 000 | M[0] | M[1] | M[2] | M[3]
1 | 001 | M[8] | M[9] | M[10] | M[11]
1 | 000 | M[4] | M[5] | M[6] | M[7]
1 | 010 | M[20] | M[21] | M[22] | M[23]
1 | 010 | M[16] | M[17] | M[18] | M[19]
1 | 001 | M[8] | M[9] | M[10] | M[11]
1 | 000 | M[4] | M[5] | M[6] | M[7]
1 | 010 | M[20] | M[21] | M[22] | M[23]
16
miss
1 | 010 | M[16] | M[17] | M[18] | M[19]
1 | 000 | M[0] | M[1] | M[2] | M[3]
1 | 000 | M[4] | M[5] | M[6] | M[7]
1 | 010 | M[20] | M[21] | M[22] | M[23]
2
hit
0
1
0
1
0
1
0
1
0
1
0
1
0
1
0
1
0
1
0
1
0
1
0
1
1 | 000 | M[0] | M[1] | M[2] | M[3]
1 | 001 | M[8] | M[9] | M[10] | M[11]
1 | 000 | M[4] | M[5] | M[6] | M[7]
1 | 010 | M[20] | M[21] | M[22] | M[23]
M H M M

## Slide 32: Worst Case for Set Associative
Worst case for DM was repeating pattern of 2 into same cache slot (HR = 0/n)
  Set associative for N > 1: HR = (n-2)/n
Worst case for N-way SA with LRU?
  Repeating pattern of at least N+1 that maps into same set
  Back to HR = 0:
000 M[0-3]
001 M[8-11]
0, 8, 16, 0, 8, …
M
M
M
010 M[16-19]
000 M[0-3]
M
001 M[8-11]
M
Notes: For lecture
Another sample string to try 0 1 2 3 0 8 11 0 3

## Slide 33
Question: What is the TIO breakdown for the following cache?
32-bit address space
32 KiB 4-way set associative cache
8 word blocks
21 8 3
(A)
19 8 5
(B)
19 10 3
(C)
17 10 5
(D)
T I O

## Slide 34: Get To Know Your Instructor

## Slide 35: Agenda
Direct-Mapped Caches
Administrivia
Set Associative Caches
Cache Performance

## Slide 36: Cache Performance
Two things hurt the performance of a cache:
  Miss rate and miss penalty
  Average Memory Access Time (AMAT): average time to access memory considering both hits and misses
  AMAT = Hit time + Miss rate × Miss penalty
  (abbreviated AMAT = HT + MR × MP)
Goal 1: Examine how changing the different cache parameters affects our AMAT (Lec 12)
Goal 2: Examine how to optimize your code for better cache performance (Lec 14, Proj 2)

## Slide 37: AMAT Example
Processor specs: 200 ps clock, MP of 50 clock cycles, MR of 0.02 misses/instruction, and HT of 1 clock cycle
  AMAT = ???
Which improvement would be best?
  190 ps clock
  MP of 40 clock cycles
  MR of 0.015 misses/instruction
380 ps
360 ps
350 ps
1 + 0.02 × 50 = 2 clock cycles = 400 ps

## Slide 38: Cache Parameter Example
What is the potential impact of much larger cache on AMAT? (same block size)
  Increase HR
  Longer HT: smaller is faster
  At some point, increase in hit time for a larger cache may overcome the improvement in hit rate, yielding a decrease in performance
Effect on TIO? Bits in cache? Cost?

## Slide 39: Effect of Cache Performance on CPI
Recall: CPU Performance
CPU Time = Instructions × CPI × Clock Cycle Time
Include memory accesses in CPI:
  CPIstall = CPIbase + Average Memory-stall Cycles
  CPU Time = IC × CPIstall × CC
Simplified model for memory-stall cycles:
  Memory-stall cycles
  Will discuss more complicated models next lecture
(CC)
(IC)
Notes: Memory-stall clock cycles = Read-stall cycles + Write-stall cycles.
Reasonable write buffer depth (e.g., four or more words) and a memory capable of accepting writes at a rate that significantly exceeds the average write frequency means write buffer stalls are small.
Here we are assuming same MR and MP for reads and writes.

## Slide 40: CPI Example
Processor specs: CPIbase of 2, a 100 cycle MP, 36% load/store instructions, and 2% I$ and 4% D$ MRs
  How many times per instruction do we access the I$? The D$?
  MP is assumed the same for both I$ and D$
  Memory-stall cycles will be sum of stall cycles for both I$ and D$
Notes: I$ accessed at EVERY instruction (need to fetch from Code portion of memory!).
D$ is accessed only on loads and stores.
Naturally, you expect the I$ MR < D$ MR.

## Slide 41: CPI Example
Processor specs: CPIbase of 2, a 100 cycle MP, 36% load/store instructions, and 2% I$ and 4% D$ MRs
  Memory-stall cycles = (100% × 2% + 36% × 4%) × 100 = 3.44
  CPIstall = 2 + 3.44 = 5.44 (more than 2 x CPIbase!)
What if the CPIbase is reduced to 1?
What if the D$ miss rate went up by 1%?
I$
D$
Notes: If CPIbase = 1, CPIstall = 4.44, with memory-stall cycles accounting for 77.5% as opposed to 63.2%.
If D$ MR = 0.05, then memory-stall cycles = 3.8 and CPIstall = 5.8. Memory-stall cycles now account for 65.5% of CPIstall.

## Slide 42: Impacts of Cache Performance
CPIstall = CPIbase + Memory-stall Cycles
Relative penalty of cache performance increases as processor performance improves (faster clock rate and/or lower CPIbase)
  Relative contribution of CPIbase and memory-stall cycles to CPIstall
  Memory speed unlikely to improve as fast as processor cycle time
What can we do to improve cache performance?
Notes: For CPIbase = 1, then CPIstall = 4.44 and the amount of execution time spent on memory stalls would have risen from 3.44/5.44 = 63% to 3.44/4.44 = 77%
For miss penalty of 200, memory stall cycles = 2% 200 + 36% x 4% x 200 = 6.88 so that CPIstall = 8.88
This assumes that hit time (so hit time is 1 cycle) is not a factor in determining cache performance. A larger cache would have a longer access time (if a lower miss rate), meaning either a slower clock cycle or more stages in the pipeline for memory access.

## Slide 43: Sources of Cache Misses: The 3Cs
Compulsory: (cold start or process migration, 1st reference)
  First access to block impossible to avoid; Effect is small for long running programs
Capacity:
  Cache cannot contain all blocks accessed by the program
Conflict: (collision)
  Multiple memory locations mapped to the same cache location

## Slide 44: The 3Cs: Design Solutions
Compulsory:
  Increase block size (increases MP; too large blocks could increase MR)
Capacity:
  Increase cache size (may increase HT)
Conflict:
  Increase cache size
  Increase associativity (may increase HT)

## Slide 45: Summary
Set associativity determines flexibility of block placement
  Fully associative: blocks can go anywhere
  Direct-mapped: blocks go in one specific location
  N-way: cache split into sets, each of which have n slots to place memory blocks
Cache Performance
  AMAT = HT + MR × MP
  CPU time = IC × CPIstall × CC = IC × (CPIbase + Memory-stall cycles) × CC