## Slide 1
Instructor: Justin Hsia
CS 61C: Great Ideas in Computer Architecture
MIPS CPU Control,
Pipelining

## Slide 2: Agenda
Quick Datapath Review
Control Implementation
Administrivia
Clocking Methodology
Pipelined Execution
Pipelined Datapath

## Slide 3: Datapath Review
Part of the processor; the hardware necessary to perform all operations required
  Depends on exact ISA, RTL of instructions
Major components:
  PC and Instruction Memory
  Register File (RegFile holds registers)
  Extender (sign/zero extend)
  ALU for operations (on two operands)
  Data Memory

## Slide 4: Five Stages of the Datapath
1. Instruction
Fetch
2. Decode/
Register Read
3. Execute
4. Memory
5. Register
Write
PC
instruction
memory
+4
Register
File
rt
rs
rd
ALU
Data
memory
imm
MUX
2. Decode/
Register Read
3. Execute
4. Memory
1. Instruction
Fetch

## Slide 5: Datapath and Control
Route parts of datapath based on ISA needs
  Add MUXes to select from multiple inputs
  Add control signals for component inputs and MUXes
Analyze control signals
  How wide does each one need to be?
  For each instruction, assign appropriate value for correct routing

## Slide 6: MIPS-lite Instruction Fetch
imm16
CLK
PC
4
PC Ext
Adder
Adder
MUX
0
1
32
Instruction
Addr
Instruction
Memory
Instr Fetch Unit
nPC_sel
zero

## Slide 7: MIPS-lite Datapath Control Signals
ExtOp: 0  “zero”; 1  “sign”
ALUsrc: 0  busB; 1  imm16
ALUctr: “ADD”, “SUB”, “OR”
nPC_sel: 0  +4; 1  branch
MemWr: 1  write memory
MemtoReg: 0  ALU; 1  Mem
RegDst: 0  “rt”; 1  “rd”
RegWr: 1  write register
32
ALUctr
CLK
busW
RegWr
32
32
busA
32
busB
5
5
RW
RA
RB
rs
rt
rt
rd
RegDst
Extender
32
16
imm16
ALUSrc
ExtOp
MemtoReg
CLK
Data In
32
MemWr
0
1
RegFile
0
1
ALU
0
1
Data
Memory
WrEn
Addr
5
zero
=
nPC_sel
Instr
Fetch
Unit
CLK

## Slide 8: Hardware Design Hierarchy
system
datapath
control
state registers
combinational logic
multiplexer
comparator
code registers
register
logic
switching networks
Today

## Slide 9: Agenda
Quick Datapath Review
Control Implementation
Administrivia
Clocking Methodology
Pipelined Execution
Pipelined Datapath

## Slide 10: Processor Design Process
Five steps to design a processor:
  1. Analyze instruction set  datapath requirements
  2. Select set of datapath components & establish clock methodology
  3. Assemble datapath meeting the requirements
  4. Analyze implementation of each instruction to determine setting of control points that effects the register transfer
  5. Assemble the control logic
    Formulate Logic Equations
    Design Circuits
Control
Datapath
Memory
Processor
Input
Output
Now

## Slide 11: Purpose of Control
Controller
ALUctr
RegDst
ALUSrc
ExtOp
MemtoReg
MemWr
nPC_sel
Datapath
RegWr
Instruction<31:0>
<20:16>
<15:11>
<5:0>
<0:15>
imm16
rd
rs
rt
Instr
Memory
opcode
<25:21>
funct
<31:26>

## Slide 12: MIPS-lite Instruction RTL
Instr Register Transfer Language
addu R[rd]R[rs]+R[rt]; PCPC+4
subu R[rd]R[rs]–R[rt]; PCPC+4
ori R[rt]R[rs]+zero_ext(imm16); PCPC+4
lw R[rt]MEM[R[rs]+sign_ext(imm16)]; PCPC+4
sw MEM[R[rs]+sign_ext(imm16)]R[rs]; PCPC+4
beq if(R[rs]==R[rt]) then PCPC+4+[sign_ext(imm16)||00] else PCPC+4

## Slide 13: MIPS-lite Control Signals (1/2)
Instr Control Signals
addu ALUsrc=RegB, ALUctr=“ADD”, RegDst=rd, RegWr, nPC_sel=“+4”
subu ALUsrc=RegB, ALUctr=“SUB”, RegDst=rd, RegWr, nPC_sel=“+4”
ori ALUsrc=Imm, ALUctr=“OR”, RegDst=rt, RegWr, ExtOp=“Zero”, nPC_sel=“+4”
lw ALUsrc=Imm, ALUctr=“ADD”, RegDst=rt, RegWr, ExtOp=“Sign”, MemtoReg, nPC_sel=“+4”
sw ALUsrc=Imm, ALUctr=“ADD”, MemWr, ExtOp=“Sign”, nPC_sel=“+4”
beq ALUsrc=RegB, ALUctr=“SUB”, nPC_sel=“Br”

## Slide 14: MIPS-lite Control Signals (2/2)
add
sub
ori
lw
sw
beq
RegDst
ALUSrc
MemtoReg
RegWrite
MemWrite
nPC_sel
ExtOp
ALUctr[1:0]
1
0
0
1
0
0
X
Add
1
0
0
1
0
0
X
Subtract
0
1
0
1
0
0
0
Or
0
1
1
1
0
0
1
Add
X
1
X
0
1
0
1
Add
X
0
X
0
0
1
X
Subtract
func
op
00 0000
00 0000
00 1101
10 0011
10 1011
00 0100
Green Sheet
10 0000
See MIPS
10 0010
n/a
Control Signals
All Supported Instructions
Now how do we implement this table with CL?

## Slide 15: Generating Boolean Expressions
Idea #1: Treat instruction names as Boolean variables!
  opcode and funct bits are available to us
  Use gates to generate signals that are 1 when it is a particular instruction and 0 otherwise
Examples:
  beq = op[5]’∙op[4]’∙op[3]’∙op[2]∙op[1]’∙op[0]’
  Rtype = op[5]’∙op[4]’∙op[3]’∙op[2]’∙op[1]’∙op[0]’
  add = Rtype∙funct[5]∙funct[4]’∙funct[3]’ ∙funct[2]’∙funct[1]’∙funct[0]’

## Slide 16: Generating Boolean Expressions
Idea #2: Use instruction variables to generate control signals
  Make each control signal the combination of all instructions that need that signal to be a 1
Examples:
  MemWrite = sw
  RegWrite = add + sub + ori + lw
What about don’t cares (X’s)?
  Want simpler expressions; set to 0!
Read from row of table

## Slide 17: Controller Implementation
“AND” Logic
add
sub
ori
lw
sw
beq
“OR” Logic
RegDst
ALUSrc
MemtoReg
RegWrite
MemWrite
nPC_sel
ExtOp
ALUctr[0]
ALUctr[1]
opcode
funct
Use these two ideas to design controller:
Generate instruction signals
Generate control signals

## Slide 18: AND Control Logic in Logisim
Notes: Logisim file called “Control Plane MIPS.circ”

## Slide 19: OR Control Logic in Logisim

## Slide 20: Great Idea #1: Levels of Representation/Interpretation
lw $t0, 0($2)
lw $t1, 4($2)
sw $t1, 0($2)
sw $t0, 4($2)
Higher-Level Language Program (e.g. C)
Assembly Language Program (e.g. MIPS)
Machine Language Program (MIPS)
Hardware Architecture Description (e.g. block diagrams)
Compiler
Assembler
Machine Interpretation
temp = v[k];
v[k] = v[k+1];
v[k+1] = temp;
0000 1001 1100 0110 1010 1111 0101 1000
1010 1111 0101 1000 0000 1001 1100 0110
1100 0110 1010 1111 0101 1000 0000 1001
0101 1000 0000 1001 1100 0110 1010 1111
Logic Circuit Description (Circuit Schematic Diagrams)
Architecture Implementation
CALL HOME, WE’VE MADE HARDWARE/SOFTWARE CONTACT!!!

## Slide 21
Question: Are the following statements TRUE or FALSE? Assume use of the AND-OR controller design.
Adding a new instruction will NOT require changing any of your existing control logic.
Adding a new control signal will NOT require changing any of your existing control logic.
F F
(A)
F T
(B)
T F
(C)
T T
(D)
1 2

## Slide 22: Agenda
Quick Datapath Review
Control Implementation
Administrivia
Clocking Methodology
Pipelined Execution
Pipelined Datapath

## Slide 23: Administrivia
HW 5 due Thursday
Project 2 due Sunday
No lab on Thursday
Project 3: Pipelined Processor in Logisim

## Slide 24: Agenda
Quick Datapath Review
Control Implementation
Administrivia
Clocking Methodology
Pipelined Execution
Pipelined Datapath

## Slide 25: Clocking Methodology
Storage elements (RegFile, Mem, PC) triggered by same clock
Critical path determines length of clock period
  This includes CLK-to-Q delay and setup delay
So far we have built a single cycle CPU – entire instructions are executed in 1 clock cycle
  Up next: pipelining to execute instructions in 5 clock cycles
Clk
.
.
.
.
.
.
.
.
.
.
.
.

## Slide 26: Register-Register Timing: One Complete Cycle for addu
Clk
PC
Rs, Rt, Rd,
Op, Func
ALUctr
Instruction Memory Access Time
Old Value
New Value
RegWr
Old Value
New Value
Delay through Control Logic
busA, B
Register File Access Time
Old Value
New Value
busW
ALU Delay
Old Value
New Value
Old Value
New Value
New Value
Old Value
Register Write
Occurs Here
32
ALUctr
clk
busW
RegWr
32
busA
32
busB
5
5
Rw
Ra
Rb
RegFile
Rs
Rt
ALU
5
Rd
Clk-to-Q
Setup Time
Notes: Let’s take a more quantitative picture of what is happening.
At each clock tick, the Program Counter will present its latest value to the Instruction memory after Clk-to-Q time.
After a delay of the Instruction Memory Access time, the Opcode, Rd, Rs, Rt, and Function fields will become valid on the instruction bus.
Once we have the new instruction, that is the Add or Subtract instruction, on the instruction bus, two things happen in parallel.
First of all, the control unit will decode the Opcode and Func field and set the control signals ALUctr and RegWr accordingly. We will cover this later.
While this is happening (points to Control Delay), we will also be reading the register file (Register File Access Time).
Once the data is valid on busA and busB, the ALU will perform the Add or Subtract operation based on the ALUctr signal.
Hopefully, the ALU is fast enough that it will finish the operation (ALU Delay) before the next clock tick.
At the next clock tick, the output of the ALU will be written into the register file because the RegWr signal will be equal to 1.
+3 = 45 min. (Y:25)

## Slide 27: Register-Register Timing: One Complete Cycle for addu
Clk
PC
Rs, Rt, Rd,
Op, Func
ALUctr
Instruction Memory Access Time
Old Value
New Value
RegWr
Old Value
New Value
Delay through Control Logic
busA, B
Register File Access Time
Old Value
New Value
busW
ALU Delay
Old Value
New Value
Old Value
New Value
New Value
Old Value
Register Write
Occurs Here
32
ALUctr
clk
busW
RegWr
32
busA
32
busB
5
5
Rw
Ra
Rb
RegFile
Rs
Rt
ALU
5
Rd
Clk-to-Q
Setup Time
Notes: Let’s take a more quantitative picture of what is happening.
At each clock tick, the Program Counter will present its latest value to the Instruction memory after Clk-to-Q time.
After a delay of the Instruction Memory Access time, the Opcode, Rd, Rs, Rt, and Function fields will become valid on the instruction bus.
Once we have the new instruction, that is the Add or Subtract instruction, on the instruction bus, two things happen in parallel.
First of all, the control unit will decode the Opcode and Func field and set the control signals ALUctr and RegWr accordingly. We will cover this later.
While this is happening (points to Control Delay), we will also be reading the register file (Register File Access Time).
Once the data is valid on busA and busB, the ALU will perform the Add or Subtract operation based on the ALUctr signal.
Hopefully, the ALU is fast enough that it will finish the operation (ALU Delay) before the next clock tick.
At the next clock tick, the output of the ALU will be written into the register file because the RegWr signal will be equal to 1.
+3 = 45 min. (Y:25)

## Slide 28: Single Cycle Performance
Assume time for actions are 100ps for register read or write; 200ps for other events
Minimum clock period is?
Instr | Instr fetch | Register read | ALU op | Memory access | Register write | Total time
lw | 200ps | 100 ps | 200ps | 200ps | 100 ps | 800ps
sw | 200ps | 100 ps | 200ps | 200ps |  | 700ps
R-format | 200ps | 100 ps | 200ps |  | 100 ps | 600ps
beq | 200ps | 100 ps | 200ps |  |  | 500ps
What can we do to improve clock rate?
Will this improve performance as well?
  Want increased clock rate to mean faster programs
Notes: 1.25 GHz

## Slide 29: Agenda
Quick Datapath Review
Control Implementation
Administrivia
Clocking Methodology
Pipelined Execution
Pipelined Datapath

## Slide 30: Pipeline Analogy: Doing Laundry
Ann, Brian, Cathy, and Dave each have one load of clothes to wash, dry, fold, and put away
  Washer takes 30 minutes
  Dryer takes 30 minutes
  “Folder” takes 30 minutes
  “Stasher” takes 30 minutes to put clothes into drawers
A
B
C
D

## Slide 31: Sequential Laundry
Sequential laundry takes 8 hours for 4 loads
T
a
s
k
O
r
d
e
r
B
C
D
A
30
Time
30
30
30
30
30
30
30
30
30
30
30
30
30
30
30
6 PM
7
8
9
10
11
12
1
2 AM

## Slide 32: Pipelined Laundry
Pipelined laundry takes 3.5 hours for 4 loads!
T
a
s
k
O
r
d
e
r
B
C
D
A
12
2 AM
6 PM
7
8
9
10
11
1
Time
30
30
30
30
30
30
30

## Slide 33: Pipelining Lessons (1/2)
Pipelining doesn’t help latency of single task, just throughput of entire workload
Multiple tasks operating simultaneously using different resources
Potential speedup = number of pipeline stages
Speedup reduced by time to fill and drain the pipeline: 8 hours/3.5 hours or 2.3X v. potential 4X in this example
6 PM
7
8
9
Time
B
C
D
A
30
30
30
30
30
30
30
T
a
s
k
O
r
d
e
r

## Slide 34: Pipelining Lessons (2/2)
Suppose new Washer takes 20 minutes, new Stasher takes 20 minutes. How much faster is pipeline?
  Pipeline rate limited by slowest pipeline stage
  Unbalanced lengths of pipeline stages reduces speedup
6 PM
7
8
9
Time
B
C
D
A
30
30
30
30
30
30
30
T
a
s
k
O
r
d
e
r

## Slide 35: Agenda
Quick Datapath Review
Control Implementation
Administrivia
Clocking Methodology
Pipelined Execution
Pipelined Datapath

## Slide 36: Recall: 5 Stages of MIPS Datapath
1) IF: Instruction Fetch, Increment PC
2) ID: Instruction Decode, Read Registers
3) EX: Execution (ALU) Load/Store: Calculate Address Others: Perform Operation
4) MEM: Load: Read Data from Memory Store: Write Data to Memory
5) WB: Write Data Back to Register

## Slide 37: Pipelined Datapath
Add registers between stages
  Hold information produced in previous cycle
5 stage pipeline
  Clock rate potentially 5x faster
1. Instruction
Fetch
2. Decode/
Register Read
3. Execute
4. Memory
5. Write
Back
PC
instruction
memory
+4
Register
File
rt
rs
rd
ALU
Data
memory
imm
MUX

## Slide 38: Pipelining Changes
Registers affect flow of information
  Name registers for adjacent stages (e.g. IF/ID)
  Registers separate the information between stages
    You can still pass information around registers
  At any instance of time, each stage working on a different instruction!
Will need to re-examine placement of wires and hardware in datapath

## Slide 39: More Detailed Pipeline
Examine flow through pipeline for lw

## Slide 40: Instruction Fetch (IF) for Load
Components in use are highlighted
For sequential logic, left half means write, right half means read

## Slide 41: Instruction Decode (ID) for Load

## Slide 42: Execute (EX) for Load

## Slide 43: Memory (MEM) for Load

## Slide 44: Write Back (WB) for Load
There’s something wrong here! (Can you spot it?)
Wrong register number!

## Slide 45: Corrected Datapath
Now any instruction that writes to a register will work properly

## Slide 46: Get To Know Your Staff
Category: Movies

## Slide 47: Agenda
Quick Datapath Review
Control Implementation
Administrivia
Clocking Methodology
Pipelined Execution
Pipelined Datapath (Continued)

## Slide 48: Pipelined Execution Representation
Every instruction must take same number of steps, so some will idle
  e.g. MEM stage for any arithmetic instruction
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
Time

## Slide 49: Graphical Pipeline Diagrams
Use datapath figure below to represent pipeline:
IF
ID
EX
Mem
WB
ALU
I$
Reg
D$
Reg
1. Instruction
Fetch
2. Decode/
Register Read
3. Execute
4. Memory
5. Write
Back
PC
instruction
memory
+4
Register
File
rt
rs
rd
ALU
Data
memory
imm
MUX

## Slide 50: Graphical Pipeline Representation
I
n
s
t
r
O
r
d
e
r
Load
Add
Store
Sub
Or
I$
Time (clock cycles)
I$
ALU
Reg
Reg
I$
D$
ALU
ALU
Reg
D$
Reg
I$
D$
Reg
ALU
Reg
Reg
Reg
D$
Reg
D$
ALU
RegFile: right half is read, left half is write
Reg
I$

## Slide 51: Instruction Level Parallelism (ILP)
Pipelining allows us to execute parts of multiple instructions at the same time using the same hardware!
  This is known as instruction level parallelism
Recall: Types of parallelism
  DLP: same operation on lots of data (SIMD)
  TLP: executing multiple threads “simultaneously” (OpenMP)

## Slide 52: Pipeline Performance (1/3)
Use Tc (“time between completion of instructions”) to measure speedup
  Equality only achieved if stages are balanced (i.e. take the same amount of time)
If not balanced, speedup is reduced
Speedup due to increased throughput
  Latency for each instruction does not decrease

## Slide 53: Pipeline Performance (2/3)
Assume time for stages is
  100ps for register read or write
  200ps for other stages
What is pipelined clock rate?
  Compare pipelined datapath with single-cycle datapath
Instr | Instr fetch | Register read | ALU op | Memory access | Register write | Total time
lw | 200ps | 100 ps | 200ps | 200ps | 100 ps | 800ps
sw | 200ps | 100 ps | 200ps | 200ps |  | 700ps
R-format | 200ps | 100 ps | 200ps |  | 100 ps | 600ps
beq | 200ps | 100 ps | 200ps |  |  | 500ps

## Slide 54: Pipeline Performance (3/3)
Single-cycle
Tc = 800 ps
Pipelined
Tc = 200 ps
Notes: Here using Tc as “time between completion of instructions.”

## Slide 55: Pipelining and ISA Design
MIPS Instruction Set designed for pipelining!
All instructions are 32-bits
  Easier to fetch and decode in one cycle
Few and regular instruction formats, 2 source register fields always in same place
  Can decode and read registers in one step
Memory operands only in Loads and Stores
  Can calculate address 3rd stage, access memory 4th stage
Alignment of memory operands
  Memory access takes only one cycle
Notes: MIPS originally stood for Microprocessor without Interlocked Pipeline Stages

## Slide 56
Question: Assume the stage times shown below.
Suppose we remove loads and stores from our ISA. Consider going from a single-cycle implementation to a 4-stage pipelined version.
The latency will be 1.25x slower.
The throughput will be 3x faster.
F F
(A)
F T
(B)
T F
(C)
T T
(D)
1 2
Instr Fetch | Reg Read | ALU Op | Mem Access | Reg Write
200ps | 100 ps | 200ps | 200ps | 100 ps

## Slide 57: Summary
Implementing controller for your datapath
  Take decoded signals from instruction and generate control signals
  Use “AND” and “OR” Logic scheme
Pipelining improves performance by exploiting Instruction Level Parallelism
  5-stage pipeline for MIPS: IF, ID, EX, MEM, WB
  Executes multiple instructions in parallel
  Each instruction has the same latency
  Be careful of signal passing (more on this next lecture)