## Slide 1: Introductory Topics
EE122 TAs past and present

## Slide 2: Comprehension
How fast is my speech?
  ~1000 ft/s (speed of sound)
  ~125 words/minute
What about Steve Woodmore?
  ~1000 ft/s (speed of sound)
  ~640 words/minute (maybe)
How long would it take:
  to hear me or Steve, if we shout “Help” (very loudly) from Stanford? (~40 miles [~200,000 feet] away)
  me or Steve to dictate War and Peace? (~600,000 words)
N.B. If-I-am-actually-speaking-far-too-fast
o r w a y t o o s l o w l y, let me know!
  propagation delay
transmission delay

## Slide 3: Transmission Delay

## Slide 4: Transmission Delay
Time taken to push data onto link
Measured from
  when the first bit of data is pushed onto the link to
  when the last bit of data is pushed onto the link
Limited by the Bandwidth of the link

## Slide 5: Propagation Delay

## Slide 6: Propagation Delay
Time taken by data to traverse a link
Limited by the speed of light
Latency of a link is the propagation delay to traverse the link

## Slide 7: Transmission and Propagation Delay
Propagation delay
Transmission delay
A
B
A
B
Packet

## Slide 8: Queuing Delay

## Slide 9: Queuing Delay
Time a packet spends in a buffer/queue of a switch / router
Only when arrival rate > service rate
Especially when packet arrivals are bursty

## Slide 10: Bursty

## Slide 11: Not Bursty

## Slide 12: Queuing Delay
A
B
C
Transmission delay doubles
Brown packet waits for half the trans. delay of blue packet
Queuing delay

## Slide 13: No Queuing Delay
A
B
C
Transmission delay doubles
Brown packet does not have to wait

## Slide 14: End-to-End Delay
Propagation delay
Transmission delay
Queuing delay
Processing delay
Sum of all delays
End-to-End Delay
+

## Slide 15: Round Trip Time (RTT)
Time for packet to reach a destination AND a response to return
A
B
Packet
Response

## Slide 16: Worksheet
Propagation delay
Transmission delay
A
B
Size of transfer / Bandwidth of link
Physical distance / Speed of light
A
B