## Slide 1: Middleboxes & Network Appliances
EE122 TAs Past and Present

## Slide 2: What is a middlebox?
“A middlebox is defined as any intermediary device performing functions other than the normal, standard functions of an IP router on the datagram path between a source host and destination host.” [RFC 3234]

## Slide 3
Is it on the data path?
No
Why are you even asking this.
Yes
Is it a router or a switch?
Yes
No
It’s a Middlebox
It’s a router or a switch (duh).

## Slide 4: Example: Firewalls
You are building one of these in Project 3!
- Blocks traffic determined to be malicious.
Often based on an “Access Control List” of filters for what is acceptable/unacceptable.
Example: DROP src.port != 80

## Slide 5: Example: Proxy
Intermediates connections between multiple clients and external web servers.
Key benefit: Caching
  One user accesses New York Times in the morning, after which 100 more access it as well. With a proxy, pay for 1/100 the bandwidth.

## Slide 6: Example: Network Address Translator
Allows multiple clients using private IP addresses to share a public IP address.
Invented to solve IPv4 Address Exhaustion
Your home network almost certainly uses a NAT.

## Slide 7: Example: Network Address Translator
Private IP Address Ranges:
-10.0.0.0/8, 172.16.0.0/12, 192.168.0.0/16
Not publicly routable – reserved for use within a private network only.

## Slide 8: Example: Network Address Translator
Mr. NAT
Mr. Scott: 10.0.0.5
Mr. Panda: 10.0.0.4
Ms. Mittal: 10.0.0.3
Internal | External
Mr. NAT: 169.229.49.103

## Slide 9: Example: Network Address Translator
Mr. NAT
Mr. Scott: 10.0.0.5
Mr. Panda: 10.0.0.4
Ms. Mittal: 10.0.0.3
Internal | External
Mr. NAT: 169.229.49.103
Dst: 7.6.5.4 p80
From: 10.0.0.5 p 5678

## Slide 10: Example: Network Address Translator
Mr. NAT
Mr. Scott: 10.0.0.5
Mr. Panda: 10.0.0.4
Ms. Mittal: 10.0.0.3
Internal | External
10.0.0.5, 5678 | 5678
Mr. NAT: 169.229.49.103
Dst: 7.6.5.4 p80
From: 10.0.0.5 p 5678

## Slide 11: Example: Network Address Translator
Mr. NAT
Mr. Scott: 10.0.0.5
Mr. Panda: 10.0.0.4
Ms. Mittal: 10.0.0.3
Internal | External
10.0.0.5, 5678 | 5678
Mr. NAT: 169.229.49.103
Dst: 7.6.5.4 p80
From: 169.229.49.103
p 5678

## Slide 12: Example: Network Address Translator
Mr. NAT
Mr. Scott: 10.0.0.5
Mr. Panda: 10.0.0.4
Ms. Mittal: 10.0.0.3
Internal | External
10.0.0.5, 5678 | 5678
Mr. NAT: 169.229.49.103
Dst: 7.6.5.4 p80
From: 169.229.49.103
p 5678
Dst: 169.229.49.103
p 5678
From: 7.6.5.4 p80

## Slide 13: Example: Network Address Translator
Mr. NAT
Mr. Scott: 10.0.0.5
Mr. Panda: 10.0.0.4
Ms. Mittal: 10.0.0.3
Internal | External
10.0.0.5, 5678 | 5678
Mr. NAT: 169.229.49.103
Dst: 10.0.0.5
p 5678
From: 7.6.5.4 p80

## Slide 14: Example: Network Address Translator
Mr. NAT
Mr. Scott: 10.0.0.5
Mr. Panda: 10.0.0.4
Ms. Mittal: 10.0.0.3
Internal | External
10.0.0.5, 5678 | 5678
Mr. NAT: 169.229.49.103
Dst: 10.0.0.5
p 5678
From: 7.6.5.4 p80

## Slide 15: Example: Network Address Translator
Mr. NAT
Mr. Scott: 10.0.0.5
Mr. Panda: 10.0.0.4
Ms. Mittal: 10.0.0.3
Internal | External
10.0.0.5, 5678 | 5678
Mr. NAT: 169.229.49.103
Dst: 7.6.4.2 p80
Src: 10.0.0.4
p 5678

## Slide 16: Example: Network Address Translator
Mr. NAT
Mr. Scott: 10.0.0.5
Mr. Panda: 10.0.0.4
Ms. Mittal: 10.0.0.3
Internal | External
10.0.0.5, 5678 | 5678
10.0.0.4, 5678 | 9943
Mr. NAT: 169.229.49.103
Dst: 7.6.4.2 p80
Src: 10.0.0.4
p 5678

## Slide 17: Example: Network Address Translator
Mr. NAT
Mr. Scott: 10.0.0.5
Mr. Panda: 10.0.0.4
Ms. Mittal: 10.0.0.3
Internal | External
10.0.0.5, 5678 | 5678
10.0.0.4, 5678 | 9943
Mr. NAT: 169.229.49.103
Dst: 7.6.4.2 p80
Src: 169.229.49.103
P 9943

## Slide 18: Example: Network Address Translator
Mr. NAT
Mr. Scott: 10.0.0.5
Mr. Panda: 10.0.0.4
Ms. Mittal: 10.0.0.3
Internal | External
10.0.0.5, 5678 | 5678
10.0.0.4, 5678 | 9943
Mr. NAT: 169.229.49.103
Dst: 7.6.4.2 p80
Src: 169.229.49.103
P 9943

## Slide 19: Problems & Answers

## Slide 20: (1)
(a) L7
(b) L3 (Block this IP address), L4 (Block this port), L7 (Block this DNS address)
(c) L3 and L4 (IP addresses and Ports)

## Slide 21: (2)
There is no correct answer!
People have argued about this for years.
Pro:
Some are performance optimizations
Many cannot be implemented at app layer
Con:
Unexpected impact at application layer
Often implement redundant behaviors

## Slide 22: (2)
There is no correct answer!
People have argued about this for years.
Pro:
Some are performance optimizations
Many cannot be implemented at app layer
Con:
Unexpected impact at application layer
Often implement redundant behaviors

## Slide 23: (3)
(a) dest addr/port rewritten, checksum recalc'd, delivered to 10.0.0.6:4113 (Mr. Scott)
(b) src addr/port rewritten, checksum recalc'd, delivered to 8.5.3.2 (some Internet person)

## Slide 24: (4)
There are only 65336 unique TCP port numbers. If Mr. Scott has 65336 TCP connections open, Ms. Mittal will not be able to open another, and her connection will either reset or time out because the NAT has run out of port numbers to allocate.

## Slide 25: (5)
Mr. Panda’s server is behind a NAT. Because NATs only establish mappings for outgoing connections, Mr. Pandas incoming requests are dropped at the NAT.
Mr. Panda could set up his server to send out fake “SYN” packets on port 252. This technique is called “hole-punching.”

## Slide 26: (6)
(a) 100 MB / 5min is 2.7 Mbps
(b) 1% of that -> 27Kbps