## Slide 1: Wireless

## Slide 2: Hidden Terminals
2
A talks to B
C senses the channel
  C does not hear A’s transmission
C talks to B
Signals from A and B collide
Carrier Sense will be ineffective – need to sense at receiver
A
B
C
transmit range
Collision
Notes: 2

## Slide 3: Exposed Terminals
3
B talks to A
C wants to talk to D
C senses the channel and finds it busy
C remains quiet (when it could have transmitted)
Carrier sense would prevent a successful transmission
  But we do carrier sense anyway (why?)
A
B
C
D
Notes: 3

## Slide 4: Key Points
No concept of a global collision
  Different receivers hear different signals
  Different senders reach different receivers
Collisions are at receiver, not sender
  Only care if receiver can hear the sender clearly
  It does not matter if sender can hear someone else
  As long as that signal does not interfere with receiver
Goal of protocol:
  Detect if receiver can hear sender
  Tell senders who might interfere with receiver to shut up

## Slide 5: MA with Collision Avoidance (MACA)
5
Before every data transmission
  Sender sends a Request to Send (RTS) frame containing the length of the transmission
  Receiver responds with a Clear to Send (CTS) frame
  Sender transmits
  Receiver sends an ACK; now another sender can send data
When sender doesn’t get a CTS back, it assumes collision
When you hear a CTS, you keep quiet until scheduled transmission is over (hear ACK)
sender
receiver
other node in
sender’s range
RTS
ACK
data
CTS
Notes: 5

## Slide 6: MACA, con’t
6
If other nodes hear RTS, but not CTS: send
  Presumably, destination for first sender is out of node’s range
  Can cause problems when a CTS is lost
sender
receiver
other node in
sender’s range
RTS
data
CTS
data
Notes: 6

## Slide 7: Hidden Terminals
7
A sends RTS
B sends CTS
C also hears CTS
  C doesn’t transmit
Collision avoided!
A
B
C
transmit range
RTS
CTS
Data
CTS
Notes: 7
http://www-inst.eecs.berkeley.edu/~ee122/fa07/

## Slide 8: Exposed Terminals
8
B sends RTS to A
C gets this RTS as well
C cannot hear A’s CTS
C can also transmit!!
A
B
C
D
RTS
CTS
RTS
A
B
C
D
Transmission
can be done
Can’t hear CTS
A
B
C
D
Notes: 8

## Slide 9: Problem 3 Cheating
A
B
C
D
A
B
C
D
Can C improve it’s performance by “cheating” and ignoring the CTS messages
exchanged between A and B?
Notes: 9
http://wwwhome.math.utwente.nl/~haanr/Data/paper_WCNC05.pdf

## Slide 10: Problem 3 Cheating
A
B
C
D
Can D improve it’s performance by “cheating” and ignoring the CTS messages
exchanged between A and B?
A
B
C
D
Notes: 10
http://wwwhome.math.utwente.nl/~haanr/Data/paper_WCNC05.pdf

## Slide 11: Problem 4: (a)
Gagged Station:
RTS (1)
CTS (2)
CTS (2) for A
RTS (3)
A
B
C
D
A
B
C
Transmission
Not done
D
Notes: 11
http://wwwhome.math.utwente.nl/~haanr/Data/paper_WCNC05.pdf

## Slide 12
A
B
C
D
RTS (3)
CTS (4)
CTS (4) for A
A
B
C
D
A
B
C
D
E
E
RTS (1)
RTS (1) for E
C can’t hear this
C is now masked
CTS (2)
C doesn’t get to know that A and B are communicating
Problem 4: (b)
Masked Station:

## Slide 13: Problem 4: (c)
Fairness?
Starvation?
RTS (1)
CTS (2)
CTS (2) for A
RTS (3)
A
B
C
D
A
B
C
Transmission
Not done
D
Notes: 13
http://wwwhome.math.utwente.nl/~haanr/Data/paper_WCNC05.pdf

## Slide 14: Problem 5: Frame Sizing
14
Too small frames
Comparable to size of RTS / CTS messages
Large overhead!
Notes: 14