UNIVERSITY OF CALIFORNIA

College of Engineering

Department of Electrical Engineering and Computer Sciences

EE 130/230M	Prof. Liu & Dr. Xu

Spring 2013

Solution to Homework Assignment #7

Problem 1: pn Diode Charge Control Model

Given: junction area A = 100 m2; minority-carrier lifetimes (n = 10-6 s (p side) and (p = 10-7 s (n side); T = 300K.

Since the minority carrier concentrations (np and pn) are enhanced within the quasi-neutral regions, the diode is forward biased.  The majority carrier concentrations (pp and nn) are not significantly enhanced, however, so low-level injection conditions prevail.

- Since low-level injection conditions prevail, the “Law of the Junction” holds: within the depletion region and at the edges of the depletion region, np=ni2 ( exp{qVA/kT}.

np and pn each are enhanced by a factor 1010 at the edges of the depletion region,

so 1010 = exp{qVA/kT} ( VA = (kT/q) ( ln(1010) = 10 × (kT/q) ( ln(10) = 10 × (60 mV) = 0.6 V.

- pp = NA = 1016 cm-3 and nn = ND = 1018 cm-3

- np(-xp) = np(-xp) – np0(-xp) = 1014 – 104 ( 1014 cm-3.  pn(xn) = pn(xn) – pn0(xn) = 1012 – 102 ( 1012 cm-3

The majority carrier concentrations (pp and nn) are not significantly enhanced within the quasi-neutral regions, so low-level injection conditions prevail.

- From Lecture 4, Slide 16 the electron mobility for NA =1016 cm-3 is n =1200 cm2/V(s and the hole mobility for ND =1018 cm-3 is p =150 cm2/V(s.

The electron diffusion constant Dn= n( (kT/q)=1200×0.026=31.2 cm2/s.

The hole diffusion constant, Dp= p( (kT/q)=150×0.026=3.9 cm2/s.

The electron minority carrier diffusion length = 55 m

And the hole minority carrier diffusion length= 0.624 m

- Excess minority carrier charge is stored within the quasi-neutral regions:

QP = qApn(xn) Lp = 1.6×10-19×(100×10-8)×1012× 6.24×10-4 = 9.98×10-17 C    (624 holes)

QN = (qAnp(-xp) Ln = (1.6×10-19×(100×10-8)×1014× 5.5×10-3 = 8.8×10-14 C  (550,000 electrons)

- The diode current is found using the charge control model:

Ip(xn) = QP/(p= 9.98×10-17/10-7 = 9.98×10-10 A

In(-xp) = (QN/(n = 8.8×10-14/10-6 = 8.8×10-8 A

I = Ip(xn) + In(-xp) = 8.9×10-8 A

The current is dominated by electron injection from the more heavily doped n side into the p side.

Problem 2: pn Junction Small-Signal Model

- From Problem 1, IDC= 8.9×10-8 A. The small-signal resistance R = (kT/q)/ IDC=0.026/8.9×10-8 =2.9×105 .

Since the n-type side is degenerately doped (ND = 1018 cm-3), we should use the equation on Slide 20 of Lecture 3 to find the reduction in band gap energy on the n side:

=35meV

The built-in potential is then

= (1.12-0.035)/2 + 0.026×ln(1016/1010)=0.902V

The depletion width

Depletion capacitance

Diffusion capacitance

Total capacitance C=Cj+ CD = 0.39×10-11 F.

A schematic of the small-signal model is shown below.

- Under reverse bias, the stored minority carrier charge within the quasi-neutral regions is negligible and so the depletion capacitance (CJ) is the dominant component of small-signal capacitance.  From  Lecture 13 Slide 14,

The plot of 1/C2 vs. VA is shown below.

Extrapolating to zero, the x-intercept occurs at VA = Vbi = 0.902 V.

Problem 3: Transient Response of a pn Junction

- From Lecture 13 Slide 20 the storage delay time is = 10-6 ( ln(1+1) = 0.693 s

- Assuming that the diode turns on from i = 0 (QN = 0 and QP = 0) at 2 μs we can adapt the equation from Lecture 14 Slide 3 to obtain

where t' = t ( 2 μs.

Problem 4: Photodiode

- hole diffusion equation within the quasi-neutral n-type region is

In steady state (Δpn/(t = 0.

Far away from the junction (x ( ∞) in the quasi-neutral region(2Δpn/(x2 = 0.  Therefore

- Under steady state conditions, the hole diffusion equation within the quasi-neutral n-type region is

for which the general solution is

where x' is defined to be 0 at the depletion region edge on the n side (ref. Lecture 10 Slide 12).

Assuming low-level injection so that the Law of the Junction (ref. Slide 8 of Lecture 10) holds, the boundary conditions are

Because exp(x'/LP) → ∞ as x'→ ∞, the only way the second boundary condition can be satisfied is for A2 to be zero.

With A2 = 0, the first boundary condition yields

The hole diffusion current density is then:

Similarly, under steady state conditions the electron diffusion equation within the quasi-neutral p-type region is

for which the general solution is

where x'' is defined to be 0 at the depletion region edge on the p side and increases with distance into the quasi-neutral p-type region, i.e. it is in the negative x direction (ref. Lecture 10 Slide 12).

Again assuming low-level injection, the boundary conditions are

Following the same reasoning as for pn above, we obtain

The electron diffusion current density is then:

The total diode current I = AJ, where

(Note that there is a minus sign in front of Jn(x'') because x'' is in the negative x direction.)

(Note that Dpp = Lp2 and Dnn = Ln2.)

- The diode current is given by the ideal diode equation with an additional negative term due to illumination when GL ≠0, i.e. the ideal I-V curve is shifted down by an amount equal to IL.

Since IL ( GL, the shift downward increases proportionately with GL as shown in the plot below.