## Slide 1: EE232: Lightwave Devices
Prof: Ming Wu
GSI: Kevin Han
Discussion 1/17/18

## Slide 2: EE232 overview
Lectures will mainly cover lasers and detectors
Discussions will mainly cover other photonic devices – waveguides, couplers, modulators
Lumerical FDTD and related applications will be used throughout discussion and for final project
Dual microring resonator
CdS nanowire laser
Notes: Unusual plasmonic laser structure

## Slide 3: Today: intro to FDTD
General FDTD simulation and E&M concepts
Example: DVD reader

## Slide 4: General simulation concepts
The finite-difference time domain (FDTD) method simulates Maxwell’s equations in the time domain:
Constitutive relations:
Pros: easy to implement, covers wide frequency range in single simulation, can handle most material types
Cons: meshing can be tricky, large simulations difficult
    Can extract far field using post-processing

## Slide 5: General simulation concepts
FDTD evaluates Maxwell’s equations on a grid, eg.
…
Source: Wikipedia
(Faraday’s law)

## Slide 6: General simulation concepts
Source
Object
Radiation

## Slide 7: General simulation concepts
Computational domain
Source
Object
Truncation boundary
Radiation

## Slide 8: Boundary conditions
Computational domain
Perfectly matched layer (PML)
Source
Object
Radiation

## Slide 9: Perfectly matched layer (PML)
Artificial material that absorbs radiation without reflection
This is perhaps the most common way to truncate a computational domain.
Disadvantages:
  Some reflections from PML can occur. This can be minimized by ensuring that radiation hits PML at a 90 degree angle; i.e. place PML far from any scatterer or use circular computation domain if possible
  Magnitude of reflections is wavelength dependent
  Additional computational complexity: PML needs to be meshed and the fields need to be solved in this region

## Slide 10: Other boundary conditions
Perfect electrical conductor (PEC): All radiation is reflected
Perfect magnetic conductor (PMC): Less common
Periodic boundary condition: Used for periodic structures. Need only simulate a unit cell.
Source: Griffiths, Intro to Electrodynamics

## Slide 11: Other boundary conditions
Symmetric and anti-symmetric boundary: used when simulation has a mirror symmetry, to reduce simulation time by factor of 2, 4, or 8

## Slide 12: Example
Line current source
Source: Jianming Jin, “Theory and Computation of Electromagnetic Fields”

## Slide 13
Source: Jianming Jin, “Theory and Computation of Electromagnetic Fields”

## Slide 14
Source: Jianming Jin, “Theory and Computation of Electromagnetic Fields”

## Slide 15
Source: Jianming Jin, “Theory and Computation of Electromagnetic Fields”

## Slide 16: FDTD code implementation for previous example
< 50 lines of MATLAB code!
%Electric flux (Dz)
Dz(2:M-1,2:N-1)=...
(1./beta_x(2:M-1,2:N-1)).*(alpha_x(2:M-1,2:N-1).*Dz_negt(2:M-1,2:N-1)...
+(epsilon/delx)*(Hy(2:M-1,2:N-1)-Hy(1:M-2,2:N-1))...
-(epsilon/dely)*(Hx(2:M-1,2:N-1)-Hx(2:M-1,1:N-2))-epsilon*Jz(2:M-1,2:N-1));
%Electric field intensity (Ez)
Ez(2:M-1,2:N-1)=...
(1./beta_y(2:M-1,2:N-1)).*(alpha_y(2:M-1,2:N-1).*Ez_negt(2:M-1,2:N-1)...
+(1/epsilon)*beta_z(2:M-1,2:N-1).*Dz(2:M-1,2:N-1)...
-(1/epsilon)*alpha_z(2:M-1,2:N-1).*Dz_negt(2:M-1,2:N-1));
%Apply Etan=0 B.C
Ez(1:M,25)=0;
%Update field components
Ez_negt=Ez;
Hx_negt=Hx;
Hy_negt=Hy;
Dz_negt=Dz;
Bx_negt=Bx;
By_negt=By;
for n=1:1:timesteps
Jz(src_X,src_Y)=exp(-0.5*(((n-1)*delt)/(2*period))^2)*sin(omega*(n-1)*delt);
%Size of grids
%Bx,Hx M rows, N-1 columns
%By,Hy M-1 rows, N columns
%Dz,Ez M rows, N columns
%Magnetic flux (Bx, By)
Bx(1:M,1:N-1)=(1./beta_y(1:M,1:N-1)).*(alpha_y(1:M,1:N-1).*Bx_negt(1:M,1:N-1)-...
(epsilon/dely)*(Ez_negt(1:M,2:N)-Ez_negt(1:M,1:N-1)));
By(1:M-1,1:N)=(1./beta_z(1:M-1,1:N)).*(alpha_z(1:M-1,1:N).*By_negt(1:M-1,1:N)+...
(epsilon/delx)*(Ez_negt(2:M,1:N)-Ez_negt(1:M-1,1:N)));
%Magnetic field intensity (Hx, Hy)
Hx(1:M,1:N-1)=(1./beta_z(1:M,1:N-1)).*(alpha_z(1:M,1:N-1).*Hx_negt(1:M,1:N-1)+...
(1/mu)*beta_x(1:M,1:N-1).*Bx(1:M,1:N-1)-...
(1/mu)*alpha_x(1:M,1:N-1).*Bx_negt(1:M,1:N-1));
Hy(1:M-1,1:N)=(1./beta_x(1:M-1,1:N)).*(alpha_x(1:M-1,1:N).*Hy_negt(1:M-1,1:N)+...
(1/mu)*beta_y(1:M-1,1:N).*By(1:M-1,1:N)-...
(1/mu)*alpha_y(1:M-1,1:N).*By_negt(1:M-1,1:N));

## Slide 17: Propagating to far-field
FDTD can generally only simulate near-field effects due to need to mesh entire region
Often we are interested in the fields far away from simulation ()
Source: Wikipedia

## Slide 18: Propagating to far-field
Can calculate far-field using equivalence principle:
  Pick a closed surface enclosing sources
  Run simulation and record fields on surface
  Replace fields on surface with equivalent current sources
  Use radiation equations to determine E1, H1 fields in far-field
Source: Balanis, Antenna Theory
Vector potential A
Current source J
Can pick to be zero

## Slide 19: How a DVD works
Source: http://functionalcd.weebly.com/
Basic idea: Laser is scanned over DVD. If laser beam encounters pit the light
will be scattered away and will not reach the photodetector (Binary 1). Otherwise,
most laser light is reflected back toward the photodetector (Binary 0).

## Slide 20: How a DVD works
Source: Wikipedia

## Slide 21: FDTD simulation
PML
PML
PML
PEC
Polycarbonate (n=1.55)
Laser
650nm
Aluminum
120nm
320nm
Using Lumerical FDTD, we would like to optimize the dimension of the “pit” such that we maximize the amount
of laser light scattered.
pit
land
We will assume focused Gaussian spot for 650nm laser.
PML / PEC boundary conditions will be utilized to truncate the computational domain.
We will use FDTD to calculate the far-field light radiation
scattered by the pit.

## Slide 22: Next time
Install Lumerical FDTD Solutions
Walk-through creating and running simulation of DVD pit
Analyze results
Investigate modifying pit height

## Slide 23: Installing FDTD Solutions
https://www.lumerical.com/register.html
Use @berkeley.edu address

## Slide 24: Installing FDTD Solutions
Log in here:
You will get an email with the license code
Download FDTD Solutions
Extract zip file
Run the installer
Start the program
https://www.lumerical.com/portal/workshop.html?ec=CDF54A

## Slide 25: Installing FDTD Solutions
Check email for activation code
Enter it here
Click Activate

## Slide 26: Lumerical FDTD program

## Slide 27: Create ‘land’ geometry
We will create a rectangle consisting of Aluminum.
To create a rectangle and edit the properties:
  Structures  Rectangle
  Right click on rectangle in Objects Tree; select Edit object

## Slide 28: Create ‘land’ geometry

## Slide 29: Create ‘land’ geometry

## Slide 30: Create simulation window
To create a simulation window and edit the properties:
  Simulation  Region
  Right click on FDTD in Objects Tree; select Edit object

## Slide 31: Create simulation window

## Slide 32: Create simulation window

## Slide 33: Create simulation window

## Slide 34: Create simulation window

## Slide 35: Create simulation window
Hint: Click FDTD in the Objects Tree then click Zoom extents icon on the left-hand side

## Slide 36: Create source
To create a simulation window and edit the properties:
  Sources  Gaussian
  Right click on source in Objects Tree; select Edit object

## Slide 37: Create source

## Slide 38: Create source

## Slide 39: Create source

## Slide 40: Create source

## Slide 41: Create field monitor
To create a simulation window and edit the properties:
  Monitors  Frequency-domain field and power
  Right click on DFTMonitor in Objects Tree; select Edit object

## Slide 42: Create field monitor

## Slide 43: Create time-domain monitor
To create a simulation window and edit the properties:
  Monitors  Frequency-domain field and power
  Right click on DFTMonitor in Objects Tree; select Edit object

## Slide 44: Create time-domain monitor

## Slide 45: Create movie monitor
To create a simulation window and edit the properties:
  Monitors  Movie
  Right click on MovieMonitor in Objects Tree; select Edit object

## Slide 46: Create movie monitor

## Slide 47: Run simulation
Click the Run icon

## Slide 49: Analyze field-monitor
Right-click reflection  visualize  E
Click lambda in the Parameters window.
Drag the slider until Value ~ 0.650

## Slide 50: Far-field calculation
In the Result View, right-click farfield and click Calculate
Set the wavelength to 0.651841 and click Far Field settings.
Set the material index to 1.55

## Slide 51: Far-field calculation
In the Result View, right-click farfield and click Visualize

## Slide 52: Far-field calculation
These results are not too interesting. All we are observing is the simple reflection of a laser beam from a metallic surface.
Let’s add a DVD ‘pit’

## Slide 53: Create ‘pit’ geometry
We will create a rectangle consisting of Aluminum.
To create a rectangle and edit the properties:
  Structures  Rectangle
  Right click on rectangle in Objects Tree; select Edit object

## Slide 54: Create ‘pit’ geometry

## Slide 55: Create ‘pit’ geometry

## Slide 57: Far-field
Lobes indicate that light is scattered away at angles

## Slide 58: How to maximize scattering?
Polycarbonate (n=1.55)
Aluminum
pit
land
Some of the rays (red) will hit the pit and reflect back with a phase change of
Other rays (blue) will hit the land and reflect back with a phase change of
Destructive interference for
What happens to the light? It’s scattered away!
We can quickly calculate that we need for destructive interference to occur.
d
Let’s loosely think of the laser beam as impinging optical rays.

## Slide 59: How to maximize scattering?
Polycarbonate (n=1.55)
Aluminum
pit
land
What if
Then we have constructive interference and we should expect that most light will be reflected straight back as if there was no ‘pit’ present.
Let’s test this out...
Then we need
d

## Slide 60: Far-field
Most light is scattered straight back as if ‘pit’ is not present!

## Slide 61: Far-field comparison
pit
land
120nm
pit
land
240nm