## Slide 1: Agenda for today
Today we will do another tutorial example together to continue introduction to Lumerical FDTD software.
  Task #1: Tune the resonance frequency of a gold nanobar using the parametric sweep feature of Lumerical FDTD.
  Task #2: Calculate the Q-factor of the resonant mode
Next week: Begin discussing waveguide simulations

## Slide 2: Optimizing gold nanobar resonance
Gold nanobars behave like dipole antennas and resonantly scatter light.
Resonance length is roughly (same as dipole antenna) but typically smaller than this because of kinetic inductance (i.e. electron lags behind field causing the “plasmonic” effect).

## Slide 3: Optimizing gold nanobar resonance
PML
PML
PML
Using Lumerical FDTD, we would like to optimize the length of a gold nanobar such that the resonance wavelength of the nanobar is roughly 800nm
We will use broadband plane wave source to excite the gold nanobar embedded in air medium.
Computational domain will be terminated by PML on all sides
PML
nanobar
length
Plane wave

## Slide 4: Create ‘nanobar’ geometry
We will create a rectangle consisting of gold.
To create a rectangle and edit the properties:
  Structures  Rectangle
  Right click on rectangle in Objects Tree; select Edit object

## Slide 5: Create ‘nanobar’ geometry

## Slide 6: Create ‘nanobar’ geometry

## Slide 7: Create simulation window
To create a simulation window and edit the properties:
  Simulation  Region
  Right click on FDTD in Objects Tree; select Edit object

## Slide 8: Create simulation window

## Slide 9: Create simulation window

## Slide 10: Create simulation window

## Slide 11: Create simulation window

## Slide 12: Create mesh refinement
To create a simulation window and edit the properties:
  Simulation  Mesh
  Right click on mesh in Objects Tree; select Edit object

## Slide 13: Create mesh refinement

## Slide 14: Create mesh refinement

## Slide 15: Create source
To create a simulation window and edit the properties:
  Sources  Plane wave
  Right click on source in Objects Tree; select Edit object

## Slide 16: Create source

## Slide 17: Create source

## Slide 18: Create source

## Slide 19: Create field monitor
To create a simulation window and edit the properties:
  Monitors  Frequency-domain field and power
  Right click on DFTMonitor in Objects Tree; select Edit object

## Slide 20: Create field monitor

## Slide 21: Create field monitor

## Slide 22: Create movie monitor
To create a simulation window and edit the properties:
  Monitors  Movie
  Right click on MovieMonitor in Objects Tree; select Edit object

## Slide 23: Create movie monitor

## Slide 24: Create transmission box
To create a simulation window and edit the properties:
  Analysis  Optical Power
  Select Transmission box and hit Insert

## Slide 25: Create transmission box
z (um) = 0

## Slide 26: Run simulation
Click the Run icon

## Slide 27: Analyze transmission box
Right-click trans_box  visualize  t
Select Abs for the Scalar Operation

## Slide 28: Analyze transmission box
Transmission box measures net power that leaves the box.
The nanobar absorbs energy and therefore the net power is negative because of loss.
We observe resonance peak close to 950nm. Let’s try to optimize nanobar length to push the resonance closer to 800nm

## Slide 29: Parameter sweep
Let’s fine-tune the nanobar length so that resonance peak occurs closer to 800nm.
Click the icon Create New Parameter Sweep in the Optimizations and Sweeps toolbar.
Right-click sweep and click Edit

## Slide 30: Parameter sweep

## Slide 31: Parameter sweep
Click Run icon

## Slide 32: Analyze parameter sweep
Right click Sweep, select Visualize  Absorption
Select Abs for scalar operation

## Slide 33: Analyze parameter sweep
Nanobar length of 200nm provides resonance peak at 800nm.
Change the nanobar geometry such that y-span is 200nm and re-run the (non-parametric sweep) simulation to analyze the field-monitor data.

## Slide 34: Analyze field-monitor
Right-click nanobarField  visualize  E
Click lambda in the Parameters window.
Drag the slider until Value ~ 0.8
Dipole-mode
Field is large at both ends of the nanobar

## Slide 35: Movie monitor

## Slide 36: Q-factor of resonance

## Slide 37: Q-factor of resonance
Less ambiguous if we measure the Q-factor in the time domain.
Recall for a general “cavity”
Therefore if we plot the field energy on dB scale we can take the linear slope of the line (m) and relate it to Q as:

## Slide 38: Create time monitor
To create a simulation window and edit the properties:
  Monitors  Field time
  Right click on TimeMonitor in Objects Tree; select Edit object

## Slide 39: Create time monitor

## Slide 40: Analyze time-domain result
Run simulation
Right-click timeMonitor Visualize

## Slide 41: Analyze time-domain result
Next we must linear fit the energy curve. This can be done through Lumerical scripting interface.
Can also export data and use scripting to fit (Matlab, Python, Excel, etc)

## Slide 42: Create time monitor
Q = 7.5