## Slide 1: Agenda for today: Waveguides
Today we will use Lumerical MODE and FDTD to examine the properties of optical waveguides.
  1) Basic waveguide theory – Slab waveguide
  2) Waveguide mode simulation using Lumerical MODE
  a. Calculate 1D slab waveguide modes
  b. Calculate silicon photonic waveguide modes (demo)
  3) Using mode port source in Lumerical FDTD (demo)

## Slide 2: Optical waveguides
Slab waveguide
Ridge waveguide
Rib waveguide
Step-index optical fiber
An optical waveguide has the general property that there is always a material with high refractive index () surrounded by a material with lower refractive index ()
Light is confined by total internal reflection
in ray optics picture
Need wave optics to solve for guided modes
Ref: Chuang, Ch. 7

## Slide 3: What is a waveguide mode?
A mode (in general) is a time-harmonic solution to Maxwell’s equations (∝ eiωt)
A waveguide mode is a stable propagating mode with the special property that its spatial field distribution does not change with propagation (in the absence of loss)
Waveguide modes are determined by the cross-sectional refractive index profile of the waveguide
Waveguide modes are wavelength dependent
Wang et al. Opt. Express 20, 15547-15558 (2012)

## Slide 4: Waveguide mode properties / figures-of-merit
Effective index: 
  This number depends upon waveguide design and mode. Larger number means mode is more tightly confined to waveguide core.
Modal dispersion:
Modal group velocity:
  Velocity at which energy flows
Group velocity dispersion:
  Different wavelengths travel at different speeds down waveguide! Units are time per unit wavelength per unit length. Particularly important for fiber optic cable.

## Slide 5: Effective index
Each mode has an effective index that can be defined by:
The effective index tells you how tightly the mode is confined to the waveguide core
  Guided mode 
  Tightly confined to the core 
  Weakly confined to the core 
  Unguided or radiating modes 

## Slide 6: Effective index
Small effective index
Large effective index

## Slide 7: Lumerical MODE
Lumerical MODE is a finite difference frequency-domain solver that can be used to find waveguide modes
1D or 2D cross-section of a waveguide is discretized and simulated. MODE will solve for each mode and display the mode properties (e.g. , etc)
Single-mode optical fiber
Photonic crystal fiber

## Slide 8: Basic waveguide theory
Time-harmonic electromagnetic fields in a source-free region must satisfy the vector Helmholtz equation
The electric-field and magnetic-field vectors in general will have components in the x, y, and z directions.
Writing out the equation for Ex:

## Slide 9: Basic waveguide theory
Solve by separation of variables
Plug back into scalar Helmholtz equation to find:
The same can be done for the other electric and magnetic field components. Usually some field components are either exactly zero or very small and can be ignored.
Important result!

## Slide 10: Solving for waveguide modes: General approach
Assume propagation in the z-direction: E, H ∝
Make an educated guess for the form of the solution in each dielectric region Traveling wave: Standing wave: Decaying wave:
Plug educated guess back into the Helmholtz equation and apply boundary conditions at interfaces to find characteristic equations that will allow you to solve for

## Slide 11: Planar slab waveguide
x
y
z
d/2
For TE mode the E-field only has a component in the y-direction. Assuming we are trying to solve for a wave guided along the z-direction we also recognize that the structure is y-invariant
therefore we can simplify the scalar Helmholtz equation as:
Slab waveguide has two types of modes transverse electric (TE) and
transverse magnetic (TM)

## Slide 12: Planar slab waveguide
x
y
z
d/2
The general solution will take the form:
Slab waveguide has two types of modes transverse electric (TE) and
transverse magnetic (TM)

## Slide 13: Planar slab waveguide
x
y
z
d/2
Further simplify as (even solutions):
Slab waveguide has two types of modes transverse electric (TE) and
transverse magnetic (TM)
Field decays into cladding layers
Standing wave solution in core

## Slide 14: Planar slab waveguide
x
y
z
d/2
Further simplify as (odd solutions):
Slab waveguide has two types of modes transverse electric (TE) and
transverse magnetic (TM)
Field decays into cladding layers
Standing wave solution in core
Field decays into cladding layers

## Slide 15: Planar slab waveguide
x
y
z
d/2
Slab waveguide has two types of modes transverse electric (TE) and
transverse magnetic (TM)
Plug back into the wave equation and apply boundary conditions to find:
Even solutions
Odd solutions

## Slide 16: TE modes
TE0
TE2
TE1

## Slide 17: Simulating slab waveguide with Lumerical MODE
Open MODE software
Create new rectangle: Structures > Rectangle

## Slide 18: Create waveguide core

## Slide 19: Create waveguide core

## Slide 20: Create 1-D FDE simulation region

## Slide 21: Create 1-D FDE simulation region

## Slide 22: Create 1-D FDE simulation region

## Slide 23: Calculate modes
Click Run
Set wavelength to 1.55 and click Calculate Modes

## Slide 24
Mode list
Field profile

## Slide 25: Mode analysis
There are a lot of modes here! But remember, not all of these modes are guided. Only modes with are guided modes
Guided modes
Unguided radiating modes

## Slide 26: Mode analysis (guided modes)
TE0
TM0
TE1
TM1

## Slide 27: Mode analysis (unguided modes)
Notice: There is no exponential decay in the cladding! Power will be radiated
into the cladding as these unguided “modes” propagate down waveguide
Example #1
Example #2

## Slide 28: Waveguide cutoff
Let’s run a parameter sweep to plot effective index as a function of slab core thickness
You should set your minimum mesh spacing to 10nm for this analysis

## Slide 29: Waveguide cutoff

## Slide 30: Waveguide cutoff
Click run button:
When done, select sweep, select all results in Result View (bottom left), right click > Visualize > New Visualizer

## Slide 31: Waveguide cutoff
TE1, TM1 cutoff
No cutoff for
TE0, TM0
See Chuang 7.1.2
ncore
ncladding

## Slide 32: Rectangular waveguide
Pure TE and TM modes do not exist instead we have hybrid modes (all field components exist for each mode).
BUT, the transverse components of fields dominate and so they are often called quasi-TE and quasi-TM (often we even drop the term quasi)
x
y
z
Cross-section

## Slide 33: Silicon photonic ridge waveguide
Silicon substrate
silicon
Buried oxide (BOX)
220nm
3m

## Slide 34: Waveguide modes
Silicon thickness of 220nm for silicon-on-substrate (SOI) substrate is somewhat standardized
We often desire waveguide to contain only a single mode
Our goal is to determine the silicon ridge width such that that waveguide is single mode
Open Silicon_Photonic_Ridge_Waveguide.lms from the bcourses website
You will see a silicon photonic ridge waveguide with 220nm height and 900nm width.
Use MODE to calculate the guided modes.

## Slide 35: 900nm width ridge waveguide
Quasi-TE00
Quasi-TE10
Quasi-TM00
Ex dominates,
1 lobe in x,
1 lobe in y
Ex dominates,
2 lobes in x,
1 lobe in y
Hx dominates,
1 lobe in x,
1 lobe in y

## Slide 36: Single-mode waveguide
Run the parametric sweep on the silicon ridge width and plot for each of the modes on the previous slide as a function of

## Slide 37: Single-mode waveguide
Single mode
Mode crossing: Mode1 switches from TE to TM
Multimode

## Slide 38: Single-mode waveguide
Single mode
Mode crossing: Mode1 switches from TE to TM
Multimode
Note: Lumerical indexes modes by effective index, while we usually want to sort by spatial distribution

## Slide 39: Single-mode waveguide
Index mode by eigenmode
Index mode by spatial distribution

## Slide 40: Mode source in FDTD
When running FDTD simulation we often want to excite a particular waveguide mode
This can be done using a mode source in Lumerical FDTD.
Open the file Silicon_Photonic_Waveguide_Port_Source.fsp from bcourses
This Lumerical FDTD simulation file contains 3D silicon photonic ridge waveguide that we just simulated with ridge height of 220nm and ridge width of 500nm to ensure single mode operation

## Slide 41: Mode source in FDTD
Click Sources  Mode
Select the geometry tab first

## Slide 42: Mode source in FDTD

## Slide 43: Mode source in FDTD
Click Visualize Data

## Slide 44: Mode source in FDTD
A movie monitor has already been added at the x = 0 plane so that we can see the wave propagate down the waveguide
Click Run

## Slide 45: Movie monitor
y
z
ridge
air
BOX

## Slide 46: Limitation to port source
Caution should be used when applying port source
Port source mode is only calculated at the center frequency therefore there will be some mode mismatch (i.e. reflections) at other frequencies.
Keep this in mind if you are running a broadband simulation.