## Slide 1: Discussion today: Grating couplers
Today we will discuss how we can couple light between optical fibers and on-chip photonic waveguides. In particular we will focus on grating couplers.
Today we will cover the theory of grating couplers. Next week we will put the theory to use and design a silicon photonic grating coupler.

## Slide 2: Coupling into and out of waveguides
Dilemma: how do we couple light to and from an optical fiber to an integrated on-chip photonic waveguide?
10
300nm
Optical fiber
on-chip waveguide

## Slide 3: End-fire coupling
Pros: Coupling efficiency can be very good
Cons: Poor tolerance to misalignment. Costly to manufacture.
Optical fiber (not to scale)
lens
photonic waveguide
Side view

## Slide 4: Nanotaper coupler
Pros: Coupling efficiency can be very good. Lens not needed
Cons: Poor tolerance to misalignment. Requires advanced lithography equipment
Optical fiber (not to scale)
Single mode silicon waveguide
Taper to ~100nm  spatial extent of mode becomes large
Top view

## Slide 5: Top coupling
How can we couple light from a confined waveguide mode to an optical fiber placed above the waveguide?
Optical fiber (not to scale)

## Slide 6: Grating coupler
By periodically notching the waveguide we can make a diffraction grating such that light that is diffracted off the rulings will constructively interfere toward a direction into the optical fiber
Optical fiber (not to scale)

## Slide 7: Grating coupler
We choose the diffraction period () such that scattering from individual rulings constructively interferes at the desired angle
Scattering from individual ruling
Optical fiber (not to scale)

## Slide 8: Grating coupler
We can write a relationship between the diffraction angle () and the periodicity () of the grating

## Slide 9
Let’s use ray optics to determine the condition for two rays reflected off adjacent rulings to constructively interfere at an angle .
We choose grating periodicity () such that the path length difference () results in constructive interference between Ray 1 and Ray 2.
This will happen when phase difference between Ray 1 and Ray 2 are integer multiples of 2π.
Ray 1
Ray 2

## Slide 10
Ray 1
Ray 2
Phase of Ray 2
Phase of Ray 1

## Slide 11: Coupling into waveguide
By reciprocity we can use the same grating to couple light into a waveguide.
But, let’s examine this problem slightly differently.
Optical fiber (not to scale)

## Slide 12: Waveguide coupling
What if I send light onto a waveguide (without a grating) as shown below?
How much power can I couple into the waveguide?

## Slide 13: Waveguide coupling
The answer is precisely zero

## Slide 14: Waveguide coupling
Let’s do the math:
At the air-waveguide interface (x = 0), the tangential component of electric field must be continuous:
This implies a phase matching condition:
(incident)
(reflected)
(transmitted)

## Slide 15: Waveguide coupling
We can write as:
Therefore:
But, for a guided mode we know that that the effective index must be greater than and as a result This requires which is of course impossible!
We cannot couple light into a guided mode without dealing with this phase match condition.

## Slide 16: Waveguide coupling
But, for a guided mode we know that that the effective index must be greater than and as a result This requires which is of course impossible!
We cannot couple light into a guided mode without dealing with this phase match condition.

## Slide 17: Waveguide coupling
Another way of seeing this is to recall that a guided mode must decay exponentially away from the core. In other words, is imaginary in the cladding. (If is real, it is radiating!)
But incident mode must have real components, so cannot couple to guided mode.
Can we create an evanescent mode from incident mode?

## Slide 18: Prism couplers
Can use prism placed close to waveguide to satisfy phase matching condition
Evanescent mode in region couples to guided mode
Same mechanism used in beamsplitters
Used mainly for refractive index measurement of thin films (eg. metricon in Nanolab)

## Slide 19: Grating coupler
What if we have the following geometry?

## Slide 20: Grating coupler
At the boundary of and we can write
is a periodic function describing the height variation of our grating. Thus we can write using a Fourier series

## Slide 21: Grating coupler
At the boundary of and we can write
Now our new phase matching requirement is:
for some .
Clearly, , therefore:

## Slide 22: Grating coupler
This is the same phase matching requirement that we derived under the ray optics model.
By properly choosing and we can now phase match!

## Slide 23: Grating examples

## Slide 24
http://www.oxford-instruments.com/businesses/nanotechnology/plasma-technology/campaigns/sem-competition-winner-%281%29

## Slide 25
Source: Imec

## Slide 26: Design example
Design the grating period such that light is diffracted out at a 10° angle for 1st order diffraction
Assume
10°

## Slide 27: Comments
Today we have shown how to calculate the diffraction angle of a grating coupler but we have not said anything about the intensity of the light that will diffract at that angle or in other words we do not yet know the coupling efficiency.
This requires more rigorous theory or simulation tools.
Next class: Numerical design of a grating coupler using Lumerical FDTD