## Slide 1: Discussion today: Grating couplers
Today we will design and simulate a silicon photonic grating coupler using Lumerical FDTD

## Slide 2: Silicon photonic grating coupler design
Optical fiber (not to scale)
220nm

## Slide 3: Silicon photonic grating coupler design
Using hand analysis we will estimate desired grating period () to achieve and use Lumerical FDTD to fine-tune the design.

## Slide 4: Silicon photonic grating coupler design
What value do we use for ?
This is somewhat ambiguous, we can use an average value of effective index in the “thick” region and the “thin” region of the grating.
220nm

## Slide 5: Lumerical simulation
Open gratingCoupler.fsp
To avoid lengthy simulation time, we will simulate a 2D grating
Using the mode source calculate the effective index in the “thick” and “thin” part of the grating.

## Slide 6: Effective index calculation (“thin” region)
Right-click waveguide_source
Click Edit object
Click Select mode
Click Calculate modes
The only guided mode has effective index 2.351

## Slide 7: Effective index calculation (“thick” region)
Move the waveguide source to x = -0.1
The new effective index is 2.86

## Slide 8: Hand design
Design an out-coupler grating for angle of 13° at a wavelength of 1.55µm
Notice that only one order m = 1 is supported for this grating
m = 0 → 2.6/1.45 > 1
m = 2 → 2*1.55/0.682 = 4.5 > 2.6

## Slide 9: Change grating period (pitch)
Right click on grating_coupler_2d and click Edit object

## Slide 10: Field monitor above grating
We wish to monitor the power transmitted out of the grating
Right click aboveMonitor and select Edit Object
monitor

## Slide 11: Field monitor above grating

## Slide 12: Out-coupler simulation
Move the x-position of the waveguide source to -12.5µm and simulate.
Right-click on 2DMonitor and select VisualizeE
Right-click on aboveMonitor and select VisualizeT
Right-click on aboveMonitor and select Visualize Farfield all

## Slide 13: Power coupled out of the grating
Light diffracted into the substrate
Light diffracted out of the grating
Go to Parameters box on bottom left
Select lambda, set scroll bar on right to 1.55 um

## Slide 14: Power coupled out of the grating
Our design is close but slightly off
Target wavelength

## Slide 15: Grating angle sensitivity to wavelength

## Slide 16: In-coupler grating design
Let’s see how well our grating coupler works for coupling light into a waveguide.
Go back to Layout mode
Right-click waveguide_source→Disable
Right-click source→Enable. This is a Gaussian source we will use first to approximate the fiber.

## Slide 17: Gaussian source

## Slide 18: Gaussian source

## Slide 19: Gaussian source

## Slide 20: Power coupled into the waveguide
We will use modeMonitor to see the shape of the mode at various wavelengths
monitor

## Slide 21: Power coupled into the waveguide

## Slide 22: In-coupler grating simulation
Simulate
Right-click on 2DMonitor and select VisualizeE
Right-click on modeMonitor and select VisualizeT

## Slide 23: Power coupled into the waveguide
Power coupled into waveguide
Power lost into the substrate

## Slide 24: Power coupled into the waveguide
Again our “back of the envelope” design is slightly off, but not bad!
Target wavelength

## Slide 25: Fiber in-coupling to grating
Back to Layout mode
Disable Gaussian source
Enable fiber analysis group
cladding
core
cladding

## Slide 26: Pitch optimization
Using more realistic fiber geometry let’s optimize the grating pitch so that the coupling peaks at 1.55µm.
A sweep plan has already been generated called pitchSweep. This will sweep the pitch from 650nm to 700nm.
Run pitchSweep at home (this will run 20 simulations and may take a while)
Right-click pitchSweep and select VisualizeModeT

## Slide 27: Pitch optimization
By choosing pitch of 653nm we can maximize the coupling at a wavelength of 1.55µm
* Need to do
Scalar operation→Abs again

## Slide 28: Pitch optimization
Change grating pitch to 653nm
Run simulation
Right-click on 2DMonitor and select VisualizeE
Right-click on modeMonitor and select VisualizeT

## Slide 29: Pitch optimization
Power coupled into waveguide
Power lost into the substrate

## Slide 30: Pitch optimization
Target wavelength

## Slide 31: Position optimization
Coupling efficiency will be dependent upon the position of the fiber with respect to the grating
A sweep plan has been generated to sweep the fiber +/- 3 microns in the x-direction.
  Note: It’s actually easier here to move the x-position of the grating but this accomplishes the same thing
Run xSweep at home (this will run 20 simulations and may take a while)
Right-click xSweep and select VisualizeModeT

## Slide 32: Position optimization
We can see here that we should shift our fiber
position by 0.5 micron to maximize coupling efficiency

## Slide 33: Next discussion
Next discussion we will close the grating coupler topic by showing how to extract the grating S-parameters and how to import into the photonic circuit solver Lumerical Interconnect.
This will be particularly useful for the final project if you wish to simulate large structures.