## Slide 1: Discussion today: Photonic circuit simulation
Today we will introduce Lumerical INTERCONNECT, a systems level photonic circuit simulator (think SPICE for photonics).
  Simple introductory example: Fabry-Perot resonator simulation in INTERCONNECT
  More complicated example: Extract S-parameters from FDTD simulation and import into INTERCONNECT

## Slide 3: Fabry-Perot etalon example
a1
b1
b2
a2 = 0
Cavity
Mirror 1
Mirror 2
Question: What is the power transmission through Fabry-Perot etalon?

## Slide 4: S-parameter
We can generalize the Fabry-Perot cavity (and other optical components) to
a two-port representation which is fully defined by a scattering matrix (S-parameters).
This is completely analogous to electrical circuits.
Optical component
Two-port representation

## Slide 5: Fabry-Perot etalon example
Question: What is the power transmission through Fabry-Perot etalon?
a1
b1
b2
a2 = 0
Mirror 1
Mirror 2
b’1
a’1
b’2
a’2
r1
r2
L

## Slide 6: Fabry-Perot etalon example
a1
b1
b2
a2 = 0
Mirror 1
Mirror 2
b’1
a’1
b’2
a’2
r1
r2
L

## Slide 7: Fabry-Perot etalon example

## Slide 8: Fabry-Perot etalon example
Free spectral range (FSR)
R = 0.5
n = 2.8
L = 10µm

## Slide 9: Fabry-Perot etalon simulation
Open INTERCONNECT
Add two Mirror and one Straight waveguide elements to the simulation space (click and drag)

## Slide 10: Fabry-Perot etalon simulation
Change the following properties:
  Mirror  Reflectivity = 0.5
  Waveguide  Length = 10μm Mode 1 effective index = 2.8 Mode 1 group index = 2.8
Add one Optical Network Analyzer to simulation space (AnalyzersOptical)
Change the following properties:
  ONA  Number of input ports = 2 Frequency range = 50 THz Number of points = 1000

## Slide 11: Fabry-Perot etalon simulation
Note: Port 1 should be connected to the input port of the ONA

## Slide 12: Fabry-Perot etalon simulation
Run the simulation
Click ONA in the Element tree. In the Results view right-click Input 2  Mode 1  transmission  Visualize  New Visualizer

## Slide 13: Fabry-Perot etalon simulation

## Slide 14: Grating S-parameter
Optical fiber (not to scale)
a2
b2
a1
b1
Mode expansion monitor
Mode expansion monitor

## Slide 15: Grating S-parameter
How do we get the field coefficients
Lumerical has built-in mode expansion monitor that can determine these coefficients and allow us to extract S-parameters.
The mode expansion assumes field can be expanded using the eigenmodes such that:
and are the complex modal coefficients and will be returned by the mode expansion monitor. Important: the coefficients are normalized to 1 V/m!

## Slide 16: Simulation #1
Optical fiber (not to scale)
a2
b2
b1
Mode expansion monitor
Mode expansion monitor
Necessary to deal with Lumerical normalization

## Slide 17: Simulation #2
Optical fiber (not to scale)
b2
b1
Mode expansion monitor
Mode expansion monitor
Necessary to deal with Lumerical normalization
a1

## Slide 18: Grating S-parameter extraction
Open Lumerical FDTD file grating_coupler_S_param.fsp
Open Lumerical script S_param_extraction.lsf (click and drag into FDTD window)
You will see grating geometry that we simulated at the end of last discussion plus the addition of mode expansion monitors.
The script will run the simulation twice and automatically extract the S-parameters using the mode expansion monitors and save to a txt file.
Run the script.

## Slide 19: Grating S-parameter extraction
Strong reflections back toward source

## Slide 20: Grating S-parameter extraction
Open the Lumerical INTERCONNECT file grating_coupler_interconnect.icp

## Slide 21: Import S-parameter
Select grating coupler 1 S-parameter symbol and within the Property View  Standard  s parameters file name, double click filename and click Open
Select the txt file grating_S.txt
Repeat for grating coupler 2.
Open the Lumerical script file grating_coupler_interconnect.lsf (click and drag into window or click icon)
Run the script.

## Slide 22: Grating + waveguide simulation
Combined S-parameter
Reflectance / Transmittance
Fabry-perot oscillations

## Slide 23: Summary
This approach of extracting S-parameters and using INTERCONNECT to run a system level circuit simulation has two primary benefits:
  Break large simulation up into smaller simulations to reduce memory requirement (may be useful for final project).
  Import empirically extracted S-parameters to build physically based model of a full system.