## Slide 1: Discussion today
Using Lumerical INTERCONNECT we will simulate a full 50Gbps (25Gbps X 2) 2-channel WDM optical link.
Today we will look at the following:
  Discuss ring resonator in INTERCONNECT
  Import MODE results of effective index as a function carrier density into INTERCONNECT
  Design and draw schematic of WDM optical link
  Analyze results using eye-diagram

## Slide 2: Analyzing ring resonator modulator in INTERCONNECT
Create the following circuit in INTERCONNECT consisting of
  DC source (Sources→Electrical→DC Source)
  Optical Network Analyzer (Analyzers→Optical→Optical Network Analyzer)
  Ring Modulator (Modulators→Optical→Optical Ring Modulator)
Click and drag to draw connections

## Slide 3: Ring resonator modulator model in INTERCONNECT
Select ring resonator object and change in Property View:
  Standard
    Specify frequency of 193.1 THz
    Specify length of 60e-6 m
    Set load from file to True
    Select measurement filename and set to mod_neff_V.dat (data of vs. V - created in MODE last time)
  Waveguide
    Specify group index 2.57 (from MODE)
    Set loss to 7 dB/m (from last time we had ~0.07 dB/cm loss in simulation)
    Set effective index to 0 (think of this as change in effective index)
    Set coupling coefficient 1 and 2 to 0.025

## Slide 4: Ring resonator modulator model in INTERCONNECT
The ring resonator modulator model in INTERCONNECT is not documented very well.
The resonator length and group index is used to set the free spectral range (FSR) and loss of the ring resonator but not used to set the absolute resonance frequencies.
Instead we explicitly state what the resonance frequency should be.
(proof: take of )
FSR
(recall , and )

## Slide 5: Effect of voltage on transmission spectrum
Click Root Element in Element Tree
Set Simulation sample rate to 1e11 Hz (otherwise will give an error)
Run simulation to populate Result View

## Slide 6: Effect of voltage on transmission spectrum
Create a sweep to vary the reverse bias voltage between 0 and 3V
Right click, Edit

## Slide 7
Run sweep.
Plot Transmission data (Right-click reverse, Visualize→T)

## Slide 8: Effect of voltage on transmission spectrum
With applied voltage, the transmission dip shifts away from the center frequency
(click Scalar operation -> Abs)

## Slide 9: Effect of voltage on transmission spectrum
Open the script plot_ring_modulator_data.lsf (drag into simulation window), and run it
Plots the transmission at the center frequency as a function of applied voltage.

## Slide 10: 50GBps (2x25GBps) 2-channel WDM
fiber
CW lasers
Transmitter
Receiver
Det.
Data in (25GBps per channel)
Det.
Data out
=1552.8 nm
= 1551.2 nm
(200 GHz channel spacing)

## Slide 11: 50GBps (2x25GBps) 2-channel WDM
Open the INTERCONNECT file 2_channel_WDM.icp
This schematic contains a full 2-channel optical link consisting of 2 ring resonator modulators at the transmitter and 2 ring resonator filters at the receiver.

## Slide 12: 50GBps (2x25GBps) 2-channel WDM
Click Run
Plot the power at the Optical Spectrum Analyzer after each ring resonator modulator (select object, in Result View right click mode 1→signal and Visualize)

## Slide 13
After 193.065 THz modulator
After 193.265 THz modulator
Power shifted to sidebands
Recall:
FT

## Slide 14
After 193.065 THz filter
After 193.265 THz filter

## Slide 15: Non-return to zero (NRZ) vs. return to zero (RZ)
1
0
1
1
0
Time
Time
RZ signal
NRZ signal

## Slide 16: Non-return to zero (NRZ) vs. return to zero (RZ)
RZ requires twice as much bandwidth as NRZ
One advantage of RZ is less interference between successive pulses
http://www.keysight.com/upload/cmc_upload/All/SLDPRE_6_Return_Zero_Methodo.pdf

## Slide 17: Eye diagram
Superimpose the oscilloscope trace of many different bit streams on top of each other. If there is good margin between “1” and “0” you should see something like a human eye.
etc.

## Slide 18: Eye diagram
SNR can be used to estimate bit-error rate (BER), given some distribution of noise (typically Gaussian)
Source: edn.com

## Slide 19: 50GBps (2x25GBps) 2-channel WDM
Plot the result of the eye diagram monitors on the far right
Select object, Result View, right click eye diagram and Visualize

## Slide 20
193.065 THz eye
193.265 THz
eye
Very good “eyes” since no noise included