## Slide 1: Agenda for today
Today we will do another tutorial example to continue introduction to Lumerical FDTD software.
  Task #1: Tune the resonance frequency of a gold nanobar using the parametric sweep feature of Lumerical FDTD.
  Task #2: Calculate the Q-factor of the resonant mode
Next week: Begin discussing waveguide simulations

## Slide 2: Gold nanobar antennas
Gold nanobars behave like dipole antennas and resonantly scatter light.
Resonance length is roughly (same as dipole antenna) but typically smaller than this because of kinetic inductance (i.e. electron lags behind field causing the “plasmonic” effect).

## Slide 3: Circuit model of dipole antenna
Let’s analyze dipole antenna using circuit model
+
+
+
-
-
-
E
I
B
C
C
L
L
L
C
L
R = Rrad + Rloss
Lumped circuit:
See: www.physics.princeton.edu/~mcdonald/examples/cap_antenna.pdf
h
a
Pretty close to
In reality,
(depends on wire radius)

## Slide 4
PML
PML
PML
Using Lumerical FDTD, we would like to optimize the length of a gold nanobar such that the resonance wavelength of the nanobar is roughly 800nm
We will use broadband plane wave source to excite the gold nanobar embedded in air medium.
Computational domain will be terminated by PML on all sides
PML
nanobar
length
Plane wave
Optimizing gold nanobar resonance

## Slide 5: Create ‘nanobar’ geometry
We will create a rectangle consisting of gold.
To create a rectangle and edit the properties:
  Structures  Rectangle
  Right click on rectangle in Objects Tree; select Edit object

## Slide 6: Create ‘nanobar’ geometry

## Slide 7: Create ‘nanobar’ geometry

## Slide 8: Create simulation window
To create a simulation window and edit the properties:
  Simulation  Region
  Right click on FDTD in Objects Tree; select Edit object

## Slide 9: Create simulation window

## Slide 10: Create simulation window

## Slide 11: Create simulation window

## Slide 12: Create simulation window

## Slide 13: Create mesh refinement
To create a simulation window and edit the properties:
  Simulation  Mesh
  Right click on mesh in Objects Tree; select Edit object

## Slide 14: Create mesh refinement

## Slide 15: Create mesh refinement

## Slide 16: Create source
To create a source and edit the properties:
  Sources  Plane wave
  Right click on source in Objects Tree; select Edit object

## Slide 17: Create source
Bloch/periodic: most common. Technically should only be used for PBCs, will cause diffraction effects at edges for PML. OK far from edges.
BFAST: used for angled plane waves with PBCs.
Diffracting: used for diffraction from rectangular aperture (set by source size).

## Slide 18: Create source

## Slide 19: Create source

## Slide 20: Create field monitor
To create a monitor and edit the properties:
  Monitors  Frequency-domain field and power
  Right click on DFTMonitor in Objects Tree; select Edit object

## Slide 21: Create field monitor

## Slide 22: Create field monitor

## Slide 23: Create movie monitor
To create a monitor and edit the properties:
  Monitors  Movie
  Right click on MovieMonitor in Objects Tree; select Edit object

## Slide 24: Create movie monitor

## Slide 25: Create transmission box
To create a transmission box and edit the properties:
  Analysis  Optical Power
  Select Transmission box and hit Insert

## Slide 26: Analysis tab
Contains specialized analyses using grouped objects and scripts
More on this later…

## Slide 27: Create transmission box

## Slide 28: Run simulation
Click the Run icon

## Slide 29: Analyze transmission box
Right-click trans_box  visualize  T
Select Abs for the Scalar Operation

## Slide 30: Analyze transmission box
Transmission box measures net power that leaves the box.
The nanobar absorbs energy and therefore the net power is negative because of loss.
We observe resonance peak close to 950nm. Let’s try to optimize nanobar length to push the resonance closer to 800nm

## Slide 31: Parameter sweep
Let’s fine-tune the nanobar length so that resonance peak occurs closer to 800nm.
Select Optimizations and Sweeps toolbar.
Click the icon Create New Parameter Sweep
Right-click sweep and click Edit

## Slide 32: Parameter sweep

## Slide 33: Parameter sweep
Click Run icon

## Slide 34: Analyze parameter sweep
Right click Sweep, select Visualize  Absorption
Select Abs for scalar operation

## Slide 35: Comparison with theory
Not even close to !
What’s wrong?
Nanobar length (nm)
Resonance wavelength (nm)
Simulation
Circuit model

## Slide 36
We forgot kinetic inductance!
Electron motion lags with respect to applied field
Comparison with theory
N electrons
A
electron density
electron mass
C
R = Rrad + Rloss
Lumped circuit:
L = Lf + Lk
See: EE236A

## Slide 37: Comparison with theory
Much better match by including Lk
Nanobar length (nm)
Resonance wavelength (nm)
Simulation
Circuit model
Circuit model with Lk

## Slide 38: Analyze parameter sweep
Goal was resonance at 800 nm Nanobar length of 200 nm
Change the nanobar object such that y-span is 200nm and re-run the (non-parametric sweep) simulation to analyze the field-monitor data.

## Slide 39: Analyze field-monitor
Right-click nanobarField  visualize  E
Click lambda in the Parameters window.
Drag the slider until Value ~ 0.8
Dipole-mode
field is large at both ends of the nanobar

## Slide 40: Movie monitor

## Slide 41: Q-factor of resonance

## Slide 42: Q-factor of resonance
Less ambiguous if we measure the Q-factor in the time domain.
Recall for a general “cavity”
Therefore if we plot the field energy on dB scale we can take the linear slope of the line (m) and relate it to Q as:

## Slide 43: Create time monitor
To create a time monitor and edit the properties:
  Monitors  Field time
  Right click on TimeMonitor in Objects Tree; select Edit object

## Slide 44: Create time monitor
XY view

## Slide 45: Analyze time-domain result
Run simulation
Right-click timeMonitor Visualize E
For energy density

## Slide 46: Analyze time-domain result
Next we must linear fit the energy curve. This can be done through Lumerical scripting interface.
Can also export data and use scripting to fit (Matlab, Python, Excel, etc)

## Slide 47: Create time monitor
Q = 7.5

## Slide 48: Next time
Intro to waveguides and MODE simulation