## Slide 1: Today
Intro to optical modulation
Coupled mode theory
Ring resonators
Next time: simulation of ring resonator using Lumerical DEVICE.

## Slide 2: Single wavelength / channel optical communication
The simplest optical communication scheme is single wavelength / channel communication.
The light from a single laser (VCSEL, DFB laser, etc.) is electrically-modulated and sent through a single or multimode fiber.
The light is detected at the other end of the fiber and converted back into electrical signal.
Tx
Optical fiber
λ1
Rx
Modulator
Electrical signal in
Electrical signal out

## Slide 3: Single wavelength / channel optical communication
10GB/s transceiver
850nm VCSEL
Max Range ~300m
Short reach data center applications
Source: Finisar
Transmitter Optical Sub-Assembly

## Slide 4: Wavelength division multiplexing (WDM)
Tx
Tx
Tx
Optical fiber
λ1
λ2
λN
λ1
λ2
λN
Rx
Rx
Rx
Optical multiplexer
Optical demultiplexer
Many wavelengths are sent down the same optical fiber
Capacity is increased by N times, N = # wavelengths

## Slide 5: Wavelength division multiplexing (WDM)
The International Telecommunications Union (ITU) has standardized the telecom wavelengths and spacing. The C-band is commonly used for dense WDM (DWDM).
Source: Cisco

## Slide 6: Attenuation and dispersion in silica fibers
1300 nm is minimum dispersion point
1550 nm is minimum attenuation point
Source: photonicswiki.org

## Slide 7: Wavelength division multiplexing (WDM)
Tx
Tx
Tx
Optical fiber
Rx
Rx
Rx
Optical multiplexer
Optical demultiplexer
What is inside the box?
λ1
λ2
λN
λ1
λ2
λN

## Slide 8: Silicon photonics
Silicon photonics has emerged recently as a new technology for photonic communication.
Pros:
  Large index contrast  reduced size of optical components
  Leverage existing silicon infrastructure and expertise
  Photonics and electronics can coexist (in principle)
Cons:
  Silicon is a “dark” material
  Difficulty in coupling light
  Large thermo-optic effect

## Slide 9: Silicon photonics
For the next three class periods we will discuss strategies to demodulate and modulate optical signals
We will primarily focus on ring resonator based designs although by no means the only way to multiplex or demultiplex light.
First, we need to discuss one important passive optical component called the directional coupler.

## Slide 10: Mode coupling between waveguides
What happens if I excite the fundamental mode of Waveguide A and place waveguide B nearby?
Waveguide A
Waveguide B
Light in

## Slide 11: Mode coupling between waveguides
The mode in Waveguide A happily travels down the waveguide and does not “feel” the effect of Waveguide B since it is too far away
Light in

## Slide 12: Mode coupling between waveguides
Now, what if waveguide A and waveguide B are placed right next to each other. The fundamental modes of each waveguide are coupled and will form a “supermode”.
What if we excite the supermode?
Waveguide A
Waveguide B
Light in

## Slide 13: Mode coupling between waveguides
The “supermode” happily travels down the waveguide
Light in
Waveguide A
Waveguide B

## Slide 14: Mode coupling between waveguides
Now, what if I excite only one waveguide and then bring both waveguides into close proximity to each other?
Light in
Waveguide A
Waveguide B

## Slide 15: Mode coupling between waveguides
Energy periodically sloshes back and forth between both waveguides.
Waveguide A
Waveguide B

## Slide 16: Mode coupling between waveguides
Power in Waveguide A
Power in Waveguide B

## Slide 17: Mode coupling between waveguides
For , complete coupling of power from Waveguide A to Waveguide B occurs
For , zero coupling of power from Waveguide A to Waveguide B occurs
  is a geometry dependent coupling strength term and has units of inverse length.

## Slide 18: Mode coupling: Mechanical analogy
This “sloshing” of energy back and forth between waveguides seems odd but is also observed between other coupled systems including two coupled mechanical pendulums.

## Slide 19: Mode coupling: Mechanical analogy

## Slide 20: Mode coupling: quantum analogy
H0 is the energy in an individual mode
H1 is the overlap energy of the two modes
(“supermodes”)
E-fields in phase
Constructive
interference
E-fields out of phase
Destructive
interference
Notes: H=\left( \begin{matrix} H_0 && H_1 \\ H_1 && H_0\end{matrix}\right)
\Psi_1 = \left(\begin{matrix} 1 \\ 1\end{matrix}\right),
\Psi_2 = \left(\begin{matrix} 1 \\ -1\end{matrix}\right) \\ \\
E_1=H_0+H_1, \; E_2=H_0-H_1

## Slide 21: Mode coupling: quantum analogy
H0 is the energy in an individual mode
H1 is the overlap energy of the two modes
(“supermodes”)
Also see Chuang 8.2
Oscillation between the two waveguides
Start in one waveguide
E-fields in phase
Constructive
interference
E-fields out of phase
Destructive
interference
Notes: H=\left( \begin{matrix} H_0 && H_1 \\ H_1 && H_0\end{matrix}\right)
\Psi_1 = \left(\begin{matrix} 1 \\ 1\end{matrix}\right),
\Psi_2 = \left(\begin{matrix} 1 \\ -1\end{matrix}\right) \\ \\
E_1=H_0+H_1, \; E_2=H_0-H_1
\Psi(0)=\left(\begin{matrix} 1 \\ 0 \end{matrix}\right) = \Psi_1+\Psi_2 \\ \\
\begin{align*}
\Psi(t)&=\Psi_1e^{-i(H_0+H_1)t/\hbar}+\Psi_2 e^{-i(H_0-H_1)t/\hbar}\\
&=e^{-iH_0t/\hbar}\left(\begin{matrix} \cos{H_1 t/\hbar} \\ i \sin{H_1 t/\hbar}\end{matrix}\right)
\end{align*}

## Slide 22: Ring resonator
Light traveling down waveguide can couple to resonant mode within the ring resonator
Resonance wavelength occurs when light accumulates a phase shift of when traveling around the ring:
Waveguide
Ring Resonator
Chuang 8.4
Notes: \left(\begin{array}{c}b_1 \\ b_2 \end{array} \right) = \left(\begin{array}{cc}\beta_a & K_{ab} \\ K_{ba} & \beta_b \end{array} \right )\left(\begin{array}{c} a_1 \\ a_2 \end{array}\right)

## Slide 23: Ring resonator
Waveguide
Ring Resonator
*
*
U
Lossless (power conserved):
Notes: U=\left(\begin{array}{cc} t & i\kappa \\ i\kappa^* & t^* \end{array} \right )
|t|^2+|\kappa|^2=1

## Slide 24: Ring resonator
Waveguide
Ring Resonator
*
*
Power conservation:
Define
Circulation condition:
(phase change in ring)
(loss in ring)

## Slide 25: Power transmission

## Slide 26: Ring resonator example

## Slide 27: Ring resonator all-pass filter
Ring resonator with low waveguide loss ( can be used an all-pass filter with phase delay
What use do we have for this? Large change in phase at resonance introduces group delay  optical buffer, dispersion compensation, delay for Mach-Zehnder interferometer.

## Slide 28: Ring resonator all-pass filter
Light in
Light out
Mach-Zehnder interferometer (MZI)
Destructive interference at output if delay stage introduces phase shift.
Traditional delay stage incorporates non-linear medium which will have refractive index change with applied voltage. Delay stage length may need to be
millimeters long to get phase shift.
Light in
Light out
Mach-Zehnder interferometer (MZI)
w/ ring resonator delay stage
Compact delay stage

## Slide 29: Add/Drop ring resonator filter
Ring resonator shown on previous page can be used as a notch filter however we need to precisely match the transmission coefficient to the loss coefficient in the ring which in practice is not easy.
Adding another waveguide bus allows you to couple the light out of the ring thus forming a bandpass filter.
Waveguide
Ring Resonator
Input
Through
Drop

## Slide 30: Add/Drop ring resonator filter
drop
through

## Slide 31: Add/Drop ring resonator filter
Input
Through
Drop
Input
Through
Drop

## Slide 32: WDM demultiplexing
Basic implementation
(in)
Detector
Detector
Detector
Detector

## Slide 33: Comments on ring resonators
Higher order filters can be constructed by adding several rings in series.
Resonant frequency of ring resonator is very sensitive to process variation (variation in effective index) and temperature.
Practical ring resonators for use in a real-world environment need integrated temperature control to stabilize and adjust resonance frequency.
Optics Express Vol. 23, Issue 16, pp. 21527-21540 (2015)

## Slide 34: Modulation with ring resonators
Resonance frequency sensitivity to effective index can be exploited for modulation of light
The index of refraction of silicon can be modified by injecting (or removing) free carriers by applied bias
Nature 435, 325-327 (19 May 2005)

## Slide 35: Modulation with ring resonators
Nature 528, 534–538 (24 December 2015)

## Slide 36: Next week
We will discuss modulation with ring resonators and begin designing a modulator based on change in refractive index of silicon with applied bias, using Lumerical DEVICE.