## Slide 1: EE40 Lecture 10 Josh Hug
7/17/2010

## Slide 2: Logistics and Lab Reminder
If you have not submitted a spec and want to do a custom Project 2, talk to me right after class
HW4 due today at 5
HW5 due Tuesday at 2PM (it will be short, and up by 5 PM today)
As requested, all reading assignments for next week will be posted tonight
We expect you to understand lab concepts. For example, the Schmitt Trigger:
  Do you know what they are and what they do?

## Slide 3: HW Clarification
There are a bunch of hints on the bspace forums
“Zero state response” and “zero input response” are terms that I haven’t used in lecture, but they’re really easy and they’re in the book
  Zero input response: The response you get with f(t)=0 [same as homogeneous solution]
  Zero state response: The response you get with y(0)=0 [complete response with initial condition equal to zero]

## Slide 4: To the board…
For LC and RLC circuits

## Slide 5: RLC Circuits
They are important, but not so much for digital integrated circuit design
They do play a role in the world of analog circuits, but that’s a bit specialized for us to spend a great deal of time
  Usually care more about “frequency response” than the actual shape of the response in time
If you want to learn more about analog circuit design (it is hard and probably awesome), see EE

## Slide 6: Let’s step back a second
Earlier this week, I said capacitors are good for
  Storing energy
  Filtering
  Modeling unwanted capacitances in digital circuits
We’ve discussed the first case pretty heavily now, and filtering will come in great detail next week
For now, let’s talk about delay modeling

## Slide 7: Application to Digital Integrated Circuits (ICs)
When we perform a sequence of computations using a digital circuit, we switch the input voltages between logic 0 (e.g. 0 Volts) and logic 1 (e.g. 5 Volts).
The output of the digital circuit changes between logic 0 and logic 1 as computations are performed.

## Slide 8: Digital Signals
Every node in a real circuit has capacitance; it’s the charging of these capacitances that limits circuit performance (speed)
We compute with pulses.
We send beautiful pulses in:
But we receive lousy-looking pulses at the output:
Capacitor charging effects are responsible!
time
voltage
time
voltage

## Slide 9: Circuit Model for a Logic Gate
As we’ll discuss in a couple of weeks, electronic building blocks referred to as “logic gates” are used to implement logical functions (NAND, NOR, NOT) in digital ICs
  Any logical function can be implemented using these gates.
A logic gate can be modeled as a simple RC circuit:
+
Vout
–
R
Vin(t)
+

C
switches between “low” (logic 0)
and “high” (logic 1) voltage states

## Slide 10: Logic Level Transitions
Transition from “0” to “1”
(capacitor charging)
time
Vout
0
Vhigh
RC
0.63Vhigh
Vout
Vhigh
time
RC
0.37Vhigh
Transition from “1” to “0”
(capacitor discharging)
(Vhigh is the logic 1 voltage level)
0

## Slide 11: Sequential Switching
What if we step up the input,
wait for the output to respond,
then bring the input back down?
time
Vin
0
0
time
Vin
0
0
Vout
time
Vin
0
0
Vout

## Slide 12: Pulse Distortion
The input voltage pulse width must be long enough; otherwise the output pulse doesn’t make it.
(We need to wait for the output to reach a recognizable logic level, before changing the input again.)
0
1
2
3
4
5
6
0
1
2
3
4
5
Time
Vout
Pulse width = 0.1RC
0
1
2
3
4
5
6
0
1
2
3
4
5
Time
Vout
0
1
2
3
4
5
6
0
5
10
15
20
25
Time
Vout
+
Vout
–
R
Vin(t)
C
+
–
Pulse width = 10RC
Pulse width = RC

## Slide 13: Example
V
in
R
V
out
C
Suppose a voltage pulse of width
5 ms and height 4 V is applied to the
input of this circuit beginning at t = 0:
R = 2.5 kΩ
C = 1 nF
First, Vout will increase exponentially toward 4 V.
When Vin goes back down, Vout will decrease exponentially
back down to 0 V.
What is the peak value of Vout?
  The output increases for 5 ms, or 2 time constants.
   It reaches 1-e-2 or 86% of the final value.
  0.86 x 4 V = 3.44 V is the peak value
t = RC = 2.5 ms

## Slide 14
0
0.5
1
1.5
2
2.5
3
3.5
4
0
2
4
6
8
10
Vout(t) =
4-4e-t/2.5ms for 0 ≤ t ≤ 5 ms
3.44e-(t-5ms)/2.5ms for t > 5 ms
{

## Slide 15: Parasitic Capacitances
We’ll discuss these parasitic capacitances in the context of digital integrated circuits right after midterm 2

## Slide 16: AC Inputs
We’ve discussed to this point how we deal with constant and weird mathematically ideal inputs
Next we’ll discuss sinusoidal inputs or AC inputs, useful for, in order of increasing generality:
  Finding 60 Hz wall voltage response
  Finding response to inputs that can be approximated by a sum of sinusoids (e.g. square waves)
  Finding “frequency response”

## Slide 17: Solving Circuits with AC Sources
In principle, we can use the MPHS to solve the circuit below:
Will finding the homogeneous solution be difficult?

## Slide 18: Solving Circuits with AC Sources
Will finding the particular solution be difficult?

## Slide 19: Solving Circuits with AC Sources
Will finding the particular solution be difficult?

## Slide 20: Phasors
Solving simple resistive circuits
  Hard way (kitchen sink method)
  Easy way (node voltage)
Op-amp circuits
  Hard way (taking limits as )
  Easy way (summing point constraint)
    Requires negative feedback, which can be hard to identify
Circuits with memory
  Hard way (solving ODE)
  Easy way (intuitive method)
    Requires DC sources
  Next will come an easy method for AC sources

## Slide 21: Two Paths
Particular Solution Connector Route
Trigonometry
Hell
Solving ODEs
Using Impedances and Phasors
Solution Town
MPHS Limited

## Slide 22: Basic Idea and Derivation of Impedances
Naïve way is to pick a particular solution which looks like
  Unnecessary algebra and trigonometry
Instead, we’ll just replace the source by a new source and solve this new problem
Waitttttttttttt, what?
  Ok this may seem a little weird, we’re replacing the voltage source with a new one that we just made up, and sure it is also complex valued, but just trust me.

## Slide 23: New Voltage Source Problem
Homogeneous solution is just
Pick particular solution , plug in:
Divide by

## Slide 24: New Voltage Source Problem
Divide by
Solve for
Particular solution is

## Slide 25: To Recap
AC source made it hard to find particular solution:
So we just replaced the annoying source, giving us:
This gave us the particular solution:

## Slide 26: The Inverse Superposition Trick
Our complex exponential source is actually useful
Superposition tells us that our output will just be the sum of the effect of these two sources

## Slide 27: Inverse Superposition
Superposition tells us that our output will just be the sum of the effect of these two sources
Luckily for us, all complex numbers are the sum of their real and imaginary parts
Just find real part and we’re done!

## Slide 28: Real Part of Expression
Finding the real part of the expression is easy, it just involves some old school math that you’ve probably forgotten (HW5 will have complex number exercises)
Key thing to remember is that complex numbers have two representations
  Rectangular form:
  Polar form:

## Slide 29: Real Part of Expression
What we have is basically the product of two complex numbers
Let’s convert the left one to polar form
  Rectangular form:
  Polar form:

## Slide 30: Real Part of Expression

## Slide 31: Real Part of Expression
Superposition tells us that our output will just be the sum of the effect of these two sources
Thus, particular solution (forced response) of original cosine source is just the real part

## Slide 32: Wait…. That was easier?
What we just did was mostly a derivation
Only have to do the hard math one time
  Sort of like intuitive method for DC sources
What’s the “easy way” to find a particular solution, now that we did the hard math one time?

## Slide 33: Impedance
For a complex exponential source:
Rewrite as:
Let
Looks a lot like…
voltage divider

## Slide 34: Impedance Method for Solving AC Circuits
With a little more derivation, we can unveil a very powerful technique: impedance analysis:
  Replace capacitors by
  Replace inductors by
  Replace resistors with
  Replace source(s) with constant source with same magnitude (phasor representation)
Then treat the whole thing like a resistive circuit to get “phasor” version of particular solution
Optionally, convert back into time variable

## Slide 35: Impedance Analysis
Requires sinusoidal source
Reduces any network of capacitors, inductors, and resistors into a big set of algebraic equations
  Much easier to deal with than ODEs
Only gives you the particular solution, but we usually don’t care about the homogeneous solution

## Slide 36: Impedance Analysis Example
On board

## Slide 37: Extra Slides
Impedance example to help you on HW#5