## Slide 1: EE40 Lecture 5 Josh Hug
6/30/2010

## Slide 2: General Info
Lab #2 today
HW1 grades up on bspace
Make up lab next week
  Date TBA
Discussions going back to 2 hours
HW2 still due Friday at 5 PM
  It is long, you should be half done
  Get started tonight if you haven’t started yet
  Don’t forget about the discussion board
  Don’t forget there are other human beings who are also working on this homework

## Slide 3: The Need for Dependent Sources
Suppose you build a circuit such that vo=vi/1000, to be used as a power supply
  E.g. R1=332.667Ω, R2=R3=R4=1Ω
Consider what happens when you
attach a load to the power supply,
for example, a resistor
Vin
Vout
RL

## Slide 4: Operational Amplifiers
Dependent Sources are handy
  Allows for decoupling
Only one problem:
  They don’t exist
The “Operational Amplifier” approximates an ideal voltage dependent voltage source
  Very very cool circuits
  Analog IC design is hard

## Slide 5: Most Obvious Op-Amp Circuit
e.g. A=1/1000
  We’ll ignore power supply ports for now

## Slide 6: One Problem
The “open loop gain” A is:
  Hard to reliably control during manufacturing
  Typically very large (A > 1,000,000)
  Fixed for a single device
Negative feedback helps us overcome these issues

## Slide 7: Simple Op-Amp Circuit with Negative Feedback
On the board:
b

## Slide 8: Negative Feedback Op-Amp Circuit
Assuming A is very big…

## Slide 9: Op-Amp Circuit
Output voltage is independent of load!
One op-amp fits all, just tweak your resistors!
Output is independent of A!

## Slide 10: Wait, so whoa, how did that happen?
Let’s consider what happened to :
and for large A…
Where ε represents some tiny number
b

## Slide 11: The Voodoo of Analog Circuit Design
For large A:
The “negative feedback” forces to be extremely close to
This very tiny difference between and gives us vo

## Slide 12: The Voodoo of Analog Circuit Design
For large A:
No longer focus on how op-amp drives the output, but instead on how it drives its own input!
The gain “A” disappears, since if it’s really big, the op-amp just forces
For this circuit:

## Slide 13: Consequence of Negative Feedback
This input forcing property generalizes to all circuits with “negative feedback”
Specifically, in any circuit where vo is connected back to (and not to ), we have the property that
We’ll approximate this by assuming that
  Not actually equal, otherwise the op-amp would not do anything
  However with A>1,000,000, this approximation is incredibly accurate
    Less error from this approximation than component variation, temperature variation, etc.

## Slide 14: Approach to Op-Amp Circuits
An op-amp connected in a negative-feedback configuration does the following:
  Forces
  Can approximate by
Our prior approach was to replace the op-amp by dependent source and solve
This opens up a new approach

## Slide 15: Approach to Op-Amp Circuits
If there’s only negative feedback:
  Assume
  Assume and
If there’s no feedback or positive feedback, replace the op-amp with equivalent dependent source and solve
“Summing-point constraint”

## Slide 16: Negative Feedback Amplifiers
Concept was invented on a ferry to Manhattan by Harold Stephan Black during his morning commute to Bell Labs in Manhattan in 1927, originally sketched out on a blank spot of his New York Times
The idea is bizarre, but really epic
  Completely revolutionized electronics
  9 years before patent office believed it
  and

## Slide 17: If you’re a little lost
Don’t fret, the idea is weird
At first, just keep in mind the important thing:
  An op-amp with negative feedback has the properties that
    and
Later, if you want to show that this really works, do an op-amp circuit from scratch by replacing the op-amp with a voltage source, and you’ll get the same answer

## Slide 18: Example using the Summing-Point Constraint
b

## Slide 19: Summing-Point Constraint
You don’t have to use the summing-point constraint
However, it is much faster, albeit less familiar and thus a little tricky at first

## Slide 20: Op-Amp Circuits
There are a bunch of archetypical circuits, the one we’ve studied so far is the “non-inverting amplifier”
Voltage follower
Inverting amplifier

## Slide 21: Board Problems Time
Let’s go through some problems on the board

## Slide 22: And then we were done…
We did some op-amp problems in class and then called it a day here, next slides will appear on Friday

## Slide 23: Op-Amps – How Good Are They Exactly?
Of course, Op-Amps aren’t perfect
  You can’t drive every device in the universe from one op-amp
How do we measure how good a voltage source is?
  Looking at its Thevenin equivalent
  Lower Thevenin resistance is better

## Slide 24: Measuring the Quality of a Source
If you attach a resistive load, then the output voltage is:
If you want Vout to be 99% of VTH, then:
–
+
VTH
RTH
RL
Vout
+
–
So basically, for loads which are more than 99 times the Thevenin resistance, you get >99% of the Thevenin voltage
Lower RTH is better, can handle
smaller loads

## Slide 25: Source Quality Example
Suppose you build a circuit such that vo=vi/1000, to be used as a power supply
Vin
Vout
RL
–
+
1/1000V
2/3Ω
a
b
RL=99*2/3Ω=66Ω
66Ω load gets 99% of VTH

## Slide 26: Thevenin Equivalents of Op-Amp circuits
Can look at Thevenin equivalent of an op-amp circuit at its output terminals:
Just like converting a simple resistor based voltage attenuator:
–
+
1/1000V
2/3Ω
a
–
+
VTH
RTH
vo