## Slide 1: EE40 Lecture 6 Josh Hug
7/2/2010

## Slide 2: General Info
HW2 due today at 5PM
HW3 out, due TUESDAY at 2PM
There will be an optional pre-midterm HW available Tuesday
No lecture Monday
Labs as usual on Tuesday
No lab Wednesday
Midterm next Friday in class
  12:10-1:30 [be on time!]
  No electronic devices
  One 8.5”x11” (or A4) sheet of paper
    Handwritten anything you want, both sides

## Slide 3: Op-Amps – How Good Are They Exactly?
We’ve been studying ideal op-amps
Of course, real Op-Amps aren’t perfect
  For example, you can’t drive every device in the universe from a real op-amp
How do we precisely state the quality of a voltage source?
  Look at its Thevenin equivalent
  Lower Thevenin resistance is better

## Slide 4: Example: Batteries
Real voltage sources, like batteries, have a limit to how much current they can draw
  Called “internal resistance”
  This internal resistance often varies with charge status, load attached, temperature, and more
  Just like Thevenin resistance
–
+
VTH
RTH
Vout
+
–
e.g., a car battery supplies 12 Volts, and can supply at most 200 amps, what is its internal resistance?
12V/200A=0.06Ω

## Slide 5: Measuring the Quality of a Source
If you attach a resistive load, then the output voltage is:
If you want Vout to be 99% of VTH, then:
–
+
VTH
RTH
RL
Vout
+
–
So basically, for loads which are more than 99 times the Thevenin resistance, you get >99% of the Thevenin voltage
Lower RTH is better, can handle
smaller loads

## Slide 6: Source Quality Example
Everyone’s favorite resistive power supply again, vo=vi/1000
Vin
Vout
RL
–
+
1/1000V
2/3Ω
a
b
RL=99*2/3Ω=66Ω
66Ω load gets 99% of VTH

## Slide 7: Thevenin Equivalents of Op-Amp circuits
Can find Thevenin equivalent of an op-amp circuit at its output terminals:
Just like finding Thevenin equivalent of a simple resistor based voltage attenuator at its output terminals:
–
+
1/1000V
2/3Ω
a
–
+
VTH
RTH
vo

## Slide 8: Thevenin of Inverting Amplifier
Assuming that the op-amp here is IDEAL, what’s the best way to find the Thevenin equivalent circuit?
  We’ve already derived that it’s a perfect voltage source!
–
+
VTH
RTH
vo

## Slide 9: But if you really want to…
Technically you should take limits here but we are lazy…

## Slide 10: What’s wrong?
Our op-amp model is missing something
  That’s why it’s the “ideal” op-amp model
  We’ll now introduce the “resistive” op-amp model
Ideal
Resistive Op-Amp Model

## Slide 11: Resistive Op-Amp model
Takes in to account the fact that
  Some current flows into the input terminals
  The op-amp cannot source all device in the universe (output resistance is non-zero)

## Slide 12: Output Resistance of Inverting Op-Amp
On board (using resistive model of op-amp)
Output Resistance
  Tells us how small our load can be before we start losing signal fidelity

## Slide 13: Input Resistance
Resistance at the input terminals of a device
Tells us how much current will be generated for a fixed input voltage
  Useful, for example, to find power needed to power a device (at that input)

## Slide 14: Input Resistance of Inverting Amplifier
What is the input resistance of an inverting amplifier using ideal op-amp model?
What is the input resistance of an inverting amplifier using resistive op-amp model?
(See sec 15.42 in book)

## Slide 15: Why are these quantities useful?
Input resistance tells us how much current (power) our input signal needs to provide
Output resistance says how small of a load we can drive

## Slide 16: Why are these quantities useful?
An iPod provides roughly 1V signal output with 20Ω internal resistance
Speakers might be 4Ω resistance
Connect iPod directly to such speakers
  Internal resistance dominates

## Slide 17: Why are these quantities useful?
–
+
1V
20Ω
iPod
Rs
–
+
4Ω
Speakers

## Slide 18: Bad Amplifier (Small Rs)
Very small Rs
  iPod must supply 50mW
  Output resistance is large (can’t drive speakers)
–
+
1V
20Ω
iPod
Rs
–
+
4Ω
Speakers

## Slide 19: Good Amplifier
Rs=1000, Rf=3000, A=106, Rt=1000
–
+
1V
20Ω
iPod
Rs
–
+
4Ω
Speakers
Must provide 1 mW
2.93V
0.00133Ω

## Slide 20: Op-Amp Saturation
Remember those power ports we’ve been ignoring?
They specify the maximum and minimum voltage that our op-amp can deliver
  If
    Op-Amp output is
  If ,
    Op-Amp output is
  If ,
    Op-Amp output is

## Slide 21: Op-Amp Saturation Example
,
If A=3:
Vin | Vo
-5 V | -12V
-1V | -3V
2V | 6V
1,512,312V | 12V
12V
-12V
4V
-4V

## Slide 22: Positive Feedback
On the board

## Slide 23: That’s all forOp-Ampsks
No class Monday
Enjoy weekend (doing op-amp problems)