# EE 245 / NEEM 6441: Introduction to MEMS Design

# Homework 2: Beams and Electrostatics

- Calculate the deflection of a beam under its own weight.  Assume the beam is rectangular with length L, width a, and thickness b.  Assume it is made up of a uniform material with density  and Young’s modulus E.

  - Calculate , the bending moment at position

  - Calculate , the deflection at position

  - Calculate

  - Approximate  using a lumped-parameter model (assume that all of the mass is located at the tip).  How much error does this approximation introduce?

  - How long can we make a polysilicon beam before it deflects 1 μm under its own weight?  Let .

- You would like to design a thread from which you can suspend yourself, like Spiderman.  What cross-sectional area do you need?  If the thread is round, what is its diameter?  Let .

  - You want to use silicon: .

  - You want to use spider silk.  Actual properties vary considerably, but assume .

- Your buddy at Stanford is designing a suspension for an actuator with long travel in the x-direction (a few hundred μm).  Travel in the y-direction should be constrained.  Here’s what he came up with.

  - Is this a good design?

  - If not, propose a simple improvement to this layout (no numbers required).

- Let’s analyze a gap-closing electrostatic actuator with interdigitated fingers.  We will make this actuator using a DRIE process with an aspect ratio  and a minimum feature size , in a thin film with thickness , on a wafer with thickness , in a material with a density , and apply a voltage .

    - Assume that we have somehow added a thin gap-stop layer that will prevent the actuator from shorting after it pulls in.

    - Assume that this actuator operates against a constant-force load  in the -direction.

    - Neglect fringing fields.

  - Calculate the maximum value of  that this actuator can support.

  - Calculate the ratio of  to layout area.

  - Calculate the ratio of  to the combined mass of the structure and the substrate underneath it.

  - Put some numbers into your answer for (c) ( from problem (1), you choose the rest).  Can this structure allow a microrobot to lift itself without massive gear or lever mechanisms?

  - Calculate the maximum work supplied to the load in one cycle.

  - Calculate the electrical energy input per cycle, assuming that we have hooked this structure up to a control circuit that limits the total charge stored in the actuator to twice the zero-deflection charge.

  - What is the energy efficiency?

  - Assume that top comb in the figure is anchored somehow.  Suggest at least one modification to reduce the pull-in force on the bottom comb.

# Text boxes

x

y

g

a

b

Length ,  fingers

y

x